## Slide 1: Introduction to FPGA acceleration
Marco Barbone
m.barbone19@imperial.ac.uk
Introduction to FPGA acceleration
14/04/2021

## Slide 2: About me
M.Sc. in Computer Science and Networking Scuola superiore Sant’Anna & Università di Pisa
CERN OpenLab Summer student
Research Software Engineer, Maxeler Technologies
Ph.D. Student, Custom Computing research group, Imperial College London, Supervisor Prof. Wayne Luk
Member of Imperial College CMS group
Associate Ph.D. Student, The Institute of Cancer Research, London
Software engineer, Intel

## Slide 3: What is an FPGA?
https://www.xilinx.com/content/dam/xilinx/imgs/kits/u200-hero-p.jpg https://www.intel.com/content/dam/altera-www/global/en_US/support/boards-kits/stratix10/mx_fpga/stratix10mxboardtop.jpg/_jcr_content/renditions/cq5dam.web.1920.1080.jpeg https://en.wikipedia.org/wiki/Field-programmable_gate_array
A field-programmable gate array (FPGA) is an integrated circuit designed to be configured by a customer or a designer after manufacturing – hence the term "field-programmable".

## Slide 4: Microsoft’s Project Brainwave
“Microsoft’s Project Brainwave is a deep learning platform for real-time AI inference in the cloud and on the edge. A soft Neural Processing Unit (NPU), based on a high-performance field-programmable gate array (FPGA), accelerates deep neural network (DNN) inferencing, with applications in computer vision and natural language processing. Project Brainwave is transforming computing by augmenting CPUs with an interconnected and configurable compute layer composed of programmable silicon.”
https://www.microsoft.com/en-us/research/project/project-brainwave/
https://www.microsoft.com/en-us/research/blog/microsoft-unveils-project-brainwave/

## Slide 5: Amazon EC2 F1
Amazon EC2 F1 instances use FPGAs to enable delivery of custom hardware accelerations. F1 instances are easy to program and come with everything you need to develop, simulate, debug, and compile your hardware acceleration code, including an FPGA Developer AMI and supporting hardware level development on the cloud. Using F1 instances to deploy hardware accelerations can be useful in many applications to solve complex science, engineering, and business problems that require high bandwidth, enhanced networking, and very high compute capabilities. Examples of target applications that can benefit from F1 instance acceleration are genomics, search/analytics, image and video processing, network security, electronic design automation (EDA), image and file compression and big data analytics.
https://aws.amazon.com/ec2/instance-types/f1/

## Slide 6: DNA Sequencing: DRAGEN Platform
The DRAGEN Platform enables labs of all sizes and disciplines to do more with their genomic data. The DRAGEN Platform uses highly reconfigurable field-programmable gate array technology (FPGA) to provide hardware-accelerated implementations of genomic analysis algorithms, such as BCL conversion, mapping, alignment, sorting, duplicate marking, and haplotype variant calling.
https://www.illumina.com/products/by-type/informatics-products/dragen-bio-it-platform.html

## Slide 7: Genomics DNA sequencing
The dataflow architecture for Smith-Waterman Matrix-fill and Traceback alignment stages, to perform short-read alignment on NGS data that delivers ×18 speedup over the respective Bowtie2 standalone components, while our codesigned Bowtie2 demonstrates a 35% boost in performance.
https://ieeexplore.ieee.org/document/8892144

## Slide 8: FPGAs fill the gap between software and hardware
Circuits
Electrons
Microarchitecture
Program
Machine Language
Interpreter
Circuits
Electrons
Microarchitecture
Program
Machine Language
Circuits
Electrons
Program
Microarchitecture
Interpreted program
Compiled program
FPGA implementation
Performance
Fixed
Programmable

## Slide 9: Field Programmable Gate Array
FPGA is a reconfigurable substrate
  Reconfigurable functions, interconnection of functions, input/output
FPGAs fill the gap between software and hardware
  higher throughput than software
  lower latency than software
  more flexibility than hardware
Onur Mutlu, Digital Design and Computer Architecture, Spring 2020
Not always true!

## Slide 10: Latency
FPGAs achieve lower latency than software:
  latency in the order of microseconds
  latency constant and predictable
CPUs are not suitable as thread overhead is ≈ 10 microseconds
GPUs are even worse since PCIe bus sys-call requires milliseconds
Examples:
  Ultra low latency trading
  CERN trigger system
https://www.velvetech.com/blog/fpga-in-high-frequency-trading/
https://indico.cern.ch/event/557251/contributions/2245644/attachments/1310074/2143323/thea_trg_intro_isotdaq2017.pdf

## Slide 11: Throughput

## Slide 12: Throughput
Maxeler MaxCompiler

## Slide 13: FPGA Accelerator Card
https://eu.mouser.com/
Price $8,707.34

## Slide 14: GP-GPU
https://www.nvidia.com/en-us/design-visualization/store/
5120 CUDA cores
Price $8,999

## Slide 15: CPU
https://www.amazon.com/
64 cores
Price $4,985 + RAM
FPGA: $8,707.34
64-CORE CPU: $4,985 + RAM
5120 CUDA cores GPU: $8,999

## Slide 16
FPGA have higher throughput than CPUs (and GPUs) if the workload:
  Has many branch mispredictions
  Has many cache faults
CPU: Intel(R) Core(TM) i7-8700 CPU @ 3.20GHz
L1 latency = 2 cycles
L2 latency = 15 cycles
L3 latency = 32 cycles
https://github.com/DiamonDinoia/cpp-learning/blob/master/cache-latency/cache_test.c

## Slide 17: Simulator example
void main_loop() {
while (true) {
for (x=0; x<ROW; x++) {
for(y=0;y<COL;y++){
switch (cell_to_char(PLANET[x][y])) {
case 'S':
if(UPDATE[x][y]==0 && shark_rule2(pw, x, y, k, l)==ALIVE) {
shark_rule1 (pw ,x , y, k, l);
}
break;
case 'F':
if(UPDATE[x][y]==0){
fish_rule4(pw, x, y, k, l);
fish_rule3(pw, x, y, k, l);
}
break;
}
}
}
}
}
https://github.com/DiamonDinoia/wator/

## Slide 18
int shark_rule2 (wator_t* pw, int x, int y, int *k, int* l){
int i=0;
long rand=random();
motion move[4];
if (DEATH[x][y]==pw->sd) {
DEATH[x][y]=0;
PLANET[x][y]=char_to_cell('W');
BIRTH[x][y]=0;
return DEAD;
}
if(DEATH[x][y]<pw->sd){
DEATH[x][y]++;
}
if (BIRTH[x][y]<pw->sb){
BIRTH[x][y]++;
return ALIVE;
}
if (BIRTH[x][y]==pw->sb) {
BIRTH[x][y]=0;
inizialize_motion(pw, x, y, move);
i=partialsort(move, 'W');
if(!i){
return ALIVE;
}
new_coordinate(x, y, k, l, rand%i, move);
return ALIVE;
}
return ERROR;
}
Total of 9 branches in 50 lines of code

## Slide 19: Metrics
perf record -e branch,branch-misses `./wator
[ perf record: Woken up 108 times to write data ]
[ perf record: Captured and wrote 28.441 MB perf.data (620737 samples) ]
perf report -n --symbols=main_loop

## Slide 20
316K branches
304K branch-misses

## Slide 21
https://github.com/sslotin/amh-code/blob/main/branching/plot.ipynb

## Slide 22: Workload Examples
FPGA | GPU
Sparse Matrix | Dense Matrix
Sparse Graph | Dense Graphs
Graph Neural Network | Convolutional Neural Network
Decision tree | 
(Monte-Carlo) Simulation | 
Genomics computation | 
https://ieeexplore.ieee.org/document/8685122

## Slide 23
Particle
Proton
Electron
Photon
Process a
Process b
Process c
Process n

## Slide 24: FPGA Programming

## Slide 25: FPGA Design Flow
Problem Definition
Hardware Description Language (HDL)
Verilog, VHDL
Bitstream Generation
Logic Synthesis
Placement and Routing
Programming the FPGA
Xilinx Vivado
Intel Quartus
High-level Synthesis (HLS)
Google XLS MaxCompiler
Vivado HLS
oneAPI
Place & Route
might take days!

## Slide 26
 | CPU | GPU | FPGA
Engineering time | short | medium | very long
Compilation time | short | short | very long
Debugging | easy | medium | hard
Maintainability | easy | medium | hard

## Slide 27
Avoid running Place and Route
  Simulate VHDL, Verilog using ModelSim
ModelSim is slow!
  It is possible to execute very small testbenches in a reasonable amount of time

## Slide 28: FPGA Design Flow
Problem Definition
Hardware Description Language (HDL)
Bitstream Generation
Logic Synthesis
Placement and Routing
Programming the FPGA
High-level Synthesis (HLS)

## Slide 29
https://github.com/google/xls
It generates a
X86-64
executable from
source

## Slide 30: High-level Synthesis (HLS)
Using HLS toolchains makes unit testing possible in a reasonable amount of time
It is easy to interface with a reference software implementation to compare the results
It makes FPGA programming much less cumbersome

## Slide 31: Double floating-point multiplication in Verilog
double_multiplier multiplier_39759952(
.clk(clk),
.rst(rst),
.input_a(wire_39069600),
.input_a_stb(wire_39069600_stb),
.input_a_ack(wire_39069600_ack),
.input_b(wire_39795024),
.input_b_stb(wire_39795024_stb),
.input_b_ack(wire_39795024_ack),
.output_z(wire_39795168),
.output_z_stb(wire_39795168_stb),
.output_z_ack(wire_39795168_ack));
https://github.com/dawsonjon/fpu/blob/master/double_multiplier/test_bench.v
Using a library
function!

## Slide 32
https://github.com/google/xls

## Slide 33: Scheduling
multiplier
a
b
c
adder
7 clock cycles
Delay here!

## Slide 34: FPGA Programming with HLS
 | CPU | GPU | FPGA Sim | FPGA Hw
Engineering time | short | medium | medium | medium
Compilation time | short | short | short | Very long
Debugging | easy | medium | medium | medium
Maintainability | easy | medium | medium | medium

## Slide 35: HLS
Advantages:
  simplify programming
  reduces engineering time
  Allows “rapid prototyping”
Disadvantages:
  Nowadays HLS still achieves less performance than hand-written optimized Verilog/VHDL

## Slide 36: Performance
HLS still requires significant engineering effort depending on the size of the problem
Hardware builds still take significant amount of time
What if the FPGA does not perform as hoped?
Reengineer the problem and start from scratch?
Optimize the code a build several times?

## Slide 37: Performance Modelling

## Slide 38: Software engineering
Given problem P you are tasked to solve it:
  Select the “best algorithm”
  The one with lower computational complexity?
  Linearize memory accesses
38
When using accelerators there are additional complications:
  PCIe bandwidth is limited
  The accelerator have on-die memory and on-chip memory

## Slide 39: Performance Modelling Objective
To understand the major factors that dictate performance when using compute co-processors
  Bandwidths and latencies of the various interconnects
  The capacities of different memories
  Impact of data movements
  Accelerator specific properties, e.g., for FPGA
    Hardware/arithmetic operations space
    Clock frequency
    Fine-grain tunable numeric operations and their impact
    Other custom computing approaches, e.g., compression
39
Accelerator compute capabilities
Georgi Gaydadjiev, Advanced Parallel Programming 2019-20

## Slide 40: FPGA Performance
FPGA Performance is predictable
There is no context switch, garbage collector or any background process
The bitstream will be executed the same number of clock cycles every time
The number of clock cycles needed can be computed easily
Further read: Nils Voss et al. (2021), On Predictable Reconfigurable System Design
https://doi.org/10.1145/3436995

## Slide 41: Modern Intel PC Architecture
https://www.notebookcheck.net/fileadmin/Notebooks/News/_nc3/Intel_12th_gen_alder_lake_architecture_z690_block_diagram.png

## Slide 42: Xilinx Alveo U250 Data Center Accelerator Card
42
64 GB DDR4 @600MHz
4 channels of 64-bit 16G RDIMMs
available bandwidth: 77 GB/s
or 2,400 MT/s
16x PCI-Express
Power = 225W
100 Gbit Eth
(QSFP28) x 2
54MB On-chip Memory
available at 38 TB/s
Georgi Gaydadjiev, Advanced Parallel Programming 2019-20

## Slide 43: Modern System Architecture
PCIe 3.0 (x16) | 15.75 GB/s
PCIe 4.0 (x16) | 31.51 GB/s
43
77 GB/s
100 Gbit
Ethernet
https://en.wikipedia.org/wiki/DDR4_SDRAM https://c1.neweggimages.com/ProductImageCompressAll1280/19-118-122-V19.jpg https://www.xilinx.com/products/boards-and-kits/alveo/u250.html

## Slide 44: CMS Particle Track Reconstruction Callgraph
Våge, Liv H
Bottleneck

## Slide 45
If compute bound -> optimize the algorithm, increase clock frequency
If I/O bound, find a strategy to reduce the I/O (caching, compression accelerate other portion of the code)
Repeat until theoretical limit reached

## Slide 46: Performance Model example

## Slide 47
Performance Model example

## Slide 48: Performance Model example
Setup |  | Total time (s)
DFE + NUFFT on CPU |  | 16.07058
All on CPU (C++) |  | 24.72233
All on CPU (MATLAB) |  | 65.118
CPU + NUFFT on GPU |  | 18.43535
DFE + NUFFT on GPU |  | 9.78360

## Slide 49: FPGA Design Flow (simplified)
Problem Definition
Hardware Description Language (HDL)
Bitstream Generation
Logic Synthesis
Placement and Routing
Programming the FPGA
Modelling and performance prediction
High-level Synthesis (HLS)
Final Architecture
Architecture
Benchmark

## Slide 50: Monte Carlo example

## Slide 51: Elastic scattering
A simulation of e-/e+ transport considering only elastic scattering as possible interactions described by scattering of spin-less e-/e+ on an exponentially screened Coulomb potential
Source: Kotlarchyk M. Scattering theory. Encyclopedia of Spectroscopy and Spectrometry, 1999.

## Slide 52: Monte Carlo Simulation
Many particles are simulated to achieve statistical significance
Source: Kotlarchyk M. Scattering theory. Encyclopedia of Spectroscopy and Spectrometry, 1999.
Scattered radiation
final position

## Slide 53: Workload selection
Not all workloads benefits from FPGA acceleration!
FPGA have higher throughput than CPUs (and GPUs) if the workload:
  Has many branch mispredictions
  Has many cache misses
  (optional) Embarrassingly parallel
  (optional) Independency
Monte Carlo fits all!

## Slide 54: Workload partitioning -- Decide the acceleration target
Determine the acceleration potential accounting for the major factors that dictate performance when using compute co-processors:
  Bandwidths and latencies of the various interconnects
  The capacities of different memories
  Impact of data movements
  Accelerator specific properties, e.g., for FPGA
    Hardware/arithmetic operations space
    Clock frequency
    Fine-grain tunable numeric operations and their impact
    Other custom computing approaches, e.g., compression
54
Accelerator compute capabilities
Courtesy of Georgi Gaydadjiev, Advanced Parallel Programming 2019-20

## Slide 55: Requirements
We assume that FPGA should achieve 10x speed-up (over a modern parallel CPU) to be worth the engineering-effort
The simulation of one particle requires 34.5 iterations on average
Assuming an FPGA architecture capable of computing 1 iteration per clock cycle to achieve a 10x speed-up the FGPA clock frequency should be 250Mhz
Alternatively, a parallelism > 1 at a lower clock frequency

## Slide 56: Modelling
Data requirements
Arithmetic operations
Measured
FPGA resources
limiting factor
Parallelism

## Slide 57: Resource measurements
Memory requirements for line 14-15:
sizeof(double)*longiDistNumBin + sizeof(double)*transDistNumBin

## Slide 58: Resource measurements (continued)
2 single-precision floating-point additions
2 single-precision floating-point multiplications
Check the resource table: https://www.xilinx.com/html_docs/ip_docs/pru_files/floating-point.html#virtexu
2 DSPs for addition + 3 DSPs for multiplication = 10 DSPs

## Slide 59: Model findings
Parallelism = 1
  DSP utilization = 127
  On-chip memory requirement = 10Mb
The VU9P FPGA used in this study has 6840 DSP and 345Mb on-chip memory
The architecture requires 1.86% DSPs and 3.35% on-chip memory resources
Theoretical parallelism while aiming at consuming at most 50% of the on-chip memory resources is 15
Limiting factor

## Slide 60: Resulting architecture
Particle
RNG (96bits/clk)
Particle simulator
Raw data
Aggregation
Particle
RNG (96bits/clk)
Particle simulator
Raw data
CPU
FPGA
Parallel instances

## Slide 61: Final design
Maxeler MaxCompiler

## Slide 62: Measurement results
Parallelism = 15
  DSP utilization = 1904 (27%)
  On-chip memory requirement = 300Mb (86%) (scheduling overhead)
Higher parallelism could limit the achievable clock frequency

## Slide 63: Test configurations
Hardware:
AMD Ryzen 5900x 12-cores 3.7GHz (4.8GHz) CPU
Xilinx's Alveo U200 Data Center accelerator card Xilinx VU9P FPGA
Toolchain:
MaxCompiler 2021.1
Vivado 2019.2
OpenMP

## Slide 64: Test configurations (continued)
Simulation configuration:
100M histories
6 MeV beam
Water
The FPGA clock frequency was limited to 200MHz

## Slide 65: Performance measurements
The FPGA accelerated version is:
110x faster than multi-core implementation (12-cores)
10x cost-equivalent speedup
The theoretical 128x does not account for overhead and CPU data aggregation
Using MaxCompiler the architecture achieves 300Mhz resulting in a
160x speedup

## Slide 66: Performance measurements
Chart: 
| Parallel | FPGA
Speedup | 1 | 113.1378

## Slide 67: Summary
FPGAs are becoming widely used in industry as accelerators for suitable challenges (ultra low latency inference, graph processing and genomics)
Recent toolchain developments making programming FPGAs more accessible
FPGAs can be multiple orders of magnitude faster than CPUs and GPUs when accelerating suitable workloads
Following a formal methodology and HLS toolchains high performance can be achieved with no previous FPGA programming experience

## Slide 68: Current projects

## Slide 69: Training AI on FPGA
Collaboration between:
  Imperial College London
  University of Pisa (Avalanche developers)
  CERN (hls4ml)
Part 1: select training algorithms suitable for FPGA
Part 2: integrate the training algorithm into hls4ml

## Slide 70: Continual AI on FPGA
Collaboration between:
  Imperial College London
  University of Pisa (Avalanche developers)
  CERN (hls4ml)
Part 1: investigate FPGA-compatible continual AI strategies
Part 2: FPGA design and implementation

## Slide 71: Neutrino Energy Reconstruction with GNN at Hyper-K
Collaboration between:
  Imperial College London
  The Hyper-Kamiokande experiment
Pure Machine Learning project that requires to design and optimize a GNN

## Slide 72: Contact us
If interested send an email to:
m.barbone19@imperial.ac.uk
subject: [Info-Application] [Project name]
Details such as: start-end date
If you will be working full-time or part-time during that period
Logistics with your home institution will be left to you! (e.g., finding a home institution supervisor
Attach your CV!

## Slide 73: FPGA Architecture (Backup)
Look-Up Tables (LUT) and Switches
Andre DeHon, “The Density Advantage of Configurable Computing”, Computer, 2000

## Slide 74
3-bit input LUT (3-LUT)
input (3 bits)
output (1 bit)
Data Input
Multiplexer (Mux): Selects one of the data input corresponding to select input
3
Select Input
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
3-LUT can implement any 3-bit input function
Onur Mutlu, Digital Design and Computer Architecture, Spring 2020

## Slide 75: DSP block
https://www.xilinx.com/support/documentation/user_guides/ug579-ultrascale-dsp.pdf

## Slide 76: Example
Maxeler MaxCompiler

## Slide 78
Rejection sampling
Inversion method
F(u) {
  do { generate (U) }
  while ( U > threshold);
  Return U;
}
At compile time invert F
F(u) {
  u = generate (U);
  Return
}
No while loop!

## Slide 79
Rejection sampling
Inversion method
RNG
Sample
Stall
Stall
RNG
Value
Inverse
Source: https://www.doc.ic.ac.uk/~wl/papers/iee07dt.pdf
Inversion method is the most efficient on FPGA (Thomas2006)