Muon Cooling for a Neutrino Factory and Muon Collider
Muon Front End Status
Chris Rogers,
Accelerator Science and Technology Centre (ASTeC),
Rutherford Appleton Laboratory

---
Overview
- Revised baseline
  - Shorter bunch train
- Verification and Quality Assurance
  - Physics model verification
  - Lattice verification
- Alternate Lattice Development
  - Bucked coil lattice
  - Magnetically insulated lattice
- Transmission losses and mitigation
  - Proton absorber
  - Chicane
- Future Plans

---
Baseline Front End
- Adiabatic B-field taper from Hg target to longitudinal drift
- Drift in ~1.5 T, ~100 m solenoid
- Adiabatically bring on RF voltage to bunch beam
- Phase rotation using variable frequencies
  - High energy front sees -ve E-field
  - Low energy tail sees +ve E-field
  - End up with smaller energy spread
- Ionisation Cooling
  - Try to reduce transverse beam size
  - Prototyped by MICE
- Results in a beam suitable for acceleration
Taper
Bunch
Rotate
Drift
Cool

---
High Energy Muon Facilities
New Baseline D. Neuffer
`
- Re-baseline to make shorter front end
  - Shorter bunch train
    - So perhaps easier kickers/decay ring
  - Less hardware
    - So front end is cheaper
  - Muon capture similar performance
Old:
New:
Taper
Bunch
51 m
Rotate
52 m
Drift 110 m
Cool up to 100 m
Taper
Bunch
32 m
Rotate
45 m
Drift 80 m
Cool 90 m

---
Code Verification
- Mostly automated monitoring of physics process model
  - Talks to ICOOL, G4Beamline, G4MICE, ...
- Need to add field model monitoring

---
Lattice Verification – P. Snopok
- Performance comparison
  - G4Beamline
  - ICOOL
- Very good match between G4BL and ICOOL
- Less good match for secondary particles
  - Expect GEANT4 physics models are better in this case

---
Bucked lattice – A. Alekou
Baseline
- Reduced magnetic field on RF cavities
  - May enable higher accelerating voltage
- Slightly higher equilibrium emittance
Bucked

---
Insulated lattice – D. Stratakis
- Magnetically insulated lattice
  - B-field perpendicular to E-field
  - Suppress break down on RF cavities
- Similar performance to old FS2A lattice
  - Some technical issues still in design

---
Beam power
- Beam power
  - Rather high
  - Obviously significant losses
  - Calculated using kinetic energy of beam
  - Normalised to 4 MW/8 GeV
- Beam power of secondaries is rather high

---
Heat deposition
- Top plot is change in beam power/length
  - Includes decay losses
  - Includes loss/gain from RF acceleration
  - Includes loss in windows/LiH
- Bottom plot is power deposited/length
  - Transmission losses excluding decays
- Verified in G4Beamline (P Snopok)
- For comparison
  - ISIS rule of thumb is < 1 W/m proton loss
    - So that the machine doesn't become radioactive => remote handling
    - 2-3 orders of magnitude too high
    - What about leptons?
  - Worry about quench limit on superconducting equipment
    - ~kW per magnet
    - Cost of cryogenic cooling

---
Mitigation Strategy
proton
absorber +
collimators
p-, m-
p+, m+
- Clearly heat deposition is significant
- Three issues:
  - Activation of the linac
  - Heat load on superconductors
  - Radiation damage (to e.g. superconductors)
- These losses are 2-3 orders of magnitude too high
- Try:
  - Proton absorber for low momentum protons
    - Protons stop quicker than pions/muons in material
  - Chicane for high momentum particles
  - Transverse collimation
    - Take out particles with large transverse amplitude at a convenient point away from sensitive hardware
bend
out
bend
back
dump
p, p-, m-
p+, m+
bend
out
field
taper
target
station
dump

---
Momentum Distribution of protons
- Proton momentum distribution of beam at target
  - Most protons have p < 1 GeV/c
  - Nb no protons with p < 0.2 GeV/c (MARS cut-off?)
- Proton power distribution of beam at target
  - Plot is power in beam vs minimum cut-off
  - e.g. Pcut = 1 GeV/c => power of all protons with 1 < p < 7 GeV/c
    - Upper cut is to get rid of primaries
  - About 50% of proton power is in protons with p > 1 GeV/c

---
Proton absorber
- Try carbon proton absorber
  - Cylindrical plug in beam line
  - 10 cm Carbon removes protons below ~ 600 MeV/c momentum
  - Takes out about 30-40% of proton beam power
  - Slight degradation in front end performance
  - May prefer Beryllium
- Removes protons with p <~ 600 MeV/c

---
Test particles
- Aim is to get clean cut on particles in chicane
  - Dispersion function 0 up to maximum momentum
  - Dispersion function large after maximum momentum
- Look at test particle amplitude vs momentum after chicane
  - Test particles initially on-axis
  - Measure how far from the axis they are
    - In x-px-y-py phase space
    - Normalised to matched beam ellipse

---
Muon Chicane - Preliminary
- Bent solenoid chicane
  - One chicane for both signs
  - Optics still under optimisation
  - Removes protons with p > 600-700 MeV/c
- Beam dumps need work
  - How does beam get out of solenoids?
- Optimisation continues
m+
m-
No chicane
Chicane

---
Future Plans
- Await results from Fermilab Muon Test Area
  - Give better idea of maximum peak field we can achieve in RF cavities
- Further work needed on transmission loss mitigation
  - Improved optics design for chicane
  - Investigate Beryllium proton absorber
  - Transverse collimator design
  - Figure out geometry for practical beam dumps
  - Integrate with full lattice
- Alignment and tolerance study
  => Instrumentation
- Engineering input becoming more important
  - Magnet design
  - Ionisation cooling absorber design
  - RF cavity design
  - Beam dump, proton absorber and collimator engineering design
  - Can no longer use MICE designs and wave hands