## Slide 1: Using GPUs with HTCondor 9.8+/10.x
European HTCondor Workshop 2022
Todd Tannenbaum / John (TJ) Knoeller

## Slide 2: How things have worked for a long time…

## Slide 3: GPU Support in HTCSS EP
This one line in your config file
use feature:gpus
tells the EP to:
  Discover GPU devices in the server
  Advertise their capabilities in slot ads
  Assign individual GPU devices to slots
    Static slots: assign evenly across all slots
    Partitionable slots: assign GPUs to dslots as per job request
  Tell CUDA or OpenCL libs about the GPUs assigned in the slot
  Monitor utilization of GPU cores and GPU memory

## Slide 4: Job Submit File
executable = my_cuda_job
request_cpus = 1
request_memory = 1GB request_gpus = 1 queue

## Slide 5: What is new with GPUs in HTCSS 10 ?

## Slide 6: Let's say your server has multiple GPU devices…

## Slide 7: Failures with Multi-GPU servers
GPU0
GPU1
GPU2

## Slide 8: Failures with Multi-GPU servers
GPU0
GPU1
GPU2

## Slide 9: Failures with Multi-GPU servers
GPU0
GPU1

## Slide 10: Failures with Multi-GPU servers
GPU0
GPU2
"Index" identifiers are not stable!
GPU1

## Slide 11: Failures with Multi-GPU servers
GPU-c4a646d7
…but "uuid" identifiers are stable,
and thus used by default in HTCSS 10
GPU-8AC64982
GPU-BB7246CC

## Slide 12: Take a GPU offline
Take a GPU offline with a reconfig of the Startd
Offline GPU ids are not assigned to new dynamic slots
Offline GPUs are not in AvailableGPUs list
Requires stable GPU ids to work properly
  Stable GPU ids are the default (-short-uuid)
  Works with GPU indexes only if the GPU is not hung
Notes: If a GPU is producing bad results, sometimes it is desireable to disable it for use by HTCondor without restarting the whole machine.
This can be done by adding it to the configuration as an OFFLINE GPU. This works well when you are using stable GPU ids such as
uuids and short uuids. It can work with GPU indexes as well, but only if the cuda runtime has not reassigned indexes since
condor_gpu_discovery was first run.

## Slide 13: Challenges with heterogeneous Multi-GPU servers
Titan RTX
Tesla V100
Titan RTX

## Slide 14: Challenges with heterogeneous Multi-GPU servers
TITAN RTX
TESLA V100
TITAN RTX
Should pslot have DeviceName="TITAN RTX" or DeviceName="TESLA V100" ?

## Slide 15: Nested ClassAd attributes to the rescue in HTCSS 9.8+
GPUs = 1
TotalGPUs = 3
AssignedGPUs= { GPU_c4a646d7 GPU_6a96bd13 }
AvailableGPUs = { GPU_c4a646d7 }
GPU_6a96bd13 = [
Capability=7.5;
Id = "GPU_6a96bd13";
DeviceName="TITAN RTX";
DeviceUuid="6a96bd13-70bc-6494-6d62-1b77a9a7f29f";
GlobalMemoryMb=24220; ]
GPU_c4a646d7 = [
Capability=7.0;
DeviceName="TESLA V100"; ...
Notes: This is the partitionable slot ad, when one of the GPUs is assigned to a child slot. The important thing to notice here is AssignedGPUs shows 2 gpu ids, but Available GPUs just has 1 GPU property set.
AssignedGPUs is the GPUs permanently assigned to the slot and its children. AvailableGPUs is the properties of the GPUs that are available for matchmaking.

## Slide 16: Job Submit File
executable = my_cuda_job
request_cpus = 1
request_memory = 1GB request_gpus = 1
require_gpus = DeviceName == "TITAN RTX" queue

## Slide 17: Job Submit File
executable = my_cuda_job
request_cpus = 1
request_memory = 1GB request_gpus = 1
require_gpus = Capability > 7.0 queue

## Slide 18: Targeted binding of GPUs to slots
New multi-line STARTD slot resource configuration
  SLOT_TYPE_1 @=slot1 CPUs = 50% Memory = 50% GPUs = 2 : Capability > 7.0 @slot1
Evaluated against each GPU property ad
  Affects binding of GPUs into static slots and p-slots

## Slide 19: NVIDIA Multi-Instance GPU (MIG) Support
Good News: Some NVIDIA GPUs have MIG capability
  Split a GPU device into up to 7 MIGs
  Each MIG behaves like a smaller GPU device
  The GPU can no longer be used directly
  (MIGs are usually heterogenous, GlobalMemoryMb will vary)
Bad News: NVIDIA changed APIs drastically
Good News: HTCSS now discovers the MIGs
  (And hides the MIG parent GPU)
Bad News: GPU Utilization monitoring not yet supported for MIG devices
Notes: Very recent GPUs from NVIDIA such as the A100 can be statically partitioned into up to 7 smaller virtual GPU devices that NVIDIA calls MIGs.
This partitioning has to be re-done each time the machine is started and before the Startd runs condor_gpu_discovery.
But with these conditions, MIGs work with HTCondor.
There are some qualfications about using MIGs that we will go into in a later slide

## Slide 20: NVIDIA Multi-Instance GPU (MIG) Support, cont
Admin needs to split-up the MIG GPU however they wish before starting the EP
Future work: HTCSS dynamically splits up MIGs ?
Notes: Very recent GPUs from NVIDIA such as the A100 can be statically partitioned into up to 7 smaller virtual GPU devices that NVIDIA calls MIGs.
This partitioning has to be re-done each time the machine is started and before the Startd runs condor_gpu_discovery.
But with these conditions, MIGs work with HTCondor.
There are some qualfications about using MIGs that we will go into in a later slide

## Slide 21: MIGs
Lots of caveats from NVIDIA
  Big differences between driver 460 and 470
  Only one MIG can be used per-process
  Use long uuid name, (Short uuid name not supported)
  CUDA device enumeration does not see them
  GPU forgets MIGs on reboot
MIGs "just work" in HTCondor 9.0
  Must be set up before the Startd runs discovery
    Restart required to re-run discovery
Notes: There are many caveats to using MIGs with the CUDA runtime that we expect to be relaxed or removed in the future.
CUDA_VISIBLE_DEVICES can only list a single MIG device, but the Startd does not know this and will not prevent a job from requesting multiple MIGs
Short uuids do not work to identify the MIG devices, only the full uuids work.
If *any* GPU on a machine has MIG devices, normal emumeration of GPUs by condor_gpu_discovery can no longer see the non-MIG GPUs.
There is an alternate library and API (nvml) that must be used when MIG devices are present, and this API does not provide as many device properties.
It is possible to put a MIG capable GPU in MIG mode, but not define any MIG partitions. A GPU in this configuration is unusable.

## Slide 22: Speaking of future work… Multiple Jobs Sharing a GPU

## Slide 23: What you can do TODAY: Multiple jobs sharing a GPU (the unsafe way)
New arguments to condor_gpu_discovery in 9.0
  -repeat : duplicate GPU ids
  -divide : duplicate GPU ids and reduce advertised GPU memory
  Add to GPU_DISCOVERY_EXTRA config knob
  GPU_DISCOVERY_EXTRA = -divide 2
Notes: With that explanation behind us, you can see how sharing a GPU becomes a simple matter of having the same GPU id show up more than once in DetectedGPUs.
This works because (in HTCondor 8.8 and later) GPU ids are not required to be unique.
In HTCondor 8.8 you must do this by writing a wrapper script around condor_gpu_dscovery and modifying the DetectedGPUs attribute.
You may also want to modify the GlobalMemoryMb attribute(s).
Beginning with HTCondor 9.0 condor_gpu_discovery will repeat GPU ids when passed the –repeat or –divide argument.
If –divide is used, then the memory property attribute will also be modified.

## Slide 24: Upcoming - safer GPU sharing
New slot splitting protocol
  Schedd will request that partitionable slot be split into N slots that share the same GPU
  Schedd will do this only for jobsets that request GPU sharing
    Share GPUs only with your own jobs

## Slide 25
This work is supported by NSF under Cooperative Agreement OAC-2030508 as part of the PATh Project. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the NSF.