## Slide 1
Acknowledgements:
F. Batsch, H. Damerau , David Amorim , Kyriacos Skoufaris , Fulvio Boattini,
Max Topp-Mugglestone, I. Karpov, Elias Metral, Scott Berg,
Luca Bottura, Alexej Grudiev, Daniel Schulte
Reports of the working groups: Acceleration and collider
by Antoine Chance (CEA Paris-Saclay)
and Christian Carli (CERN)

## Slide 2: High Energy Complex working group
Acceleration to high energy (after rec. linacs)
  Pulsed synchrotrons challenging
    Very fast magnet ramping (power, eddy ..)
    Orbit variations with fixed SC and cycled NC magnets
    Circumference variations and longitudinal dynamics
  FFAs (vertical) an alternative
Collider ring
  Very challenging conditions for lattice
    Small b*, short bunches, large energy spread..
    High energy, neutrino radiation
    Chromatic effects and compensation …..
  Iterations with WGs on magnet design, beam loss, MDI, radiation protection ..
Dedicated sessions on Wednesday
and Thursday afternoon
Contributions to and interaction with many WGs
(MDI, magnets, beam loss, RP, RF ..)
Wednesday 14:00
6/R-012
Thursday 14:00
40/S2-D01

## Slide 3: Rapid Cycling Synchrotron
norm. cond. RCS
hybrid RCS 1.5 TeV
hybrid RCS
Both in the same tunnel
hybrid RCS 5 TeV
Chain of rapid cycling synchrotrons, counter-rotating m+/m- beams  63 GeV  0.31 TeV  0.75 TeV  1.5 TeV ( 5 TeV)
Hybrid RCSs have intersecting normal conducting (NC) and superconducting (SC) magnets
The studies presented aim to determine the RF (cavity) and lattice parameter (number of RF stations, momentum compaction factor,…)
Courtesy: Heiko Damerau
Detailed parameter table: https://cernbox.cern.ch/index.php/s/I9VpITncUeCBtiz

## Slide 4: RCS2: Case SC first with 5 dipoles and 208 cells
That is possible to get a path length variation of about 1 cm. However, the cell is very compact.
Although the energy ramp is quasi-linear, the synchronous phase varies by more than 10 degrees.
The voltage is assumed to be constant in the cavity.

## Slide 5: Magnet cycling
Multi-step optimization: Bref calculation, Circuit parameters, optimization of free oscillation, Active Filter contribution
Promising steps towards an analytic model of the vFFA have been made!
Courtesy: Fulvio Boattini

## Slide 6
6
Results for each RCS and with and without induced voltage / intensity effects:
Similar behaviour for RCS 2&3, no change for nRF > 48
Lower Qs allows for slightly smaller number in RCS 2&3,
e.g. nRF = 24 and 16
Influence of small nRF on two bunches to be investigated
6
Synchrotron tune and number of RF stations
(TESLA-like cavities)
RCS1, De (std)
RCS2, De (std)
RCS3, De (std)
nRF=24
nRF=16
nRF=32
Courtesy: Fabian Batsch

## Slide 7
14 October 2022
7
Beam transport though the RCS chain:
Evolution of bunch parameter
7
How do the bunch length, energy spread and emittance evolve when propagating the bunch through not one, but all RCS?
All RCS with nRF=48
Unmatched bunch remains main problem, emittance growth 90%
F. Batsch

## Slide 8: Mode stability prediction Transverse stability in RCS 1
  Stability threshold (single turn) Rs/Q ~ 100 [MΩ/m] / f2 [GHz2]
  This HOM at 2.45 GHz:
    [Rs/Q]threshold = 100/2.452 = 16.7MΩ/m
    [Rs/Q]total = 2.1 MΩ/m
HOM below the predicted stability limit by factor 8
Courtesy: David Amorim

## Slide 9: Alternatives to RCS vFFA
Development of analytic tools to modelize the 3D orbit
Promising steps towards an analytic model of the vFFA have been made!
Courtesy: Max Topp-Mugglestone

## Slide 10: 10 TeV collider
Courtesy: Kyriacos Skoufaris

## Slide 11: Collider: a tremendous chromatic correction scheme
Courtesy: Kyriacos Skoufaris

## Slide 12: Neutrino Radiation for a realistic Collider
Courtesy: Christian Carli
Wobbling: first proposals to generate some parabola pieces with a cycled vertical dipoles.

## Slide 13: Transverse impedances for & 3 TeV and 10 TeV collider
Courtesy: David Amorim

## Slide 14: Conclusion Pulsed synchrotron and FFA
The design of resistive magnets has begun. Shaping correctly the reference field ramp is essential to optimize the maximum power to be delivered. Optimization with RF has started.
First longitudinal studies show that 1.3 GHz TESLA Cavity is suited for muon acceleration in the RCSs. Short-range wakefields and beam loading are huge but seem manageable. A large number of RF stations is needed to ensure a sufficiently low synchrotron tune between the stations. If done, beam is transported with % level emittance growth in each RCS.
A parametric model is under development to make easier the coupling between magnet, RF, optics, stability constraints.
One Low losses SRF cavity was investigated from transverse stability for RCS1. The most critical HOM remains below the stability threshold with a margin factor ~8 for this single mode.
Analytic vFFA modelling is close to a solution under a set of approximations and to be applied to a muon ring resign.

## Slide 15: Conclusion Collider
Extensive use of combined function magnets with independent control of their multipolar components in order to evenly distribute the muon decay products and to minimize the collider length.
Different designs for the Final Focusing scheme that aim to mitigate the BIB. The BIB reduction due to dipolar components was so far found lower than expected, but the study is still ongoing.
The Chromatic Correction scheme has been designed. Arc design with Flexible Momentum Compaction cells that control the momentum compaction factor, the linear chromaticity and the 2π closing of the trajectory with independent knobs.
Dose generated at earth surface due to showers generated by nu interactions is a serious issue.
Time-dependent vertical deformation of the whole arc proposed as mitigation measure.
With a 100-turn damper transverse beam stability would require at least 25 mm radius with Tungsten at 300 K for the 10 TeV collider.

## Slide 16: Next steps
A lot of parameters for the RCS need to be optimized:
  Decay rate: RF voltage and ramp rates better distributed between the different rings
  Synchronous phase ⇔ higher voltage ⇔ emittance budget.
  Beam optics: dedicated arc cells integrating RF cavities.
  Magnet’s ramping functions to reduce power consumption.
  Better Matching between the different rings to reduce emittance growth.
The transverse stability study will continue (more detailed cavity models, same studies for other RCS, adding counter-rotating beam, impact of chromaticity correction and needs for mitigation).
Completion of vFFA analytic tools to go to a design of vFFA ring.
Magnet design for FETS-vFFA ring has been carried out. Prototype magnet due for construction over the next few months.

## Slide 17: Next steps Collider
The next steps for the collider is to refine the location of the straight sections, the Final Focusing design for a better control of the Beam Induced Background and the Chromatic Correction scheme.
Estimation of key parameters as well their tolerances for the: minimum aperture, maximum allowed magnetic fields, maximum beta values out of the IR, chromaticity values, etc…
Feasibility of the Time-dependent vertical deformation to be studied.
Collective effects: Include additional instability mitigation measures to help reach tighter chamber radii (positive chromaticity, Landau damping with octupoles).Simulate a more detailed vacuum chamber when available. Include the second, counter-rotating, beam effects. Investigate other potential shielding materials
Collider and RCS relie on a close interaction between WP2/5/6/7.
A lot of technical issues are addressed but still a lot of work before saying that such a complex is feasible but that is why MuC is motivating ;-).

## Slide 18
Thank you
for your attention

## Slide 19
Backup

## Slide 20: MuCol Milestones

## Slide 21: Parameters and tools: RF – The TESLA cavity
Studies are based on the 1.3 GHz Tesla cavity (design report: Phys. Rev. ST Accel. Beams 3, 092001, 2000)
 see talk by A. Yamamoto
Relevant beam parameter
  Bunch population 2.54x1012, eL=0.01 eVs  large intensity effects
  Bunch current 20.4 / 18.8 / 10.0 mA  2x430 kW per cavity
  700 / 374 / 532 cavities in ring, distributed over nRF RF stations
  Synchronous phase 45° (above transition: gtr = 20.41, 600 < g < 14200)
TESLA Cavity parameter (9 cells, L=1.06 m):
  fRF = 1.3 GHz  harmonic number h = 25957 to 46367
  R/Q = 518 W, total Rs = 306 GW
  Gradient 30 MV/m
  QL = 2.2e6 (for beam loading compensation with f = 320 Hz)
From design report
From design report
(with 30 MV/m accelerating gradient)
Courtesy: Fabian Batsch

## Slide 22: Parameters and tools: General parameter
Detailed parameter table: https://cernbox.cern.ch/index.php/s/I9VpITncUeCBtiz
 | RCS1314 GeV | RCS2750 GeV | RCS31.5 TeV
Circumference, 2pR [m] | 5990 | 5590 | 10700
Energy factor, Eej/Einj | 5.0 | 2.4 | 2.0
Repetition rate, frep [Hz] | 5 (asym.) | 5 (asym.) | 5 (asym.)
Number of bunches | 1m+, 1m- | 1m+, 1m- | 1m+, 1m-
Bunch population | 2.5x1012 | 2.3x1012 | 2.2x1012
Survival rate per ring | 90% | 90% | 90%
Acceleration time [ms] | 0.34 | 1.04 | 2.37
Number of turns | 17 | 55 | 66
Energy gain per turn, DE [GeV] | 14.8 | 7.9 | 11.4
Acc. gradient for survival [MV/m] | 2.4 | 1.3 | 1.1
Acc. field in RF cavity [MV/m] | 30 | 30 | 30
Max. RF voltage for fs=45° [GV] | 20.9 | 11.2 | 16.1
Courtesy: Fabian Batsch