## Slide 1: Heat Load Estimation and Dry Cooling Scheme Proposal for Sigrum
Torsten Koettig, Rob van Weelderen,
with inputs from Patricia Tavares Coutinho Borges De Sousa and Aleksandra Onufrena (CERN)

## Slide 2: Content
Heat load estimation, updated
Dry cooling scheme
R&D options
Open points to address

## Slide 3: Heat loads at 4.7 K and 60 K
Parameters:
1 Dipole + 1 pair CL 2.5 kA (Dry + HTS)
2 Quadrupoles + 2 pairs CL 350 A (Dry + HTS)
Supports in G10, 30 cm, 15 cm heat intercept @ 60 K
60 K thermal shield and CL intercept
30 layer MLI @ 60 K
10 layer MLI at 4.7 K
5 W heat load on cold mass (Mikko)

## Slide 4: Heat loads at 4.7 K and 60 K
Parameters:
1 Dipole + 1 pair CL 2.5 kA (Dry + HTS)
2 Quadrupoles + 2 pairs CL 350 A (Dry + HTS)
Supports in G10, 30 cm, 15 cm heat intercept @ 60 K
60 K thermal shield and CL intercept
30 layer MLI @ 60 K
10 layer MLI at 4.7 K
5 W heat load on cold mass (Mikko)

## Slide 5: Heat loads at 4.7 K and 60 K
Parameters:
One common cryostat
3 Dipoles + 1 pair CL 2.5 kA (Dry + HTS)
3 Quadrupoles + 3 pairs CL 350 A (Dry + HTS)
Supports in G10, 30 cm, 15 cm heat intercept @ 60 K
60 K thermal shield and CL intercept
30 layer MLI @ 60 K
10 layer MLI at 4.7 K
5 W heat load on cold mass per dipole (Mikko)

## Slide 6: Heat loads at 4.7 K and 60 K
Parameters:
One common cryostat
3 Dipoles + 1 pair CL 2.5 kA (Dry + HTS)
3 Quadrupoles + 3 pairs CL 350 A (Dry + HTS)
Supports in G10, 30 cm, 15 cm heat intercept @ 60 K
60 K thermal shield and CL intercept
30 layer MLI @ 60 K
10 layer MLI at 4.7 K
5 W heat load on cold mass per dipole (Mikko)

## Slide 7: Cooling comparison
Summary |  |  |  | 2 stage |  |  |  |  |  |  | He refrigerator |  |  |  | 
 |  |  |  | PT 425 |  |  |  |  |  |  |  |  |  |  | 
Cryostats | 1 | 2 to 4 | Total Q | # |  | Cost | Q_el in kW | kCHF/a |  |  | Total Q | Green 2008 | 2022 | Q_el in kW | kCHF/a
 | Q in W | Q in W | in W |  |  | kCHF |  |  |  |  | in W | kCHF | kCHF |  | 
T= 4.7 K | 9.008 | 24.18 | 33.2 | 13 |  | 845 | 143 | 125 |  |  | 33.188 | 304.2 | 760.6 |  | 
T= 60 K | 322.78 | 439.52 | 762.3 | 9 |  |  |  |  |  |  | 50 | 393.8 | 984.6 |  | 
 |  |  |  |  |  |  |  |  |  |  | 100 | 609.5 | 1523.7 | 50 | 65.7
Two-stage Pulse Tube Refrigerators vs. He cryoplant
It needs:
a dedicated cryocooler- satellite box (incl. 2 add. PTR) + distribution system
electrical insulators for the CL!

## Slide 8: Cooling comparison
Two-stage GM Cryocooler vs. He cryoplant
Sumitomo GM RDE-418D4 4K Cryocooler
Summary |  |  |  | 2 stage |  |  |  |  |  |  | He refrigerator |  |  |  | 
 |  |  |  | PT 425 |  |  |  |  |  |  |  |  |  |  | 
Cryostats | 1 | 2 to 4 | Total Q | # |  | Cost | Q_el in kW | kCHF/a |  |  | Total Q | Green 2008 | 2022 | Q_el in kW | kCHF/a
 | Q in W | Q in W | in W |  |  | kCHF |  |  |  |  | in W | kCHF | kCHF |  | 
T= 4.7 K | 9.008 | 24.18 | 33.2 | 19.0 |  | 855 | 152.0 | 133 |  |  | 33.188 | 304.2 | 760.6 |  | 
T= 60 K | 322.78 | 439.52 | 762.3 | 16 |  |  |  |  |  |  | 50 | 393.8 | 984.6 |  | 
 |  |  |  |  |  |  |  |  |  |  | 100 | 609.5 | 1523.7 | 50 | 65.7
Is there an option to reduce the number of PTC?

## Slide 9: Remote cooling circuit R&D at the Cryolab at CERN
PhD thesis of A. Onufrena at the University of Twente

## Slide 10: Remote cooling arrangements
Compressor
Pump
Cooling interface
1 bar
(LP)
4-5 bar
(HP)
~1 bar
Very effective heat exchangers !!!
Compressor
Pump
Cooling interface
1 bar
(LP)
4-5 bar
(HP)
~1 bar
T~ 4.5 K
T~ 4.5 K
4.5 K
T~ 55 K
8 K
T~ 55 K
8 K
T~ 55 K
Parameters:
Boost cooling performance
Separation of PTC and CIF
SC/Sub-cooled Liquid
PTC orientation OK, if
Separate cryocooler box
T gradients in single phase flow
Pump
Compressor
Cooling interface
1 bar
(LP)
4-5 bar
(HP)
~4-5 bar
T~ 4.3 => 4.7 K

## Slide 11: Critical components: compact CFHEXs
Main design features:
Concentric tube-in-tube CFHEX with stacked copper mesh as fins
Large “wetted” area + compactness
High radial & low axial thermal conductivity (due to wire-wire interfaces)
Scalable, demonstrates an ease of manufacturing, and adaptable to many applications
Great candidate for a high-effectiveness compact heat exchanger!
Hot flow
Cold flow
Cold flow
0.1 m
Cryocooler envelope
Inlet flow:
, ,
Outlet flow:
, ,
Remote envelope
CFHEX 2
CFHEX 1
CFHEX 3
Radiation shields
Experimental
cooling interface (CIF)
2-stage GM cryocooler
Joule-Thomson expansion
1st stage
2nd
stage

## Slide 12: Critical components: compact CFHEXs
[1] A. Onufrena, et al. “Cryogenic Performance of a Compact High-Effectiveness Mesh-Based Counter-Flow Heat Exchanger”, Cryogenics, 2022
Inner tube-mesh interface
Axial conduction
CFHEX numerical model was built and correlated with experimental data [1]
Test results have shown that inner tube-to-mesh interface conductance and axial conduction have a strong influence on effectiveness
Novel CFHEX design proposed (patenting in progress)

## Slide 13: Critical components: compact CFHEXs
NTU=18.6 ( %)
NTU = 55 ( %)
Very high experimental performance achieved with the novel mesh-based CFHEX design
NTU >124 ( %)

## Slide 14: System performance results
Cryocooler envelope
3.7 bar
1.3 bar
Remote envelope
CFHEX 2
CFHEX 1
CFHEX 3
Boost: 0.4 W at 4.6 K at 0.7 m distance from the 2nd stage (demonstrated already) !
2-stage
GM
cryocooler
10 K
0.4 W @ 4.6 K
2-stage
GM
cryocooler
0.4 W at 8.8 K at the 2nd stage
Introduction of a remote cooling loop with 100 mg/s
2-stage
GM
cryocooler
50 K
10 K
1.3 W @ 4.5 K
5.3 bar
1.0 bar
Cryocooler envelope
Remote envelope
CFHEX 2
CFHEX 1
CFHEX 3
Boost: 1.3 W at 4.5 K at 0.7 m distance from the 2nd stage
Next step: remote cooling loop at nominal conditions
( 150 mg/s)
Experimentally demonstrated
50 K
40 K
8.8 K

## Slide 15
Applications: dry SRF cavity cooling
Test setup to study dry colling (system performance, flow in the capillary)
Dry cooling principle

## Slide 16
Application to Sigrum
Subcooled 4 bar cooling loop
Subcooled 4 bar cooling loop – high Q
3-4 x
Pushing the limits is one of our current R&D topics in the Cryolab

## Slide 17: Summary
Can we refine the heat loads?
Study of the thermal interface to the cold mass at T< 4.7 K
Thermal gradients along the cooling channel and perpendicular
Quadrupoles, heat load and more
Rotation angle of the gantry => feedthroughs, which are rotating, cold and leak-tight?
Options to cool the prototype, in LHe and then dry (incl. the cooling tube already)
Remote cooling R&D will proceed in the Cryolab