## Slide 1
R. Ballabriga on behalf of the CERN-ICCUB collaboration
EP-ESE-ME, CERN
Esplanade des particules 1
1217 Meyrin, Suisse
rafael.ballabriga@cern.ch
The FastIC project: From the FastIC ASIC to FastIC+ and FastRICH

## Slide 2: Outline
FastIC project context
Architecture
Readout
Measurements (Linearity, Energy resolution, SPTR, CTR)
Derivatives of FastIC (FastIC+, FastRICH)
Summary

## Slide 3
The FastIC project: context

## Slide 4
Fast Timing
detectors
Front-End
Multi Channel
ASIC
Time-to-
Digital-
Conversion
The FastIC project: motivation
FastIC (65nm, 2020)
FastIC addresses limitations from NINO (2004, 0.25mm): mainly non-linearity of the energy measurement and power consumption
Highly configurable:
Singled ended, differential and summation of 4 single-ended channels to explore benefits of segmentation of detector areas
Positive and negative polarity
Large range of input capacitances
Large dynamic range (with positive and negative polarity readout)
~30 ps r.m.s. Jitter (electronics) (Hamamatsu S13360-3050CS, 3600x50mm microcells, 4.5VOV, wirebonded) + Linear energy measurement (~2.5 % error) up to 20 mA peak (12mW single ended channel)
Collaboration between CERN (KT funded) and University of Barcelona (ICCUB)
SiPMs, MCPs, PMTs

## Slide 5
The FastIC project: Architecture

## Slide 6: Single Ended (Positive Polarity) configuration
Notes: Front-End
Current mirror with double feedback loop
Low Frequency loop: Controls the DC voltage of the input node. Enabling the adjustment of the voltage of the SiPM individually to equalize the SiPM performance to compensate non-uniformities in gain or PDE.
High Frequency loop: Common gate regulated cascode configuration to keep low input impedance at signal bandwidth.
Design strategy:
Dominant pole is set at the input node. This means that the stability is not compromised when connecting a high capacitance SiPM.
Current copy generation.
Time And Trigger measurement
Time path:
Leading edge discriminator. Information on ToA in rising edge
Produces non-linear ToT response
Low level Trigger: Same architecture as the Fast time path. A trigger pulse is provided by performing an OR between the trigger signals of all channels. The trigger level is adjustable and usually set above the Dark Count Rate (DCR) noise, i.e. to a few photoelectrons to filter these events. Thought for pixelated crystals
Cluster Level Trigger: A trigger pulse is obtained as a discriminated sum of a fraction of the input signal. For monolithic crystals where light (signal is spread)
Time Signal as Trigger: The Time signal can also be used as Trigger in cases where high sensitivity is required and the events are close to the single photoelectron level.
Energy path:
- Transimpedance amplifier ~5ns peaking time
- Shaper (nominal peaking time 30 to 50ns
(can be made faster at the expense of decrease in linearity)
- Peak detector and hold
Ramp generator and voltage comparator. The slope of the ramp can be adjusted.
The Ramp can be triggered by the two flavours of trigger, by the time signal and also by an external signal (external trigger) used for the calibration of the pedestals.

## Slide 7: Single Ended (Negative Polarity) configuration

## Slide 8: Differential configuration

## Slide 9: Implementation: combination of signals
Front-End
TDC
Large area SiPM → Large Cdet
Large area SiPMs can have an equivalent detector capacitance higher than 1 nF
This high input capacitance degrades the slew-rate

## Slide 10: Strategy to cope with large detectors
+
Front-End
TDC
Segment SiPMs to cover same area → Cdet/4
Segmentation: Cover same area with m smaller sensors.
  Potential improvement of the slew-rate by a factor of m ()
  Series noise contribution is approximately constant w.r.t. segmentation
    (i.e. )
Potential reduction of σt by a factor
m: physical channels = 4
Sum of m uncorrelated contributions
The series noise is proportional to the detector capacitance, which reduces a factor sqrt(m)

## Slide 11: SUM4 (Positive Polarity) configuration

## Slide 12: SUM4 (Negative Polarity) configuration

## Slide 13
The FastIC project: readout system

## Slide 14: Evaluation system
Aims of the evaluation system:
  Basic operational test & debug ASIC functionalities
  Initial electrical characterization and linearity analysis.
  Initial benchmark i.e. evaluate the FastIC chip by comparison
    With respect previous designs (NINO, HRFlexTOT)
    Using reference SiPM sensor:
      Hamamatsu S13360-3050CS
      FBK NUV-HD
  Interface with other sensor based on adaptor board
  Signal acquisition:
    FPGA-based TDC (45ps time bin)
    Differential sLVS link to external system

## Slide 15: Evaluation system
Custom sensor board
FastIC generic board
  2 FastICs on QFN64 (16 channels)
  Reference SiPM sensors included
  The board can be used stand alone
FPGA board
  FPGA board for slow control, acquisition and additional biasing.
  Multichannel TDC is implemented in the FPGA (45ps time bin)

## Slide 16
The FastIC project: measurements

## Slide 17: Time waveforms
FastIC provides a measurement of time and energy per channel in two consecutive pulses
Time is encoded in the rising edge of the first pulse
Energy is encoded on the width of the second pulse. The readout is based on HRFlexToT architecture*
*D. Sanchez, S. Gomez, et. al. "HRFlexToT: A High Dynamic Range ASIC for Time-of-Flight Positron Emission Tomography" 2021, IEEE TRPMS, https://doi.org/10.1109/TRPMS.2021.3066426

## Slide 18
Linearity of the energy measurement
An electrical SiPM-like signal is injected into the FastIC for energy evaluation using an AWG
Linearity error is below 3% over the whole dynamic range
Saturation is reached at 25 mA input current (positive polarity) and 20 mA (negative polarity)
Summation in the energy is linear, independently of the channels added
This makes FastIC very versatile and suitable for LYSO/LSO, BGO, Cherenkov, Monolithic, etc.
S. Gomez

## Slide 19
The FastIC project: measurements with sensors

## Slide 20: SiPM measurements
Positive Input stage
SiPM S13360-3050CS operated at 60V of HV (Over-voltage ~7.6V)
1PE,2PE,3PE,...
2PE,3PE,...
3PE, 4PE,...
4PE,5PE,...
SiPM Hamamatsu
S13360-3050CS
3mm
3mm
S. Gomez, D. Sanchez
Notes: Note:
1. Uncorrelated noise: the main source of noise on a SiPM came from "false" avalanche
pulses, triggered by thermally generated carriers on the active junction. Each of those
pulses are the result of a thermally generated electron that initiates an avalanche in
the high ﬁeld region, for this reason, the uncorrelated noise depends on the Vov applied
to the SiPM. This signal is generated even at dark conditions and are identical to
the "real" signals from a light source, that noise is called Dark Count Rate (DCR).
The number of dark pulses is typically given in units of kHz/mm2. Furthermore, it
depends on the microcell ﬁll-factor and the depleted region width. Importantly, the
DCR is reduced a 50% factor every time the temperature decreases 10 degrees [39].
Nevertheless, this reduction reaches a limit where the DCR is not reduced that much
anymore, due to other phenomena like tunneling generation.
2. Correlated noise: this type of pulses are mainly due to (1) at the same microcell by
afterpulsing or (2) caused by optical light coming from an adjacent cell, where in this
case it is called optical crosstalk.
a) Afterpulsing: on every avalanche process during the photoconversion, there is
a probability that some carriers become trapped in defects in the silicon. After
a certain delay, the trapped carriers are released, leading to a possible second
avalanche (typically exponential distribution from the release times) after some
nanoseconds from the original one. If the release time is smaller than the recharge
time of the cell, the charge contained in this afterpulse will be smaller compared
with a normal cell signal. Moreover, the afterpulse can be induce optically by the
secondary photons generated during the avalanche process, that can be reabsorbed
in the neutral region and the carriers will be diﬀused to the depleted region and
trigger a second avalanche.
b) Crosstalk: as mentioned above, several secondary optical photons are emitted
during the carriers avalanche process. Typically 2 to 3 · 10−5 NIR photons are
emitted in isotropic directions for a single avalanche. Those photons can reach
neighboring cells and trigger a second instantaneous avalanche, resulting in a
signal output of amplitude and charge N times the single cell signal, with N the
number of optical crosstalk photons absorbed. There are three main transport
paths used by the optical photons to reach a neighboring cell (ﬁgure 2.9): (1)
direct crosstalk, where an adjacent cell triggers and avalanche right after the
primary one is detected, the NIR photons travels directly in straight line. (2) The
NIR photons escape from the cell and is being reﬂected in the window cover and
bounces back to a next by cell, or (3) reﬂected from the bottom of the substrate.
2 and 3 are also called delayed crosstalk. An extensive study on the crosstalk
characterization can be found in[40, 41].

## Slide 21: Setup for SPTR measurement
Laser (405 nm) – 40 ps FWHM pulse width
S. Gomez

## Slide 22: SPTR measurement
S. Gómez
Hamamatsu S13360-3050CS (3x3 mm2 50mm cell pitch, VOV=11V)
SPTR= 176 ± 5 ps FWHM
FBK NUV-HD Low Field V2 (3.12x3.2 mm2 40mm cell pitch, VOV=10.5V)
SPTR= 151 ± 5 ps FWHM

## Slide 23: Energy resolution measurement
The Energy Resolution was measured with a 22Na source
The TDC implemented in the FPGA was used to digitize the data
Crystal: LYSO:Ce:0.2%Ca 3.13x3.13x20mm3
SiPM: Hamamatsu S13360-3050CS (3x3 mm2 50mm cell pitch, VOV=3V)
Compton edges and gamma peaks are used to calibrate the nonlinearities of the SiPM*
Energy resolution expressed in FWHM/m [%].
Energy resolution of 511 keV 22Na ~9%
*D. Sanchez, S. Gomez, et. al. "HRFlexToT: A High Dynamic Range ASIC for Time-of-Flight Positron Emission Tomography" 2021, IEEE TRPMS, https://doi.org/10.1109/TRPMS.2021.3066426
S. Gómez

## Slide 24: Coincidence Time Resolution
S. Gómez

## Slide 25: Coincidence Time Resolution
S. Gómez
Crystal: LSO:Ce:0.2%Ca 2x2x5 mm2, LY=39.2 ph/keV, td=~32ns
SiPM: Hamamatsu S13360-3050CS (3x3 mm2 50mm cell pitch, VOV=8V)
CTR= 104 ± 3 ps FWHM

## Slide 26: Coincidence Time Resolution
S. Gómez
Crystal: LSO:Ce:0.2%Ca 2x2x3 mm2, LY=39.2 ph/keV, td=~32ns
SiPM: Hamamatsu S13360-3050CS (3x3 mm2 50mm cell pitch, VOV=8V)
CTR= 93 ± 3 ps FWHM
Crystal: LSO:Ce:0.2%Ca 2x2x3 mm2, LY=39.2 ph/keV, td=~32ns
SiPM: NUV-HD LF V2 (3.12x32 mm2, 40mm cell pitch, VOV=6.1V)
CTR= 76 ± 2 ps FWHM

## Slide 27
FAST TIME
DEVELOPMENTS
EP-ESE-ME
FastIC Analog
8 channels
FastIC Analog:
Analog chip
Generic
Wide range CDET
Large dynamic range
Signal summing
Used with external TDC
Not radiation hard
Design completed (CERN-UB)

## Slide 28
FAST TIME
DEVELOPMENTS
EP-ESE-ME
FastIC Analog
8 channels
FastIC Analog:
Analog chip
Generic
Wide range CDET
Large dynamic range
Signal summing
Used with external TDC
Not radiation hard
FastIC+
8 channels
Medical
Applications
FastIC+:
Analog and Digital chip
Generic
Wide range CDET
Large dynamic range
Signal summing
Used with internal ~25ps bin TDC
Not radiation hard
Design completed (CERN-UB)
Design ongoing (CERN-UB)

## Slide 29
FAST TIME
DEVELOPMENTS
EP-ESE-ME
FastIC Analog
8 channels
FastIC Analog:
Analog chip
Generic
Wide range CDET
Large dynamic range
Signal summing
Used with external TDC
Not radiation hard
FastIC+
8 channels
Medical
Applications
FastIC+:
Analog and Digital chip
Generic
Wide range CDET
Large dynamic range
Signal summing
Used with internal ~25ps bin TDC
Not radiation hard
FastRICH
LHCb
16 channels
FastRICH:
Analog And Digital chip
Application specific
Smaller range CDET (PMTs/Small SiPMs)
Small dynamic range (single photon operation)
No signal summing
Internal TDC (~25ps bin TDC)
~2ns Gate (duration/phase programmable)
CFD
Radiation hard
Design completed (CERN-UB)
Design ongoing (CERN-UB)
Design ongoing (CERN-UB)

## Slide 30: Towards FastRICH
FastRICH is based on the experience from the CERN-UB team on the design of FastIC for the readout of fast detectors
The design involves major changes in the analog part, the implementation of a TDC and a full digital readout
The chip provides a radiation hard (TID and SEE), low power and compact system for the LHCb RICH detector for interfacing with the detector on one side and on the other with lpGBT/optical links
The chip aims at reducing the amount of data generated
  With Zero Suppressed Readout
  A programmable ~2ns Shutter signal
  A Constant Fraction Discriminator (CFD)
And also a configurable number of output links (1/2/4) to adapt to the occupancy of the different regions of the experiment

## Slide 31
FAST TIME
DEVELOPMENTS
EP-ESE-ME
FastIC Analog
8 channels
FastIC Analog:
Analog chip
Generic
Wide range CDET
Large dynamic range
Signal summing
Used with external TDC
Not radiation hard
FastIC+
8 channels
Medical
Applications
FastIC+:
Analog and Digital chip
Generic
Wide range CDET
Large dynamic range
Signal summing
Used with internal ~25ps bin TDC
Not radiation hard
FastRICH
LHCb
16 channels
FastRICH:
Analog And Digital chip
Application specific
Smaller range CDET (PMTs/Small SiPMs)
Small dynamic range (single photon operation)
No signal summing
Internal TDC (~25ps bin TDC)
~2ns Gate (duration/phase programmable)
CFD
Radiation hard
Future Roadmap
Emphasis on module
Analog and Digital chip
Pixelized, Sensor co-design, hybrid integration
More channels
Smaller range CDET
Large dynamic range
No signal summing
Used with internal TDC
Future
developments
Design completed (CERN-UB)
Design ongoing (CERN-UB)
Design ongoing (CERN-UB)

## Slide 32: Summary of results with FastIC
Single Photon Time Resolution (SPTR) measurements
  Blue light laser (PiL040X, 405nm, jitter <3ps, pulse width<45ps)
  Agilent MSO 9404A, 4GHz, 20GS/s
  18oC Temperature
  176 ±3ps FWHM (HPK SiPM S13360-3050CS, 3x3mm2 VOV=10.6V)
  151 ±3ps FWHM (FBK HD-NUV Low Field SiPM, 40mm cell, 3.12x3.12mm2 VOV=10.6V)
  Fits with the initial spec ~30psrms contribution from electronics with large SiPM
Coincidence Time Resolution (CTR) measurements
  LSO:Ce:0.2%Ca 2x2x3mm3
  93 ±3ps FWHM (HPK SiPM S13360-3050CS, 3x3mm2 VOV=8V)
  76 ±2ps FWHM (FBK HD-NUV Low Field SiPM, 40mm cell, 3.12x3.12mm2 VOV=6.1V)
Linearity error <3% up to 25mA (+ polarity stage) or up to 20mA (- stage)
9% energy resolution for 511keV (LYSO:Ce:0.2%Ca 3.13x3.13x20mm3)
R5900 Hamamatsu PMT, 800V.
  Jitter of ~340 ps FWHM, which corresponds to the intrinsic PMT time uncertainty when detecting tens of photons.
Two spin-off projects: FastIC+ and FastRICH
FBK HD-NUV Low Field SiPM at 6.1 V of over-voltage.
HPK S13360-3050PE SiPM at 8 V of over-voltage.
CTR measurement with 2 × 2 × 3 mm3 LSO:Ce0.2%Ca crystals
coupled to FBK (a) and HPK (b) devices in coincidence (20 K events used).