Minimum Spaning Tree
Gérald Grenier
IPN Lyon, Université Lyon 1
DHCAL Analysis/Software meeting, January 5th 2011
Follow-up work by Guillaume Garcia and Daniel Foster on MST
Daniel's code to compute MST have been set-up in a Marlin Processor
Processor available in the SVN : https://svn.in2p3.fr/calice/analyse/trunk/SDHCAL-offline-tools/MARLIN_SDHCAL/
2 new processors :
SDHCAL_mst_processor : compute MST
SDHCAL_EMfractionProcessor : to study MST capabilities to predict the EM fraction of a shower.

---
Reminder's from last Daniel's talk....
Minimum Spanning Tree
- A hit corresponds to a vertex
- An edge corresponds to a link between two vertices
  - To each edge we associate a certain weight

---
Reminder's from last Daniel's talk....
Minimum Spanning Tree
- Spanning tree:
  - Graph that includes all vertices
  - Contains no cycles
- Minimum spanning Tree:
  - Spanning tree with the lowest weight
Minimum spanning tree

---
Reminder's from last Daniel's talk....
Weight of an edge
- Weight depending on metric
- Metric
  - is determined by
    - Transversal factor nr
    - Longitudinal factor nz
  - is relative to detector geometry
Detector geometry

---
SDHCAL_mst_processor
Marlin steering file main parameters :
CaloHitCollections : list of input CalorimeterHit Collections
SimCalorimeterHit : list of input SimCalorimeterHit Collections
LongitudinalWeight : nz factor
TransversalWeight : nr factor
Longitudinal_start_end_step : to compute many mst with loop on nz value
Transversal_start_end_step : to compute many mst with loop on nr value
OutputMSTcollection : The weights stored as LCGenericObject
The processor compute the mst and produce histograms for the given
 LongitudinalWeight and TransversalWeight parameters
The processor stores the MST weights in the ouput collections for the
LongitudinalWeight and TransversalWeight parameters and for all the
values corresponding to the loop by Longitudinal_start_end_step and
Transversal_start_end_step.
The MST output LCIO object contains an array of float with
Longitudinal weight value (position=0)
Transversal weight value (position=1)
MST weights sorted in ascending order (position>=2)

---
Some MST weight distributions
Mokka simulation of single Klong in à la Videau Geometry.
Almost 4000 events per energy point.
nr=nz=1
Only hits due to EM particles in shower

---
Some MST weight distributions
Mokka simulation of single Klong in à la Videau Geometry.
Almost 4000 events per energy point.
nr=nz=1
Only hits due to hadronic particles in shower

---
Some MST weight distributions
Hits with contribution from EM particles
Clear dependence on energy in the first bin
Evolve in the right direction if it should estimate EM
fraction in a shower.

---
Some MST weight distributions
Hits without contribution from EM particles
Clear dependence on energy in the first bins.

---
Some MST weight distributions
Distribution from all hits.
Energy dependant features still visible.
Might serve as input for energy estimation

---
Final remarks
The mst computation is available as a Marlin Processor.
There are signs that mst weight can be used to improve energy estimation.
Trying to produce root and lcio files with lots of mst weights to do further study.
These files will appear in calice grid Storage Element under
/grid/calice/SDHCAL/Marlin/mst_v1
as soon as the calice grid will be functionnal again (for me).