## Slide 1: Top Cryostat Mechanical integration CERN TE-MSC, EN-MME, RTU and UNIBS
Luca Piacentini, Diego Perini, Toms torims,
Luca Dassa, Jānis Vilcāns, Andris Ratkus, Stefano Uberti
VPP-IZM-CERN-2020/1-0002

## Slide 2: Outline
Dipole and quadrupole data & assumptions
External and internal supporting systems
Mechanical integration and insulation vacuum interconnection
Cryogenic integration
Information transfer/envelope system

## Slide 3: Dipole and quadrupole data/assumptions
Earlier than 2/03 | 2/03/2022 HITRIplus meeting | 17-18/05/2022 HITRIplus 2nd meeting | 
1,5 m | 1,65 m * | 1,65 | Bending radius
310 mm | 170 mm | 310 mm | Yoke Outer Radius
2,5 tons | 1.5 tons | 2,5 tons | Mass
Earlier than 2/03 | 2/03/2022 HITRIplus meeting | 17-18/05/2022 HITRIplus 2nd meeting | 
1,5 m | 1,65 m * | 1,65 | Bending radius
310 mm | 170 mm | 310 mm | Yoke Outer Radius
2,5 tons |  | 2,5 tons | Mass
* Compatible with the bending radius of the latest beamline studied by CNAO
Dimensions have been scaled with a ratio: 17/31
By courtesy of G. Ceruti
Since the work was ongoing before the 2nd HITRIplus meeting, dimensions were set on 170 mm and mass 2 tons

## Slide 4: Dipole and quadrupole data/assumptions
Geometry?
Mass?
-> Supports
Dimension margin + support structure margin
Assumptions
Diameter = 380 mm
Length = 285 mm
Length ftf = 365 mm
Mass = 400 kg

## Slide 5: External and internal supporting system
What are the problems:
Due to tolerance chain, deformations, measuring errors ecc… the position of ALL COMPONENTS (SC Dipoles, NC quadrupoles, SC quadrupoles) is uncertain. But can be thought as contained within an error box (position-rotation = 6 degrees of freedom DOF)
How:
need of a positioning system and adjustment system
Characteristics:
Able to maintain the following characteristics around 360°
Designed to work like this:
Not like this:
“Or in all other different from 0°”

## Slide 6: External and internal supporting system
What are the problems:
Due to tolerance chain, deformations, measuring errors ecc… the position of ALL COMPONENTS (SC Dipoles, NC quadrupoles, SC quadrupoles) is uncertain. But can be thought as contained within an error box (position-rotation = 6 degrees of freedom DOF)
How:
need of a positioning system and adjustment system
Characteristics:
Able to maintain the following characteristics around 360°
Able to compensate errors in a given workspace
Stiff, to reduce displacements and deformations
Possibly Iso-static, to reduce localized stresses
Compact
Low complexity: easy to assembly/manufacture - easy to operate
Not expensive
6 DOF & 6 constrains
Parallel Mechanisms?

## Slide 7: External and internal supporting system
Parallel Mechanisms
DOI 10.1007/978-3-642-36929-2
Simplicity in adjusting mechanism (push/pull screws) -> no additional actuation systems (hydraulic)
Stiffness -> no length adjustment of the legs
Simplicity of the guide structure (compactness)
Error minimization -> no guides in series
6 DOF schemes

## Slide 8: External and internal supporting system
External supports (cryostats and warm components)
**solution not yet integrated
Internal supports (SC dipoles and SC quadrupoles)

## Slide 9: External and internal supporting system
Code for force evaluation
Forces results
Deformation < +- 0.1 mm
Dimensions

## Slide 10: External and internal supporting system
Forces
Rods deformation < +- 0.1 mm
Dimensions
By courtesy of Jānis Vilcāns
*in a preliminary stage
**yet to implement
By turning the 6 screws we can adjust all 6 DOF (only passive adjustment is foreseen)
Required R&D on internal supports thermomechanical behaviour

## Slide 11: Mechanical integration and insulation vacuum interconnection
Gained space by studying ad hoc leg configuration for dipoles

## Slide 12: Mechanical integration and insulation vacuum interconnection
Required R&D on a large diameter short bellow:
Stiffness estimation
Impact on the flexibility between the 3 bodies

## Slide 13: Cryogenic integration
Cold Mass IN
Cold Mass OUT
Thermal Shield OUT
Thermal Shield IN
* Not calculated

## Slide 14: Cryogenic integration
800 mm
650 mm
Cold Mass IN
Cold Mass OUT
Thermal Shield IN
Thermal Shield OUT
Current bus
As in LHC, eccentricity is introduced to free space at the bottom

## Slide 15: Cryogenic integration
Design and Testing of Real Scale MgB2 Coils for SUPRAPOWER 10 MW Wind Generators (cern.ch)
Rotary joint feasibility?
R&D on cryogenic transfer line flexibility

## Slide 16: Information transfer/envelope system
Collect data and updates
Set Margins and Envelopes
Keep track of Impact
Example:

## Slide 17: Thank you for the attention!