## Slide 1: Vertex fitting
Intro/Caveats
Vertex fitting
Recent updates
More to come
Franco Bedeschi, INFN
Phys. Performance meeting
July, 2022
OUTLINE

## Slide 2: Introduction
Vertex fit is already available in many existing packages
  ….. That’s the problem:
  Using it usually means you also buy a complex infrastructure
Goal here is to provide a simple standalone code
  Easy to insert in FCC framework
  Based on ROOT libraries only
  More complex implementations can come later

## Slide 3: Vertex fit (1)
Input:
  Array of observed tracks
    5 parameters + Cov. Matrix
    Assume perfect helix
      D, f0, C, cot q, z0
Output:
  3D vertex + covariance
Method:
  c2 minimization with constraints
    Vary parameters and phase and force all tracks to cross at same point

## Slide 4: Vertex fit (2)
The c2:
  i, Ci = track parameters and covariance matrix
  si = helix phases, = Lagrange multipliers
  Solve by linearization and iteration on si (mean is 4 iterations)
Solution:

## Slide 5: Performance (1)
Example: 100,000 events, 3 tracks, RV (0-1.5 cm), pt (0.5-1.0 GeV)

## Slide 6: Performance (2)
Example: 100,000 events, 2 tracks, RV (0-1.5 cm), pt (0.5-1.0 GeV)

## Slide 7: Implementation
Code location:
  https://github.com/delphes/delphes/tree/master/external/TrackCovariance
    VertexFit.cc, VertexFit.h (basic vertex fitting)
    VertexMore.cc, VertexMore.h (additional features)
How to call:
  Track loop:
  pr[Ntr] = new TVectorD(obsPar); // Parameters
  cv[Ntr] = new TMatrixDSym(covMat); // Error matrices
  VertexFit* Vtx = new VertexFit(Ntr, pr, cv); // Vertex fit TVectorD xvtx = Vtx->GetVtx(); // Vertex found TMatrixDSym covX = Vtx->GetVtxCov(); // Vertex covariance Double_t Chi2 = Vtx->GetVtxChi2(); // Fit Chi2

## Slide 8: Additional features (1)
Add/remove track from existing fit:
  AddTrk(TVectorD *par, TMatrixDSym *Cov);
  RemoveTrk(Int_t iTrk);
    Useful in vertex finding loops
Set starting radius:
  SetStartR(Double_t R);
    Separate seagulls and cowboys
    Default is expand at P.C.A.
    New feature in DELPHES to provide lowest hit coordinates
Add vertex constraint:
  AddVtxConstraint(TVectorD xv, TMatrixDSym cov);
    Useful in primary vertex finding

## Slide 9: Additional features (2)
Updated track parameters after vertex fit:
  GetNewPar(Int_t i)
  GetNewCov(Int_t i) // Diagonal covariance
  Correlations:
    GetNewCov(Int_t i, Int_t j) // <Par_i*Par_j>
    GetNewCovXvPar(Int_t i) // <Xv*Par_i>

## Slide 10: Helper class: VertexMore
Invocation: VertexMore* VM = new VertexMore(Vtx);
Track momentum/errors at vertex:
  TVector3 GetMomentum(Int_t i)
  TMatrixDSym GetMomentumC(Int_t i)
  Total vertex momentum/error:
    TVector3 GetTotalP()
    TMatrixDSym GetTotalPcov()
  TMatrixDSym GetBigCov()
    Full xv, p1, p2, …. pn covariance matrix
Charged vertex only for now!
  Vertex track parameters/errors:
    TVectorD GetVpar()
    TMatrixDSym GetVcov()
    Can then use as track in vertexing chain (e.g. BsDs K)
    Problem with charged vertex tracing in DELPHES
Bs
Ds
K
K
K
p
f

## Slide 11: In progress
Multiple mass constraint:
  AddMassConstraint (Double_t Mass, Int_t Ntr, Double_t* masses, Int_t* list)
  Eg. Dsf p (fKK)
    Constrain simultaneously f and Ds mass in vertex fit
      Call twice before refit
  Coded and tested locally
    Waiting for fixing tracking problem in DELPHES
Including neutrals

## Slide 12: Conclusions
Fast vertex fitting code dependent only on ROOT libraries is provided
  Very simple to use without any overhead
  Most common features included and more coming
Coming (hopefully) soon:
  Easy new features:
    Mass constraining (basically complete)
    Pointing contraint (math done)
  Hard new features:
    Dealing with neutrals