## Slide 1: Collider Of Tomorrow: The Cool Copper Collider & The Muon Collider
Precision Electroweak to Discoveries at the Energy Frontier
From
based on US Snowmass 2021-22 discussions
https://www.muoncollider.us/ https://muoncollider.web.cern.ch/

## Slide 2: Physics Case for the Energy Frontier
From
Higgs Factory
O(10) TeV
Shovel Ready
Further Research

## Slide 3: Higgs Central to Many Fundamental Topics
Percent level Higgs couplings deviations from SM values  BSM physics at 10 TeV
e+ e– Higgs Factory  Energy Frontier (10 TeV) Muon Collider

## Slide 4: Particles & Interactions of The Standard Model
Interactions by exchange of vector bosons
The edifice on which SM is built: The complex scalar doublet, with non-zero VEV, results in masses for W+/W– and the Z & massive Higgs. Fermions also get mass interacting with H.
Matter Particles (fermions)

## Slide 5: Higgs Field is Special Electro-Weak Symmetry Breaking
50 years ago, gauge theory unified electro-weak interactions, but could not accommodate non-zer masses for W± & Z
Coupling to Higgs field provides masses to matter particles!!
Introduction of a doublet of complex scalar fields with peculiar potential provided masses for W± & Z and left g massless!
Asserting the form of the potential requires measuring di-higgs production
The remnant fourth field degree of freedom is the Higgs Boson discovered in 2012

## Slide 6: Higgs Boson Couplings, Production and Decays
(At the LHC)
(At e+e- factories)
(At Muon Colliders)
e+
e-
m+
m-
nm
nm
(At Muon Colliders)
m+
m-
nm
nm

## Slide 7: Current Status of Golden Channels @ LHC
Our Higgs boson data sets are enabling detailed studies of the SM

## Slide 8: Current Status of Higgs Couplings

## Slide 9: What’s Next? Sub-percent Level Higgs Couplings  10 TeV BSM
Couplings Deviations found at C3 e+e–Higgs Factory  BSM @ 10 TeV Muon Collider

## Slide 10: Colliders Of Tomorrow
Many Opportunities at the Energy Frontier
FCC-pp, SPPS 100 km 100 TeV ~ Eqq~15 TeV 500 - 3000 fb-1sy-1
FCC-ee, CEPC 100 km 240, 365 GeV 850, 155 fb-1sy-1
CLIC-ee 50 km 0.38,1.5, 3 TeV 150, 370, 590 fb-1sy-1
ILC-ee 31 km 250, 500 GeV 75, 180 fb-1sy-1
C3-ee 7 km 250, 500 GeV 100, 200 fb-1sy-1
HL-LHC 27 km 14 TeV ~ Eqq~ 2 TeV 200 - 500 fb-1y-1
snowmass year = 107s
mCol ~27 km 10, 15 TeV 1000 - 2000 fb-1sy-1
mCol 6 km 3, 6, 10 TeV 200, 500 fb-1sy-1
mCol 0.3 km 125 GeV 1 fb-1sy-1

## Slide 11: Implementation Task Force Evaluated Collider Types
Circular Colliders e+e–
From
Tera-Z, millions of H – very high luminosity
”Upgrade” to pp-machine for high energy
Proton Colliders (FCC-hh, SPPS/China ~100 TeV, 10s ab–1 )
Linear Colliders e+e–
Polarization, Energy Reach
From
Upgraded / Expanded facilities:
Advanced technologies: (much R&D needed)
Muon Colliders (10 TeV, 10 ab–1)
Revived interest in high-energy option due to recent advances

## Slide 12: Lepton collider Luminosity vs Landscape

## Slide 13: Luminosity / Power vs Energy from ITF
Points computed from proponent submitted parameters table
Uncertainty band is ITF judgement based on many considerations: technical design status, risk assessment, …

## Slide 14: Higgs Factories
With 5 y R&D could get physics rolling by 2040 for ~$10B

## Slide 15: Energy Frontier Machines
With 10 y R&D could get physics rolling by 2045 for ~$18B

## Slide 16: Higgs Factory Physics Timeline vis-à-vis Integrated Luminosity
Caveat – run plans are adjustable; start of physics times are different
  Technically feasible times: ILC < 12y, FCC-ee, CLIC, CEPC, C3 : 13-18y
    ILC “shovel ready” + C3 Short R&D –potential for earliest start
    FCC-ee, CLIC – post HL-LHC
  Circular colliders have shorter runs, higher luminosity
  Linear collider runs have access to polarization and higher energy
  Both provide good precision on Higgs Couplings & EWK

## Slide 17: C3 – Cool Copper Collider – New Option
Cryogenic operation improves performance
Cahill et al, PRAB 21.10 (2018): 102002
Bane et al, arXiv 1807.10195

## Slide 18: Synergies With X-Ray Photon Sources
The vast majority of ~30,000 currently operating accelerators globally are electron accelerators.
Electron accelerator R&D ranges from industrial applications to the cutting-edge development of ultimate storage rings and linear accelerator based XFELs.
This fortunate situation allows e+e– colliders to leverage these global efforts to provide a viable path to a collider reducing the R&D costs to the HEP budget.

## Slide 19: C3 – GeV – Potential Coordinates
Can fit in FNAL site with BDS improvements
LINAC 2km
BDS ~3km
Optional
LINAC 2km
BDS – similar to ILC design for 1-TeV – redesign optimally.
1% H couplings - precision
O(10)% Higgs Self Coupling

## Slide 20: Higgs Couplings from Factories

## Slide 21: Top-Yukawa and Higgs Self-Coupling
Advantages of Energy Reach
ECM (TeV) | Precision of lHHH
HL-LHC | 50%
ILC 0.5, C3 0.55 | 20%
CLIC 1.5 | 36%
CLIC 3 | 9%
mC10, FCC-hh | 4%
Double Higgs production

## Slide 22: Electroweak Observables
GigaZ is a big improvement over current status
FCC-ee TeraZ suggests even bigger leap forward in precision

## Slide 23: Oh! Lord of Rings!! Can’t we get to 10 TeV in one swoop?

## Slide 24: Innovative Muon Collider Concepts Energy Efficient Path to O(10)-TeV Colliders
Accelerator Ring LHC Tunnel?
Or FNAL Site Filler?
Minimize civil engineering cost.

## Slide 25: Muon Collider Advantages
6-10 TeV machine can fit on Fermilab site
15 TeV machine can fit in LHC/CERN tunnel
arxiv:1901.06150

## Slide 27: Muon Collider Prospects: Heavy Scalar Singlet
Higgs Smashers Guide, arXiv: 2103.14043
People are correct when they claim one should not assume pp100 ~= muCol10

## Slide 28: Higgs Compositeness & Minimal Z’ – Another place where Muon Collider Shines

## Slide 29: SUSY sparticle Searches
Ecm= 10 TeV
Ecm= 14 TeV
Ecm= 30 TeV
HLLHC
FCC-hh
Of course, FCC-hh wins in colored particle case over 10 TeV mCol

## Slide 30: Dark Matter Reach
Conservative == 10ab–1
Discovery potential for 10-TeV scale WIMPs for a variety of color/ew/hypercharge multiplets
Higgs Smashers Guide, arXiv: 2103.14043

## Slide 31: Towards Muon Collider
Critical concepts now demonstrated
  Target Solenoid
    Similar LTS parameters to ITER Central Solenoid
    Performance can be improved with a radiation resistant HTS or Cu insert
  Muon 6D Cooling
    MICE Demonstration of Emittance Cooling
    High gradient demonstration of RF operating in Tesla-class magnetic fields
    Cooling channel concepts and detailed simulation consistent with operational targets
  Muon Final Cooling
    Advances in HTS conductor/cable/magnet technology
    High Field User Magnet program operationally demonstrating magnet parameters that are rapidly approaching the MC requirements

## Slide 32: Towards Muon Collider …
Critical concepts now demonstrated
  Muon Acceleration
    Significant recent advancement in HTS-based fast-ramping magnets
    Focused effort on studying the integrated magnet/power supply efficiency issues for TeV-scale acceleration
  Collider and Detector
    Detailed studies of backgrounds that may impact physics
    Detector performance studies now demonstrate the ability to successfully measure key processes
    Concepts in development to manage off-site neutrino radiation issues
See dedicated JINST Volume for key references: Muon Accelerators for Particle Physics (MUON)

## Slide 33: Muon Collider Accelerator Challenges Beam Production : Demonstration of Ionization Cooling
MICE
Increase in particle counts at smaller amplitude with low-Z absorber in place
Nature, Vol 578, P53

## Slide 34: Neutrino Background?

## Slide 35: Muon Collider Accelerator Challenges Neutrino Radiation Mitigation
Higher the collider energy the deeper the ring needs to be. Magnetic field to dither the orbit also helps.
LHC Tunnel is 100m deep.
Mokhov & Van Ginneken

## Slide 36: Muon Collider Challenges – Beam Induced Background
Mitigation Strategies needed in spite of the optimized conical absorber
  Highly segmented detectors
  Timing cuts and energy cuts
  Doublet tracker design a la CMS tracker

## Slide 37: Can we reconstruct stuff?

## Slide 38: Muon Collider Challenges …
10+ TeV is NEW Territory a Key Areas of Investigation:
Evaluation of physics potential (including detector technology)
  Impacts of beam induced background
Neutrino Flux Mitigation
  Straight accelerator sections produce intense n beam - safety
High Energy Systems
  Acceleration sections can impact the energy reach due to cost, power, technical risk, and impact on beam quality
  10+ TeV Collider designs must be developed and fully evaluated
Cooling string demonstration to verify high brightness m beam delivery

## Slide 39: Path Forward

## Slide 40: Summary – Asia & Europe

## Slide 41: Summary – US Snowmass EF Addition

## Slide 42
Spare Slides