## Slide 1
Trigger Electronics & Data Acquisition Sridhara Dasu Original slides & graphics “stolen” from: Wesley Smith, Sergio Cittolin, Tom Gorski, Ales Svetek, Maria Cepeda, Sascha Savin, Varun Sharma, Piyush Kumar, Pallabi Das, Isobel Ojalvo, Kevin Stenson, Phil Harris, …

## Slide 2: The Scientific Process
The Detector
Software
&
Computing
Trigger Electronics
&
Data Acquisition
SCIENCE Journal Publications
Petabyte per second
Petabytes per year
Petabytes get reduced to a social media post!

## Slide 3: Proton-Proton Collisions at the LHC
 | Run-2 | Run-1
Beam energy | 6.5 TeV | 4.0 TeV
Bunches/ beam | 2556 | 1380
Protons/ bunch | 2.5x1011 | 2.2x1011
N pp Collisions Created | ~1016 | 3.5 x 1014
N Higgs Events | ~104 | ~few 102
Fetch me my needle buried in those hay stacks –
And, do it As Soon As Possible
1 event in 10 000 000 000 000 !
Notes: 1 barn = 10-24 cm-2
Proton c.s 40mb/110mb@7TeV

## Slide 4: LHC Physics & Event Rates
L = 2 x1034cm-2s-1
  50 pp events/25 ns crossing
    ~ 1 GHz input rate
    “Good” events contain ~ 50 background overlap
  1 kHz W events
  10 Hz top events
  < 104 detectable Higgs/year
Can store ~ 1000 Hz events
Select in stages
  Level-1 Triggers
    1 GHz (pp-interactions) to 100 kHz
  High Level Triggers
    100 kHz to 1000 Hz

## Slide 5: (HL) LHC Physics – Trigger Challenge
Electroweak Symmetry Breaking Scale
  Higgs (125 GeV) studies and higgs sector characterization
  Quark, lepton Yukawa couplings to higgs
New physics at TeV scale to stabilize higgs sector
  Spectroscopy of new EWK produced resonances (SUSY or otherwise)
  Find dark matter candidate
Multi-TeV scale physics (loop effects)
  Indirect effects on flavor physics (mixing, FCNC, etc.)
    Bs mixing and rare B decays
  Lepton flavor violation
    Rare Z and higgs decays
Planck scale physics
  Large extra dimensions to bring it closer to experiment
  New heavy bosons
  Blackhole production
Low PT g, e, m
Low PT B, t jets
Multiple low PT objects
Missing ET
Low PT leptons
High PT leptons and photons
Multi particle and jet events
~ Dedicated triggers (CMS) or experiment (LHCB)
Low  30 GeV

## Slide 6: LHC Data Processing to Trigger
QCD

## Slide 7: Level 1 Trigger Data

## Slide 8: L1 @ LHC: Only Calorimeter & Muon – HLT@LHC: Key additional feature - Tracker
Simple Algorithms
Reduced amounts of data
Complex Algorithms
Huge amounts of data
New tracker and level-1 track trigger envisioned for HL-LHC
L1T
HLT

## Slide 9: Xilinx Field Programmable Gate Arrays

## Slide 10: Xilinx FPGAs – Phase-1 Choice: V7 690T
Currently Deployed
HL-LHC Prototypes

## Slide 11: Key element - Multi-gigabit Opto-electronics

## Slide 12: CMS Calorimeter Trigger Run-2
Installed and commissioned in 2015, fully operational in 2016
  Connections to CTP7 from Layer-1 patch panels completed in 2015
  Connections from Layer-1 to Layer-2 via compact patch panel
    3 “pizza box” sized patch panels instead of full 56U rack with LC connectors
  Layer 2 to demux to new mGT connected
Layer-1 CTP7
Layer-2 MP7
MOLEX
FlexPlane
Layer-1 to Layer-2 Patch Panel

## Slide 13: Level-1 Calorimeter Trigger Electronics
Calorimeter Trigger Processor(CTP7 – left), and Master Processor (MP7 - right)
  CTP7 (Layer-1) – mTCA Single Virtex 7 FPGA, 67 optical inputs, 48 outputs, 12 RX/TX backplane
    Virtex 7 allows 10 Gb/s link speed on 3 CXP(36 TX & 36 RX) and 4 MiniPODs (31 RX & 12 TX)
    ZYNQ processor running Xilinx PetaLinux for service tasks, including virtual JTAG cable
  MP7 (Layer-2) – mTCA Single Virtex 7 FPGA, up to 72 input & output links
    Virtex 7 has 72 input and output links at 10 Gb/s
    Dual 72 or 144MB QDR RAM clocked at 500 MHz
MMC
Power Supplies
ZYNQ
FPGA
JTAG
USB
Interface
Rx
Tx
Rx
Tx
FPGA
1V0
2xQDR
(Bottom)
2V5
3V3
1V5
1V8
mSD
USB
mC
(Bottom)
MiniPODs
3 CXP modules
MiniPod modules
Notes: oRSC – optical Receiver Summary Card
CTP7 – Calorimter Trigger Processor
MP7 ?

## Slide 14: L1 Trigger Summary from Run-2,3
We capture the physics of interest within 100 kHz bandwidth, while discarding majority of 32 kHz of collisions

## Slide 15: CICADA – Machine Learning in L1T
Also includes new (but traditional) boosted object algorithm Pallabi Das
Unsupervised learning
“Anomaly Detection” Ho-Fung Tsoi

## Slide 16: LHC Now  HL-LHC in the Future
LS1
LS2
LS3
LS4
LS5
Run 1
Run 2
Run 3
Run 4
Run 5
Run 6
HL-LHC
Trigger-Rate: ~500 Hz
Trigger-Rate: ~1 kHz
Trigger-Rate: ~1 kHz
Trigger-Rate: ~7.5 kHz
Trigger-Rate: ~7.5 kHz
Trigger-Rate: ~7.5 kHz
CMS will be on path to exabytes of data acquired in the HL-LHC era

## Slide 17: HLLHC Parameters
Operating at 2x now
Expect Operating at 7.5x ultimately
m=200

## Slide 18: Collisions (p-p) at HLLHC
Selecting high PT clusters and tracks
Can not afford to go any higher in thresholds!

## Slide 19: Triggers  Physics

## Slide 20: CMS HLLHC Level-1 Trigger 2020
New for HLLHC

## Slide 21: Getting the crystal data out (New for HLLHC)
There are 61200 crystals to be processed – packing 25 crystals per link out of BCP you still have 2448 links at 16 Gbps to contend in the calorimeter trigger path!

## Slide 22: Getting the tracks out (New for HLLHC)
Outer tracker double layers allow track stub readout
Tracklets formed in TFP consistent with >2GeV PT. Tracks propagated in-out, matched to form track candidates
Tracklets are then fit to make a track

## Slide 23: HL-LHC L1 Trigger Challenge Xilinx – Ultrascale+ Processors
Times 2
Many times
Times 3
Times 2.5

## Slide 24: Multi-gigabit-per-second serial links
LHC
10 Gbps
HL-LHC
25 Gbps

## Slide 25: Key element - Multi-gigabit Opto-electronics

## Slide 26: Advanced Processor Prototype for HL-LHC
Wisconsin APxF Board
Xilinx VU13P or VU9P FPGA
ZYNQ-IPMC (ATCA IPMI controller)
ELM (ZYNQ-based embedded Linux endpoint)
ESM (GbE switch)
High efficiency heatsinks
Front-panel inputs
25G Samtec Firefly positions loaded – 10x12 + 1x4 (124 25 Gbps links)
TIFR built IPMC & ESM mezzanines

## Slide 27: APx – Firmware/Software
A new paradigm for firmware development
  Core firmware written in VHDL by engineers
  Gigabit link support
  Data exchange between SLRs within chip
  Test buffers
  Clock and control
Physics
  Algorithmic firmware in high-level languages like C++ written by physicists
ELM:
Control endpoint,
providing complete
board overhead
functionality
Processing FPGA:
I/O
data processor
DAQ

## Slide 28: APx-FS Resource Utilization
APd1 VU9P FPGA floorplan
100x 25G GTY links w/ support infra
Central AXI infra with MGT-based Chip2chip core
VU9P build

## Slide 29: Calorimeter Firmware Tests
Firmware prepared and tests conducted by U of Hyderabad student Piyush Kumar

## Slide 30: Particle Flow Reconstruction on FPGAs

## Slide 31: Particle Flow Implementation

## Slide 32: Particle Flow – Correlator Layer 1

## Slide 33: Particle Flow – Correlator Layer 2 th

## Slide 34: Concluding Thoughts
We in HEP are not innovators of modern computing technologies but we are amongst those who push it the most.
A team of engineers and physicists have tamed the LHC data deluge with intelligent use of telecommunications and computing technologies to enable fundamental physics discoveries.
We continue to push the technologies to the limit.
Advances in telecommunications and computing technologies are continually adapted to track increasing data volumes.
Students and postdocs are getting good training, especially in operations and firmware, for potential careers in both academia and industry – We invite you to join us in the HL-LHC adventure!