## Slide 1
SLD Compton Polarimeter
Mike Woods / SLAC Laser Safety Officer
FCC EPOL Workshop 19-30 September 2022 at CERN

## Slide 2: SLD Experiment at the SLAC Linear Collider, 1992 -1998

## Slide 3: SLAC’s Linear Accelerator Facility
FACET-II
LCLS Accelerator (and FACET-II) operate at 120 Hz
LCLS-II Accelerator operates at 1 MHz
First x-ray light from LCLS-II beam to Experimental Halls scheduled for early 2023
SLD

## Slide 4: ALR Measurement at SLD
Simple Counting Experiment
  can use all final states (no particle ID)
  no kinematic reconstruction
  no need to distinguish fermion from
anti-fermion
  no final state interaction effects
Simple Cuts to select hadronic Z events
    Energy imbalance < 0.6
    >22 GeV energy in calorimeter
    3 or more charged tracks

## Slide 5: SLD ALR Result and Systematics
 | 1992 | 1993 | 1994-5 | 1996 | 1997-8
Polarimetry | 2.7% | 1.3% | 0.64% | 0.50% | 0.50%
Energy Scale | - | - | 0.33% | 0.37% | 0.39%
Chromatic Effects | - | 1.1% | 0.17% | 0.16% | 0.15%
Bkg., detector,… | 2.4% | 0.1% | 0.06% | 0.05% | 0.07%
Total Systematic | 3.6% | 1.7% | 0.75% | 0.63% | 0.64%
Statistics | 44% | 4.3% | 2.8% | 3.7% | 1.6%
ALR Statistics and Systematic Errors

## Slide 6: SLD Compton Polarimeter

## Slide 8: Features of SLD Compton Polarimeter
Physics is well understood QED; radiative corrections <0.1%
  no atomic or nuclear physics corrections (ex. Levchuk effect in Moller polarimetry)
  reference for O(a3) corrections: M. Swartz, Phys.Rev.D58:014010,1998
Electron beam backgrounds measured with laser off pulses
Polarimetry data taken parasitic to physics data (electron detector only)
Scattering rate is high; ~1% polarization determination in a few minutes
Laser helicity selected with a pseudo-random sequence
Laser polarization determined to 0.1%
Beam-beam depolarization effects can be measured by
comparing measurements with and without collisions

## Slide 9: Electron Cherenkov Detector (CKV)
EGS4 simulation for shower from 1 electron
EGS-generated response function for CKV-7, with (solid line)
and without (dashed line) 8mm lead pre-radiator.
8mm Pb radiator
Gas is propane at 1atm; 11 MeV threshold

## Slide 10: Compton Scattering Kinematics
The cross section for Compton scattering is
where
The measured asymmetry in a channel is
Where the analyzing power is calculated from the Compton
Cross section and the channel response function, Ri.

## Slide 11: Raw Data from CKV Detector (during e- only running)

## Slide 12: CKV Analyzing Power Determination (Table Scans)
Detector resolution modifies theoretical analyzing
power by <2% for CKV7 at Compton Edge
  11 MeV detector threshold ensures EGS-based
simulation is reliable
Table scans sweep detector channels thru Compton Edge
  done daily
  give spectrometer calibration, locate Compton edge,
track detector channel gains
  determine CKV7 analyzing power to 0.2%
Use pulse height ratios for CKV7/CKV6 and
CKV8/CKV6 to track analyzing powers
between table scans. Resulting uncertainty
in CKV7 AP is 0.3%.
References: SLD Physics Note 50;
E. Torrence Ph.D. thesis, SLAC-Report-509.

## Slide 13: Radiative Corrections to Analyzing Powers 1st-order (a3) corrections
<0.1% correction to analyzing power
at Compton Edge
<0.2% corrections to cross section
See M. Swartz, Phys. Rev. D58, 014010 (1998)

## Slide 14: CKV Linearity
Electronics linearity measured
with pulser
0.2% linearity systematic
Compton asymmetry measured as a
function of background level

## Slide 15: Compton Laser System in Laser Room
/2
plate
Spectra Physics GCR-130
CP
PS
L,R
Photodiodes
Intensity
Photodiode
Laser
Photodiode
Pockels Cells
Polarizer
Polarizer
Polarizer
Remote Steering,
Focusing Control
Remote Intensity Control
/2
plate
/4
plate
Calcite Prism
CCD Camera
Laser
Transport Line
Remote Polarization Control

## Slide 16: Compton Laser Transport System
40 meters from laser to Compton IP
Each Mirror Box has 2 helicity-compensating mirrors
Transport line operates at +3psi nitrogen
Laser focused to ~0.5mm rms at Compton IP
  (50mJ in 7ns FWHM pulse)

## Slide 17: Laser Polarization Control and Analysis
Pockels Cell used for CP, PS
Calcite Prism used in Helicity Filter

## Slide 18: Laser Polarization Control
Stokes parameters
for laser polarization:
Electric Field Vector after PS Cell
in Jones Matrix notation
CP
PS
Pockels Cells
Polarizer
Remote Polarization Control
Allow for imperfect Pockels cells and
phase shifts in downstream optics

## Slide 19: Laser Polarization Scans and the laser polarization systematic error
0.1% systematic error
Abox PD (adc counts)
CP Voltage (Volts)
CP Voltage (Volts)
Residuals (adc counts)
LPSCANS
done once per hour; readout photodiodes only
ability to extinguish laser light after Helicity Filter
determines polarization purity
Laser Polarization at Compton IP (%)
CP Voltage (Volts)
CKV7 Raw Asymmetry
monitor phase shifts in laser
Polarization with continuous
Pockels cell scans
only 1/3 of data is at
nominal voltages
ESCANS

## Slide 20: Photon Cross-check Polarimeter Detectors
PGC (polarimeter gamma counter) - threshold gas (14 MeV; 1 atm ethylene) Cherenkov counter
- insertable lead pre-radiator; 1 PMT
QFC (quartz fiber calorimeter) - quartz fibers with tungsten radiators; 0.2 MeV threshold
(34 longitudinal sections, each 1 radiation length)
- 24 PMTs (10X, 10Y, SUMX, SUMY, 2 Bkgd)
24 PMTs
PMT
Insertable
Pb pre-radiators

## Slide 21: QFC Data and Systematics
Systematic | Error | Method
Energy Response | 0.2% | Beam test, MC
Detector non-uniformity | 0.3% | Beam test, MC
Detector mis-alignment | 0.1% | Beam test, MC
Angular acceptance, beam size | <0.1% | MC simulation
Optical cross talk | <0.1% | Measurement, MC
Re-scattered electrons | <0.1% | MC, in situ study
Electronics linearity | 0.5% | LED study, beam test
Electronics cross-talk | 0.1% | In situ study
Laser pickup | 0.1% | In situ study
Total | 0.6% | 
D. Onoprienko, SLD-Note-267, 1999
and Ph.D. thesis, SLAC-Report-556, 2000

## Slide 22: PGC Data and Systematics
PGC analysis described in R. Frey, SLD-Note-266, 1999
and IEEE Trans. Nucl. Sci. 45, 670, 1998
T-410
0.5” Pb
T-410
1.0” Pb
T-410
1.5” Pb
Systematic | Error | Method
Energy Response | 0.5% | Beam test, MC
Detector effects (uniformity, geometry, linearity) | 0.3% | In situ study
Laser pickup | 0.1% | In situ study
Total | 0.6% | 
SLC data with e- only, 1” Pb
No e-
e-, no laser
Jz = 1/2
Jz = 3/2

## Slide 23: Analyzing Power Systematic Error
CKV7 systematic error in analyzing power estimated at 0.3%
from table scan data that determines location of Compton edge
and accuracy of modeling detector response function
Results from cross-check Polarimeters
0.4% AP systematic error
Residual of CKV7 polarization to results from
PGC and QFC was DP/P=(0.30±0.39)%.

## Slide 24: Polarization Summary for all SLD Runs
Systematic | 1992 | 1993 | 1994/95 | 1996 | 1997/98
Laser Polarization | 2.0% | 1.0% | 0.2% | 0.1% | 0.1%
Detector Linearity | 1.5% | 0.6% | 0.5% | 0.2% | 0.2%
Analyzing Power | 1.0% | 0.6% | 0.3% | 0.4% | 0.4%
Laser Pickup | 0.4% | 0.2% | 0.2% | 0.2% | 0.2%
Lum-wting Correction | 0.2% | 1.1% | 0.17% | 0.16% | 0.15%
TOTAL | 2.7% | 1.7% | 0.67% | 0.52% | 0.52%
 | 1992 | 1993 | 1994/95 | 1996 | 1997/98
Lum-wted Polarization | 22.4 ± 0.6 % | 63.0 ± 1.1% | 77.23 ± 0.52 % | 76.16 ± 0.40 % | 72.92 ± 0.38 %
Ph. D. Students: R. Elia, SLAC-Report-429, 1994; R. King, SLAC-Report-452, 1994
A. Lath, SLAC-Report-454, 1994; T. Junk, SLAC-Report-476, 1995
E. Torrence, SLAC-Report-509, 1997; J. Fernandez, SLAC-Report-519, 1999
P. Reinertsen, SLAC-Report-537, 1998; D. Onoprienko, SLAC-Report-556, 2000.

## Slide 25: “17 Hz Problem” in the 1994 Run
Reflection from inverter (added due to BPM miswiring in downtime)
causes every 7th pulse to be off-energy
Observe i) phasing of off-energy pulse wrt laser pulse shifts every 40s
ii) large scatter in electron polarization measurements
Implemented triggering of laser on 6th machine pulse rather than the 7th
every ~10 seconds, to ensure beam
backgrounds for laser off pulses identical
to beam backgrounds for laser on pulses.

## Slide 26: Arc Spin Rotation
Spin precession in the SLC arc is nearly resonant
with vertical betatron oscillation
1. Vertical betatron oscillation in a quadrupole string
2. Vertical betatron oscillation with horizontal dipoles added
Spin
axis perpendicular
to trajectory
electron trajectory
SLC arc consists of 23 achromats.
Each achromat
  20 combined function magnets
  Spin precession of 10850
  Betatron phase advance of 10800
SLC arc spin bumps
  Launch into arc with electron spin vertical
  Two orthogonal ‘spin bumps’ allow arbitrary control
  Optimize spin bumps to minimize total precession in
  the arcs reducing polarization dependence on energy

## Slide 27: Luminosity-weighted Beam Polarization
Spin Diffusion
- incoming beam divergence
- disruption angles
  x=(-0.24 ± 0.08)% correction for 1997/98 run
Depolarization due to beamstrahlung spin flip
- expect effect to be <0.1%
- effect measured to be <0.001 by comparing polarization measurements with and
  without positrons present
  x=(0.0 ± 0.1)%
1. Chromatic Effect
- determine n(E) from automated wire scans (every 4 hours) at point of high dispersion
  P(E) by varying beam energy (optimize spin bumps to minimize)
  L(E) from optics models and measured dependence of Z production on beam energy
  x=(+0.12 ± 0.08)% for 1997/98 Run

## Slide 28: Summary
  0.5% precision achieved
  CKV table scans + laser Pockels Cell voltage scans for optimization, calibration + determining systematics
  many systematic checks performed (e.g. with QFC and PGC detectors)
  enabled SLD’s precise parity violation measurements
  data taken parasitic to physics data
  some dedicated beam time needed for systematics studies
  polarimeter measures average beam polarization, so need to address luminosity-weighted polarization
  many details are in references given, including 8 Ph.D. theses