## Slide 1: ECAL plan for construction PEBS meeting on 10th of January 2011 EPFL, Lausanne
Tatsuya NAKADA

## Slide 2: Boundary conditions
Funding from the ESA PRODEX programme through Swiss space office
  partnership with industry, already during the R&D phase
  50% or more funding has to go directly to industry
Following steps needed
  Specification us
  Conceptual design mainly by us
  Engineering design by industry with our input
  Call for tender by PRODEX
  Construction mainly by industry
  Assembly us or industry
  Testing us
Proposal
submission
to
PRODEX

## Slide 3: For RPODEX submission
Contact with three companies
  APCO can do only mechanics
  RUAG can do both mechanics and electronics
  ALMATEC more like an engineering office
Plan to discuss with RUAG and ALMATEC to converge to a technical design, starting with mechanics first
Specification needs to be finalised soon
PRODEX submission in Spring 2011

## Slide 4: Specification
Current specification:
  Active area = 873 × 873 mm2
  Converter 3mm thick Ti
  Scintillator bar = 7.75 × 873 × 3 mm3
  108 bars/layer
  3 layers/superlayer and 7 (x-y-…) superlayers
  Total thickness = (3+3) × 21 =126 mm and 17.3 X0
  Weight = 120 kg/superlayer, total of 840 kg
  Readout unit = 12 bars × 3 layers = 36 channels
  Total number of channel = 2268

## Slide 5: Specification
Specification is driven by
  Active area ← acceptance match to the rest
  Total thickness ← required energy reach i.e. energy measurement up to multi TeV needed + payload limitation
  Converter thickness, scintillator bar width ← e-p separation i.e. ~104 + total number of channels limited by the power
  Readout unit depends on the FE-chip, i.e. 32 or 36 channels
  Superlayer configuration ← readout unit configuration + weight portable by two people

## Slide 6: Specification
Specification is driven by
  Active area basically fixed: ~90×90 cm2
  Total thickness basically fixed to >~15 X0?
  Converter thickness: could still be optimized?
  Scintillator bar width: could still be optimized?
  FE-chip: if VATA Chip, 32 channels → Superlayer = 2 or 4 layers unless lose some channels, if the converter thickness >~ 3 mm, 4 layers too heavy unless split
  Some more simulation studies planned: e-p separation vs converter thickness by the end of January e-p separation vs scintillator bar width by the middle of February