## Slide 1: STEAM Simulation of Transient Effects in Accelerator superconducting Magnet circuits
Emmanuele Ravaioli and Mariusz Wozniak
on behalf of the STEAM team:
Lennard Bender, Bernardo Bordini, Marvin Janitschke, Tim Mulder, Emmanuele Ravaioli,
Erik Schnaubelt, Arjan Verweij, Andrea Vitrano, Mariusz Wozniak
with thanks to all the past STEAM members
19th July 2022
https://espace.cern.ch/steam

## Slide 2: What drives the development?
Vision
Achieve specialized, trusted, consistent, repeatable and sustainable software tools and models for rapid Simulation of Transient Effects in Accelerator superconducting Magnet circuits.
Mission
Develop capability and know-how for simulation with an appropriate utilization of established and modern technology. Engage community in framework adaptation and validation by sharing well documented tools and models. Support tools that are part of STEAM and welcome integration with externally developed code.
Values
continuity, readiness, simplicity, recognition, completeness, maintainability

## Slide 3: Simulation of Transient Effects in superconducting Accelerator Magnets circuits
LHC
Challenges / Opportunities:
Multi-domain – need to include thermal, electromagnetic and circuit domains
Multi-physics – need to couple above domains, often between software tools
Multi-rate – need to include fast transient effects in long time scale simulations
Multi-scale – need to account for small scale effects in large scale simulations
STEAM is being used in several flagship projects at CERN:

## Slide 4
STEAM framework
Conductor
Magnet
Circuit
Cooperative-simulation
(Consecutive) Analysis
Parametric (analysis)
(comparison to)
Measurements
Dakota***
STEAM SDK
Materials properties
PyBBQ
LEDET
LEDET
ProteCCT
SIGMA
FiQuS
PSPICE**
COSIM
BBQ
STEAM SDK
STEAM SDK
PSPICE library
* Text based (YAML) and Roxie files, and tdms files, ** Commercial circuit solver, *** Tool from Sandia Labs
STEAM SDK
Conductor
Input Data*
Magnet
Circuit
Analysis
Parametric
Meas. config
Co-sim.
Meas. data
some functionality is under active development
STEAM SDK
STEAM SDK
SING

## Slide 5
STEAM framework
Conductor
Magnet
Circuit
Cooperative-simulation
(Consecutive) Analysis
Parametric (analysis)
(comparison to)
Measurements
Dakota***
STEAM SDK
Materials properties
PyBBQ
LEDET
LEDET
ProteCCT
SIGMA
FiQuS
PSPICE**
COSIM
BBQ
STEAM SDK
STEAM SDK
PSPICE library
* Text based (YAML) and Roxie files, and tdms files, ** Commercial circuit solver, *** Tool from Sandia Labs
STEAM SDK
Conductor
Input Data*
Magnet
Circuit
Analysis
Parametric
Meas. config
Co-sim.
Meas. data
some functionality is under active development
STEAM SDK
STEAM SDK
SING
Gmsh+GetDP
C
TDMS

## Slide 6
Note: All figures are only meant to give a rough estimation
STEAM project in the last few years and future trends
STEAM
30%
LHC
50%
HL-LHC
5%
HFM
15%
Other
10%
Physics
10%
Matlab
5%
Java
35%
Python
60%
Applications
Develop circuit or magnet models, validate them, perform simulations,…
40%
Development
Develop new program features, code maintenance, enhance automation…
5%
COMSOL
35%
Gmsh
GetDP

## Slide 7: Key points on software development
Separate input files (data) and software (code)
The above is versioned in separate repositories on CERN GitLab
Input files are text based – a must for version control of models
Code repositories have good test coverage. We use CI with CERN Gitlab
Single Source of Truth (SSOT) for model inputs – common input file - YAML
SSOT for material properties – write it once for all the tools and repackage
Due to point 1., we aim to keep to minimum the use of Jupyter notebooks
However, we are compatible as a user friendly GUI / “frontend”, although with limited functionality
We maintain tools in a few languages, but aim to maximize python use
We use commercial tools, but long term aim to only use free software
C
Gmsh
GetDP

## Slide 8: Integration of tools
ROXIE files
ModelData
ROXIE
files parser
Conductor,
Geometry,
Circuit,
Mesh,
Solution,
Options,
data
STEAM SDK
SIGMA model
FiQuS
FiQuS (GetDP)
Gmsh API
Comsol
compiler
Comsol model
SIGMA
FiQuS input file
.data
.iron
.mod
.cadata
.bhdata
.map2d
LEDET input file
LEDET
Java script
Quench model
LEDET
COMSOL
Show real example and IDE
and more…

## Slide 9
TRANSIENTS
Energy extraction and quench-back
Quench heater induced quench
CLIQ induced quench
Powering
Electrical arc
Frequency transfer measurement
No-Insulation coils
MAGNET TYPES
Cos-theta
Block-coil
Common coil
Canted Cos-Theta (CCT)
Solenoid, pancake coils
CONDUCTOR TYPES
Nb-Ti
Nb3Sn
Bi-2212
YBCO
CIRCUIT TYPES
Stand-alone magnets
Nested circuits
Series-connected magnets
…many combinations of those
LEVEL OF DETAIL
Circuit → Magnet → Cable → Wire → Filament
No single tool can do it all. Therefore, we have many tools connected by the framework.
Scope of STEAM framework

## Slide 10: Which physics is included in the STEAM models – and which isn’t
Main takeaways: 1. Transients in superconducting circuits are complex. 2. We try to include as much relevant physics as it is practical in each tool, but each includes simplifications. 3. We can’t simulate everything (yet ;))
ELECTRICAL CIRCUITS
Electrodynamics
Non-linear components (Diodes, thyristors)
Empirical model of magnet eddy-currents
Parasitic capacitance to ground
Cold Diode heating effect
Busbar self-inductance
Power converter control
Dependence of inductance on current
Heating effect in EE resistor
Mutual coupling between busbars of different circuits
…
MAGNETS
Non-linear material properties
Quench development and ohmic loss
1D, 2D and 3D thermal diffusion
Inter-filament coupling loss
Inter-strand coupling loss
Iron-yoke saturation effect on self-inductance
Cooling to thermal sink (collars, bore, wedges)
3D magnetic field
Persistent-currents loss
Mechanics
Eddy currents in metal elements
Accurate helium cooling
Hysteresis in iron yoke
…

## Slide 11
BBQ (BusBar Quench)
vQ
Temperature [K]
x [m]
Temperature-development along
length of conductor
→ To simulate 1D+1D quench propagation in superconducting busbars
→ New development: PyBBQ (Python program, finite difference solver)
→ Future development: BBQ based on GetDP
Comsol (FE) based BBQ tool drawbacks (mainly commercial licence and lack of input file) are being addressed.
Finite difference BBQ coded in python (PyBBQ) is being developed
Finite difference LEDET can be used for BBQ simulation
Finite element tool based on GetDP is planned to be developed

## Slide 12
LEDET (Lumped-Element Dynamic Electro-Thermal)
→ To simulate electro-magnetic and thermal transients in superconducting magnets in 2D and 3D geometry using finite-differences method

## Slide 13
SIGMA (STEAM Integrated Generator of Magnets for Accelerators)
→ To simulate electro-magnetic and thermal transients in superconducting magnets in a 2D geometry using a finite-elements (FE) model

## Slide 14: Finite Elements Quench Simulator (FiQuS)
2D Example for quadrupole MQXA
3D Example of a CCT magnet
3D Example of a NI HTS coil
B and M calculation for LEDET
Stand-alone quench simulations
Thermal transient and steady state sim.
HTS coils ramp up and down simulations
HTS coils quench simulations
Coils with insulation, no-insulation, partial- insulation.
B and M calculation for LEDET
Eddy currents in the formers
Temperature of the formers
No plans for a stand alone quench simulation
Induced currents in all metal parts.
Joule heating due to induced currents.
IFCC and ISCC to be introduced.
<- 2D coupled Th-EM for E-CLIQ
GMSH for E-CLIQ
Gmsh used to create 3d models of small demonstrator formers that can be 3d printed.
GetDP
Gmsh

## Slide 15
ProteCCT (Protection of Canted-Cosine-Theta) type magnets
→ To simulate electro-magnetic and thermal transients in canted-cosine-theta (CCT) using finite-differences method

## Slide 16
SING (STEAM Integrated Network Generator)
Circuit.cir file
Circuit schematic
→ SING is used to automatically generate PSPICE and LTSPICE circuit models relying on shared sub-components. The tool was re-written in Python (ParserPSPICE) in 2022.
→ Automatic generation of frequency-domain model of a magnet in resistive or superconducting state starting from STEAM input files.
YAML file with circuit information
(SING)
ParserPSPICE
Frequency-domain model generator
Magnet or circuit impedance vs frequency
R, L, C calculation
Solve
PSPICE frequency model

## Slide 17
COSIM (Co-operative Simulation)
→ To run co-operative simulations of models developed in different software
→ Main use case is to couple magnet level models to circuit models

## Slide 18
(Consecutive) Analysis
→ To programmatically setup folders, change model parameters, and run models
→ Done with a dedicated yaml file per analysis to allow to keep history of what was done
→ Records which versions of software have been used for analysis
→ Greatly simplifies model setup and allows for changes to the reference models.
Setup folder
Load reference model
Change something in the model
and give it a new number
Change something else in the model
and give it yet another number
Run both models

## Slide 19
Parametric (analysis)
Example of Uncertainty Quantification
Other capabilities:
Parametric studies
Design of Experiment
Optimization
→ Benefits from text-based input files for models, virtually any input can be changed
→ Works ‘on top’ of consecutive analysis files, so complicated sequence of steps is possible (WIP)
→ Works with cooperative-simulations, so multitool parametric setups are possible (WIP)

## Slide 20
Measurements and simulations comparison
→ Allow defining equivalent signals in measurements and simulation files
→ This is done using yaml input files for consistency with other input files
→ Simple operations of for example adding v-taps signal for a total signal are supported
→ Can be done per magnet type or modified to individual magnet and test setup
MBRD magnet
Show real example

## Slide 21
Library of Material Properties
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SitePages/Material%20Properties.aspx
https://gitlab.cern.ch/steam/steam-material-library
https://gitlab.cern.ch/steam/steam-ledet-material-library
→ We share our material property database with users to support a community of users across different labs/universities and to help model cross-checking
Work has been done to allow a use the same material properties (coded in C) across tools written in Python, MATLAB and FE solvers (Comsol, GetDP i.e. FiQuS).
MEX
DLL
C++
C
GetDP

## Slide 22
STEAM model library: change in tools and/or input files
Software | 2021 | 2022
BBQ | Manual in COMSOL | Manual in COMSOL
PyBBQ | - | Yaml + Python API
FiQuS | - | Yaml + Python API
SIGMA | Notebook + Java .jar | Notebook + Java .jar
LEDET | Notebook + Python API | Yaml + Python API
ProteCCT | Manual in Excel | Yaml + Python API
SING | Notebook + Java .jar | Yaml + Python API
COSIM | Notebook + Java .jar + Python API | Yaml + Python API (foreseen for the end of 2022)

## Slide 23
STEAM framework (recap)
Conductor
Magnet
Circuit
Cooperative-simulation
(Consecutive) Analysis
Parametric (analysis)
(comparison to)
Measurements
Dakota***
STEAM SDK
Materials properties
PyBBQ
LEDET
LEDET
ProteCCT
SIGMA
FiQuS
PSPICE**
COSIM
BBQ
STEAM SDK
STEAM SDK
PSPICE library
* Text based (YAML) and Roxie files, and tdms files, ** Commercial circuit solver, *** Tool from Sandia Labs
STEAM SDK
Conductor
Input Data*
Magnet
Circuit
Analysis
Parametric
Meas. config
Co-sim.
Meas. data
some functionality is under active development
STEAM SDK
STEAM SDK
SING

## Slide 24: STEAM LIBRARY

## Slide 25: STEAM applications
LHC
Versioned library of validated models of all magnets and all circuits
Scripts to rapidly reproduce specific events (different initial current, quench location and time, energy-extraction timing, etc) in specific circuits (different warm resistance, energy-extraction resistance, etc)
Assist in understanding and reproducing unexpected transients during operation
HL-LHC
Versioned library of validated models of all magnets and all circuits (ready for the String test)
Parametric studies, failure analyses, and worst-case identification (hot-spot temperature, voltages to ground)
Assist in understanding and reproducing unexpected transients during testing
HFM and external collaborations
Develop quench protection models for new/less explored magnet concepts (CCT, curved CCT, …)
Develop capability to model new quench protection systems (Secondary-CLIQ, external-CLIQ, …)
Integrate HTS and non-insulated (NI) coils into the STEAM framework
LHC

## Slide 26: STEAM superconducting magnet circuit library
Magnet type | Self-protected (3D) | EE + quench-back | QH | CLIQ | Co-simulation | Short-circuit | NI
Multipole | √ | √ | √ | √ | √ | √ | 
Solenoid | √ | √ |  |  | √ |  | 
CCT | √ | √ |  |  | w.i.p. |  | 
Curved CCT | w.i.p. | w.i.p. |  |  | w.i.p. |  | 
Pancakes | w.i.p. |  |  |  |  |  | w.i.p.
~60 magnet models, all validated, including the great majority of LHC and HL-LHC magnets
~50 models of circuit types, all validated, including all LHC circuit types
Magnet/circuit models in the frequency domain available as well, but very few are validated

## Slide 27: LHC TRANSIENTS

## Slide 28: Example of simulated quenches and FPA in an RB circuit
M. Janitschke, TECH
Quench #2
Quench #3
Quench #4
Quench #5
Quench #1
Circuit and magnet currents
Voltages across the magnets
Earth current
Simulations of specific fast power abort (FPA) events in RB circuits are generated automatically based on the information provided by the LHC-SIGMON notebooks

## Slide 29: Example of simulated quench and FPA in an Inner Triplet circuit
FPA without trim current
FPA with trim current
Circuit schematic
Reference FPA curves simulated for different initial currents in the nested power converters
Currents through the magnets and free-wheel Diodes and thyristors are not measured and can be assessed only by simulations

## Slide 30: Example of simulated quench and FPA in an IPQ circuit
F. Murgia, TECH
Magnet current
Temperature in the coil turns
Voltage to ground distribution
Simulations can bring additional information regarding the magnet behavior. In this example, we see the temperature distribution at the end of the discharge (note the hotter turns in contact with QH) and the voltage to ground distribution at different times (note the periodic pattern due to magnet symmetry).

## Slide 31: Example of simulated quench and FPA in an IPD circuit
M. Janitschke, TECH
Magnet current
Temperature in the coil turns
Temperature of the QH strips
Simulations can bring additional information regarding the magnet behavior. In this example, we see the temperature distribution at the end of the discharge (note the hotter turns in contact with QH) and the temperature of the QH strip (note that they get hotter than the coil).
(0.1 s offset)

## Slide 32: Example of simulated quench and FPA in 600 A circuits
M. Janitschke, TECH
Reference FPA curves simulated for all circuit types at different current levels
Simulations provide a useful reference to analyze FPA events and understand unusual events
Currents through magnets and parallel resistors (if present) are not measured
Discharges without Energy Extraction
Discharges with Energy Extraction

## Slide 33: Example of simulated quench and FPA in a 600 A undulator circuit -1
From LHC Project Report 894
Circuit current measured by the DCCT
DCCT
Very difficult to understand, let alone analyze, such a difficult transient with the available measurements
Note that the parallel resistors also act as quench heaters

## Slide 34: Example of simulated quench and FPA in a 600 A undulator circuit -2
Currents of 8 coils
and 7 parallel resistors
Temperature in the coil turns vs time
Evolution of the temperature in the coil turns
To simulate this transient, the software must include quench development, thermal diffusion from the resistors to the turns and among turns, longitudinal quench propagation, mutual coupling between coils and parallel resistors, coupling loss,…
Parallel resistors acting as QH
Parallel resistors acting as QH

## Slide 35: Example of simulated quench and FPA in a 600 A undulator circuit -3
Time of quench for each turn
Main cause of quench
for each turn
Peak power deposition
due to coupling loss
Simulating this transient offers additional insights. In this example, we see the time and cause of quench for each turn, which brings additional understanding of the magnet+circuit behavior
In this example, coupling loss is responsible for quenching ~30% of the turns

## Slide 36: Example of simulated quench in a 120 A circuit
Voltage distribution
Magnet current and hot-spot T
Temperature evolution in the coil turns
T evolution in coil cross-section
3D model of a self-protecting magnet coil during a quench discharge
Coupling loss is included in the simulation as well
Simulation time <1 h

## Slide 37: Simulated electrical, magnetic, thermal model of persistent currents
Current versus time
Differential inductance versus current
Hysteresis and IFCL loss versus time
Average magnetization versus average field
Included: average magnetization in each strand, hysteresis loss, effect of persistent currents on the magnet differential inductance

## Slide 38: HL-LHC TRANSIENTS

## Slide 39: MQXFBP2 trimmed powering tests -1
Thanks to F. Mangiarotti
Currents in the circuit
Voltages across the four coils
Voltages to ground at t=150 ms
Co-simulation between MQXF magnet model [LEDET] and electrical circuit [PSPICE]
Good agreement achieved between simulations and measurements

## Slide 40: MQXFBP2 trimmed powering tests -2
Thanks to F. Mangiarotti
Currents in the circuit
Voltages across the four coils
Voltages to ground at t=150 ms
Good prediction capability demonstrated (after non-uniform RRR in the wire was modeled, see next slide)
Simulations allow assessing the peak voltages to ground when voltage taps are unavailable or too coarse

## Slide 41: Effect of non-uniform RRR within the Nb3Sn/Cu wire
Thanks to B. Bordini, F. Mangiarotti, G. Willering
Courtesy of B. Bordini
Coil resistance during warm-up
Extra ohmic heating due to wire Cu RRR non-uniformity
During MQXFS7b model magnet test, resistive voltage much higher than expected was observed in one coil
The observed transients were reproduced by including in the LEDET software the option to model the wire thermal evolution assuming three Cu regions with different RRR: high RRR (~160) Cu outside the barrier, medium RRR (~80) Cu inside the barrier in the core, low RRR (<10) Cu inside the barrier between filaments.
Wire cross-section

## Slide 42: HL-LHC Inner Triplet circuit simulations
Failure analysis to identify the worst-case scenario for each circuit component (crowbars and current leads of the main and trim power converters, warm and cold Diodes, …) and allow their dimensioning
Analysis performed by combining one PSPICE circuit with 6 LEDET magnet models in a co-simulation
Courtesy of S. Yammine

## Slide 43: Simulations of an intermittent short-circuit in an 11 T dipole magnet
D2U
D2L
D1L
D1U
Rshort
Thanks to G. Willering
Analysis performed with a combination of LEDET and PSPICE magnet models
Experimental observations qualitatively reproduced with the developed model [Note: The analysis remains inconclusive: no clear evidence of a short-circuit]

## Slide 44: STEAM USERS

## Slide 45
2nd STEAM workshop [October 2021, indico]
UPDATES ON STEAM DEVELOPMENT
PRESENTATIONS FROM STEAM USERS
HANDS-ON SESSIONS ON ALL THE TOOLS
Figures from the presentations at the workshop by D. Davis, D. Delkov, V. Ferrentino,
M. Janitschke, V. Marinozzi, M. Mentink, X. Sarasola, O. Tranum Arnegaard, M. Wozniak

## Slide 46: SOME HIGHLIGHTS FROM 2022

## Slide 47: Some highlights from 2022

## Slide 48: WHY STEAM COULD BE USEFUL FOR YOU

## Slide 49: Why STEAM could be useful to YOU
We can offer help to
Obtain reference cases for transients in LHC and HL-LHC magnets and circuits (quenches, ELQA high-voltage tests, power-converter switching-off, energy-extraction switch opening, transfer function measurements, suspected failures…)
Understand the behaviour of non-trivial circuits (magnet chains, parallel paths, nested magnets, etc)
Assess the impact of proposed changes to circuit hardware or operation modes
Study failure scenarios
Identify worst-case scenarios for circuit components
Attempt to reproduce unexpected events or observations
Develop simulations for R&D quench detection and protection techniques
Benchmarking simulation programs, especially when new features are developed
Provide boundary conditions for analyses of other systems
Obtain material properties in various forms
Enhanced integration between measurements and STEAM library at all levels

## Slide 50
Design
Manufacturing
Testing
Operation
Failure cases considered when designing a magnet
Worst-case scenarios used to define electrical design criteria
Integrating new quench protection systems into the design at early stage
Assessment of new quench protection concepts
Information on wires, cables, coils, magnets, circuits is linked to models
Influence of coil electrical order on peak voltages to ground assessed
Frequency transfer measurements at different stages
Automatic simulation of each proposed test plan
Systematic validation of the simulation results
Proposed non-standard tests can be evaluated
Unexpected transients can be analyzed and reproduced
The same model that has been validated is used to understand and reproduce unexpected events
All conductor, magnet, circuit models can be linked in consistent co-simulations
Effect of hardware (EE, power supply crowbars,…) or operation changes (quench detection thresholds, EE timing,…) can be evaluated
Some practical examples to continue and enhance cooperation between STEAM and CERN magnet lifetime

## Slide 51
A BIG THANK YOU TO THE SM18 TEAM
FOR THEIR CONTINUOUS SUPPORT!

## Slide 52: Useful links
STEAM website | http://cern.ch/steam
STEAM Workshop | https://indico.cern.ch/event/1060073/
STEAM meetings | https://indico.cern.ch/category/11772/
Section publications | https://twiki.cern.ch/twiki/bin/view/TEMPEPE/SectionPapers
Section technical notes | https://twiki.cern.ch/twiki/bin/viewauth/TEMPEPE/SectionVariousContributions
Section talks | https://twiki.cern.ch/twiki/bin/view/TEMPEPE/SectionTalks

## Slide 53: ANNEX

## Slide 54: Examples of what STEAM models were used for in 2021
LHC
Frequency
domain
Quench
Heaters
Short
circuits
SC effects
Simulate an internal short-circuit in an MB magnet (in RB, main dipole circuit)
Analyse earth current in RB circuits during quenches and FPA
Simulate powering transients of an MCBY magnet with an internal short-circuit
Assess the consequences of raising MB quench detection thresholds (worst-case analysis)
Analyse quench protection of Q1 magnet in RQX.R1 with non-conform quench heater discharge unit
Calculate the effect of quench-heater field on the beam, including the effects of beam-screen shielding and inter-filament coupling currents in the magnet coil
Simulate quench-heater protection of MQY magnet at T=1.9 K
Reproduce the measured frequency-domain impedance of MB magnets measured in the tunnel, including the effect of neighbouring magnets
Assess when quench-back is expected in 600 A circuits
Simulate the effects of persistent-currents on the powering transients in LHC circuits

## Slide 55: Examples of what STEAM models were used for in 2021
HL-LHC
Frequency
domain
Baseline verification
Validation and Predictions
Systematic measurement/simulation comparison during events in various test campaigns SM18
Simulation of transients in CCT-type magnet, and validation with MCBRD prototype magnet data
Simulate proposed MQXF special trimmed powering tests
Explain the observed extra ohmic loss in coils made of conductor with non-uniform RRR
Estimate the effect of QH discharge on voltages across coils and quench-antenna coils
Verification of baseline quench protection for various HL-LHC circuits
Parametric analyses and worst-cases for all circuit components in HL-LHC Inner Triplet circuit
Analyse quench protection of HEL larger solenoids
Uncertainty quantification by automatically performing hundreds of parametric simulations
Simulate of the effects of additional insulation layers between quench heaters and coil
Propose MQXF coil electrical order that minimizes the expected peak voltage to ground
Frequency transfer function analysis of one MQXF coil

## Slide 56: STEAM superconducting circuit library
Circuit family | Number of circuit types | Number of circuits | Circuit protection
Main dipole | 1 | 8 | QH + By-pass Diode + EE
Main quadrupole | 1 | 16 | QH + By-pass Diode + EE
Inner triplets | 1 | 8 | QH
Individually powered dipoles | 3 | 16 | QH
Individually powered quadrupoles | 7 | 78 | QH
600A - with EE | 11 | 200 | EE
600A - without EE | 10 | 192 | Self-protecting
600A undulators | 1 | 2 | EE + Parallel resistors acting as QH
80A-120A circuits | 10 | 300 | Self-protecting
60A circuits | 2 | 752 | Self-protecting
Total | 47 | 1572 | 
EE = Energy-extraction system. QH = Quench Heaters |  |  | 
All LHC circuit types are modelled in the Circuit Library, with the exception of the inner triplet nested correctors.
Models of individual circuits can be generated on demand (small differences in warm resistance, EE, etc).
Models of HL-LHC magnet circuits are being prepared following the same approach.

## Slide 57: Example of simulated quench and FPA in an RQ circuit
D. Pracht and M. Janitschke, TECH
Fast power aborts at 8-12 kA
Fast power aborts at 5-7 kA
Fast power aborts at 2-4 kA
Reference FPA curves simulated for different current levels
Currents through the magnets and cold Diodes are not measured and can be assessed only by simulations

## Slide 58: Example of unusual transient to analyze – quench in RU.R4
Circuit current drops suddenly...?
Then bounces back up...?
from LHC Project Report 894
Hint: Parallel resistor is also a quench heater and heats up pretty quickly…

## Slide 59: Some topics worked on in 2022
M. Wozniak, E. Ravaioli, A. Verweij, "Co-Simulation of Quench Behaviour of HL-LHC Dipole Canted Cos-Theta Orbit Corrector Prototypes"
A. Vitrano, M. Wozniak, E. Schnaubelt, T. Mulder, E. Ravaioli, A. Verweij, "An open-source finite element quench simulation tool for superconducting magnets"
T. Mulder, E. Schnaubelt, M. Wozniak, E. Ravaioli and A. Verweij, "External Coil Coupled Loss Induced Quench (E-CLIQ) System for Protection of LTS Magnets"
E. Ravaioli, A. Verweij, M. Wozniak, "Analysis of an internal electrical short in an LHC orbit-corrector magnet with a 3D multiphysics simulation"
E. Schnaubelt, M. Wozniak, S. Schöps, "Quench Simulation of No-Insulation HTS Coils With 3D FEM Using a Thin Shell Approximation"
B. Caiffi, L. Bender, A. Bersani, S. Farinon, A. Foussat, F. Levi, F. Mangiarotti, D.Novelli, A. Pampaloni, E. Ravaioli, E. Todesco, G. Willering, "Protection Scheme Effectiveness Study for the Hi Luminosity LHC MBRD magnet"
S. Yammine,..., E. Ravaioli,..., et al., "Experimental Program of the HL-LHC Inner Triplet String Test at CERN"
… as a list of abstracts accepted for ASC2022
CCT
HTS
E-CLIQ
LHC