## Slide 1: A preliminary study of the target and capture channel for the Muon Collider
A. Portone, P. Testoni (F4E Barcelona)
L. Bottura, A. Kohlemainen (CERN)
12/10/2022

## Slide 2: SUMMARY
Starting from the hybrid solution of US-MAP [1-3] with 5 resistive coils and 19 SC coils (2.4 m bore) we compute for such design field on axis, field on coils, stresses etc.
  Field on axis follows B-formula by Sayed-Berg [4] with wider plateau @ 20 T
  Coils stresses/fields seems manageable
  Large bore magnetic energy (~3 GJ) and global forces
  Coupling forces between resistive and SC coil set to be managed carefully
We develop an alternative solution with 18 SC coils (HTS), 1.2 m constant bore and engineering current density similar to (1) (i.e. max(JE)40 A/mm2):
  Field on axis within 1% accuracy Sayed-Berg formula over 16 m channel length
  Magnetic energy < 1 GJ
  Advantages brought by HTS and smaller bore! However its feasibility needs verification (shielding?)

## Slide 3: REFERENCES
R.J. Weggel, N. Souchlas, H.G. Kirk, V.B. Graves, K.T. McDonald, A TARGET MAGNET SYSTEM FOR A MUON COLLIDER AND NEUTRINO FACTORY, TUPS053 Proceedings of IPAC2011, San Sebastián, Spain
R.J. Weggel, N. Souchlas, H.K. Sayed, J.S. Berg, H.G. Kirk, X. Ding, V.B. Graves, K.T. McDonald, DESIGN OF MAGNETS FOR THE TARGET AND DECAY REGION OF A MUON COLLIDER/NEUTRINO FACTORY TARGET TUPFI073 Proceedings of IPAC2013, Shanghai, China
C. Rogers, Overview of target, capture and cooling complex, https://indico.cern.ch/event/1147941/
H.K. Sayed and J. S. Berg, Optimized capture section for a muon accelerator front end, PHYSICAL REVIEW SPECIAL TOPICS - ACCELERATORS AND BEAMS 17, 070102 (2014)

## Slide 4: HYBRID (NC+SC) DESIGN (US-MAP): Field, Forces and Stresses

## Slide 5: INPUT DATA
Resistive coils (5):
Rmin = 0.178 m
Superconducting coils (19):
Rmin(HF) = 1.2 m

## Slide 6: FIELD ON AXIS

## Slide 7: CURRENTS AND MAGNETIC ENERGY
2.89 GJ
1.05 GJ
ATLAS main toroid

## Slide 8: SMEARED STRESSES AND AXIAL FORCE

## Slide 9: FIELD AND VECTOR POTENTIAL

## Slide 10
Von Mises stresses svM

## Slide 11: STRESSES
Hoop stresses
sj
Axial stresses
sZ

## Slide 12: OUTPUT DATA
 | Max B (T) | FR (N) | Fz (N) | Max SR (Pa) | Max SZ (Pa) | Max Sj(Pa)
Coil1 | 19.66 | 7.75E+07 | 4.20E+06 | -5.65E+07 | -2.41E+07 | 4.90E+07
Coil2 | 19.91 | 1.50E+08 | 2.08E+05 | -5.32E+07 | -2.88E+07 | 5.02E+07
Coil3 | 19.87 | 9.39E+07 | -2.07E+06 | -6.44E+07 | -3.04E+07 | 4.95E+07
Coil4 | 18.59 | 4.05E+07 | -1.30E+06 | -7.64E+07 | -3.63E+07 | -3.34E+07
Coil5 | 15.88 | 1.34E+07 | -5.35E+05 | -3.30E+07 | -1.47E+07 | -1.43E+07
Coil6 | 15.33 | 1.54E+09 | 4.64E+08 | -2.66E+07 | 1.14E+08 | 2.96E+08
Coil7 | 12.98 | 0.00E+00 | 0.00E+00 | 1.11E+07 | -1.85E+08 | 2.10E+08
Coil8 | 13.84 | 2.14E+09 | -4.14E+08 | 7.63E+07 | -1.74E+08 | 2.70E+08
Coil9 | 7.79 | 8.07E+06 | -2.59E+06 | -2.18E+07 | -4.34E+07 | 2.23E+08
Coil10 | 7.16 | 1.07E+08 | -2.64E+07 | -5.25E+06 | -3.36E+07 | 1.52E+08
Coil11 | 5.02 | 2.66E+07 | -8.57E+06 | -1.22E+06 | -4.04E+07 | 1.25E+08
Coil12 | 4.16 | 2.69E+07 | -5.75E+06 | -1.28E+06 | -1.88E+07 | 9.10E+07
Coil13 | 3.32 | 1.33E+07 | -2.74E+06 | -9.30E+05 | -1.53E+07 | 7.10E+07
Coil14 | 2.94 | 1.07E+07 | -1.67E+06 | -8.98E+05 | -9.19E+06 | 5.29E+07
Coil15 | 2.55 | 6.18E+06 | -7.66E+05 | -7.64E+05 | -6.78E+06 | 3.92E+07
Coil16 | 2.18 | 4.79E+06 | -2.95E+05 | -6.64E+05 | -4.09E+06 | 2.96E+07
Coil17 | 1.84 | 3.98E+06 | -1.57E+05 | -5.79E+05 | -3.23E+06 | 2.46E+07
Coil18 | 1.71 | 3.53E+06 | -1.47E+05 | -5.33E+05 | -3.21E+06 | 2.22E+07
Coil19 | 1.58 | 2.85E+06 | -1.04E+05 | -4.37E+05 | -2.63E+06 | 1.99E+07
Coil20 | 1.51 | 2.66E+06 | -7.65E+04 | -4.17E+05 | -2.62E+06 | 1.85E+07
Coil21 | 1.41 | 2.27E+06 | -5.70E+04 | -3.52E+05 | -2.22E+06 | 1.71E+07
Coil22 | 1.39 | 2.19E+06 | -3.05E+04 | -3.46E+05 | -2.19E+06 | 1.64E+07
Coil23 | 1.34 | 2.04E+06 | -4.42E+04 | -3.24E+05 | -2.20E+06 | 1.57E+07
Coil24 | 1.29 | 3.63E+06 | -4.53E+05 | 4.67E+05 | -6.91E+06 | 1.50E+07
Peak axial force: 464 MN
Cumulative axial force:
464 MN
Peak hoop stress:300 MPa

## Slide 13: A 3D VIEW AND SOME ISSUES
500 tons
20 tons
Single cryostat ? Longitudinal forces are significant, require space, and result in additional heat loads
The gravity support of the warm radiation shield (approx 300 tons) should go through the cryostat

## Slide 14: HTS (PRELIMINARY) DESIGN: Field, Forces and Stresses

## Slide 15: OPTIMAL FIT OF FIELD ON AXIS
Reference field formula (Sayed-Berg [4])
With Bi=20 T, Bf=1.5 T, Lt=15 m
-1<z(m)<15

## Slide 16: FIELD ON AXIS

## Slide 17: COMPARE FIELD ON AXIS
Blue = US-MAP
Red = OPT. FIT

## Slide 18: CURRENTS AND MAGNETIC ENERGY
1 GJ !!!

## Slide 19: SMEARED STRESSES AND AXIAL FORCE

## Slide 20: FIELD AND VECTOR POTENTIAL

## Slide 21
von Mises stresses svM

## Slide 22: STRESSES
Hoop stresses: sj
Axial stresses: sZ

## Slide 23: COILS OUTPUT DATA
 | Rc(m) | Zc(m) | DR(m) | DZ(m) | I(MA)
Coil1 | 0.800 | -1.694 | 0.400 | 1.012 | 3.820
Coil2 | 0.800 | -0.682 | 0.400 | 1.012 | 10.124
Coil3 | 0.800 | 0.329 | 0.400 | 1.012 | 17.535
Coil4 | 0.800 | 1.341 | 0.400 | 1.012 | 18.321
Coil5 | 0.800 | 2.353 | 0.400 | 1.012 | 12.916
Coil6 | 0.800 | 3.365 | 0.400 | 1.012 | 8.825
Coil7 | 0.667 | 4.376 | 0.133 | 1.012 | 5.250
Coil8 | 0.667 | 5.388 | 0.133 | 1.012 | 4.203
Coil9 | 0.667 | 6.400 | 0.133 | 1.012 | 3.227
Coil10 | 0.667 | 7.412 | 0.133 | 1.012 | 2.621
Coil11 | 0.667 | 8.424 | 0.133 | 1.012 | 2.173
Coil12 | 0.667 | 9.435 | 0.133 | 1.012 | 1.909
Coil13 | 0.622 | 10.447 | 0.044 | 1.012 | 1.591
Coil14 | 0.622 | 11.459 | 0.044 | 1.012 | 1.485
Coil15 | 0.622 | 12.471 | 0.044 | 1.012 | 1.335
Coil16 | 0.622 | 13.482 | 0.044 | 1.012 | 1.343
Coil17 | 0.622 | 14.494 | 0.044 | 1.012 | 1.077
Coil18 | 0.622 | 15.506 | 0.044 | 1.012 | 1.728
Coil mass 111 tons

## Slide 24: FIELD, FORCES AND SMEARED STRESSES
 | Max B (T) | FR (N) | Fz (N) | Max SR (Pa) | Max SZ (Pa) | Max Sj(Pa)
Coil1 | 9.23 | 5.51E+07 | 3.57E+07 | -2.04E+06 | -3.93E+07 | 9.11E+07
Coil2 | 16.22 | 2.80E+08 | 1.19E+08 | -1.26E+07 | -9.83E+07 | 2.93E+08
Coil3 | 20.14 | 6.99E+08 | 1.20E+08 | -2.42E+07 | -1.43E+08 | 4.49E+08
Coil4 | 20.34 | 7.71E+08 | -6.04E+07 | -2.61E+07 | -1.46E+08 | 4.53E+08
Coil5 | 18.16 | 4.46E+08 | -1.05E+08 | -1.68E+07 | -1.24E+08 | 3.66E+08
Coil6 | 13.25 | 2.12E+08 | -6.95E+07 | -1.18E+08 | -1.53E+08 | 1.94E+08
Coil7 | 9.08 | 9.62E+07 | -1.96E+07 | -1.31E+08 | -3.16E+08 | 1.24E+08
Coil8 | 6.39 | 5.12E+07 | -8.76E+06 | -2.25E+06 | -4.39E+07 | 9.52E+07
Coil9 | 4.84 | 2.96E+07 | -4.54E+06 | -1.44E+06 | -2.48E+07 | 5.43E+07
Coil10 | 3.76 | 1.90E+07 | -2.45E+06 | -9.13E+05 | -1.48E+07 | 3.29E+07
Coil11 | 3.05 | 1.29E+07 | -1.40E+06 | -6.20E+05 | -9.77E+06 | 2.17E+07
Coil12 | 2.56 | 9.28E+06 | -1.08E+06 | -1.54E+07 | -2.18E+07 | 1.64E+07
Coil13 | 2.24 | 6.97E+06 | -5.23E+05 | -1.38E+07 | -4.46E+07 | 2.64E+07
Coil14 | 1.86 | 5.56E+06 | -3.30E+05 | -3.01E+05 | -1.10E+07 | 2.28E+07
Coil15 | 1.69 | 4.52E+06 | -1.79E+05 | -2.50E+05 | -9.15E+06 | 1.87E+07
Coil16 | 1.58 | 4.27E+06 | -2.31E+05 | -2.47E+05 | -7.73E+06 | 1.64E+07
Coil17 | 1.59 | 3.14E+06 | 1.35E+05 | -2.44E+05 | -8.78E+06 | 1.63E+07
Coil18 | 1.74 | 4.97E+06 | -1.22E+06 | -4.17E+05 | -1.03E+07 | 2.02E+07
Peak axial force: 120 MN
Cumulative force:
±275 MN
Peak hoop stress: 453 MPa

## Slide 25
SOLDERED HTS STACK
COPPER FORMER
COOLING CHANNEL
COPPER SLEEVE
STAINLESS STEEL JACKET
D. Uglietti et al 2015 Supercond. Sci. Technol. 28 124005
M. Takayasu et al., IEEE TAS, 21 (2011) 2340
Zachary S Hartwig et al 2020 Supercond. Sci. Technol. 33 11LT01
G. Celentano et al., IEEE TAS, 24 (2014), 4601805
Y. Nagato et al., Nucl. Fus., 55 (2015) 053021
T. Mulder et al., IEEE TAS, 26 (2016), 4803605
SUPERCONDUCTOR OPTIONS

## Slide 26
MUCOL TARGET SOLENOID CABLE |  | 
Copper diameter | 0.02 | (m)
Hole diameter | 0.006 | (m)
Jacket outer dimension | 0.035 | (m)
HTS stack width | 0.006 | (m)
HTS stack thickness | 0.006 | (m)
number of stacks | 4 | (-)
A non-Cu | 0.000144 | (m2)
A hole | 0.000028 | (m2)
A Cu | 0.000142 | (m2)
A Jacket | 0.000911 | (m2)
A cable | 0.001225 | (m2)
f non-Cu | 0.12 | (-)
f Cu | 0.12 | (-)
f Jacket | 0.74 | (-)
JE non-Cu (20 K 20 T) | 400 | (A/mm1)
JE cable (20 K, 20 T) | 47 | (A/mm1)
JE Cu (20 K, 20 T) | 406 | (A/mm1)
SOLDERED HTS STACK
COPPER FORMER
COOLING CHANNEL
COPPER SLEEVE
STAINLESS STEEL JACKET
35
20
Operating current: 60 kA
Operating field: 20 T
Operating temperature: 20 K
Jacket fraction: 74 %

## Slide 27: Conclusions
There are many magnetic configurations that provide a suitable B(s) profile in the target and capture section. We explored one possible choice based on:
  Modular magnetic configuration (constant bore, identical coil geometry) to simplify the magnet
  Use of HTS to provide the desired field, avoiding the resistive insert, and operating at temperature higher than liquid helium (virtual increase in COP by a factor 4)
We found that the system mass and stored magnetic energy can be reduced (by a factor 2), as well as the cumulative attractive force between coils (by a factor 1.75)
This looks interesting enough to follow-up. The suitability of this variant needs to be studied further, integrating beam, target, shielding, cryogenic and vacuum requirements