## Slide 1: MSC-MME Collaborative work on materials characterization
21/07/2022 – Updates on samples to test
MSC - MME Collaborative work on Materials' Characterization #2 (21 July 2022) · Indico (cern.ch)

## Slide 2
Selected key-topics
Samples for the first phase
Study approach and procurement of samples

## Slide 3
Selected key-topics
Samples for the first phase
Study approach and procurement of samples

## Slide 4
Nb3Sn magnets design
Mechanical Characterization of Nb3Sn
Stress Limits & Degradation
Behavior at interfaces
Modeling techniques in FEA
Collared vs B&K structures
Insulations & Epoxy resins
Instrumentation form design phase
Geometrical interferences

## Slide 5
Mechanical characterization of Nb3Sn
  Understand the impact of the variables in a cable stack (number of strands, diameter of them, Cu fraction, identify irreversible strain regions… );
  Initial toe: material vs structural effect;
  CTEs;
Behaviour at interfaces
  Impregnated regions (cable to wedge) vs normal contact regions (midplane);
  Effect of surface irregularities;
  Effect of medium materials;
Modelling techniques in FEA
  Definition of adequate material modelling techniques for 2D and 3D FEA (RT and cold).

## Slide 6
Selected key-topics
Samples for the first phase
Study approach and procurement of samples

## Slide 7
[1] Ten Kate HHJ et al (1991) Development of an experimental 10 T Nb3Sn dipole magnet for the CERN LHC. IEEE Trans Magn 27(2):1996–1999
[1]
keystone angle
width
mid-thickness
Thin edge: high compaction
Thick edge: lower compaction
Cable configurations in samples
keystone compensated:
attempts to be cable-representative
It is not simply a matter of stress decomposition; we also have varying stiffness across the width.
p
Let’s discuss about it
keystone not compensated:
attempts to be coil-representative

## Slide 8
* We are in fact assuming that the rectangular configuration should be the reference.
First sample campaign
The first samples should address this issue.
We are looking for a cable both in keystoned and non-keystoned version.
First goal is to understand which version of keystoned cable is more representative of the rectangular one*.
Assumed reference
vs.

## Slide 9
Selected key-topics
Samples for the first phase
Study approach and procurement of samples

## Slide 10
Study approach
The first tests will address the issue of the keystone, laying the bases for the real test campaign.
A second important step would be to look at local effects at the interfaces:
  Cable stack to universal testing machine tooling
  Cable stack to cable stack
  Intermediary polymide sheets (Kapton) and other medium materials
  Cable stack to impregnated wedge
Then, we can investigate the impact of the resin volume fraction (stack compaction).
Across this study we will consider the reproducibility of the results with material models combinations in FEA. Hence, CMM measurement and surface characterization should be carried throughout.

## Slide 11
Samples procurement
We are grouping:
  Available cables (Cu, SC, keystoned and rectangular)
  RHT molds for cable stacks;
  Impregnation molds for cable stacks;
Roughly by the end of August this material and knowledge should be centralized, so that we can proceed with drawing a testing matrix a more detailed plan.