## Slide 1: Status w31 2022
Fredrik PG

## Slide 2: Timeline
Milestones achieved:
TPX lens arrived
Pulsed proton source characterized
C foil installed in chamber
Milestones remaining:
Hg,Cd,Na lamps not arrived
but they have been shipped
MCP feedthroughs still missing.

## Slide 3: A simple proton source
Powersupply tripping at 300uA
FI
MCP
+5kV
Protons
Electrode placed near plasma and biased to +0 to +5kV.
5mA, 0-20kV Heinzinger power supply acquired
SHV feedthrough borrowed from MIRACLES
Stable proton beam observed from 200V to 5kV
Beam on
def on
def off
plasma off
Deflector

## Slide 4: TOF of pulsed proton source, at different bias voltages
0.3 mbar plasma pressure
Temp of plasma

## Slide 5: What are these peaks?
3us
10us
16us
19us
23us
3us -> 270eV protons
10us, 270eV 12 amu
16us, 270eV 30 amu
19us, 270eV 44 amu
23us, 270eV 65 amu
Hole caused by beam?

## Slide 6: Transmission through 12nm thick C-foil
Example: With 200V we expect 85% transmission with a beam energy of 185(25) eV resulting in 5.5us/m TOF
200 eV p+ beam
Beam energy TOF
Transmission through 12nm foil

## Slide 7: H(2s) production using C-foil
+3000V
C-foil
MCP
+200 V
Grid
0V
0V
+50V
H(2s)
H+
H*
H*
366 nm
2.5us
-50V
-10V
0V
Stable proton beam observed
For testing laser excitation to Rydberg states we can use the C foil with a 200eV proton beam.
Unfortunately the TOF will be too short for any Deexcitation studies..

## Slide 8: SIMION simulation of setup
12cm
+3000V
+50V
0V
0V
300eV
Detector for 2s detection?
OBS: Ions field ionized have a TOF of roughly 1.2us
while ions not produced in FI region have a TOF of 3us.
This could be used for discrimination.

## Slide 9
Installation of foil (ongoing)
Excitation region:
Ion beam filtering
FI region
C foil
Study TOF after installation of foil at different beam energies.

## Slide 10: Voltage applied on Longitudinal FI electrodes
Fast protons are filtered when increasing voltage on FI
0.3mbar plasma pressure biased at +3kV

## Slide 11: At 3kV voltge compared.

## Slide 12: Stability of source