## Slide 1
The Third Direct Detection Talk
(title amended on Slide 7)
Prisca Cushman
University of Minnesota
14th UCLA Symposium on Dark Matter
Los Angeles, CA March 29 – April 1 2023

## Slide 2: Direct Detection is like playing CLUE
We have a well-established crime scene
But we don’t know who did it
nor what weapons they have in their arsenal

## Slide 3
Prime Suspect:
The WIMP
in the Cosmos with the …
Weakly Interacting Massive Particle
Gravity
E&M
Weak
Strong
The Weak Interaction is allowed and provides the right relic density with a simple thermal equilibrium model in the early Universe. But no smoking gun yet.

## Slide 4: The Prime Suspect is still on the loose!
Weak
But his hideout is well-known
and currently staked out.
But here is where I am having some trouble with the title assigned by the
conference organizers:
“Direct Detection without Noble Gases”

## Slide 5
That covers all the rest of the rooms
and other suspects

## Slide 6
and plenty of new interactions
?
Light Mediator
?
Heavy Mediator
That covers all the rest of the rooms
and other suspects

## Slide 7: 2017 Cosmic Visions mapped DM mass to generic coupling
Weak
?
?

## Slide 8: Direct Detection without Noble Gases
Weak
?
?
of Particle DM
>
Liquids
below a TeV
And I will cede CCDs and (most) sub-GeV dark matter to Rouven who speaks next

## Slide 9: Nuclear Recoiling Dark Matter Future – Snowmass View
One experiment proves dark matter interacts with SM particles with force(s) other than gravity
Multiple experiments not only confirm the detection,
They are essential to probing the nature of the interaction.
Spin-independent searches will reach the neutrino fog by mid-century
LXe TPCs will then probe atmospheric neutrinos
LAr (TPCs and Scintillating bubble chambers) probe solar n
Solid state bolometers spawn
  small phonon-only (TES readout of LHe, Al2O3, Ga As, Si)
  and voltage-assisted phonon amplification (Ge, Si…)
Charge-only devices (CCDs and HPGe) cut a swath
Along with gas proportional chambers with light noble gas
with large overlap
Xenon
Argon
Ge,CaWO4
Spin-dependent phase space is wide-open at lower masses
but technology to probe deep at 10 – 100 GeV/c2 is well-developed
sSD reach can’t take advantage of the coherent A2 enhancement
Si, LHe, Al2O3,
Ga As
Neon

## Slide 10: Snowmass gave us a new mantra: Delve deep and Search wide Experimental Strategy for the next 20 years
Noble Liquids continue to look for the prime suspect: Large exposure, good NR discrimination
Solid State
Phonons + SuperCDMS, EDELWEISS, CRESST. Target lower mass DM with excellent NR discrimination.
Tension: Max exposure + NR discrimination… or … Low threshold (small crystals, NTL amplification)
Phonon only: Remove charge noise and expand your choice of target (TESSERACT)
Charge only: DAMIC, SENSEI CCDs. Sub-GeV ER dark matter, single electron sensitivity
CDEX Point-contact Ge detectors. Can you make a 0nbb detector with low enough threshold to do a light DM search?
Annual Modulation Program NaI crystal arrays with very low background and stable conditions
Bubble chambers: Insensitive to electron-recoil DM  the best discrimination possible PICO program: Freon (and other fluorocarbons) gives access to spin-dependent NR interactions.
Nucleation Threshold determined by T, P  no energy information except by tuning conditions SBC (Scintillating bubble chambers) Use scintillation of noble liquids to measure the energy event-by-event.
Current plan with LAr  go for the ~ 1GeV NR, no spin-dependence. Target CEnNS as well as DM
Gas Detectors: Light DM mass: e.g. NEWS-G spherical proportional chamber with Ne + CH4
Probe below the neutrino fog with directional information (e.g. CYGNUS)
Technology is advanced, but exposure is challenging.

## Slide 11: Summary of Spin-dependent target opportunities
73Ge (7.73%) <Sn> = .46
29Si (4.68%) <Sn> = .13
17O (0.037%) <Sn> =.5
129Xe (26%) <Sn>= .33
131Xe (21%) <Sn>= - .27
neutron coupling
7Li (92.4%) <Sp>=.5
127I (100%) <Sp>= .31
23Na (100%) <Sp>= .25
133Cs (100%) <Sp>= - .37
proton coupling
<Sn> = -.11 <Sp>=.44
proton & neutron coupling
PICO (CF3I, C3F8 )
Couples to net nuclear spin JN
1H (100%) <Sp> = .5
19F (% depends on fluorocarbon)
6Li (7.6%)
<Sn> = .472 <Sp>= .472
LXe TPCs
CDMS,EDELWEISS
DAMIC/SENSEI, CDMS
CRESST (CaWO4)
CRESST(LiAlO2 , Li2MoO4)
NaI (and CsI) DAMA, SABRE, ANAIS,
COSINE-100, COSINUS
Snowball (H2O)
CRESST (LiAlO2 , Li2MoO4)

## Slide 12: Nuclear Recoiling Dark Matter: SD targets & technology
But you still have to make a detector out of it.
And in the end, we do not have a spin-analyzing detector, just relative signals in multiple targets.
PICO superheated bubble chambers
Freon (C3F8), also CF3I earlier  proton coupling
Will require new vessel materials to move into the blue
PICO-2L
PICO-60
PICO-40L
PICO-500
LXe TPCs
Bolometers with SD crystals
Supercooled H2O
EDELWEISS, SuperCDMS n-coupling at lower masses
CRESST is exploring new SD crystals with Lithium
XENON, LZ, PandaX  DARWIN cover n-coupling,
but the xenon neutrino fog is decades higher than the fluorine neutrino fog
New technology could be a liquid/solid phase change detector like Snowball

## Slide 13: SI Solid State Players
SNOLAB: SuperCDMS
DAMIC, SENSEI, Oscura
Modane EDELWEISS DAMIC-M
Gran Sasso
CRESST
DAMA/LIBRASABRE North
COSINUS
JinPing
CDEX
CCD-based Point Contact HPGe,
NaI Annual Modulation
Cryogenic Bolometers
Stawell (SUPL) SABRE South
Yangyang
COSINE-100
Canfranc
Anais

## Slide 14: High Purity Germanium Detectors : CDEX at JinPing
CDEX-10 operating now
Runs at liquid nitrogen temperatures
Excellent energy resolution
Doubles as a neutrinoless double beta decay detector
  Get the threshold low enough  DM detector
Use energy resolution to beat down background
No evt by evt ER vs NR discrimination
Some pulse shape discrimination
205 kg-d exposure with 10 kg array of 9 detectors
C10B-Ge1
Ethresh = 160 eVee, sE = 219 eVee FWHM at 10.37 keV

## Slide 15: Principles of Cryogenic Solid State Phonon Detection
Small heat capacity is key!
Large sensitivity (big DT) for a tiny DE deposition.
Tens of mK  dilution fridge infrastructure.
GeNTD: Neutron-transmutation-doped sensors. Ge wafer with T-dependent resistance induced by neutron irradiation doping. Sensitive to thermal phonons.
TES: Transition-edge sensors. Tungsten film operated near Tc and read out by SQUIDs. Dominated by athermal phonons. Sensitive to DT ~0.1 mK
QET: Quasiparticle-trap-assisted Electrothermal-feedback TES: Arrays of Al fins transmit quasiparticles to the TES. Increases collection area without increasing sensor capacitance and maintains athermal phonon properties.
thermal bath
CRESST
EDELWEISS
CDMS
Energy deposition (temperature) is measured by

## Slide 16: Phonons supplemented by a second channel
+ Ionization
+ Scintillation
Vbias
Silicon or
CDMS and EDELWEISS
CRESST

## Slide 17: Yield-based Discrimination Nuclear Recoil (NR)events are “quenched” relative to Electron Recoils (ER)
Q(Si) and Q(Ge): NR Quenched by factor ~ 3
Charge to Heat ratio
Light to Heat ratio
Large quenching factors Q(O) ~ 9; Q(W) ~ 40
SuperCDMS
CRESST
EDELWEISS
COSINUS (welcome to the gang!)
Q(Na) ~ 3
Q(I) ~ 20
Caution: Q is dependent on Energy. Tend to lose NR signal when moving to low mass DM  Calibration required
Small Q requires additional rejection of ER using E-field shaping, timing, veto channels

## Slide 18: electrodes provide field shaping and surface rejection
EDELWEISS FID800
SuperCDMS SNOLAB 1.4 Kg Ge iZIP
Interleaved
Interdigitized
EDELWEISS - III

## Slide 19: High Voltage Mode (SuperCDMS and EDELWEISS)
iZIP and FID: Low bias voltage (2-5 V) gives background-free mode  NTL phonons negligible Ratio of ionization to primary phonon signal is unambiguous
Interleaved phonon and charge sensors on both sides Provides 106 ER/NR discrimination and surface rejection
HV: High bias voltage (~ 100 V) pushes to lower thresholds  NTL phonons dominate. The total phonon signal is larger (amplification means lower thresholds), but it is essentially a measure of the charge signal read out through the phonon channel
Two different modes of operation
Etot ~ Er Y(Er) e Vb
e
NTL
phonons
Work done by Vb in drifting electron-hole pairs
releases additional NTL phonons
Etot = Er + Neh e Vb = Er 1 + Y(Er) e Vb
e

## Slide 20: SuperCDMS SNOLAB Detectors
iZIP
Double-sided readout with E-field-shaping provides z-dependence and surface rejection
HV
No charge readout required. Optimized for phonon energy resolution and collection efficiency (35% coverage) Improved position resolution and double outer ring to sharpen fiducial cut.
Two target materials Ge (1.4 kg) and Si (0.6 kg)
10 cm diameter and 3.3 cm thick

## Slide 21: SuperCDMS TES and collection fin design follows function
Aluminum fins
TES
Charge collection
iZIP
Double-sided readout with E-field-shaping provides z-dependence and surface rejection
HV
No charge readout required. Optimized for phonon energy resolution and collection efficiency (35% coverage) Improved position resolution and double outer ring to sharpen fiducial cut.

## Slide 22: SuperCDMS Strategy Complementary Targets and Multiple Functionality
22
Tower 1 (iZIP)
Tower 2 (HV)
Tower 3 (HV)
Tower 4 (iZIP)
profile likelihood
Mode
HV
iZIP
Project Goals assume Optimum Interval, no prior knowledge of backgrounds. To reach full potential, a profile likelihood analysis will use iZIP background data in the fit.

## Slide 23: Pushing even deeper into the nucleon-coupled DM landscape
Arrays of small 0V
phonon-only detectors
High Voltage
driven by phonon resolution
spt ~ 30 meV  M ~ 50 MeV
driven by charge leakage and ionization resolution
Small HV detectors with e/h sensitivity
Plus new ideas in ER rejection
Phonon + Ionization
Wide-open parameter space at low mass
Exposure is not the driving force
Smaller detectors achieve lower thresholds
Surface runs can provide world-leading results
All of this can happen in the existing SNOLAB cryostat and shielding. Improvements in detector performance can be used to circumvent backgrounds.
Pushing down to the neutrino floor requires exposure and reduced bkgd
Improve ionization resolution and reduce leakage currents or
HV with eh sensitivity

## Slide 24: SuperCDMS is already using small 0 V and single eh-sensitive HV detectors
HVeV (Si or Ge, 1 cm2 x 4 mm). Like a small HV detector with single e-h resolution.
Improving “environmental” phonon-only backgrounds
Phonon resolution in the spt ~ 1 eV range now.
Advances in stress-related bkgds will get to 100 meV
A mosaic of sub-eV spt CPDs on 2 towers can get to masses of 50 MeV
ER events are in the peaks, NR fills in gaps A mosaic of these on 2 SuperCDMS towers can get to the n-fog in 0.5 – 5 GeV range
0V (aka CPD). A thin, phonon-only device with SuperCDMS TES readout

## Slide 25: Will also push deep into Sub-GeV Electron Recoiling regime
cryogenic phonon detectors are well-suited for these searches.
sensitivity to 1–100 eV deposited energy
enabled by small bandgaps ~1 eV
and excellent energy resolution.
Light DM in the 1-100 MeV range
DM scattering off electrons or collective excitations
Extend cross section by 4 - 5 orders of magnitude.
Dark photon and ALPs in the 1-100 eV range.
Absorption by electrons or collective excitations
Improvements in leakage and resolution drives these limits.
  100 times better reach in kinetic-mixing parameter ϵ
  1000 times better reach in gae.

## Slide 26: Same themes in the EDELWEISS program
EDELWEISS - III Large exposure underground for 5 – 30 GeV WIMPs
870 g Ge bolometers with 200 eVee threshold
24 detectors in low background cryostat operated at ~ 18 mK
EDELWEISS – sub-GeV (surface and underground)
33 g Ge bolometers exploring two modes:
LV detectors: Maintain yield discrimination at low energy. Run above ground, collaboration with RICOCHET CEnNS
RED20 18 eV (RMS) heat resolution + 55 eV energy threshold
To get to 10 eV, need to move from FETs to HEMTs
HV detectors: NTL phonon amplification
RED30 Add top and bottom electrodes and run underground
s = 1.8 eVee at 70 V

## Slide 27: EDELWEISS goes athermal
NOW: new 100 nm thick, 20 mm diameter spiral NbSi TES sensor lithographed on a 200 g Ge crystal
Run underground in NTL mode (data next pg)
Future Edelweiss sub-GeVProgram
Cryosel = Thermal Bolometer with NTD thermistor
running at 200 V with 20 eV phonon resolution
Can identify athermal phonons from heat-only events using the NbSi TES
Superconducting Single Electron Device
NbSi TES

## Slide 28: Inelastic scattering extends access to lower mass NR An NR below threshold can be seen in the ER channel.
Migdal Effect
Readjustment of the electron cloud after NR
can spit out an electron of a few hundred eV.
RED20
NbSi
CRESST-III
Xenon-1T

## Slide 29: Inelastic scattering extends access to lower mass NR An NR below threshold can be seen in the ER channel.
Migdal Effect
Readjustment of the electron cloud after NR
can spit out an electron of a few hundred eV.
RED20
NbSi
CRESST-III
Xenon-1T
CDMSLite
CDEX-10

## Slide 30: Inelastic scattering extends access to lower mass NR An NR below threshold can be seen in the ER channel.
Migdal Effect
Readjustment of the electron cloud after NR
can spit out an electron of a few hundred eV.
RED20
NbSi
CRESST-III
Xenon-1T
Bremsstrahlung Probability is 3-4 orders of magnitude less
arxiv:2203.02594
CDMSLiteBrem
Surface runs (MIGDAL) CPD (Si with TES readout)
CDMSLite
CDEX-10

## Slide 31: CRESST – III Program
Recent Spin Independent Limits
New Spin Dependent Limits
Two 10g LiAlOs crystals in LNGS Lithium: 92.4% 7Li (p), 7.6% 6Li (p,n)
Planning for a 100 detector underground exposure
upgrade LNGS cryogenic infrastructure
Develop TES mass production
Continue to improve crystal purity
CRESST has already moved to smaller detectors for improved resolution
arXiv:1904.00498

## Slide 32: A Common challenge: Understanding the Nuclear Recoil Scale at lower energies
?
?
LXe TPC style in-situ neutron scattering is not an option for cryo bolometers
Silicon
Germanium
DD generator
D2 reflector
LUX in-situ
Calibration

## Slide 33: SuperCDMS Nuclear Recoil Scale Measurements at low energy
  Neutron beam at the TUNL facility
  Used a “portable” ADR fridge and a Silicon HVeV
  Next campaign in 2024 with a Germanium HVeV

## Slide 34: SuperCDMS Nuclear Recoil Scale Measurements at low energy
  Neutron beam at the TUNL facility
  Used a “portable” ADR fridge and a Silicon HVeV
  Next campaign in 2024 with a Germanium HVeV
DD generator at FNAL NUMI hall (~300 mwe)
Use the NEXUS fridge and backing array
Run both HVeV with full-scale SuperCDMS HV

## Slide 35: SuperCDMS Nuclear Recoil Scale Measurements at low energy
  Neutron beam at the TUNL facility
  Used a “portable” ADR fridge and a Silicon HVeV
  Next campaign in 2024 with a Germanium HVeV
DD generator at FNAL NUMI hall (~300 mwe)
Use the NEXUS fridge and backing array
Run both HVeV with full-scale SuperCDMS HV
Photo-neutron Source: (88Y or 124Sb) gammas on 9Be
Soudan Lab, Ge iZIP run in CDMSlite mode
Soudan

## Slide 36: SuperCDMS Nuclear Recoil Scale Measurements at low energy
  Neutron beam at the TUNL facility
  Used a “portable” ADR fridge and a Silicon HVeV
  Next campaign in 2024 with a Germanium HVeV
DD generator at FNAL NUMI hall (~300 mwe)
Use the NEXUS fridge and backing array
Run both HVeV with full-scale SuperCDMS HV
Photo-neutron Source: (88Y or 124Sb) gammas on 9Be
Soudan Lab, Ge iZIP run in CDMSlite mode
Developing new neutron capture technique
SNOLAB Si HV in UMN cryo lab exposed to PuBe source of thermal neutrons
Measure nuclear recoil after neutron capture, tag de-excitation g
Soudan

## Slide 37: Good Progress, but further work is required to establish confident interpretation of low mass DM limits from Ge and Si
Ge CDMSlite photoneutron
Silicon NR response falls faster than Lindhard
Quenching in Germanium may depend on temperature or internal electric field
IMPACT
n-capture

## Slide 38: Summary
The role of cryogenic bolometer experiments in this strategy
Near term, large exposure searches which probe NR DM at lower masses
Good sensitivity to inelastic NR (Migdal) and ER dark matter
Active R&D on small detectors which can push deep into ER dark matter
Improvements in the ionization yield discrimination (HEMTs, leakage current, charge resolution)
Coordinated effort to measure NR quenching in Ge, Si
Development of HV alternatives to access lowest energies down to single eh charge sensitivity
Improve phonon resolution without the complication of charge
A multi-experiment Strategy for the future based on “Delve Deep and Search Wide”
The strategy requires development of multiple targets and their readout technology in parallel
Not only because we don’t know where the DM is, but also
because understanding the nature of the interaction will require multiple targets
We have a program that can explore down to the neutrino fog in most scenarios
Not finding a signal (in a particular section of phase space) is as important as finding it.
There is no guarantee that there is only one type of dark matter This decade has produced a wealth of candidates with arguments as compelling as the WIMP

## Slide 39: Backup Slides

## Slide 40: There are a lot of solutions consistent with the gravitational evidence
Search Wide

## Slide 41: Not finding a vanilla WIMP is an incredible scientific accomplishment
Delve Deep

## Slide 42: It puts any new signal in context
A signal! An eye fits into the theory of an animal.
Use its size and what you know about
animals to look for where the tail should be
The region without an animal now tells you which direction it is facing and its environment
check here!

## Slide 43: The model may require you to look with a different sort of detector
A tail!

## Slide 44: Iterate with a new round of active model-building
A signal!
An eye fits into the theory of an animal.
Use its size and what you know about animals to look for where the tail should be
And the region without an animal now tells you
which direction it is facing.
check here!
?
Check a distinguishing feature

## Slide 45: And hope there is a technology available to look there
An ear fits the elephant model better than the rhino model

## Slide 46: And this is still just one part of the jungle

## Slide 47: Multiple SD targets are necessary for best constraints
Example from 2010. Superheated droplet detectors
Using the n-coupled Xenon10 results improved the SIMPLE (C2ClF5) p-coupled results.
| ap| < 0.32, |an| < 0.17
for 50 GeV/c2 WIMP
Current constraints are an order of magnitude better. Note that the players are LXe TPCs and Freon bubble chambers

## Slide 48: Develop new in situ technique Nuclear Recoils induced by neutron capture (n,g) of thermal neutrons
Capture spectrum depends on yield model and detector resolution. Here shown for
two yield models and two resolutions
Use NaI to tag events
with escaped gammas:
these represent “pure” NR.
Running now with large NaI array and new
Si HV detector with
better resolution

## Slide 49: Neutron capture observed Yield again shows low energy suppression in silicon.
Fit data to simulated ER + NR
For NR, choose a yield model.
Data shows a clear (ng) feature
Yield models all require a neutron capture component (by 25s)
Best fit using the Sorenson yield model clearly indicates suppression and possible threshold.

## Slide 50: Measure Y(Er) in Germanium using a photo-neutron source
Last set of runs before disassembling Soudan Facility
Illuminated the SuperCDMS array of germanium iZIPs
For each run, one iZIP was in CDMSlite HV mode.

## Slide 51: Measure Y(Er) in Germanium using a photo-neutron source
Data without Be disk
Data with Be disk
Geant4 MC

## Slide 52
CDMSlite result
Inconsistent with recent Collar measurement.
Is Yield T-dependent?
Or modified by internal field?
Uncertainty dominated by statistics and precision of neutron scattering cross sections
Likelihood fit to modified Lindhard
Soudan CDMSlite photo-neutron source results for germanium
https://arxiv.org/abs/2202.07043

## Slide 53: Measure Y(Er) in Silicon
Liq. Scint. EJ-301/309
Neutron Beam Energy  En
1.9 MeV pulsed (2.5 MHz) protons on LiF target
Tune to the 28Si elastic scattering resonance (56 keV)
Neutron scattering angle  Er
Backing Array (26 PMTs) at 2 distances
3 “lone wolf” to reference large angles
Also measure TOF and g backgrounds
Silicon Detector  total phonon energy
HVeV (0.93 g) with 2 TES channels
Energy Resolution: sp ~ 3 eV
Charge Resolution: seh ~ 0.03 e/h
Etot = Er + ENTL
NTL
phonons

## Slide 54: Yield has significant consequences to our low mass reach in Silicon
..
Yield model previously used for SuperCDMS project limits
All our Si project limits were based on a modified Lindhard (green)that passes through Chavarria ‘16

## Slide 55: The CEnNS Connection
SuperCDMS
CRESST
EDELWEISS
MInER
nu-cleus
Two 3x3 arrays of 6g CaWO4 + 4g Al2O3
read out by W TES
HV, iZIP
Al2O3 + QET
TRIGA research nuclear reactor at TAMU with moveable core
Ricochet

## Slide 56: Recent Excess workshop identifies further clues
Rate differs by x 10 in ”identical” Al2O3 detectors
CPD (both underground and at surface)
EDELWEISS “heat only” events
Relaxing after cooldown is a feature consistent with microfracture stresses

## Slide 57
A Strategy for Low-Mass Dark Matter Searches with Cryogenic Detectors in the SuperCDMS SNOLAB Facility. https://arxiv.org/abs/2203.08463
small 0V
Large HV,
medium iZIP
Nucleon-coupled dark matter (50 MeV – 5 GeV)
dark matter mass (GeV/c2)
dark matter mass (GeV/c2)
Large = SNOLAB (260 cm3)
Medium = 10 cm3
Small = 1 cm3
Dark blue = SNOLAB limits with 4 Towers (in our 7-tower cryostat).
Light blue = In-hand small detector mosaics filling two towers running at 80% duty cycle for 4 yrs.
Dark Grey = Mosaics of upgraded detectors (see next slide) in two towers.
Three two-tower scenarios can fit in the the cryostat and run in parallel.

## Slide 58
yellow line: parameter space consistent with the hint from white dwarf cooling.
heavy mediator
light mediator
dark matter mass (MeV/c2)
dark matter mass (MeV/c2)
dark photon mass (keV/c2)
ALP mass (keV/c2)
A Strategy for Low-Mass Dark Matter Searches with Cryogenic Detectors in the SuperCDMS SNOLAB Facility. https://arxiv.org/abs/2203.08463
Dark photon kinetic mixing ALP effective coupling
J. Cosmo. Astro. Phys. 2016, 057
Light DM coupled to dark photon
pink lines are sharp targets for MA’ = 3 Mc from 2017 cosmic visions workshop
Dark blue: SNOLAB limits with 4 Towers (in our 7-Tower cryostat)
Light blue: In-hand small detector mosaics filling two towers running at 80% duty cycle for 4 yrs.
Dark Grey: Mosaics of upgraded detectors in two towers.
Three two-tower scenarios can fit in the the cryostat and run in parallel.