## Slide 1: TAXS and TAXN ABSORBERS - OVERVIEW
F. Sanchez Galan, HL-LHC WP8 leader
15-08-2022

## Slide 2: Scope Machine-experiment interface
Absorbers to protect the inner triplets and dipoles from the collision debris generated at the interaction point.
Target Absorber for Secondary (TASTAXS)
Target Absorber for Neutrals (TANTAXN)

## Slide 3: Scope – from TAS to TAXS @ P1& P5
TAXS will replace TAS, which are embedded in the forward shielding, at the limit of the experimental cavern and LHC tunnel.
Functionality and design principles will be kept.
Dedicated water cooling to cope with the increased deposited energy, optimised engineering based on experience.
.

## Slide 4
TAXS in CMS Forward Shielding
TAXS absorber (~3.5 T Cu)
Rotating shielding
Fixed Iron nose

## Slide 5
TAXS in ATLAS Forward Shielding
TAXS absorber
and shielding (cradle)
Movable: Octagonal shielding (JFS), cylindrical shielding (JFC)
TAXS
Courtesy of M. Raymond

## Slide 6: TAXS
Cooling (piping), temperature monitoring system (thermocouples) & inserts for supporting rods integrated
4 TAXS (Cu absorbers) 2 Iron shieldings

## Slide 7: TAXS ASSEMBLY
7
LOWER COPPER (no OHFC) CLAMSHELL
UPPER COPPER (no OHFC) CLAMSHELL
BEAM TUBE
COPPER (OHFC)
60 mm ID
SUPPORT CRADLE (only for assembly purposes)
THERMOCOUPLES,
PIPING
Engineering and detailed drawings will be provided by CERN.

## Slide 8: TAXS (4 units)

## Slide 9: TAXS (4 units)

## Slide 10: TAXS shielding/cradle (2 units)
Precise positioning of TAXS via supports/rails

## Slide 11: Scope – from TAN to TAXN @ P1& P5
A new absorber will replace the LHC inside the TAN to protect D2.
External St36 shielding will be kept

## Slide 12: TAXN
Engineering and detailed drawings will be provided by CERN.
Alignment supports provided by CERN.

## Slide 13
13
Lower base plate
Upper base plate
Absorber box
Junction box
Side shielding (2)
Upper shielding
Marble
Beam tube
vacuum chamber
Jacks (3)
The TAN consists of two major sub-assemblies:
- Absorber Box
- Steel Shielding.
TAN ASSEMBLY

## Slide 15
Details of the Cu absorber top slot, ancillaries, supports, slots for cooling pipes and thermocouples

## Slide 16
Absorber supports: Round, plane and slot assembly (sphere and steel 100Cr6 tempered part > 60HRC )

## Slide 20
TAXN absorber (4 units, Cu)
TAXS absorber (4 units, Cu)
Ancillaries (absorber supports/piping, manifolds)
Cradle/Shielding (2 units, cast iron)
Marble shielding (4 units)
Sarcophagui (6-8 units)
TAXN top cover (2 units)
Material deliverables

## Slide 21
FABRICATION/ASSEMBLY PLAN (Q/A) To be prepared by the manufacturer and accepted in a Production Readiness Review
  Lead technician, single contact point for technical discussions.
  Testing & metrology resources.
Non- material deliverables

## Slide 22
The major components of the Acceptance Criteria include the following:
Dimensional checks (Fiducialization measurements). Fitting of the absorbers around the beampipe is key factor for the performance.
Manufacturing record, material certificates
Pressure tests (piping)
Continuity checks for thermocouples
Ancillaries and special tooling needed for handling will be delivered with the absorbers
Acceptance criteria

## Slide 23: Summary:
Design done at CERN
Procurement/manufacturing of components according to CERN drawings and detailed specifications.
Assembly & acceptance tests at factory and and reception tests at CERN with on-site support of industrial contractors (ex.: mechanical assembly, welding, quality control)

## Slide 24
Deliverables
Q3 2024 - Q1 2025

## Slide 25: Thanks