## Slide 1: CCPC-ECS (brief status) & A Tester for the OT FE Electronics
André Massafferri & Antonio Pellegrino
Rio de Janeiro, 15-12-2011
Introduction
  Why a FE Tester
  tester functionalities
Toward a new FE Tester
  design
  time scale
  open questions
CCPC-ECS
  brief status
  First prototype; block diagram & Pinout

## Slide 2: CCPC-ECS Status
concept: generic mezzanine to connect any device to control room
PCIe, I2C, JTag, SPI  CCPC  1Gbs Eth
R&D and mass production: CBPF-Rio
focus on TELL40:
> OnBoard implementation due vertical limitation (ATCA)
> integration discussed in last october in Marseille
PCIe, JTag (& maybe SPI) very useful
I2C not needed due intrinsical control system in ATCA
Validation board: Automatic Testing system for HW & SW
documentation: technical note & specs & Talk
> available for next Electronics meeting

## Slide 3: CCPC-ECS Status (cont’d)
Software low-level on Linux:
> access registers of any Altera FPGA via PCIe OK
> load any Altera FPGA via JTag OK
> I2C control to any device (Temp,Biasing ...) OK
> SPI communication to be done
> PCIe ECS interface our next Benchmark
Low Speed protocols implemented in Cyclone IV FPGA
PCIe  Cyclone IV  I2C, JTag, SPI
I/O flexibility
> Firmwares (except SPI) OK
Prototypes: CCPC-ECS & Validation boards
> both in production  ready Feb/2012
> five 2nd versions  mid 2012
(Brasil, CERN, Marseille*, Lausanne, ...?)

## Slide 4: First Prototype Block Diagram
RJ45
Eth 1Gbs
CON
1xUSB
CON
LVDS
C
O
N
C
C
P
C
Switch
PCIe
CLK
PCIe
C
O
N
D
E
V
I
C
E
LVDS
VGA
adapter
POWER (5V0,3V3,1V5,1V2,1V0)
12V
IP HW
FPGA
Cyclone IV
IP SW
config
external
monitor
1xPCIe
1xPCIe
GPIO(JTag)
1xPCIe
nanoETX-TT Kontron
mezzanine
1xCLK PCIe
6xCLK PCIe
6xPCIe
N x GPIO
4xSPI
4xJTag
8xI2C
flexibility

## Slide 5: First Prototype Pinout
SAMTEC: QMS-078-04.25-L-D-PC4 (device) QFS-078-04.25-L-D-PC4 (ECS)

## Slide 6: Switching topic
A Test Bench for the upgraded OT FE Electronics mass production

## Slide 7: OT FEE Overview
Bridge
C-Frames
Modules
229 FE Boxes
Distribution of LV,HV, ECS/TFC, etc.
straw tubes modules

## Slide 8: FE Electronics (the present one)
Front end box (full size):
channels
4  (32 ch) HV Boards
16 ASDBLR chips
4 OTIS TDC chips
1 GOL chip: 1.6 Gbit/s
HV
TFC&ECS
LV
Data Fiber
MASS PRODUCTION:
500 GOL/AUX Boards
2.000 OTIS TDC Boards
4.000 ASDBLR Boards
2.000 HV Boards
ASDBLR
OTIS
GOL/AUX

## Slide 9: Why a FE Tester?
MASS PRODUCTION:
500 GOL/AUX Boards
2.000 OTIS TDC Boards
4.000 ASDBLR Boards
2.000 HV Boards
A fully automatized FE Tester was mandatory given the large size of the production
Although we tested individually all boards inside a FE Box, a final global test proved invaluable:
  FE assembly defects  ~1/3 of FE Box re-assembled
  synchronicity between 4 OTIS in one FE Box could be checked
We did NOT use ODIN and Tell1, but generated TFC internally and read data asynchronously (see next slides):
  simple setup, ready ahead of time (2 extra Nikhef FTE for 1 year)
  but could not check synchronicity (Bxid, L0id, etc.)

## Slide 10: FE Test Setup
FE Under Test
PC Linux
Atlas Slink “Gola”
Optical Link Data
Inj. “flipper-box”
Altera Board
SPI
TFC + I2C
PC Windows
USB-2-JTAG
JTAG

## Slide 11: FE Tester Functions
Test of global functionality of fully assembled FE-Boxes:
  Analog input signal injection (mimicking straw-like signal)
  Internal Generation of ECS & TFC
  Data Acquisition (Fiber  Disk)
Threshold Scan
Input signal amplitude scan
ASDBLR Testpulse (hi/lo even/odd)
Input signal delay Scan
L0 delay scan
…

## Slide 12: Threshold Characteristics
For a Gaussian Noise, fit efficiency curve with “Erf” and use 50% point as the best estimator

## Slide 13: Threshold Characteristics (cont’d)
Measure hit efficiency profile for each channel, fit Erf to data and determine Vthr[50%] and noise
Hit Efficiency = C2 / C1
Channel-to-channel uniformity within ~50 mV!
Vthr[50%] = 77.92 DAC
noise = 3.03 DAC
Analogously for input pulse amplitude scan

## Slide 14: Timing Tests
About 1.2 TDC channels (~0.5 ns)
Includes Test-Setup resolution etc.
Hit Delay Scan
Fit straight line to data and reject if poor linearity (large 2)

## Slide 15: Noise Tests
OK
Noisy channels

## Slide 16: L0 Delay Checks
L0 Delay
L0 Delay

## Slide 17: In summary: Test Sequence
Threshold characteristics :
Amplitude Scan with input signal  Vthr50%, noise, cross-talk, etc.
Thr Scan with input signal  Vthr50%, noise, cross-talk, etc.
Thr Scan with Testpulse (lo/hi)  Vthr50%, noise, cross-talk, etc.
Noise :
  Thr Scan without input signal
Timing :
    TDC spectra of all channels
    Input delay scan over the full time range
L0 scan :
  L0 Delay Scan in steps of ½ BX
Analysis
  Control histograms automatically generated for all tests, fitting, etc.
All test results available via the Web

## Slide 18: What we learned
quality of production excellent thanks to systematic and meticulous testing
should have (did not!?) tested also high data-load with random triggers
  check synchronicity (mainly Bxid)
we used up >90% of our spares (mainly in commissioning in 2009 and 2010)
  buuuut… repaired all defect FE Boxes!!
  without retaining functional FE Testers, we’d be dead by now!
  FE Tester not only important in production, for whole life cycle!
FE Box transport needs care!?
  Not much use testing, if lousy transport after test!?
  corollary: needs FE Tester also at CERN
GOOD!
NOT GOOD!

## Slide 19: Goal of the project
What tester do we need for the upgraded OT FE?
a tester who can receive the GBTx data
a tester using GBT/GBT-SCA for TFC/ECS
a tester capable of writing “raw” data to disk
  Real time? What bandwidth? Well, let’s say at least “bursts” of O(10,000) consecutive events (a “step” in a threshold/delay scan!)
  histogramming in FPGA? Yes, please!
  data analysis in FPGA? No, thanks!
a tester who can be itself controlled via TCP/IP GbE
  mainly to configure a “step” run (e.g. 33 threshold steps of 10k evts)
  extra controls needed (e.g. SPI) ? Probably not…
When do we need it?
Basic blocks 2nd half next year, 1st prototype in 2013, 3 instances by 2014
CBPF/Nikhef cooperation (aimed at OT), support by Marseille & LHCb Online
Question: commonalities with other test benches??

## Slide 20: The Perfect Answer!
Based on proposal by J-P Cachemiche & A. Massafferri
Data from FE
TFC/ECS
Data to PC

## Slide 21: Overview of OT 40MHz Upgrade
HV cable
Control
Fiber
We have 432 of these objects (FE Boxes in OT)
  36 per C-Frame (12 C-Frames)
OTIS Boards (and ASIC) need replacement
GOL/AUX Board (and ASIC) needs replacement
HV and ASDBLR Boards may remain unchanged
(12-fib. Ribbon)
(2 fibers)
LV cable
So, Tester physical interfaces to/from FE Box are:
  12-fibers ribbon (data: 4 or 8 GBTx)
  2 fibers (bi-directional TFC/ECS)

## Slide 22: Modified FE Test Bench
FE Under Test
PC Linux
Atlas Slink “Gola”
Optical Link Data
Inj. “flipper-box”
Altera Board
SPI
TFC + I2C
PC Windows
USB-2-JTAG
JTAG
Injector can be re-used

## Slide 23: Optical Interfaces
Use input/output configurability of the 312 optical links to/from Stratix V
Snap 12
12 Data from FE
Snap 12
12 Data out to PC
Snap 12
Snap 12
6 bidirectional TFC/ECS

## Slide 24: FPGA Firmware interfaces
E.g. for data from Front-End:
GBT in
10 GbE out
I/O configure
Raw bank fmt
Burst buffering
histogramming
This part of User code (and FE injector control?) by us (CBPF + Nikhef)
However needs clarification:
will there be a TFC/ECS firmware fitting in the same Stratix V?
capable of working (e.g. STEP runs) without external hardware?
will there be basic software (C API? PVSS?) to drive the TFC/ECS?
When? Who?
  CBPF student at CERN (L. Lessa) could help  OT pilot test-case ?
TFC/ECS ?

## Slide 25: Where we are now
ASDBLRs
Stratix IV (readout and GBT emulator)

## Slide 26: How do we read & control?
ASDBLR connected to Actel TDC
all data and control lines from/to Actel via HSMC connector to Stratix IV
Actel registers (I2C) controlled by Stratix IV via 1GbE
    UDP Nikhef-made + encoding/decoding software on Linux
all data read by Stratix IV via 1GbE (UDP Nikhef-made)
At present testing through:
Ok for a while, until 1st prototype Actel TDC service board debugged, then FE test bench needed
When do we need it?
Basic blocks 2nd half next year, 1st prototype in 2013, 3 instances by 2014
CBPF/Nikhef cooperation (aimed at OT), support by Marseille & LHCb Online
Question: commonalities with other test benches??