## Slide 1
SPIDER “Swift Pipelined DigitizER”
for Timing Path Measurement
Ludovic Alvado, Nicolas Arveuf, Edouard Bechetoille, Christophe Beigbeder, Dominique Breton, Baptiste Joly, Laurent Leterrier, Samuel Manen, Hervé Mathez, Philippe Vallerand, Richard Vandaele

## Slide 2: Plan
Requirements on timing path
How to achieve the specifications
SPIDER “Swift Pipelined Digitizer” asic
  Concept
  Architecture
  Performances
Status of SPIDER development

## Slide 3: Requirements on timing path
Goal resolution down to 20psRMS to distinguish interactions
Goal dynamic range ET=[50MeV-5GeV]
Assume maximum channel occupancy of ~10% (~4MHz), under study/simulation.
Make it possible to deal with a few consecutive events (8?)
Chart: Evolution of the jitter with the amplitude of the signal (rise time =1ns, noise =1mV )
| 0.02 | 0.05 | 0.1 | 0.2 | 0.5 | 1
Jitter | 50 | 20 | 10 | 5 | 2 | 1
Theorical time resolution :
For 20ps and trise_time=1ns → SNR=50
Challenging resolution : slowest edge of 5ns (for SpaCalW) with 1mV noise → jitter of 250ps
→ reduce noise (technology/design)
→ reduce edge time (module design)

## Slide 4: How to achieve the specifications
1/ “leading edge discriminator + digital TDC “
  - bad resolution for high signal due to slope effect because the threshold is tuned for the low amplitude (for large dynamic range)
  - time walk effect needs to be compensated (by TOT or energy measurement)
  ++ high counting rate and low dead time
2/ “Waveform TDC + digital Constant Fraction Discriminator”
  - low impact on the resolution for low energy & ++ high resolution for high energy
  ++ time walk effect strongly compensated (dCFD)
  -- limitation of the counting rate and of the significative dead time
Dominique Breton’s talk will explain in detail why “Waveform TDC” offers better performances and has been chosen...
→ 2 types of time measurement chains frequently used
Plus vs Cons
Key point : resolution 20psRMS on a dynamic range of 100

## Slide 5: SPIDER “Swift Pipelined Digitizer” asic
Concept of the « pipelined analog memory »
    With this improvements, the pipelined waveform TDC is a good way to address the requirements on timing path
Reminder : a classical Waveform TDC is made of a single circular memory bank with a sampling depth of N signal points which limits the counting rate
To increase the counting rate, a multi-bank memory working like a pipeline is required and must run sequentially
To implement multi-bank memory with a reasonable size per channel (physical constraints), we define a optimized sampling window to deal with only the interesting part of the signal, which consequently reduces the size of each memory bank
To reduce the channel data rate, only the 8 samples required to make the dCFD calculation possible are sent to the companion FPGA

## Slide 6: SPIDER “Swift Pipelined Digitizer” asic
  Architecture
SPIDER block diagram

## Slide 7: SPIDER “Swift Pipelined Digitizer” asic
Main Specifications
Technology: 65nm (the most lasting technology, 10 years (?)), 1.2V power supply
Input signal : rise time from 1ns to 1.5ns, dynamic range Vin=[10mV-1V]
To achieve the time resolution of 20ps, we evaluate :
Need for a memory cell (switches & capacitor) compatible with a noise voltage around 0.5mV
Need of a resolution of 10 bits for the sampling : 10-bit Wilkinson ADC@5GHz to reduce the conversion time (200ns for 10bits i-e 8 clock periods)
Need for 128-delay-cell DLL1 running @40MHz → bin ≈ 200ps to tune the beginning of the sampling window
Need for 32-delay-cell DLL2 running from 80MHz to 640 MHz → bin ≈ 50ps to 400ps to select the sampling frequency between 2.5GHz and 20GHz

## Slide 8: First Prototype architecture
Architecture: «2 dual-bank channels»
SPIDER first prototype : contains all critical blocks
Proof of concept :
Clocks & DLLs
Memory cell in 65nm
Multi-bank operation
10-bit Wilkinson ADC @5GHz

## Slide 9: Status of the SPIDER development
Collaboration of 4 labs from IN2P3 (Clermont-Ferrand, Caen, Lyon & Orsay)
Very challenging design! Has started a few months ago.
Repartition in work packages for
    Delay Locked Loop (DLL1 & DLL2)
    Analog part (memory cell, trigger comparator, ADC comparator, ramp generator) + Sampling & ADC management (bank & writing controller + conversion sequencer)
    Counting digital part for “10-bit Wilkinson ADC & coarse time” (Gray counters, ring oscillator )
    Slow control & Readout management part (reading decoder)
    Phase Locked Loop (not critical for first prototype)
The first prototype submission is expected at the end of 2023

## Slide 10
Thank you for your attention!