## Slide 1
Ultra-sensitive Rn detection and its suppression
Ivan Štekl
Institute of Experimental and Applied Physics
Czech Technical University in Prague
1) Brief introduction of IEAP CTU (main research topics)
2) Why we need to suppress Rn caused background?
3) Rn detection (ultra-low concentrations)
4) Rn suppression
5) Rn in education
IEAP CTU was found in 2002 as a scientific and educational institute of the CTU in Prague, focusing on a research in the field of particle and subatomic physics performed in an international experiments
105 people (38 from abroad)
Notes: 1

## Slide 2
Main research subjects in IEAP CTU:
CERN – experiments ATLAS (ATLAS TPX – radiation field measurement, luminosity monitoring, theory, data processing), MoEDAL, AFP, ISOLDE (nuclear physics at CERN)
Neutrino physics – 2nEC/EC decay of 106Cd (experiment TGV – necessity to upgrade), experiment COBRA (close to end), detection of 0n and 2nbb decay of 82Se (experiment SuperNEMO), experiment LEGEND (USA/Germany – 0nbb decay of 76Ge); detection of atmospheric neutrinos in experiments KM3NeT and Baikal-GVD); detection of reactor antineutrinos
Detection of dark matter – experiment PICO in SNOLAB (Canada), detection of neutralino
Detection of high-energy cosmic rays – detection of radiation from universe (8 Timepix detectors on ISS, NASA; Timepix detector on Proba-V and RISESAT satellites; small unit VZLUSat), new projects with ESA (HardPix on-board GOMX-5 Cubesat mission, 12U, 20 kg. Launch 2023; 2x HardPix outside Lunar Gateway as part of ESA ERSA. Launch 2024).
Structure of atomic nuclei and nuclear reactions – fission, radioactive nuclei decay, super heavy nuclei, astrophysical reactions
Applications – pixel and strip detectors, imaging (X-rays and neutrons), biomedicine, hadron therapy, study of material…..
All our activities are based on international cooperation

## Slide 3: Research infrastructure of IEAP CTU
Van de Graaff accelerator
Underground laboratory LSM in Modane, France
Small underground laboratory in Prague in a nuclear shelter
2 electron microscopes
Laboratory for high-resolution X-ray radiography, 3D X-ray tomography and neutronography in IEAP,
Specialized laboratory for experimental imaging – common laboratory of IEAP and 3rd faculty of medicine of CU
Radon laboratory (ultrasensitive measurement, radon-free chambers) – common laboratory of IEAP and the National Radiation Protection Institute;
Tunable electron source and equipment for scintillators measurements – common laboratory of IEAP and the NUVIA company.

## Slide 4
Experimental techniques to observe bb-decay (no method is perfect)
bb-daughter rate
E1+E2 spectrum
E1, E2, 
Energy resolution, High (~ 100%) efficiency
Precise bb-observation, Any bb-source can be measured (test nuclear models), Potentially zero-background, Test of bb0n mechanisms
Geochemical &
Radiochemical
Calorimetric
Tracking + Calorimetric
TPC
E1, E2
Formula of experimental sensitivity
NA : Avogadro number
M : source mass
ε : efficiency
mmol : molar mass
t : time of measurement
a : Isotope abundance
NBGR : background rate
ΔE : energy resolution

## Slide 5: Ultra low background experiments (neutrino physics, DM)
SuperNEMO: measurement of double beta decay in the LSM underground laboratory in Modane, France (4 800 m w.e.) – cooperation of institutions (France, UK, Czechia, Slovakia, Russia, Ukraine, JINR)
DEMONSTRATOR = 1 module (7 kg of 82Se)
The goal is to reach a zero background level in the region of interest
of 0nbb.
Calorimeter (712 Optical Modules, plastic scintillator, PMT) is ready. Tracking detector (2034 cells running in Geiger mode and filled with a gas mixture (95% He, 4% ethanol, 1% Ar) is ready. A coil producing a 25 G magnetic field is installed.
We need gamma and neutron shielding. Data taking.
Demonstrator sensitivity for 0nbb:
T1/2 > 5.9 x1024 y (90% C.L.) and ⟨m⟩ < 0.2 - 0.55 eV

## Slide 6: Search for bb decay on excited levels of 82Se with the OBELIX spectrometer and the influence of radon background
Why we need to suppress Rn caused background?
OBELIX is a unique ultra-large volume HPGe spectrometer
Volume is 600 cm3, Mass is 3.2 kg
Relative detection efficiency is 160% and energy resolution is 2.2 keV @ 1332 keV
Record ultra-low radioactive background level due to specially constructed individual multilayer passive shield
Location: LSM (Modane, France, 4800 m.w.e.)
A source in Marinelli vessel with 6 kg of 82Se was installed on OBELIX (October of 2021) for long-term measurements in order to search for double beta decay into excited states of the daughter nucleus 82Kr, which have not yet been observed by anyone.

## Slide 7
Theoretical expectations of transition to 0+1 exited state are at the level of T1/2 ~ 5-7.5 x 1022 y (A. Barabash, F. Šimkovic).
After 10 months of exposure, OBELIX has achieved this level of sensitivity!
Look at radon peaks (the sum of the 351 keV, 214Pb, and 609 keV, 214Bi, lines from the 222Rn) we observe anomalous spikes.
The reason is unknown (open shielding, stop clean air flushing???), but it cost us a month of exposure, which we had to reject.

## Slide 8: Current results
Level | Gammas with efficiencies | Limit Т1/2 (90% CL), 1022 y |  | 
 |  | present | MPI | [1]
2+1 (776.5 keV) | 776.5 (2.416%) | 5.89 | 1.19 | 1.3
2+2 (1474.9 keV) | 776.5 (1.341%)+1474.9 (0.756%) | 4.53 | 1.02 | 1.0
0+1 (1487.6 keV) | 711.1 (2.129%) | 2.39 | 0.95 | 
 | 776.5 (2.076%) | 5.06 | 1.10 | 
 | 711.1 (2.129%) + 776.5 (2.076%) | 4.29 | 1.38 | 3.4
[1] J. W. Beeman et al., Eur. Phys. J. 75 (2015) 591.
No effect was observed in 12 months of measurement
We reached sensitivity level T1/2 ~ 5 х 1022 y (see the table below).
Measurements are in progress to reach T1/2 ~ 1023 y…

## Slide 9
Long-term studies of rare processes continue on the OBELIX
The sensitivity level of T1/2 ~ 5 х 1022 y for the double decay of 82Se into excited levels has been reached on the OBELIX spectrometer.
Within 2 years of additional measurements, it is planned to reach the level of T1/2 ~ 1023 y.
Radon is a serious problem, so protection and control is essential.
Main sources of the radon:
• Diffusion of the Rn from outside the detector
• Rn emanation of materials inside the detector.
What is needed:
• Rn detectors sensitive to ~0.1 mBq/m3 – Rn detector
• Isolation of the detectors using thin foils, glue... with low radon diffusion coefficient - Rn diffusion apparatus
• Emanation measurements of parts inside the detector - Rn emanation apparatus

## Slide 11
hemisphere stainless steel, volume = 50L
Electrostatic collection, PIN diode.
Results
HV = 12 kV, efficiency ~ 25%
Measurement of background
Remark
1 mBq/m3 means 86 decays of Rn in m3 per day
Rn detection (ultra-low concentrations)
PIN diode
[+HV 25kV]

## Slide 12
Energy[MeV]
Events[per day]
Events[per day]
Energy[MeV]
Energy spectrum measured at the beginning of background measurement (5 Bq/m3)
Background after 2 months is 111 events/day in the ROI (6.2-7.8 MeV, 214Po)
218Po
214Po
Time of measurement [day] | Sensitivity [mBq/m3]
1 | 11
7 | 3.5
30 | 1.6
75 | 1

## Slide 13
Radon concentration line
Adsorbent – active charcoal K48
Adjustable temperature of adsorbent – cooling up to - 180 ℃
Disadsorbtion of Rn from adsorbent – heating up to +135 ℃
Expected sensitivity ~ 10 mBq/m3
Honeycomb Rn detector (Volume 300 L = 6 ×50 L )
HV (-7 kV) – noise at 150 keV, Efficiency of ̴ 33%
Stainless steel thickness - 2 mm
Background of construction materials: 226Ra < 0.1 Bq/kg
Software, simultaneously data analysis (6 detectors)
Expected sensitivity of the Radon detector ~ mBq/m3

## Slide 14: Radon diffusion apparatus
1/2 - Left/right vessel; 3 - Radon source; 4 - Sensors of temperature, humidity, and pressure; 5 - Flow-meter; 6 - Air buffer; 7 - Air pump, 0.34 L /min; 8 - Air dryer
2 hemispheres separated by tested material foil (left hemisphere with high Rn activity, 38 kBq/m3; Rn penetrates into right hemisphere)
Measurement of Rn diffusion through 50 µm NYLON film
Rn suppression factor C1/C2 > 76 500; Diffusion coefficient D =4.7·10-16 m2s-1

## Slide 15: Summary of results for different materials (foils) for the SuperNEMO detector from the radon-tightness point of view.
Foils | Thickness [µm] | C1/C2 | C1/C2 normalized to 15 µm | Diffusion coefficient D [10-12 m2s-1] | Diff. length L [µm]
HDPE (2 layers) | 2×144 | 3.5 | 1.1 | 19 | 3 000
TROPAC III | 102 | > 8 300 | > 600 | < 0.0043 | < 46
TROPAC junction | 102 | > 6 300 | > 500 | < 0.0051 | < 50
Bovlon film | 0.015 | 4.0 | 4.0 | 0.84 | 633
Mylar (2 layers) | 2×20 | > 9 100 | > 2 300 | < 0.0012 | < 24
Mylar junction | 20 | 110 | 85 | 0.030 | 120
EVOH (2 layers) | 2×15 | > 31 000 | > 8 900 | < 0.00035 | < 13
EVOH + PE | 125 | 165 | 20 | 0.013 | 254
Nylon | 50 | 76 500 | 6 380 | 0.00047 | 15
PET | 1 000 | > 41 136 | > 35 | < 0.076 | < 190

## Slide 16
Apparatus for measurement of Rn emanation
Measurements of Rn emanation from glass pellets
Rn from glass pellets < 1.3 x 10-9 Bq/kg/s
Events per[6h]
Time[h]

## Slide 17
Suppression of Rn from air
Radon trapping on charcoal => Radon decays during trapping
reduction factor 100 => „retention time“ T = 606 hours (~ 25 days)
T (hours) = K (m3/kg) * m (kg) / f (m3/hour)
T – retention time of Radon in charcoal; m – mass of charcoal
f – flux of gas
K – depends on charcoal type, temperature, pressure (J. Busto, CPPM):
t (°C) 20 0 -30 -40 -50 -60
K(m3/kg) 4 12 53 78 152 272
A(222Rn) in LSM ~ 10-20 Bq/m3
Antiradon setup: 500 kg charcoal @ -50oC, 7 bars
Activity: A(222Rn) < 10 mBq/m3 !!! Flux: 150 m3/h (produced by ATEKO company, Czech Republic)

## Slide 18
Clean rooms in SURO and LSM (ISO 5, zero-dose environment)
- Anti-radon system and clean room (ISO 5) is installed in SURO and in LSM
- Suppression of all types of radioactivity (including Radon) for biological studies, preparation of detectors, enriched foils…..

## Slide 19: Medipix/Timepix collaboration (headed by M. Campbell, CERN):
e.g. Timepix3
Each pixel can be configured to operate in different mode independently to other pixels
Measuring Energy (TOT, dead time per pixel 475 ns) and Time-stamping (TOA, 1.56 ns) simultaneously
Readout modes: a) Frame-based mode (max~1300 fps); b) Data-driven mode (~40Mhits/s), dead time per pixel min. 475ns
Output data: up to 8 serial lines, 640MHz => max. data rate= 5.12 Gbps

## Slide 20
SESTRA - School Education Set with Timepix for Radiation Analysis
Particle Camera MiniPixEDU (Timepix detector, calibrated)
Control Software Pixelman Simple preview & Pixet basic (acquisition, online visualisation, etc.,)
Alfa source (241Am, 𝛼 and 𝛾 source, 9.5 kBq)
Gamma source (241Am, 𝛾 source, 300 kBq, optional)
Potassium Salt (𝛽 and 𝛾 source)
Thoriated Tungsten Electrode (𝛼, 𝛽 and 𝛾 source)
Uranium Glass (𝛼, 𝛽 and 𝛾 source)
Mounting Rails
Source Holder
Camera Holder
Aluminium, Stainless, Copper, Brass and Lead Shielding Plates
Radiography Adapter Head +Samples with Hidden Patterns
Vacuum Cleaner Grate Adapter
USB Cable
Book of detailed guidelines “Experiments Using Pixel Detector in Teaching Nuclear and Particle Physics”

## Slide 21
Demonstration OF background radioactivity caused by radon
Visualizations of the Rn caused radioactivity of the paper tissue used as an air filter at home. The filtering took 5 minutes and exposure time was 10 minutes in both cases.
Not-ventilated (left) room
Ventilated (right) room

## Slide 22
Measurement of half-life time of Po-214 (also Po-212) with high precision using TPX3 detector (student J. Jelínek)
Measurement was done in SURO, Timepix3 into barrel with high activity of Rn-222 (units to tens of MBq m-3) for 140 hours
Daughter nuclei attach to Timepix3 surface and subsequent decays were observed
The overal result of measurements is:
µs
Other recent experimental values:
µs (Bellini et al., 2013)
µs (Alexeyev et al., 2020) – no proper error
discussion
Spatial resolution of Timepix3 allowed to collect large data set (order of 107 events) in short time (approx. 6 days) while maintaining reasonable signal to noise ratio.

## Slide 23
Millennium Institute for Subatomic Physics at the High Energy Frontier, SAPHIR is based on the similar way and it looks that you are going on proper way in science:
Instrumentation R&D
International cooperation based on reciprocity
Precisely defined responsibility of your team in the collaborative research
Support of local research infrastructure
Strong theoretical team.
Posssible areas of cooperation:
Detector technologies (scintillating detectors, strip, pixel…)
Deep underground laboratories (ANDES – technologies of ultra-low background)
Space (payloads based on pixel detectors, Chile has ambitious program to space)
Detection of radiation (HPGe spectroscopy)

## Slide 24
Thank you for your attention

## Slide 25: Radon
238U radium series
232Th - thorium
Different experimental results of radon decay progenies charge obtained by different authors
Radon 222Rn and its daughters form one of the most dangerous source of background in many experiments
There are three decay “chains” that occur in nature:
the uranium series, beginning with 238U,
the thorium series, which originates with 232Th,
the actinium series, which originates with 235 U.
  Radon
  Inert noble gas,
  belongs to the 238U chain (present in any material),
  high diffusion and permeability
  wide range of energy of emitted radiation (with the daughters),
  surface contaminations with radon daughters (heavy metals),
  broken equilibrium in the chain at 210Pb level.

## Slide 26
P type coaxial HPGe detector (U-type ultra low background cryostat
located at LSM (4800 m w.e.)
Sensitive volume 600 cm3 Efficiency 162%
Energy resolution ~1.2 keV at 122 keV (57Co), ~2 keV at 1332 keV (60Co)
12 cm of arch. Pb, 20 cm of low active Pb, Radon free air
Detector “Obelix” (JINR/IEAP CTU/LSM)
100Mo
100Mo
Process | T1/2 [years]
2ν2β- decay to 0+1 [1130 keV] | 
2ν2β- decay to 2+1 [540 keV] | 
Mass of 100Mo – 2517,15 g
Total measurement time – 2288 h
The price of such detector is
250 kEUROs => you need
international cooperation

## Slide 27: Laboratoire Souterrain de Modane
Road tunnel Fréjus (France – Italy border)
Depth of ~ 4800 m.w.e. (muon suppression factor ~ 106)
Muon flux: 4 x 10-5 μ.m-2.s-1
Neutron flux: 4 x 10-2 n.m-2.s-1(fast);
1.6 x 10-2 n.m-2.s-1 (thermal)
Radon: 15 Bq.m-3
HPGe room 1
Main hall

## Slide 28
Flight Amsterodam – Santiago, 5. - 6. 12. 2021
Measurement by pixel detector during flight (only during take-off it was impossible)
Chart: Average flux of detected particles during the flight Amsterodam - Chile 5.12.2021 9:50 p.m. to 6.12.2021 11:04 a.m., detector vertically
a) 1st local maximum: appr. 80 minutes after take-off (11 p.m.)
b) 7 hours flux is relatively stable
c) After 600 minutes of flight (8:30 a.m.) flux is increasing.
The second maximum is in time 730-780 minutes of flight
(10 a.m.- 10:50 a.m.)
d) Landing is clearly visible

## Slide 29
Detection of muons during flight:
In vertical position: total number 674 (1 per 45s)
In horizontal position: total number 169 (1/170s)
Measurements during landing (last 36 minutes) – decreasing of flux is clearly visible
Time before landing = 36 minutes
Time before landing = 18 minutes
Time before landing = 3 minutes

## Slide 30: Experiments in high radiation environment: i) activities in space, ii) LHC (MoEDAL, ATLAS-TPX)
International Space Station
In orbit since 3Q 2012
380 km
5 Timepix-Lite detectors placed on ISS since 2012 (collaboration with NASA and the University of Houston).
USB-Lite interface developed at IEAP.
ESA Proba V satellite
Launched 7th May 2013
820 km
SATRAM module with Timepix detector onboard ESA satellite Proba-V.
Characterization of space radiation at LEO. TPX in open space.
Developed by IEAP and BD Sensors.

## Slide 31
VZLUSAT-1
Launch 2017
RISESAT satellite
Timepix detector as part of miniature X-ray telescope onboard VZLUSAT-1 cubesat since 2017.
The first Czech satellite since 1996.
500 km
Japanese microsatellite RISESAT (Rapid International Scientific Experiment Satellite); dimensions 50x50x50 cm, weight ~50 kg
Development led by Tohoku University and Hokkaido University
Launch 2019
500 km

## Slide 32: Data Acquisition Control Software
PIXELMAN – IEAP CTU
Acquisition and control tool for Medipix & Timepix detectors
PIXET - ADVACAM
Acquisition and control tool for Timepix & Timepix 3 detector
J-PIX – IEAP CTU
Acquisition and control tool for Timepix 3 detector currently under development fully designed in Java to be multi-platform
Typical response of Timepix device to natural background radiation:
Clearly recognizable tracks
and traces of
- X-rays
- electrons
- alpha particles
- muon
- electron-positron pair, … .