## Slide 1: SPECIFICATIONS AND STATUS OF THE NEW ELECTRON COOLER FOR THE CERN ANTIPROTON DECELERATOR (AD)
A. Rossi, C. Accettura, W. Andreazza, A. Bollazzi, C. Castro Sequeiro, J. Cenede, N. Chritin, Y. Coutron, D. Gamba, L. Joergensen, C. Machado, O. Marqversen, L. Ponce, J. A. Ferreira Somoza, Y. Thurel, A. Frassier, G. Khatri, A. Pikin, M. Sameed, A. Sinturel, T. Todorcevic, G. Tranquille, L. von Freeden
COOL23, 8th - 13th October 2023

## Slide 2: Outline
Context: the AD complex and cycle
New electron cooler specifications
Design details and timeline
A. Rossi et al. COOL23, 8th - 13th October 2023

## Slide 3: AD (Antiproton Decelerator) & ELENA (Extra Low ENergy Antiproton ring)
Sketch of the AD (circumference 182 m)
ELENA (circumference 30.4 m)
AD/ELENA experiments
~1.5 1013 protons (26 GeV) on target
~3.5 107 antiprotons captured in AD
Deceleration to the lowest energy:
    → 5.3 MeV (AD)
    → 100 keV (ELENA)
Antiprotons extracted per cycle:
    1 bunch ~3x107 (AD)
    4 bunches of ~6x106 p-bars (ELENA)
Cycle lengths:
    ~100 s (AD)
    ~15 s (ELENA)
Beam cooling
    Stochastic → 3.57 and 2.0 GeV/c
    Electron (AD) → 300 and 100 MeV/c
    Electron (ELENA) → 35 and 13.7 MeV/c
Main purpose of the facility is to provide 100 keV pbar beams to (trap) experiments!
Courtesy of Davide Gamba
Notes: Protons coming from the SPS (Super Proton Synchrotron): about 10^13 protons of momentum 26 GeV/c to produce 5×10^7 antiprotons per minute, by collision on a Iridium target.

## Slide 4: AD cycle and motivation for a new electron cooler
    Figures of merit
    Captured intensity (linked to target + DI + s-cooling performance)
    Transmission along the cycle (linked to optics control and s-/e-cooling performance)
    Cycle length (mainly driven by s-/e-cooling performance, and tollerated losses…)
    Number of cycles for physics (affected by systems - inc. e-cooling - reliability)
Courtesy of Davide Gamba
    Motivations for a new e-Cooler
    Improve e-Cooler reliability
    Reduce cycle length by 20%
    Reduce beam losses
not only with e-cooler
}
Notes: Radio frequency (RF) systems decelerate and bunch the cooled antiprotons at 3.5 GeV/c.

## Slide 5: e-Cooler specifications
Expansion of the e− beam by a factor of 2 to reduce transverse energy
}
}
More stringent to limit e− beam heating in the cooling region
}
Possible via the gun grid
}
Might be limited by space charge and other effects
CERN EDMS doc. AD-LNT-ES-0001
Determines the choice of components/spares
Notes: Cooling time increase with angular (depends on transverse e- velocity spread) and momentum (depends on longitudinal e- velocity spread) difference between e- and pbar

## Slide 6: Current e-Cooler
Antiproton Decelerator Ring (2000-today)
A. Wolf, L. Hütten and H. Poth,
Magnetic field measurements for the electron cooling device for LEAR,
EP Internal Report 84-01
Low Energy Antiproton Ring (1982-1997)
Courtesy of Gerard Tranquille

## Slide 7
Courtesy of Nicolas Chritin & William Andreazza

## Slide 8: Comparison of the current e-cooler drift to design
1984 – scaled from Wolf et al.’s measurements
Complete solenoid
Pancake solenoid
↖︎ 28 mm
on axis
↘︎ ︎28 mm
Courtesy of Luke von Freeden
”perfect” / measured magnets
Bz in direction of e− motion
By ⊥ bending plane
Bx || bending plane

## Slide 9: Comparison complete vs. pancake drift solenoid
Courtesy of Luke von Freeden
Fied error due to powering
tolerances resolution 3σ = 5PPM and ripple µ = 1m
5.3x10-6
Complete
Pancake
3.1x10-5
Fied error due to powering long term stability resolution 3σ = 1000PPM,
nom = 75%
x10-5
1.9x10-4
3 pt supports positioning toleance
3σ = 200µm
x10-4
2.4x10-5
3 pt supports positioning long term stabitly
3σ = 20µm
x10-5

## Slide 10
Electron transport simulation to validate design
Courtesy of Gunn Khatri

## Slide 11: Vacuum
Collector
Gun
NEG strips
NEG strips
NEG coating
NEG coating
NEG coating
NexTorr pumps
Similar design to ELENA e-cooler
Extensive use of NEG-strips and coating
NexTorr pump
Courtesy of Cristina Castro Sequeiro, Jose A. Ferreira Somoza, Alexandre Sinturel
DN200
No clearing electrode

## Slide 12: Results
Courtesy of Cristina Castro Sequeiro, Jose A. Ferreira Somoza, Alexandre Sinturel
Gas loads from gun and collector after ≈ 1 day operation

## Slide 13: Gun – prototype
Courtesy of Jean Cenede
Photos by Giulio Stancari
Courtesy of Alexandre Pikin
Courtesy of Gerard Tranquille
Anode – Grid – Cathode

## Slide 14: Gun CST simulations
Courtesy of Sameed Muhammed

## Slide 15: Collector
Courtesy of Jean Cenede & Yannick Coutron
Courtesy of Alexandre Frassier, Jean Cenede, Gunn Khatri

## Slide 16: BPM
Estimated resolution 90 µm
Courtesy of Ole Marqversen, Frank Guillot-Vignot, Nicolas Chritin

## Slide 17: Magnet powering
Courtesy of Yves Thurel, Alessio Bollazzi, Christophe Machado, Todor Todorcevic

## Slide 18: Test strategy
Components test separately in labs:
  Magnets tested individually for acceptance and to tune correctors, plus as an ensamble to measure steering magnets strength and prepare for operations.
  Gun and collector tested individually, with magnets equivalent to those for the final electron cooler. Possibility of measurements of the e− beam transverse profile after expansion planned but not yet implemented
  Vacuum chambers tested individually
  Powering system tested individually
Commissioning after installation foreseen to fine tune
A. Rossi et al. COOL23, 8th - 13th October 2023

## Slide 19: Rough planning
A. Rossi et al. COOL23, 8th - 13th October 2023

## Slide 20: Conclusions
A. Rossi et al. COOL23, 8th - 13th October 2023
Functional (and engineering) specifications of the new AD electron cooler have been presented
  The new device aims at improving the current performance with a better magnetic field quality, electron beam magnetic expansion, better measurements of the beams relative position, faster switching of the electron beam on/off
The design is being finalised
  The magnetic design has evolved to complete solenoids (apart from the bends), few details to be looked at
  Gun and collectors prototypes are being tested
  Powering has been defined
  Vacuum design is ~completed
  Individual component testing
Installation foreseen for 2026 and operation in 2027

## Slide 21
Thank you
A. Rossi et al. COOL23, 8th - 13th October 2023

## Slide 22: Main subsystems/components – cartoon
.
Expansion gun solenoid
Gun and collector arm solenoids
+ H/V steerers
Toroid
Toroid
Drift & H/V steer
V steer
V steer
Collector squeeze coil
Gun
Collector
BPMs
Support structure
A. Rossi – AD-CONS e-Cooler Procurement Readiness Review
Gun & Collector SY-BI
Magnets TE-MSC
Vacuum System TE-VSC
BPM SY-BI
Support and shielding
Powering (LV & HV) SY-EPC
Ancillaries
H/V Orbit Corrector
H/V Orbit Corrector
Magnet powering
HV powering