## Slide 1
COOL 2023 conference, Montreux, Switzerland, October 10, 2023
Alexander Zholents, Argonne National Laboratory
Chris Hall, RadiaSoft
A Study of the Wiggler Enhanced Plasma Amplifier for Coherent Electron Cooling
Notes: The amplifier plays a significant role in stochastic cooling. However, selection of broadband optical amplifiers is very limited impacting application of optical stochastic cooling. I will show that fast cooling of electrons/positrons can be achieved without the amplifier by a slight modification of a stochastic cooling method.

## Slide 2
Preamble
Plasma Cascade Amplifier (PCA)
Obtain a gain in microbunching by creating a runaway instability of plasma oscillations
(V. Litvinenko et al., Phys. Rev. Accel. Beams 24, 014402, 2021.)
Option 1) use
For instability one needs to modulate piecewise
 Wiggler Enhanced Plasma Amplifier (WEPA, Zholents, Stupakov)
and
in the wiggler
(G. Stupakov and A. Zholents, 13th Workshop on Beam Cooling and Related Topics, 2021)
 Plasma Cascade Amplifier (Litvinenko et al.)
Option 2) use
(in a direct analogy to a FODO channel described by Hill’s equation with piecewise periodic coefficients)
Note: WEPA requires separation of ion and electron beams, PCA does not
The amplifier to be used for Coherent Electron Cooling (CeC)
(V. Litvinenko , Y. Derbenev, Phys. Rev. Lett., 102:114801, 2009)

## Slide 3
Theory
impedance per unit length
variables
linearized continuity equation for cold plasma in the wiggler
equations
plasma frequency
Fourier transform of a density perturbation
relative energy spread
Fourier transform of a peak current

## Slide 4
Theory (2)
subsequent analysis is valid when wiggler is longer than a transient length ~ (1 - 8) cm
in the case of the wiggler impedance (G. Geloni et al., NIM A, 2005)
is space charge diffraction size
is radiation diffraction size
is incomplete gamma function
is the Meijer G-function
electron distribution in transverse coordinate

## Slide 5
Theory (3)
Impedance as a function of frequency in the case of KW=1.5, beam energy = 157 MeV, and s = 80 mm

## Slide 6
Theory (4)
three different calculation approaches agree perfectly
Curves are plotted with a small vertical offset
presented here
Stupakov, Zholents paper
numerical
Plasma frequency in the wiggler calculated using only space charge effects
Calculation approach

## Slide 7
Theory (5)
Consider evolution of the vector
Wiggler transport
Chicane transport
Unit transport
has two eigenvalues 𝐺1 and 𝐺2. If both |𝐺1 | = |𝐺2 | = 1, then the plasma
oscillation in the amplifier is stable and there is no gain in the microbunching.
The plasma oscillation is unstable when either |𝐺1 | > 1 or |𝐺2 | > 1
Wiggler of the length
Chicane with R 56
Amplifier unit

## Slide 8
Theory (6)
Since it is desirable to have in a neighborhood of and , we write approximate G1 and G2
The above formula is valid if using a drift with the length 𝑙𝑤 and 𝛾𝑧 ≡ 𝛾, in which case it is identical to the gain from the paper:
Stupakov, Baxevanis, Phys. Rev. Acc. and Beams, 2019.
Using only space charge impedance
Eigenvalues
debunching
approximate
exact
Calculated using:
𝛾 = 307, 𝐼 = 100 A, 𝜎 = 72𝜇m, 𝑅56 = 1mm,
drift 𝑙𝑤 =3.6 m, sh=2E-4

## Slide 9
Parametric study of the gain after one amplifier unit
I=100 A
R56=1 mm
k=3 mm-1
Kw=0
Kw=1.5
I=100 A
𝑙𝑤 =3.6 m
R56=1 mm
I=100 A
𝑙𝑤 =3.6 m
R56=1 mm
𝑙𝑤 =3.6 m

## Slide 10
I=100A
k=3 mm-1
Parametric studies of the gain after one amplifier unit (2)

## Slide 11
Goal of simulations
SASE FEL resonance
Kw = 1.67
To keep SASE FEL resonance outside of the amplifier bandwidth we have to use Kw< 1.67 such as kSASE > k

## Slide 12
OPAL-FEL for the wiggler sections (code MITHRA was ported to OPAL for that purpose)
Elegant for the chicanes
A. Adelmann et al., OPAL a Versatile Tool for Charged Particle Accelerator Simulations, arXiv:1905.06654, 2019.
A. Fallahi, A. Yahaghi, and F. Kārtner, MITHRA 1.0: A Full-Wave Simulation Tool for Free Electron Lasers, Computer Physics Communications, 228, pp.192-208, 2018.
Wiggler-enhanced plasma amplifier was modeled using:

## Slide 13: Benchmarking OPAL-FEL with SLAC experiment*)
Before wiggler
After wiggler
Slice central energy
Generation of attosecond x-rays at LCLS
MacArthur, et al., PRL, 2019
*) Arnau Albà et al., Computer Physics Communications, 2022
W
Regime with large
and

## Slide 14
Section of AWA beamline with APS wiggler
e-beam
1m
AWA beam energy = 45.4 MeV,
bunch charge = 300 pC, bunch length =0.25 - 0.5 mm
Phase space reconstruction from measurements using magnetic spectrometer and deflecting cavity
Wiggler period = 8.5 cm, K=10.5, gz = 11.6,
Benchmarking OPAL-FEL with ANL experiment *)
*) Arnau Albà et al., Computer Physics Communications, 2022
Experiment: wiggler-out
Experiment: wiggler-in
Regime with large
and small

## Slide 15
Lattice of a single amplifier unit used in simulations
wiggler
triplet
two chicanes
Wiggler:
length = 1.2 m
period = 3.3 cm
K = 1.5
B = 0.49 T
Chicane R56 = 1.0 mm
magnet length = 5 cm
magnet field = 0.04 T
Dispersion , hx (m)

## Slide 16: Initial electron beam
Sampling for distribution in z
  Calculate cumulative distribution function
  Numerically invert CDF
  Generate samples from Halton sequence
  Apply inverted CDF
All other distributions are Gaussian
Core:
Tails:
Longitudinal phase space

## Slide 17
Convergence of global beam parameters in many slices in bunch core was used as convergence criteria
Simulation setup
Define:
grid resolution,
energy resolution<8 keV,
grid domain,
number of macroparticles,
seed modulation amplitude.
Dn must be larger than numerical shot noise, and smaller than ~ 0.2n0/Gain to avoid gain saturation

## Slide 18
Selection of the solver’s grid resolution
Simulation with small grid resolution Dx = Dy= 2.5 mm and Dz = 7.5 nm was used as the reference
Dx = Dy=40 mm;
Dx = Dy=10 mm;
Dx = Dy=5 mm
Color coding:
Plots show deviations from reference for the beam energy, beam transverse size and emittance.
Grid resolution Dx = Dy=10 mm and Dz = 28.6 nm was chosen

## Slide 19
Calculation using 64x106 macroparticles was used as the reference
Solver grid resolution
Selection of the number of macroparticle
8 x 106 macroparticles was selected
was used
Plots show deviations from reference for the beam energy, beam transverse size and emittance.

## Slide 20: Selection of seed modulation amplitude
Need to avoid harmonic formation
Number of wigglers in the amplifier unit
I=165 A
R56=0.5 mm
lm
lm/2
lm/3
lm
lm/2
lm/3

## Slide 21: SASE FEL resonance suppression
After chicanes
After Wiggler 1
After Wiggler 3
(SASE gain=1.53/per wiggler cell)

## Slide 22
Ipeak=50 A
Dots – simulations
Solid lines – theory
Simulation results for one amplifier unit in comparison with the theory
R56 = 1 mm
sh = 2.1x10 -4
Ipeak=165 A
sh=2.15x10 -4
Use drift instead wigglers and OPAL
The agreement between simulations and theory is better without wigglers
Ipeak=165 A
Ipeak=100 A

## Slide 23
Ipeak=165 A
sh=2.15x10 -4
Ipeak=50 A
Ipeak=100 A
Dots – simulations
Solid lines – approximate theory
Ipeak=165 A
Simulations in comparison with approximate theory
Use drift instead wigglers and OPAL
The agreement between simulations and approximate theory is better, but not in the case without wigglers

## Slide 24
Dots – simulations
Solid lines – exact theory
Simulation results for two amplifier units
R56 = 1 mm
sh = 2.1x10 -4
Ipeak=165 A
Ipeak=100 A
Ipeak=50 A

## Slide 25
Wiggler number
Ipeak=50 A
k=3.76 mm-1
Ipeak=100 A
k=3.76 mm-1
Gain versus a number of wigglers in the amplifier unit (2)
Wiggler number
1
2
3
4
5
1
2
3
4
5

## Slide 26
Amplifier bandwidth is mostly affected by the energy spread and a little bit by CSR in chicanes
R56 = 1 mm
R56 = 0.5 mm

## Slide 27
Credits
Useful discussions with Gennady Stupakov are acknowledged

## Slide 28
Conclusion
WEPA is a viable candidate for the CeC amplifier. It offers a competitive gain-bandwidth product and uses smaller real estate comparing to a drift-based microbunching amplifier.
Care was taken to control for nonphysical numerical effects and limitations in the simulation.
Simulations and analytical calculations qualitatively agree but show some important differences.
Similar simulations and calculations performed for the microbunching amplifier with drifts replacing wigglers show better agreement.

## Slide 29
Backup slides

## Slide 30
Total reactive impedance
Case of a very large wiggler parameter
Kw > 7.5 such as kSASE < 0.5 mm-1
only SC
total
lW = 7.5 cm
Kw = 7.5

## Slide 31: Chicane CSR Impact on Gain
Ipeak=165 A
R56 = 1 mm

## Slide 32
Fallahi, Yahaghi, Kärtner, Computer Physics Communications, 2018
Program summary
Program Title: MITHRA
Program Files doi: http://dx.doi.org/10.17632/9f5k4zbtkg.1
Licensing provisions: GNU General Public License 3
Programming language: C++
Nature of problem: Full-wave simulation of the free electron laser radiation is accomplished by the code.
MITHRA transforms the particle positions and momenta to the bunch rest frame using the Lorentz
transformation. Electrons entering the undulator start radiating due to the induced wiggling motion. The
back-effect of the radiation on the bunch results in the modulation of the electron position, which in turn
generates a coherent radiation. This process as the main principle behind the operation of free electron
lasers is simulated using Maxwell equations, electron motion equations and relativity principles.
Solution method: Non-standard Finite Difference Time Domain (NSFDTD) combined with Particle-in-Cell
(PIC) is implemented in the Lorentz-boosted framework to calculate the FEL radiation. Parallelization
is done using both multi-threading (open-MP) and message passing interface (MPI) to maximize the
computation efficiency.
MITHRA 1.0

## Slide 33
Unlike OPAL’s static solver, which can stretch and rotate the grid as necessary to tightly enclose the bunch at each time step, FDTD requires the grid to be fixed in space because each grid point is updated using its previous values, and thus it needs to enclose the whole domain where there will be EM fields of interest during the simulation. In the case of an undulator this means that the computational domain should have the same length as the undulator, usually within a range Lu=1–100 m, but should also have a grid spacing small enough to resolve the bunch of length σz=0.1–1 mm and the resonance frequency of the radi-ation λr=0.01–100 μm, which represents an order of ∼106–1010 cells just for the longitudinal axis, extremely large even for the current state-of-the-art HPC clusters.

## Slide 34: Simulation Parameters
Number of grid points ~ 90x106

## Slide 35: Mitigating impact of finite bunch length
Regenerate tails after each wiggler to mitigate impact of spikes
spikes
(simulation domain is much shorter than bunch length)

## Slide 36
Ipeak=50 A
3 wigglers
6 wigglers (exact)
6 wigglers (approximate)
Gain versus a number of wigglers in the amplifier unit
Ipeak=50 A

## Slide 37: Gain determination using NAFF vs Bunching Factor
Bunch core
NAFF:
𝜆 = 1.22 𝜇m
Amplitude / Avg(counts) = 0.003979
Error = -0.5 %
NAFF:
𝜆 = 1.22 𝜇m
Amplitude / Avg(counts) = 0.003999
Error = -0.01 %
bunching factor
Examples using seed modulation = 0.004
Exactly 1 period of data
N - <N>
N - <N>