## Slide 1
Experiments on Electron Cooling and Intense Space-Charge at IOTA
Nilanjan Banerjee, MaryKate Bossard, John Brandt, Young-Kee Kim, Sergei Nagaitsev, Giulio Stancari

## Slide 2: The FAST/IOTA Facility
The Fermilab Accelerator Science and Technology (FAST) facility and the Integrable Optics Test Accelerator are dedicated to beam physics research.
Reached 31.5 MV/m in 2017
Operational with 150 MeV electrons since 2018.
S. Antipov et al, JINST 12 T03002, 2017.
Wide range of research areas: Non-linear integrable optics, optical stochastic cooling, photon generation, single electron dynamics, quantum statistics of undulator radiation, coherent instabilities, electron lens and more!
A. Romanov et al., JINST 16 P12009, 2021.
J. Jarvis, et al., Nature 608, 287–292, 2022.
I. Lobach et al., Phys. Rev. Lett. 126, 134802, 2021.

## Slide 3: Overview
Motivation and Conceptual Design
Beam Experiments using Electron Cooling
Hardware Configuration and Status

## Slide 4
Motivation and Conceptual Design

## Slide 5: Maximizing Brightness and Intensity
Four grand challenges of accelerator and beam physics facing the community are:
Beam Quality: Limited by heating due to Intra-Beam Scattering, resonance crossing, etc.
Beam Intensity: Limited by collective effects and particle losses.
Beam Control
Beam Prediction: Limited by error fields and non-linearity of space-charge.
J. Blazey et al, Accelerator and Beam Physics Roadmap, DOE Accelerator Beam Physics Roadmap Workshop, 2022
S. Nagaitsev et al., Proceedings Particle Accelerator Conference, 1995, pp. 2937-2939
Beam intensity
Beam density
How to maximize phase-space density of stored beam and minimize beam loss in a ring for given number of turns?
How much tune spread is needed to stabilize stored beam?
C. C. Hall et al., in Proc. IPAC'19, paper WEPTS070, 2019

## Slide 6: The Proton Program at IOTA
IOTA will be configured to recirculate 2.5 MeV protons up to .
.
G. Stancari et al, JINST 16 P05002, 2021
Features:
All (skew) quadrupoles and correctors are independently controlled.
Both bunched beam and coasting.
Single turn injection.
Electron lens/cooler with length 0.7 m.
At the Laslett tune shift of 0.5, Intra-Beam Scattering driven transverse emittance growth time-scale is a few seconds. Electron cooler must compensate for heating.

## Slide 7: Electron Cooler Design Parameters
Electron beam parameters aim to provide a cooling time of ~ 1 - 10 seconds to control equilibrium emittance at different bunch charges.
(mm) | (mA) | (A/m2) | (s)
18 | 80 | 78.6 | 0.79, 0.74, 0.94
14 | 1.7 | 2.76 | 12, 12, 13
18 | 80 | 78.6 | 0.79, 0.74, 0.94
14 | 1.7 | 2.76 | 12, 12, 13
We estimated the cooling time using the Parkhomchuk model assuming:
Flat transverse distribution of the electron beam.
Ideal solenoid field.
Matched proton beam.
For the baseline design we chose two electron coolers with an order of magnitude difference in cooling time.
M. Bossard et al., in Proc. IPAC'23, pp. 646-649, 2023.

## Slide 8: Simulations in PyORBIT with Space-Charge and Cooling
We simulate our experiments using a transverse PIC space-charge model and the Parkhomchuk model of cooling.
Cool the core of the beam.
Can’t cool large amplitude particles.
More beam loss in bunched beam.

## Slide 9
Beam Experiments using Electron Cooling

## Slide 10: Optimization of the Bare Lattice to Maximize Tune Shift
What is the maximum space-charge tune shift of stored beam we can achieve?
Optimizing the linear lattice configuration, including tunes and transverse coupling.
Compensating for specific resonance driving terms using sextupoles.
F. Asvesta et al., in Proc. IPAC'22, pp. 2056-2059, 2022.
Compensated
Simulated tune scans over 25 synchrotron periods for a Gaussian bunched beam with

## Slide 11: Interplay of Space-Charge and Coherent Instabilities
How are coherent instabilities affected by space-charge? The 2.5 MeV protons at IOTA provide strong space-charge but weak impedance.
Measure instability growth rate and head-tail amplification in the parameter space using:
Controlled wakefields generated using the wake-building feedback system.
Electron cooling to enforce an equilibrium phase-space distribution, independent of bunch charge.
R. Ainsworth et al., in Proc. HB'21, pp. 135-139, 2021.
O. Mohsen et al., in Proc. NAPAC'22, pp. 124-127, 2022.
Time (ns)
Time (ns)
Fermilab Recycler
Wakefield
Amplitude (Waker)
SC Tune Shift (Electron Cooling)
ABS: A. Burov, Phys. Rev. Accel. Beams 22, 034202, 2019.
CMM: X. Buffat et al., Phys. Rev. Accel. Beams 24, 060101, 2021.
ABS
CMM Gaussian

## Slide 12: Tunable Landau Damping with Space-Charge
Non-linear Integrable Optics enable large amplitude-dependent tune spreads while keeping single-particle dynamics stable.
Flagship project for the Integrable Optics Test Accelerator!
Electron cooling enables:
Single particle dynamics experiments with pencil beam and low energy spread.
Measurement of minimum tune spread required to mitigate coherent instabilities with space-charge.
V. Danilov and S. Nagaitsev, Phys. Rev. ST Accel. Beams 13, 084002, 2010.
S. Antipov et al, JINST 12 T03002, 2017.
A. Valishev et al., in Proc. IPAC’21, pp. 19-24, 2021.
N. Kuklev et al., in Proc. IPAC'21, pp. 1964-1967, 2021.
S. Szustkowski, PhD Thesis, Northern Illinois University, 2020.
J. Wieland et al., in Proc. IPAC'23, pp. 3230-3232, 2023.

## Slide 13
Hardware Configuration and Status

## Slide 14: Electron Cooling in 2025
D. Edstrom, IOTA/FAST department meeting, 2023.

## Slide 15: 2.5 MeV Proton Injector and IOTA RF Configuration
Injector beamline capable of delivering short pulses of 2.5 MeV protons at 1 Hz.
Broadband normal conducting RF system with two gaps, but only 30 MHz gap installed.
G. M. Bruhaug and K. Carlson, in Proc. NAPAC'16, pp. 432-434, 2016.
 | (MHz) | (V) | 
4 | 2.187 | 72 | 0.01
56 | 30.62 | 1000 | 0.04
4 | 2.187 | 72 | 0.01
56 | 30.62 | 1000 | 0.04
E. Prebys, Beams Document 4837-v1, Fermilab, 2015.

## Slide 16: Proton Beam Diagnostics
Injector: Toroid, Scanning wire, Allison scanner
Storage Ring:
DCCT: Measure injection efficiency and beam lifetime.
Beam Position Monitors
  Use LOCO to configure lattice.
  Use turn-by-turn centroid positions of pencil beams to measure single-particle dynamics.
Neutralization monitor
  Measure equilibrium transverse profile with cooling.
Ionization Profile Monitor
  Measure turn-by-turn evolution of transverse profile.
H0
H0
Bongho Kim et al., NIM A, 899, 22-27, 2018.
V. Shiltsev, NIM A, 986, 164744, 2021.
H. Piekarz et al, Beams Document 9903-v1, Fermilab, 2023.
p+

## Slide 17: Electron Lens Setup
Conceptual design of all parts exist but engineering design needs to be finalized.
Conduction cooled SC solenoid
R.C. Dhuley et al 2021 JINST 16 T03009
e- source
e- beam
Electron Tracking
D. Noll and G. Stancari, Technical Memo, Fermilab, 2015. FERMILAB-TM-2598-AD-APC.
Anode
Dispenser Cathode
Profiler
Flat beam gun
M. Bossard et al., in Proc. IPAC'23, pp. 646-649, 2023.
~3 times increase in !

## Slide 18: Electron Beam Diagnostics
Toroids: Measure beam current and losses.
Stripline BPMs: Align with the proton beam.
Profile measurement: Measure transverse profile.
Recombination Monitor: Optimize cooling performance.
Cyclotron Emission Monitor: Estimate electron density and temperature.
G. Stancari et al, JINST 16 P05002, 2021
C. Habfast, PhD thesis, Karlsruhe U., KFK-4188, 1987.
LEAR
A. Ashtari Esfahani et al., Phys. Rev. Lett. 131, 102502, 2023.
D. M. Asner et al., Phys. Rev. Lett. 114, 162501, 2015.
Project 8: CRES

## Slide 19: Conclusion
The IOTA 2.5 MeV proton program will study extreme beam conditions in future hadron synchrotrons and storage rings.
  Space-charge tune shift approaching -0.5. – Electron cooling to achieve equilibrium.
  Adjustable wakefields of arbitrary shapes and magnitudes. – Wake-building feedback system.
We have proposed a few experiments:
  Maximize tune shift for given turns, emittance growth and loss budget.
  Measure instability growth rate and head-tail amplification as a function of space-charge tune shift and ring impedance.
  Characterize single-particle dynamics of two Non-linear Integrable Optics systems and demonstrate suppression of coherent instability.
First protons in IOTA in summer 2024 and cooling in late 2025.

## Slide 20: Acknowledgements
Rob Ainsworth, Alexey Burov, Brandon Cathey, Sergei Kladov, Valeri Lebedev, Aleksandr Romanov, Alexander Valishev and the IOTA/FAST team at Fermilab.
Thank You!

## Slide 21: Appendix I: Proton Parameters
(μm) | 
4.3, 3.0 | 1.32 x 10-3
4.3, 3.0 | 1.32 x 10-3
C | 39.96 m
KE | 2.5 MeV
 | 1.83 μs
h | 4
 | Coasting or 4
 | 50 – 70 μm 5 – 11 μm (with DN)
 | 4-4.5, 3-3.5
C | 39.96 m
KE | 2.5 MeV
 | 1.83 μs
h | 4
 | Coasting or 4
 | 50 – 70 μm 5 – 11 μm (with DN)
 | 4-4.5, 3-3.5
 | Coasting | Bunched
Intensity [Current (mA)] | 6.6 x 1010 [5.79] | 1.3 x 109 [1.15]
Tune Shifts () | -0.33, -0.50 | -0.33, -0.50
IBS (s) | 10, 2.6, 300 | 14, 3.7, 420
RGS (s) | 21, 10 | 
RGS Lifetime (s) | 512, 64 (with DN) @ 1.57 x 10-10 Torr | 
 | Coasting | Bunched
Intensity [Current (mA)] | 6.6 x 1010 [5.79] | 1.3 x 109 [1.15]
 | -0.33, -0.50 | -0.33, -0.50
 | 10, 2.6, 300 | 14, 3.7, 420
 | 21, 10 | 
RGS Lifetime (s) | 512, 64 (with DN) @ 1.57 x 10-10 Torr | 
Lattice
Injector
IOTA Operation

## Slide 22: Appendix II: Electron Cooling and SC with Coasting Beam
Compared to the bunched beam simulation:
More uniform cooling in transverse
Less beam loss