## Slide 1: Persistent Layout Studies Updates
Peter van Gemmeren (ANL)

## Slide 2: No single attribute retrieval.
Switched splitting off while retaining member-wise streaming (another recent ROOT addition), so :
  svcMgr.AthenaPoolCnvSvc.PoolAttributes += [ "STREAM_MEMBER_WISE = '1'" ]
  svcMgr.AthenaPoolCnvSvc.PoolAttributes += [ "DEFAULT_SPLITLEVEL = '0'" ]
Except for two largest Container():
  New feature in POOL allows custom SplitLevel
  Avoids file size increase

## Slide 3: Almost event level retrieval
Use automatic basket optimization to write fewer events per basket, by flushing every 10 (for AOD, 5 for ESD) events and increase size for baskets outside the CollectionTree to 32K:
  svcMgr.AthenaPoolCnvSvc.PoolAttributes += [ "DEFAULT_BUFFERSIZE = '32000'" ]
  svcMgr.AthenaPoolCnvSvc.PoolAttributes += [ "ContainerName = 'TTree=CollectionTree'; TREE_AUTO_FLUSH = '10'" ]
Switch off basket optimization for all auxiliary container.

## Slide 4: Test: File Size (my personal test, still need independent verification)
Testing on voatlas51 with 2.5K ESD and ~20K AOD events
  Thanks to Ilija for getting me access to lxvoadm/voatlas51.
Produced two ESD / AOD samples:
  Full splitting and 30 MB to optimize CollectionTree.
    4512002732 Apr 2 myESD_1.pool.root
    3803552613 Apr 2 myAOD_1.pool.root
  No splitting and flushing every 5/10 events.
    4437849282 Apr 2 myESD_2.pool.root
    3681997184 Apr 2 myAOD_2.pool.root
No more file size increase!

## Slide 5: Results for Reading all events directly (all objects, timed individually)
  Full splitting and 30 MB to optimize CollectionTree:
    Total read ESD: 420 ms/event
    Total read AOD : 59 (+/- 3) ms/event
  No splitting and flushing of CollectionTree every 10/5 events:
    Total read ESD: 360 ms/event
    Total read AOD: 35 (+/- 2) ms/event
  Reading all events still is ~15 - 30% faster
    Fewer reads, ~30 x less branches only ~10 x more baskets.
      All AOD tests we run twice on different cores (same for both formats though), number between cores varied about 5% (between core 0 and 2)

## Slide 6: Results for Reading ~1% of events via TAGs (all objects, timed individually)
  1% cut on random variable in TAGs
    Ignore times for first event.
  Not yet fully retested, only AOD
    Not yet latest version, but close.
  Full splitting and 30 MB to optimize CollectionTree:
    Total read 270 ms/event
      A 1% selection ends up reading and uncompressing most data.
  No splitting and flushing of CollectionTree every 10 events:
    Total read 60 ms/event
      Only about 10% of the event data is read and uncompressed.
  Reading selected events is ~4-5 times faster.

## Slide 7: New results
No more increase in file size.
Memory consumption goes down for read and write jobs using the new layout.
  E.G.: To copy 20K AOD_1 uses 1170 MB, whereas AOD_2 only requires 890 MB.
  This is after fixing auxiliary tree optimization.
LCG 60b causes large VMEM increase for 30MB Collection Tree (Savannah #79833):
  Not yet fully understood, but tests were done with LCG 59
  New layout lowers the LCG 60b memory footprint.
Writing speeds up for AOD (not for ESD) by 20%

## Slide 8: Outlook
New ROOT storage layout with no-split / small baskets shows many improvements:
  Much faster (factor 4-5) single event reading.
  Saves lots of Virtual Memory, >100 MB
  Faster read overall (15-35%).
  For AOD, faster writing speed (>20%), but not for ESD.
Given these results, we should switch release 17 to write out in this new format.
  Changes are currently going into devval.