## Slide 1: Q1-TAXS vacuum system design
Jaime Pérez Espinós on behalf of WP12
12th HL-LHC Collaboration Meeting Uppsala (Sweden), 19-22 September 2022

## Slide 2: Contents
Q1-TAXS module design
Pumping / Ne venting lines
Integration and installation aspects with impact on the Q1-TAXS area
Summary of main open points

## Slide 3: Q1-TAXS connection - ATLAS
Q1-TAXS connection
TAXS chamber
Pumping / Ne venting lines routed along outer shielding

## Slide 4: Q1-TAXS connection - CMS
Q1-TAXS connection
TAXS chamber
Pumping / Ne venting lines routed along outer shielding

## Slide 5
Q1-TAXS module design

## Slide 6: Vacuum layout alternatives
VAX M3
VAX
M2
VAX M1
IP sector
TAXS
TAXS
Module
Q1 cryostat
1x VPNCA
2x VPIAN
2x VPNCA
NEG coating
a-C coating
Cryogenic
VAX M3
VAX
M2
VAX M1
IP sector
TAXS
TAXS
Module
Q1 cryostat
1x VPNCA
+ 1x VPIXD or + 1x VPIB
2x VPIAN
2x VPNCA
2x UHV1400 wafer
NEG coating
a-C coating
Cryogenic
BASELINE
LAST PROPOSAL (TBC)

## Slide 7: Q1-TAXS module working models
66 kg
19 kg
45 kg
Current baseline
Alternative design with NEG wafers #1
Alternative design with NEG wafers #2
Estimated weights
NEG wafers under qualification at CERN

## Slide 8: Alternative design with NEG wafers #1
Tube D204/200 (minimum diameter to fit the NEG wafers)
4 NEG wafers HV400 integrated
Double bellows system enables secondary vacuum to mitigate potential future leak on internal bellows and locate intermediate feedthrough
  Internal double bellows (same as for the VAX)
  Outer bellows (same shape convolution as for existing solution on plug-in)
2 feedthrough connections (up to 2 wafers per connection)
Distance of wafers to beam pipe is to be defined following vacuum qualification process
Integration of NEG wafer cabling and feedthroughs is open

## Slide 9: Alternative design with NEG wafers #2
Tube D340/336 used
4 NEG wafers HV400 integrated
Double bellows system enables secondary vacuum to mitigate potential future leak on internal bellows, on wafer feedthrough and on vacuum connections
  Internal double bellows (same as for the VAX)
  2x outer bellows  edge-welded bellows
2 feedthrough connections (up to 2 wafers per connection)
Distance of wafers to beam pipe is to be defined following vacuum qualification process
Design much more complex and difficult to implement (TBC)
Compression system is required
More bulky solution to integrate quick flanges DN100
He dome and outer sealing connection at TAXS side are blocking points

## Slide 10
Pumping / Ne venting lines

## Slide 11: Status of pumping lines - ATLAS
Conceptual design is defined for A-side
Baseline is to retain a symmetrical solution at C-side  GIS to be installed symmetrically on similar location (reduced height wrt A-side) (TBC)
Connection at VAX side is open. 2x alternatives are being analyzed (see next slide):
  Manual connection at JFSU octagon level  involves extending structure of M2-M3 support
  Remotely operated connection at alignment plate level  involves making space at JFC3 or TX1SP shields (detailed analysis required)
Easier installation
Hazard situation – walking area
Fragile components to be protected
Platform to be machined
Out of walking area – nonadditional protective equipment required
More complex anchor points
Uncertainty of real position of beams, cables or other equipment
JFSU - octagon
TXS1SO
Monoblock
GIS Area
TXS1SO
Monoblock
JFSU - Octagon
Stays in place
Moves during LS
DN63/60 pipe
DN38/34 pipe

## Slide 12: Status of pumping lines – ATLAS (VAX area)
Manual connection at JFSU octagon level
Remotely operated connection at alignment plate level
Extending support structure is envisaged as part of M2-M3 support
Modification on shielding is necessary
Services remain fixed to the shield
Services move with M2-M3 support

## Slide 13: Status of pumping lines – CMS (Q1-TAXS area)
Baseline is to retain routing of lines up to current LHC VAX  WP12.2.4 scope is design of new lines crossing TAXS and connection to existing pumping lines
Conceptual studies are made for right and left sides (no symmetrical solution) with lines connecting from above and from below  current baseline is to route from below (TBC from tests on WP8 Q1-TAXS area mock-up)
Integration studies of new routing of “existing” lines has been made following request by WP15
Pumping lines 5L
Lines to be dismantled
Lines to be kept

## Slide 14: Routing of pumping lines – CMS (I)
Design is ongoing for left and right sides (no symmetrical)
Multiple iterations and interfaces: WP8, WP12 (BVO), WP15 (integration + schedule/installation), CMS (integration + schedule/installation)
Routing from above
Routing from below (BASELINE)

## Slide 15: Status of pumping lines – CMS (II)
DN63/60 pipe
DN38/34 pipe
Example of line routing from above

## Slide 16: Conceptual integration studies 5R following request by WP15
Up to 3 options studied – to avoid clash with new survey device envelopes
WP15 to take a decision on next steps  possible additional scope for WP12.2.4

## Slide 17: Status of pumping lines – CMS (VAX area)
Routed between the VAX supports and FIN;
Not possible to place them below the support:
  Clearance of +/-20mm is required for alignment;
  The envelope of heating elements is considered.
Concern:
Clearance between the VAX plug-in and the venting lines  Shielding re-design is under study
Plug-in
Plug-in
FIN
FIN

## Slide 18
Integration and installation aspects with impact on the Q1-TAXS area

## Slide 19: Access to VAX in LHC
CMS access pathway
ATLAS access pathway
ATLAS pumping and venting lines  to be dismantled and removed for HL-LHC
CMS pumping and venting lines  to be retained for HL-LHC

## Slide 20: ATLAS Q1-TAXS area accessibility
Access through the LHC tunnel

## Slide 21: TAXS installation planning baseline in ATLAS
The option to anticipate the TAXS installation is under study  it would give more margin, facilitate the LHC vacuum system commissioning and enhance the installation process BUT would slightly impact the supporting configuration (see slide 26)
April 2026
October 2028

## Slide 22: CMS Q1-TAXS area accessibility (I)
Q1-TAXS area mock-up
Access possible ONLY through cavern

## Slide 23: CMS Q1-TAXS area accessibility (II)

## Slide 24: Installation sequence approach (CMS case)
Leak tightness validation of Q1-TAXS vacuum instrumentation
Q1-TAXS vacuum equipment assembly on Q1 cryostat [B]
Assembly of pumping lines and M1 support on TAXS
Experimental chamber installation and connection
Q1 installation
M2-M3 support structure installation
Leak testing of M3-to-experimental chamber connection
TAXS installation
Total/partial installation of pumping lines [A]
Leak testing of M2 and M3 interconnections
Leak testing of Q1-TAXS vacuum equipment connection to Q1
TAXS chamber to Q1-TAXS instrumentation connection
Pumping lines installation completeness (Q1-TAXS area) [A]
M2-M3 support structure pre-alignment
M2 and M3 installation [B]
M1 installation [B]
Leak testing of M1 connection to TAXS beampipe
Pumping lines installation completeness (VAX area) [A]
Leak tightness validation of pumping line connection at Q1-TAXS area
Electrical and compressed air connection checks (M1, M2, M3)
(A)
Leak tightness validation of pumping lines installed + checking and commissioning of existing bake-out
(B)
Module assembled and verified leak tight on surface. If applicable, bake out already verified on surface
(A)
(A)
(B)
(A)
(B)
M2-M3 cable pulling
Key aspect: Q1 installation before TAXS installation

## Slide 25: TAXS installation at CMS – impact on pumping line design
BASELINE: Q1 installation before TAXS installation
Pumping lines and TAXS chamber pre-assembled on FIN + TAXS
Solution involves clearance of 20 mm wrt TAXS including bake-out jackets
Q1
Q1
Shield hole machining must be optimized for transport configuration

## Slide 26: Q1-TAXS module temporary support
Closed with a blank flange
Temporary support is required to facilitate installation of Q1-TAXS module and connection to TAXS chamber once the TAXS is installed
For ATLAS, no temporary support would be required if the installation of the TAXS comes before Q1. However, depending on the relative misalignment (up to 5 mm max.) between the TAXS and Q1, it would require additional tooling to execute the connection

## Slide 27
Summary of main open points

## Slide 28: Summary of main open points
Freezing of vacuum layout, following NEG wafer test and qualification;
  Choice of best design approach;
ATLAS:
  Confirmation of GIS location at C-side;
  Cable and pumping line disconnection method and location in VAX area of ATLAS;
    Action on support and/or shielding;
  Confirmation of planning for TAXS installation;
CMS:
  Freezing of pumping line routing;
  Definition of Q1-TAXS module connection process;
  Definition of pumping line pre-installation process on plug-in (for TAXS installation) and plug-in shield modifictions.

## Slide 29: Thanks for your attention
Special thanks to Rita, Frederic, Herve, Josef, Alessio, Giuseppe, Vincent, Cedric, Oliver, Ruth, Antonio, Francisco and many others

## Slide 30: ATLAS shielding from LS3
Monoblock
TXS1SO
VAX
JFSU - Octagon
TX1SP
NEW DESIGN*
TAXS
ATLAS side A
Cradle
NEW DESIGN*
*Information provided by WP8
GIS Area
New design
Stays in place
Moves during LS
JFC_3
JFC_2
Q1
JFC_1
Nothing can remain beyond the alignment plate during LS

## Slide 31: VAX integration at pt. 1 – ATLAS
Cabling and pumping line to rise vertically at A-side
GIS A-side
Space for GIS at C-side on symmetric solution

## Slide 32
Information from the company:
With or without thermocouple
Standard 2m cables (needs to be discussed if we want a customized length).
CF16 feedthrough connection: up to 2 NEG wafers in parallel or series.
Other flanges sizes are possible for the feedthrough.
Positioning limitations? “ No problems on its positioning. The ZAO is particle free NEG sintered material. It is used in superconducting cavities.”
They offered to have a meeting to discuss about our specific application

## Slide 35: Pumping line routing in CMS

## Slide 36: Pumping line integration studies – CMS
Existing (currently installed) lines 5R
3 options considered:
  Option 1: routing pipe 1 over the water pipes; involves lowering down of pipe 2.
  Option 2: routing pipe 1 below pipe 2 (pipe 1 to cross between water pipes and wire).
  Option 3: Using another conduct for pipe 1 (available? – used for something else?)  nothing included in the 3D; involves lowering down of pipe 2? (TBC).
Pipe 1
Pipe 2
ST1553945
(WP8 model)
Passage for the lines
GIS - tunnel

## Slide 37: Pumping line integration at VAX area – CMS
Last elbow fixed to the Module 2 support  connection with module 2 checked on surface.
Previous rigid tube connected to FIN.
Bellow in between to absorb the misalignments if the position of the support is adjusted (connected to alignment plate)

## Slide 38: Q1-TAXS area mock-up - ATLAS configuration