## Slide 1
Search for solar neutrino and light dark matter in the PandaX-4T experiment
Qing Lin
（on behalf of PandaX collaboration）
University of Science and Technology of China
TAUP, 2023.08.28

## Slide 2
PandaX-4T Experiment & Its first data
2
5.6-tonne liquid xenon detector at CJPL-II;
2020-2021: Commissioning run (run0), 95 days;
2021-2022: Tritiated methane removal and run1, ~160 days
Ultrapure water shield: 13 m (H) x 10 m (D)～900 m3
TPC: 1.2 m (H) x 1.2 m (D)
3-in PMTs: 169 top/199 bottom
Sensitive volume: 3.7-tonne

## Slide 3
Solar neutrino CEvNS detection in DM experiment
4
Large underground experiment is going to be able to see Coherent Elastic ve-Nuclear Scatting (CEvNS)
Solar
SN
Atomspheric

## Slide 4
Difficulties of B8 CEvNS search
5
S1 detection eff low
S1
S2
10% detection
>90% detection
S1>2hit
S1>2PE
1.6 per year in 2.7 ton FV.
High rate of accidental pileups
Low stats of calibration
Eff?
NR calibration
ER calibration
S1=2，3hit
S2~[65,200]PE
1 -> ~ 100

## Slide 5
Waveform simulation
6
PMT dark count
Main S1
Main S2
PMT afterpulsing
Impurity photoionization;
Electron trapping at surface;
Delayed electrons
Drift time [us]
S2 width [us]
Neutron calibration
Reassembling data waveform segments
S1 width
S2 width
S2 pattern parameter
Else charge / Total charge
Good match between data and wf-sim in terms of S1/S2 shape, pattern, and waveform “dirtiness”.

## Slide 6
Machine-Learning based selection
7
Boosted Decision Tree (BDT)
S1 & S2 width
Spurious charges beside S1&S2
S2 pulse shape
Width/height ….
Difference of reconstructed positions;
Goodness-of-fit between data and sim;
Top-bottom asymmetry
WF-sim as signal sample;
Randomly paired S1-S2 as bkg sample;
18 variables as BDT input;

## Slide 7
Background budget
8
Physical bkg negligible!
cathode
ROI
Sideband
Drift time[us]
AC is the dominant bkg;
Use data with drift length > max drift length as sideband check;
Good match between data and model;

## Slide 8
Uncertainty analysis
9
Systematic uncertainties
Diff between data and sideband
Main S1
Main S2
Secondary S2
Use secondary S2s or events without S1 for checking sys.

## Slide 9
Unblinding
10
One event found after unblinding；
Statistically consistent with our expectation.

## Slide 10
First B8 CEvNS search in PandaX-4T
11
Phys. Rev. Lett. 130, 021802
Profile Likelihood Ratio method, combining 2-hit and 3-hit data;
Most stringent limit to solar neutrino flux using CEvNS channel;
Also updated the GeV DM upperlimit.

## Slide 11
S2-only approach
12
Electron burst event
Gas event
Physics event
Cathode event and gas event

## Slide 12
Background for S2-only data
13
Use fixed-dt data as estimate for cathode!
Set 3 with very high rate as template for MD
g2=17.9 PE/e

## Slide 13
Low-mass DM-e search
14
The most stringent constraints for the DM- electron interactions with mass in range of 40 MeV/c2 to 10 GeV/c2 with FDM =1, and 100 MeV/c2 to 10 GeV/c2 with FDM ∼ 1/q2
Our results challenge the freeze-out mechanism for DM mass range from 0.04 to 0.25 GeV/c2 with FDM=1, and are closing in on the freeze-in prediction with FDM ∼ 1/q2, assuming such light DM provides the entire DM abundance.
PRL 130, 261001 (2023)

## Slide 14
Summary & Prospect
15
Most stringent constraint on solar neutrino flux using CEvNS channel was obtained, using S1-S2 paired data.
We understand the bkg component of S2-only channel, mostly surface bkg from cathode and S2 pileup from micro-discharging;
Using S2-only data, the most stringent constraint on low-mass DM through DM-e scattering is given;
Analysis combining Run0 and newly taken Run1 is ongoing;
Dedicated calibration on ultra-low energy region is planned.

## Slide 15
21
Thanks for listening!

## Slide 16
Backups
21

## Slide 17
Coherent Elastic Neutrino-Nucleus Scattering (CEvNS)
3
Scientific goals of detection:
New channel for cosmic neutrino detection；
Weak mixing angle under low momentum transfer；
Non-standard neutrino interaction；
Technique for remove nuclear safeguard;
～100x

## Slide 18
Neutrino sources
18
e&𝛍 flavors;
1e6/s/cm2 @ 20m;
E<50MeV;
Observed in 2017;
Spallation neutron source
Nuclear reactor
1e13/s/cm2 @ 25 m with 3GW power;
E<2MeV;
Not observed yet;
Solar
～5e6/s/cm2 for B8 𝛎;
Mostly E<0.4MeV;
Not observed yet.

## Slide 19
Validation of bkg model
20
Use a (loose cut – final cut) sample as control for bkg validation;
Good match between data / control data both in width and S2 spectral shape