## Slide 1: One bunch at a time: wakefield damping in a distributed coupling accelerating structure
Evan Ericson, Alexej Grudiev
RF Development Meeting

## Slide 2: Overview
Motivation
SW cell design
Distributed coupling cell design
Wakefield modelling of a distribution network
Nose cone cell design
Structure & cryogenic structure performance

## Slide 3: Overview
Motivation
SW cell design
Distributed coupling cell design
Wakefield modelling of a distribution network
Nose cone cell design
Structure & cryogenic structure performance

## Slide 4: Motivation
SW structure for CLIC could have higher RF-to-beam efficiency than TW structure ~31% vs ~28% (A Standing Wave Structure Possibility For CLIC Main LINACs, Vasim Khan at HG2013 workshop)
SW cells have shown better RF breakdown performance (Study of basic RF breakdown phenomena in hight gradient vacuum structures, Dolgashev et al. at LINAC2010)
Number of cells before mode overlap π-mode: 9 π/2-mode: 83
TW structure
(source: High gradient structures and rf systems for high brightness electron linacs, Marco Diomede)
SW structure
(source: Ping Wang)

## Slide 5: Motivation
Operating using π/2-mode with biperiodic structure difficult to realize because of cells’ HOM waveguides
Biperiodic structure
(source: Electron bunchers for industrial RF linear accelerators: theory and design guide, Sergey Kutsaev)
Biperiodic structure with CLIC-G* cell
(source: A Standing Wave Structure Possibility For CLIC Main LINACs, Vasim Khan at HG2013 workshop)

## Slide 6: Motivation
Distributed coupling scheme treats cells as individual SW cavities, avoiding mode overlap
Other advantages of distributed coupling:
  Coupling between cells does not need to be a design constraint allowing cell shape to be optimized for RF performance
  Limited coupling/power flow through irises of SW cell may reduce RF breakdowns in this sensitive area
Disadvantages of distributed coupling:
  Complexity of design and fabrication
  Cost of fabrication
source: (SLAC research Activities on normal conducting RF accelerators, Sami Tantawi at Linear collider workshop 2019)

## Slide 7: Overview
Motivation
SW cell design
Distributed coupling cell design
Wakefield modelling of a distribution network
Nose cone cell design
Structure & cryogenic structure performance

## Slide 8: SW cell design
Started with CLIC-G* TW cell design
Adjusted length for π-mode
Adjusted A0, A2 of outer wall to minimize surface magnetic field
source: RF design and parameters of 2015 re-baselined 3TeV CLIC main linac AS at 12 GHz with compact couplers: CLIC-G* or TD26_vg1.8_R1_CC

## Slide 9: SW cell design

## Slide 10: SW cell design
 | unit | TW – Mid cell | SW – Opt0 | SW – Opt1 | SW – Opt2 | SW – Opt3
b | mm | 8.5249 | 8.4286 | 8.5638 | 8.4918 | 8.4709
h | mm | 8.3316 | 12.5 | 12.5 | 12.5 | 12.5
d | mm | 1.333 | 1.333 | 2.6 | 2.3 | 2.35
e |  | 1.153 | 1.102 | 2.400 | 1.600 | 1.179
f0 | GHz | 11.9949 | 11.9939 | 11.9945 | 11.9938 | 11.9946
Φ | ° | 120 | 180 | 180 | 180 | 180
Q0 |  | 5,855 | 7,133 | 6,927 | 6,937 | 6,913
R/Q0 | Ω/m | 16,466 | 11,208 | 10,962 | 11,184 | 11,350
R | MΩ/m | 96.40 | 79.95 | 75.93 | 77.58 | 78.48
vg/c | % | 1.226 | 0 | 0 | 0 | 0
Es/Ea |  | 1.98 | 2.49 | 1.80 | 1.99 | 2.09
Hs/Ea | mA/V | 3.73 | 4.43 | 4.67 | 4.62 | 4.60
Sc/Ea2 | mA/V | 0.33 | 0.30 | 0.35 | 0.34 | 0.33
Opt3: E, H, Sc fields

## Slide 11: SW cell design
Dashed line orientation | 
Horizontal | Beam dynamics transverse wakepotential threshold: 6 V/pC/m/mm
Vertical | Witness bunch positions (0.5 ns spacing)

## Slide 12: SW cell design
Iris geometry does not have strong effect on long-range wakepotentials
Issues with 4 HOM waveguide cell for distributed coupling application:
  Transverse wakepotential above threshold at 2nd bunch
  No way of coupling power into individual cells (solve this first since we might get a good wakepotential for free)

## Slide 13: Overview
Motivation
SW cell design
Distributed coupling cell design
Wakefield modelling of a distribution network
Nose cone cell design
Structure & cryogenic structure performance

## Slide 14: Distributed coupling cell design
Use design TW structure coupler cell to couple power into cell
Reduce coupler waveguides from 2 to 1 to improve damping
Match cell to power source, β = 1.93, by adjusting icw, b
b (mm) | 8.5833
icw (mm) | 5.963
f (GHz) | 11.9938
Q0 | 7,025
Qext | 3,595
R/Q (Ω/m) | 11,479
R (MΩ/m) | 80.6
Es/Ea | 2.06
Hs/Ea (mA/V) | 4.42
Sc/Ea2 (mA/V) | 0.33

## Slide 15: Distributed coupling cell design
Alternate orientation of couplers to reduce kick
Reducing symmetry from ¼ to ½ gives 2 wake polarizations
While coupler cell has input power, wakepotentials are above threshold

## Slide 16: Distributed coupling cell design
b (mm) | 8.4660
slot length (mm) | 7.55
f (GHz) | 11.9946
Q0 | 6,867
Qext | 3,508
R/Q0 (Ω/m) | 11,321
R (MΩ/m) | 77.74
Es/Ea | 2.15
Hs/Ea (mA/V) | 4.58
Sc/Ea2 (mA/V) | 0.33
Introduce HOM waveguide transition between cell and high-power waveguide
Match cell to power source by adjusting slot length, b
slot length

## Slide 17: Distributed coupling cell design
Wakepotential of this geometry (longSlot2) is lower than coupler cell but still above threshold
Impedance peaks of longSlot2 geometry almost same as 4 HOM waveguide cell but 22 GHz mode has higher Q-ext for longSlot2 geometry

## Slide 18: Distributed coupling cell design
 | Mode 1 | Mode 2 | Mode 3
f (GHz) | 17 | 22 | 28.2
Q-ext | 10 | 20 | 34
R = 2*Z | 10,000 | 22,500 | 6,200
22 GHz mode dominates wake at 2nd bunch position
 | Mode A
f (GHz) | 21.9
Q-ext | 17.5
R = 2*Z | 19,900

## Slide 19: Distributed coupling cell design
 | Mode 1 | Mode 2 | Mode 3
f (GHz) | 17 | 22 | 28.2
Q-ext | 10 | 20→15 | 34
R = 2*Z | 10,000 | 22,500 | 6,200
Reducing Q-ext of 22 GHz mode from 20 to 15 gives a wake below threshold at 2nd bunch position

## Slide 20: Distributed coupling cell design
What cell geometry has a 22 GHz mode with Q-ext = 15?
Strategy: vary w, iw
Since cell frequency is sensitive to iw, find b for every iw that gives f = 11.994 GHz
During sweeps, the cell will no longer be matched. We focused on finding a design that satisfied damping requirement before matching the cell
w
iw

## Slide 21: Distributed coupling cell design
iw
iw (mm) | b (mm) for f0 =11.994 | f (GHz) | Q_ext
8.09 | 8.4660 | 21.93 | 21
8.19 | 8.4355 | 21.90 | 19.5
8.29 | 8.4035 | 21.96 | 19.5
8.39 | 8.3703 | 21.82 | 19.75
8.49 | 8.3361 | 21.8 | 17
8.59 | 8.3008 | 21.74 | 16.5
8.69 | 8.2644 | 21.7 | 15.5

## Slide 22: Distributed coupling cell design
w (mm) | b (mm) for f0 =11.994 | f (GHz) | Q_ext
10.1 | 8.4660 | 21.93 | 21
10.2 | 8.4660 | 21.93 | 20.75
10.3 | 8.4660 | 21.93 | 20.5
10.4 | 8.4660 | 21.93 | 20.25
10.5 | 8.4660 | 21.93 | 20
10.6 | 8.4660 | 21.93 | 18.5
10.7 | 8.4660 | 21.93 | 17.5
w

## Slide 23: Distributed coupling cell design
Chose to vary w since increasing iw decreases Q0, increases surface magnetic field (heating)
Expected Q-ext = 15 for wakepotential to be below threshold but Q-ext = 17.5 was sufficient
  Q-ext of Mode 1 at 17 GHz was also affected by geometry changes
  Impedance peaks are asymmetric, fitting was done by eye
Wakepotentials of cell with different waveguide w = 10.1 mm, wVert = 10.7 mm
Vary w of vertical HOM waveguides

## Slide 24: Distributed coupling cell design
Wakepotentials are now below threshold
We can now simulate wakes of distribution network
b (mm) | 8.4395
slot length (mm) | 9.4
w (mm) | 10.7
f (GHz) | 11.9937
Q0 | 6,766
Qext | 3,557
R/Q0 (Ω/m) | 11,476
R (MΩ/m) | 77.65
Es/Ea | 2.15
Hs/Ea (mA/V) | 4.67
Sc/Ea2 (mA/V) | 0.33
w
w/2
w/2
Vary w of all HOM waveguides

## Slide 25: Overview
Motivation
SW cell design
Distributed coupling cell design
Wakefield modelling of a distribution network
Nose cone cell design
Structure & cryogenic structure performance

## Slide 26: Wakefield modelling of a distribution network
Approximate RF device feeding accelerating structure with a PEC plane
Pessimistically assume all wakefields that “see” feed network are reflected back into cell
Open Boundary
Effective Electric Boundary
Power distribution network

## Slide 27: Wakefield modelling of a distribution network
Open Boundary
Electric Boundary

## Slide 28: Wakefield modelling of a distribution network
Distance between the distribution network and the beam-axis determines the arrival time of the reflected wake

## Slide 29: Wakefield modelling of a distribution network
Offset of 100 mm between PEC plane and beam axis
Reflected modes group around non-reflected impedance modes (17, 22 GHz)
Impedance peaks are very narrow (high Q-ext, slow damping)
Different arrival, decay times for the 2 families

## Slide 30: Wakefield modelling of a distribution network
Larger offsets have lower amplitude, longer lasting reflected wakepotentials due to:
  The difference in arrival time of the modes is exaggerated
  Dispersion causes the modes to be “spread” in time

## Slide 31: Wakefield modelling of a distribution network
Can the reflected wakes be damped by increasing w or iw?
Offet of 150 mm between PEC plane and beam axis
Reflected wake is unaffected by increasing w or iw

## Slide 32: Wakefield modelling of a distribution network
Biplane cell has 5 HOM waveguides
Wakepotential at 3rd witness bunch very close to threshold
b (mm) | 8.5440
slot length (mm) | 8.95
w (mm) | 10.7
f (GHz) | 11.9937
Q0 | 6,786
Qext | 3,604
R/Q0 (Ω/m) | 10,873
R (MΩ/m) | 73.8
Es/Ea | 1.78
Hs/Ea (mA/V) | 4.69
Sc/Ea2 (mA/V) | 0.34

## Slide 33: Wakefield modelling of a distribution network
Horizontal coupler cell is fed power from the side of one of the HOM waveguides
Wakefields extracted through HOM waveguide couple weakly to high power waveguide
b (mm) | 8.5380
offset | 6
wallThickness (mm) | 1
slotWidth (mm) | 8.2
w (mm) | 10.7
f (GHz) | 11.9943
Q0 | 6,759
Qext | 3,570
R/Q0 (Ω/m) | 10,822
R (MΩ/m) | 73.1
Es/Ea | 1.78
Hs/Ea (mA/V) | 4.72
Sc/Ea2 (mA/V) | 0.35

## Slide 34: Wakefield modelling of a distribution network
Reflected wakepotential very similar to wakepotential when open boundaries are used
Wakefields in cell do not “see” distribution network
Power feed structure can be designed separately

## Slide 35: Wakepotential at 4th bunch

## Slide 36: Wakefield modelling of a distribution network
Alternating coupler cell and normal cells increases the number of HOM waveguides and potential damping

## Slide 37: Wakefield modelling of a distribution network
Doublet, triplet structures have acceptable wakes at all bunch positions
Wakepotentials of doublet, triplet structures show low amplitude mode beating after 4th bunch (0.45 m)

## Slide 38: Wakefield modelling of a distribution network
Doublet, triplet structures require:
    less feed waveguides
    coupling between cells (iris radius = 2.75 mm)
    consideration of 0 mode (doublet) or 0, π/2 modes (triplet)
    Balancing of on-axis field by adjusting cells in module

## Slide 39: Wakefield modelling of a distribution network
Horizontal coupler and triplet topologies were be combined
Surface field values of operating mode are not reported since fields need to be balanced first
w (mm) | 10.7
b (mm) | 8.5388
slotWidth (mm) | 9.78
f (GHz) | 11.9938
Horizontal coupler triplet: E, H, Sc fields

## Slide 40: Wakefield modelling of a distribution network
Motivation
SW cell design
Distributed coupling cell design
Wakefield modelling of a distribution network
Nose cone cell design
Structure & cryogenic structure performance

## Slide 41: Nose cone cell design

## Slide 42: Nose cone cell design

## Slide 43: Nose cone cell design
 |  | Nose cone | Opt1
ncrz | mm | 1.00 | -
ncry | mm | 1.00 | -
theta | deg | 45 | -
R3 | mm | 0.65 | -
R4 | mm | 0.65 | -
A0 | mm | 0.9 | 1.0355
A2 |  | 0.17665 | 0.17665
w | mm | 10.1 | 10.1
b | mm | 7.8067 | 8.5638
f | GHz | 11.994 | 11.9945
Q0 |  | 6,118 | 6,927
R/Q0 | Ω/m | 13,552 | 10,962
R | MΩ/m | 82.9 | 75.9
Es/Ea |  | 3.27 | 1.80
Hs/Ea | mA/V | 4.86 | 4.67
Sc/Ea2 | mA/V | 0.72 | 0.35

## Slide 44: Nose cone cell design
Nose cones give larger peak wake at s = 0 m than elliptical iris
Lower Q-ext of mode above 20 GHz gives faster damped wakes
Reduced radius of nose cone cell helps damping since HOM waveguides are higher % of surface
No increase in w required for wakes to be sufficiently low at 2nd bunch

## Slide 45: Nose cone cell design
Reflected wake simulations show wakepotential below threshold for offsets above 40 mm

## Slide 46: Nose cone cell design
w (mm) | 10.7
b (mm) | 7.7580
offset (mm) | 10
slotWidth (mm) | 19.2
f (GHz) | 11.9942
Horizontal coupler, triplet and nose cone topologies were be combined
Accelerating field even more unbalanced in coupling cell than for flat iris horizontal coupler triplet
Horizontal coupler nose cone triplet: E, H, Sc fields

## Slide 47: Overview
Motivation
SW cell design
Distributed coupling cell design
Wakefield modelling of a distribution network
Nose cone cell design
Structure & cryogenic structure performance

## Slide 48: Structure & cryogenic structure performance
Interest in cryogenic accelerators comes from:
  Q0 of resonant cells ↑ (source: Experimental demonstration of particle acceleration with normal conducting accelerating structure at cryogenic temperature by Nasr et al.)
  RF pulsed heating ↓ (source: High gradient experiments with X -band cryogenic copper accelerating cavities by Cahill et al.)
  Operating limits before breakdown ?
Surface magnetic field depends on cell design, not power coupling method

## Slide 49: Structure & cryogenic structure performance
 |  | 300 K | 77 K
f | GHz | 11.994 | 11.994
Ea | MV/m | 100 | 100
Hs/Ea | mA/V | 4.67 | 4.67
Hs | MA/m | 0.467 | 0.467
tp | ns | 238 | 238
rho | kg/m^3 | 8.95e3 | 8.95e3
Rs | Ohm | 0.027 | 0.011
k | W/m/K | 4.01e2 | 5.00e2
cε | J/K/kg | 385.2 | 200.0
ΔT | K | 43.59 | 22.07
Operating at 77 K, temperature increase due to pulsed heating is 50% of temperature increase when operating at 300 K
Cell parameters
Copper parameters

## Slide 50: Structure & cryogenic structure performance
CLIC DB source: What are the efficiency, gradient and breakdown indicators structure when it is fed the CLIC drive beam pulse?
Other source: What are the Pin, tp requirements for a power source if we wanted to operate a structure at 100 MV/m?

## Slide 51: CLIC drive beam source
 | unit | TW – mid cell | Opt1 | Opt1 (300K) | Opt1 (77K) | limits
Q0 |  | 5,637 | 6,927 | 6,927 | 15,586 | 
R/Q0 | Ohm/m | 16,227 | 10,962 | 10,962 | 10,962 | 
R | MOhm/m | 91.5 | 75.93 | 75.93 | 170.85 | 
Es/Ea |  | 1.98 | 1.8 | 1.8 | 1.8 | 
Hs/Ea | mA/V | 3.73 | 4.67 | 4.67 | 4.67 | 
Sc/Ea2 | mA/V | 0.33 | 0.35 | 0.35 | 0.35 | 
Eaccload avg | MV/m | 100 | 100 | 108.25 | 140.75 | 
number of bunches in train |  | 312 | 312 | 314 | 242 | 
Pin | MW | 62.3 | 56.3 | 63.6 | 63.6 | 63.5
tfill | ns | 66 | 82.0 | 87.3 | 123.1 | 
tb | ns | 156 | 156 | 157 | 121 | 
tp | ns | 222 | 238.0 | 244.3 | 244.1 | 244
RF-steady state efficiency | % |  | 47.3 | 45.4 | 59.0 | 
RF-pulse efficiency | % |  | 65.5 | 64.3 | 49.6 | 
total RF-beam efficiency | % | 28.4 | 31.0 | 29.2 | 29.2 | 
Es scaled to 200 ns | MV/m | 201 | 185 | 201 | 262 | 200 (300)
ΔT | K | 26.86 | 43.59 | 51.75 | 44.28 | 40 (cryo: ?)
Sc scaled to 200 ns | MW/mm2 | 5.50 | 3.71 | 4.38 | 7.41 | 4 (cryo: 8)
CLIC accelerating structure RF breakdown limits
with 20% margin
Efficiencies
Structure parameters
Cell parameters

## Slide 52: Other power source
 | unit | TW – mid cell | Opt1 (300K) | Opt1 (77K) | limits
Q0 |  | 5,637 | 6,927 | 15,586 | 
R/Q0 | Ohm/m | 16,227 | 10,962 | 10,962 | 
R | MOhm/m | 91.5 | 75.93 | 170.85 | 
Es/Ea |  | 1.98 | 1.8 | 1.8 | 
Hs/Ea | mA/V | 3.73 | 4.67 | 4.67 | 
Sc/Ea2 | mA/V | 0.33 | 0.35 | 0.35 | 
Eaccload avg | MV/m | 100 | 100 | 100 | 
number of bunches in train |  | 312 | 312 | 312 | 
Pin | MW | 62.3 | 56.3 | 39.81 | -
tfill | ns | 66 | 82.0 | 88.0 | 
tb | ns | 156 | 156 | 156 | 
tp | ns | 222 | 238.0 | 244 | -
RF-steady state efficiency | % |  | 47.3 | 66.92 | 
RF-pulse efficiency | % |  | 65.5 | 63.9 | 
total RF-beam efficiency | % | 28.4 | 31.0 | 42.8 | 
Es scaled to 200 ns | MV/m | 201 | 185 | 186 | 200 (300)
ΔT | K | 26.86 | 43.59 | 22.35 | 40 (cryo: ?)
Sc scaled to 200 ns | MW/mm2 | 5.50 | 3.71 | 3.74 | 4 (cryo: 8)
CLIC accelerating structure RF breakdown limits
with 20% margin
Efficiencies
Structure parameters
Cell parameters

## Slide 53: Other power source
 | unit | Opt1 (77K) | limits
Q0 |  | 15,586 | 
R/Q0 | Ohm/m | 10,962 | 
R | MOhm/m | 170.85 | 
Es/Ea |  | 1.8 | 
Hs/Ea | mA/V | 4.67 | 
Sc/Ea2 | mA/V | 0.35 | 
Eaccload avg | MV/m | 100 | 
number of bunches in train |  | 1,400 | 
Pin | MW | 39.81 | -
tfill | ns | 88.0 | 
tb | ns | 700 | 
tp | ns | 788 | -
RF-steady state efficiency | % | 66.92 | 
RF-pulse efficiency | % | 88.83 | 
total RF-beam efficiency | % | 59.4 | 
Es scaled to 200 ns | MV/m | 226 | 200 (300)
ΔT | K | 40.16 | 40 (cryo: ?)
Sc scaled to 200 ns | MW/mm2 | 5.53 | 4 (cryo: 8)
CLIC accelerating structure RF breakdown limits with 20% margin
Efficiencies
Structure parameters
Cell parameters

## Slide 54: Summary
Opt1 iris design was selected as the best SW cell design due to its low surface electric field
Horizontal coupler cell design is transparent to wakefields and allows power distribution system to be designed separately
Doublet and triplet cell designs take advantage of cell-to-cell coupling while damping wakefields
Nose cone design has high surface fields and may be better-suited for a low gradient, high efficiency application
Cryogenic structures are more “RF” efficient and have lower breakdown indicators than room temperature counterparts

## Slide 55: Summary
Recommend continuing design and optimization using cell with:
  Opt1 iris (d=2.6 mm, e=2.4) for low surface electric field
  Power coupled through the side of a HOM waveguide for minimal reflected wakefields
  Triplet module to take advantage of cell-to-cell coupling