## Slide 1: Mechanical model of the MDI

## Slide 2: Table of content
Introduction | 3 | Double bellows | 12
MDI Mechanical Model | 4 | Crotch chamber | 14
Central Chamber | 5 | Support tube | 16
Trapezoidal chamber | 6 | Structural optimization of Support Tube flanges | 21
Thickness of the chamber | 7 | Conclusion | 23
Structural analysis – chamber | 8 |  | 
Bellows constraint configuration | 10 |  | 
Single bellows | 11 |  | 

## Slide 3: Introduction
Since the FCC week 2022 some steps have been taken; some discussions were held during the MDI session.
The main themes are related with:
The modification of the central chamber design according to the Inner Vertex design.
The design of the trapezoidal chamber and its cooling according to the LumiCal requirements.
The IR bellows configuration.
The crotch chamber.
The concept of Support Tube and the integration with Inner, Middle, Outer Vertex and Vertex Disks.
The proposal of an assembly strategy.
The structural optimization of IR support structure.

## Slide 4: MDI mechanical model
Support tube
LumiCal
Trapezoidal chamber
Central chamber
Cooling
Cryomagnet
This design is based on the IDEA detector concept, in fact we are working in close contact with INFN-Pisa integrating their Inner, Medium, Outer Vertex and Vertex Disks.
IDEA detector
Bellows

## Slide 5: Central chamber
Inlet/outlet
Central chamber
1st layer Inner Vertex
The central has the following characteristics:
AlBeMet 162 as main material
Three layers from 0-90 mm from IP
0.35 mm of AlBeMet162
1 mm gap for Paraffin
0.35 mm of AlBeMet162
Paraffin as coolant
Geometry studied to integrate the central chamber with the Inner Vertex (200 µm of clearance between central chamber and Inner Vertex support)
Inlet/outlet for paraffin cooling

## Slide 6: Trapezoidal chamber
The cooling is based on an asymmetric solution, using the 50 mrad cone as the cutting profile, to assure the respect of the spatial constraint due to the LumiCal requirment.
To reduce the cooling material, the design provides five couples of channels for each side; in this way is possible to use the needed quantity of coolant and reduce the material, creating a light structure.
EBW
Two halves AlBeMet pipe
Transition
Bellows
EBW
Thick copper deposition
Main characteristics:
AlBeMet162 as main material
Chamber in two halves and assembled using EBW
Copper cooling system
A
A
A-A

## Slide 7
Thickness of the chamber
0,35 mm
1,5 mm
2 mm
Uniform thickness of the trapezoidal chamber set at 2 mm
90 mm
115 mm
156 mm
1 mm
0,35 mm

## Slide 8: Structural analysis – chamber
Loads, constraints, characteristic parameters, design
FEA (Ansys)
Temperature distribution, stress and displacement along the pipe
Paraffin flow (central chamber)
Flow rate: 0,015 kg/s
Section:68,17 mm2
Velocity: 0,3 m/s
Inlet temperature: 18°C
Convective coefficient: 900 W/m2K
Water flow (trapezoidal chamber)
Flow rate: 0,0019 kg/s
Section: 9,62 mm2 (20 different channel)
Velocity: 0,2 m/s
Inlet temperature: 18°C
Convective coefficient: 1200 W/m2K
Heat load
54 W central
130 W AlBeMet162 for each part
From CST calculations (Alexander Novokhatski (SLAC))
Chamber design (until the bellows)
Weight
chamber
Inner Vertex first layer
Constraint
Cantilevered, simply supported configuration
RESULTS
Hypothesis:
Perfect thermal contact between the materials

## Slide 9
 | Trapezoidal chamber | Central chamber
Coolant | Water | Paraffin
Maximum chamber temperature [°C] | 47,6 | 33,1
T_out coolant [°C] | 20,5 | 20,1
Von Mises stress [MPa] |  |  |  |  | 
 |  | Trapezoidal SX | Trapezoidal DX | Central IN | Central EX
BEAM | Fixed ends | 22,07 | 21,86 | 46,8 | 38,9
 | Fixed+displ | 14,65 | 10,63 | 9,69 | 17
Maximum displacement [mm] |  |  | 
 |  | X | Y
BEAM | Fixed ends | 0,031 | 0,07
 | Fixed+displ | 0,1 | 0,29
Structural analysis - chamber - results

## Slide 10
Bellows – constraint configuration
The use of Support Tube is designed to avoid overloads on central chamber during assembly and operation (thermal expansion). This solution has been obtained using two kind of bellows for the two sides of the support tube.
To understand the constraint configuration, it is useful to create a simplified scheme with bellows, support tube and chamber.
In short, in this way we can:
Protect the central chamber during the assembly procedure
Support properly the chamber bellows-to-bellows, containing the deformation
Allow the thermal deformation without compromising the chamber
1st Bellows
(named single bellows)
2nd Bellows
(named double bellows)
Chamber
Support tube
End cap
End cap
IP

## Slide 11: 1st Bellows (Single bellows)
Anchoring flange to Support Tube
IP SIDE
CRYOSTAT SIDE
Convolutions to compensate
Cryostat expansion and assembly
IP SIDE
CRYOSTAT SIDE

## Slide 12: 2nd Bellows (Double bellows)
Anchoring flange to Support Tube
IP SIDE
CRYOSTAT SIDE
Linear bearing system
Few convolutions inside Support Tube for thermal expansion
Convolutions to compensate
Cryostat expansion and assembly
IP SIDE
CRYOSTAT SIDE

## Slide 13: Bellows design considerations
It is necessary to:
insert the cooling system;
improve the supporting flanges design;
check properly the internal design in term of impedance and wake fields. (CST calculations by Alexander Novokhatski in progress);
optimize RF contact with FEA analysis.
Summary table |  |  | 
 | Single bellows | Double bellows | 
 |  | Cryostat side | Chamber side
Axial Stroke (z) [mm] | -15/+9 | -10/+6 | -2.3/+1.4
Angle [deg] | 12 | 8 | 2
Radial offset (x) [mm] | 1.15 | 0.5 | -----
Radial offset (y) [mm] | 1.54 | 0.7 | -----
The design is still in progress, some modifications have to be done to optimize the shape and dimensions.

## Slide 14: Crotch chamber
-1175 mm
Solution A:
Standard flanges
More space available for the crotch
Flanges in Helium
Solution B:
Flanges not in contact with Helium
Shorter chamber than solution A
Non standard flanges
Chart: 
| -5560 | -2500 | -90 | 0
X4 | 106.4627 | 52.5 | 10 | 10
X3 | -98.4 | -52.5 | -46.8 | -38.5 | -38.2 | -45.9 | -10 | -10
X2 | 71.1818 | 22.5 | 5 | 1 | 0.5 | 0
X1 | -71.1818 | -22.5 | -5 | -1 | -0.5 | 0
Xc | -84.7909 | -37.5 | 0
Solution A
Solution B
Work in progress
Remote vacuum connection

## Slide 15
SR MASK 2060 mm from IP
Shifted flanges
Start of circular pipe at 2550 mm from IP
2550 mm
IP
Custom flanges
It is a work in progress:
Shape
Flanges geometry
Interface with Remote vacuum connection
REMOTE VACUUM CONNECTION BLOCK
Not regular shape
Very preliminary design

## Slide 16: Support tube – description
The structure is made with a multiple layer structure:
1mm CF + 4mm HC + 1mm CF
To allow the support of the disks are necessary 6 reinforcement ribs.
The cylinder is split in two halves to simplify the assembly procedure
The Aluminium endcaps support the LumiCal and the beampipe
The support tube aims to :
Provide a cantilevered support for the pipe.
Avoid loads on thin-walled central chamber during assembly or due to its own weight
Support LumiCal.
Support the Medium, Outer Vertex and Vertex Disks.
CF=carbon fibre
HC=honeycomb
Aluminium ribs
Aluminium endcaps

## Slide 17: Support tube – loads and constraints
The aim of this analysis is to calculate the stress and displacement in each part of the cylinder (Al reinforcement, carbon fiber, honeycomb).
It is necessary to set:
Constraint configuration  double fixed ends
Loads configuration
Chamber | 50 kg
LumiCal | 70 kg + 70 kg
Vertex Disks | 6*10 kg
Outer Vertex | 15 kg
Medium Vertex | 7 kg
First guess loads (overestimated) | 
Carbon fiber/ honeycomb creation  layered section

## Slide 18: Support tube – Structural analysis – results
 | Maximum stress [MPa]
Aluminium flanges | 2.08
Aluminium ribs | 0.20
Honeycomb | 0.02
Carbon fiber | 0.60
 | Maximum displacement X [mm]
Aluminium flanges | 1.34 e-2
Aluminium ribs | 2.62 e-2
Composite | 2.80 e-2

## Slide 19: Support tube – Rail
The support tube needs to be inserted into the main detector; the idea is to use a rail, starting from the outside of the detector to allow the sliding of the cylinder.
To assure a good precision and appropriate support it is necessary to use the linear bearings; different types are available, the choice has to be made considering:
Required positioning precision
Weight of the whole structure
Necessary degrees of freedom
SECTION
After the positioning the rail will be removed, and the support tube attached to the detector

## Slide 20
Under study:
Rail support
Rail anchoring
Rails length
Geometry of the rail section
Linear bearing type
Positioning system
To continue the design, it is necessary to know:
Allowable anchoring point from detector side
Allowable space (internal detector diameter and geometry)
Hypothesized anchoring point

## Slide 21: Structural optimization of Support Tube flanges
The SIMP algorithm, based on the concept of penalty.
The Generative Design method, capable of creating a structure from an initial shape and from imposed spatial constraints.
The lattice structure with Field Driven design allows to create an infill or some area using lattice structure to maintain the geometric continuity using porous area.
The FCC project is a precious opportunity to use the most innovative techniques in mechanical design.
The structural optimization is a field in rapid developing, different techniques have been validate and more are in progress. At the moment have been evaluated three main approaches to reduce the mass maintaining the requirement in term of stress and displacement. The analysis is in progress, and this is a report of the current state of the work.

## Slide 22
These methods have been used to optimize the interface between the Support Tube of the FCC Interaction region and the detector. The first step made is a preliminary analysis to study the number and position of anchoring point for the Support Tube. After the choice of the best configuration has been performed three structural optimization for each design, using two different SIMP algorithm and a Generative Design algorithm.
After the comparison of these design has been performed a study of the final flange of the support structure, using the SIMP algorithm, the Generative Design and the lattice structure with Field Driven design.
LumiCal anchor
Chamber anchor

## Slide 23: Conclusion
Prototyping
Integration of CLD detector
Increase the level of detail of the crotch chamber and support structure
Develop of remote vacuum connection
Central chamber: inlet and outlet (thick copper deposition), cooling system
Welding for elliptical shape
Most urgent
The current central chamber design is now compatible with the Inner Vertex design.
The design of trapezoidal chamber is now compatible with LumiCal requirements.
The preliminary design of crotch chamber has been proposed.
The concept of Support Tube has been introduced and the proposal of an assembly strategy as well
The structural optimization of IR support structure is started.
Future steps

## Slide 24: \