## Slide 1
Centre-of-mass energy shifts in Z pole run
Resonant depolarization frequency  < E+b > , < E-b>  ECM (IP1,2,3,4)
Alain Blondel as member of EPOL group
-- Energy gains and losses in the ring
-- Beam Collision Offsets X Opposite Sign Vertical Dispersion (OSVD)
-- EM attraction between bunches
and their monitoring/measurement methods
Error budget on ECM : << 100 keV absolute, ~<4keV point-to-point
WORK IN PROGRESS

## Slide 2
FCC-ee beam polarization and
centre-of-mass energy calibration
arXiv:1909.12245

## Slide 4
RF = 4SRi + 4SRe + 4BS + ...  40 MeV+...
SRi
SRe
difference btw inner and external octant:
SRe - SRi  /2 x8SR  0.19 MeV
Beamstrahlung (per IP)
BS = 0 to 0.62 MeV per IR
non colliding to fully colliding beams
 = crossing angle = 30mrad
Orders of magnitude, basics
Energy gain (RF)
Synchrotron radiation (SR) 39MeV/turn
beamstrahlung (BS)
Others (transerse impedance etc.) (few MeV?)
the average energies E0 around the ring
are determined by the magnetic fields and RF frequency
same for colliding or non-colliding beams
-- measured by resonant depolarization
-- can be different for e+ and e-
ESSENTIAL TO HAVE ALL RF IN ONE POINT
RF

## Slide 5
Orders of magnitude, Longitudinal Impedance
The bunch lench increases for colliding beams  energy losses decrease.
resistive wall
Bellows
Emanuela Carideo, EPOL workshop 2
Uniformly distributed
depends on bunch length!

## Slide 6
From EPOL Workshop I (2017)
3. From spin tune measurement to center-of-mass determination s =
  3.1 Synchrotron Radiation energy loss (10 MeV @Z in 4 ‘arcs’) calculable to < permil accuracy
  3.3 Beamstrahlung energy loss (0.62 MeV per beam at Z pole), compensated by RF (Shatilov)
  3.4 layout of accelerator with IPs between two arcs well separated from single RF section
3.5 Eb+ vs Eb- asymmetries and energy spread can be measured/monitored in expt:
e+e-  + - longitudinal momentum shift and spread (Janot)
P. Janot: 5 min/exp @Z  106 + - /expt 
50 keV meast both on ECM and E+ - E-
and beam crossing angle  (error negl.)
also monitor relative ECM (p-t-p!)
z boost
D. Shatilov:
beam energy
spectrum
without/with
beamstrahlung

## Slide 7
E-J = E0- + RF/2 - SRi - BS/2
E+J = E0+ + RF/2 - 4 SRi - 3 SRe -7BS/2
E+J +E-J= E0+ + E0-+ RF - 5 SRi - 3 SRe -4BS
E+J+E-J= E0+ + E0- +SRe - SRi
E-A = E0- + RF/2 - 2SRi - SRe - 3BS/2
E+A = E0+ + RF/2 - 3 SRi - 2 SRe -5BS/2
E+A+E-A= E0+ + E0-+ RF - 5 SRi - 3 SRe - 4BS
E+A+E-A= E0+ + E0- +SRe - SRi
e+
e-
RF
RF = 4SRi + 4SRe + 4BS
-- ECM shift due to SR in  ext
-- all Ecm are the same
-- boosts measure the energy losses
-- differences between the rings will show up.
-- assumes BS energy loss before collision is on average half of full beamstrahlung
in this slide, many simplifying assumptions
-- BS same for all IP
-- energy losses same for all arcs, include SR and Long. Impedance
-- 4 effect ignored
-- E0 measured by Resonant depolarization
Orders of magnitude – ECM and Boosts
Boost(J) = E-J - E+J = E0- - E0+ + 3 SRi + 3 SRe + 3 BS  measures ¾ of E losses in J and G
Boost(A)= E-A- E+A= E0- - E0+ + SRi + SRe + BS ¼ in A and D
(other two ibid with reverse sign)
considerable information contained in the boosts measured by the experiments!
SRi
SRe

## Slide 8
No longitudinal impedance included yet
MAD-X simulation

## Slide 9
-- The centre of mass energy is equal to the ’zero’ value with great precision, (8 keV) even with beamstrahlung included
-- to be checked: the average energy that is given by resonant depolarization is not exactly E0 but close -- this is due to the virtue of having only one RF section.
-- the boosts are large and not as symmetric as expected. 3B(A)=-3B(D) = B(J)=-B(G) ;  to be understood in detail why.
Every 8 minutes the boosts are measured with a precision of 50 keV. 5keV per shift.... 0.5 keV for 30days of run. Applying the constraints can fix the energy loss model effectively.
THE GRAND TEST IN FINE: ALL MEASURED Z MASSES SHOULD BE THE SAME
Exact numbers not final!
sum of |boosts| is indeed
2X energy losses! (41.48 MeV x 2)

## Slide 10
Jorg Wenninger
boosts, Qs and orbit differences will depend on beam intensity via both beamstrahlung and variation of impedance, which somewhat compensate eachother
Important to check, since pilot bunches will have different behaviour than colliding ones!
(of course on <average energy> this is all compensated by the RF!

## Slide 11
Concludes that the energy losses can can be fit to extremely high accuracy. (and for instance the power law E4 verified by fitting the exponent)
Work in progress!..
Ivan Koop

## Slide 12
Experience from LEP: Vernier scans
No effect on ECM if no offset
NB energy spread is reduced.
Relative position of beams measured to +- 80 nanometers from one scan
From beam energy to ECM
opposite sign dispersion
ECM lowered:
precision requires going
far from maximum  loose beam?
Try beam-beam deflection?

## Slide 13
CONJECTURE:
Because the beams are crossing each other at an angle in the horizontal plane,
horizontal dispersion or offsets are not relevant
every x slice of one beam crosses every x slice of the other

## Slide 14
For FCC-ee at the Z we have in vertical direction:
Parasitic dispersion of e+ and e- beams at IP 10um
the difference is .
Sigma_y is 28nm
Sigma_E is 0.132%*45000MeV=60MeV
Delta_ECM is therefore 1.4MeV for a 1nm offset
Note that we cannot perform Vernier scans like at LEP, we can only displace the two beams by ~10%sigma_y
Assume each Vernier scan is accurate to 1% sigma_y, we get a precision of 400 keV.
the process should be simulated
we need 100 beams scans to get an ECM accuracy of 40keV – suggestion: vernier scan every hour or more.
It is likely that Vernier scans will be performed regularly at least once per hour or more. (100 per week) we end up with an uncertainty of ~10keV over the whole running period. (provided no systematic effects show up)
The dispersion must be measured as well; this can be done by using the vernier scans with offset RF frequency
this would lead to lots of Vernier scans!
critical effect is in the vertical plane, but horizontal plane should be investigated as well
vernier scans
arXiv:1909.12245

## Slide 15
This is good news because effect (problem) is 10 times smaller than we thought.... 40keV 4 keV (stat!)
but we wont believe it until we measure it! (How do we measure vertical dispersion at IP?)

## Slide 16
beam-beam deflection scans were already used at SLC, KEK and LEP
CERN-SL-96-025
https://inspirehep.net/literature/420668
Uncertainty on yopt = -5.60.1 m
is 1/40 of the vertical beam size 3.80.2 m
which was itself measured in the process

## Slide 17
beam-beam deflection measurement at FCC-ee as if in « squished perspective » looking from behind detectors endcaps
e-
e+
detector z axis
U-BPM
upstream electron
beam position monitor
located between
final focus quads and
compensating solenoid
U+BPM
D+BPM
downstream positron
beam position monitor
located between
final focus quads and
compensating solenoid
D-BPM
BPM in arc magnets
x axis
y axis
IP
d=2.1m
BPM precision over 108 bunch passages is ~1m
X

## Slide 18
1. beams collide head on
-- or at low current
1’. pilot bunches (not colliding) all the time
1’’ can be calibrated with low current vernier scan
1’’’ or occasional vernier scan
REFERENCE

## Slide 19
2. offset by y = 0.1y (=3.5nm)
opposite kick by 4rad
(Shatilov) in opposite directions for e+ and e-
movement in the BPMs by
 2 rad x 2.1m = 4.2 m
(x1000 demagnification due to optics)
with a very specific pattern of movements
Vertical beam size at the IP: 35 nm (at Z pole). Vertical offset of 0.1y leads to additional orbit angles about 2 rad for the nominal bunch population 2.5E+11. (D. Shatilov, simulation)
4.2 m
COLLISION OFFSET
4rad

## Slide 20
Measurements of offsets and Opposite Sign Vertical Dispersion (OSVD)
Purely statistical and preliminary arguments:
OFFSETS:
Four measurements of 4.2 micron displacement with 1 micron precision can be made with 108 bunch passages (assume 10000 bunches in each beam)
every 3 seconds
measurement of beam beam offset with precision of 0.1 * 35nm / 4.2 / 4 = 1/80 of beam size or ~0.4nm
NB no need of a scan in principle if a good and stable reference can be demonstrated. CAN WE USE THE PILOT BUNCHES? LEP did not have pilot bunches, but maybe we can use them? (there is a debate on this) Pilot bunches would provide 10^8 bunch measurements in 2 minutes (only 250 bunches of each beam)
Even better use a second set of (unpolarized) pilot bunches with full intensity. How many are needed? Question is asked (to M. Wendt) about impact of bunch length which is different of pilot and colliding bunches
OSVD (this requires simulation of a 4IP machine because the beam beam effect will result in cross-talk between IPs) we cannot really measure the dispersion at IP directly,
but the beams will move in opposite directions upon a change of RF frequency
we measure the opposite sign vertical dispersion (OSVD) this way! Assuming that a relative momentum change of 10-3 is feasible, this measurement corresponds to a measurement of opposite sign vertical dispersion D*y(e+)-D*y(e-) with a precision of 0.4 micrometer.
Potential is great but the devil is in the details

## Slide 21
OSVD and collision offsets -- status
THIS IS VERY PROMISING: possible shift in energy (or absence thereof ) with a precision of  20 keV each time the dispersion measurement is done.
If the pilot bunches can be used as reference because it saves large scanning across the beams
from a combination of ‘beam-beam offset scans’ (Vernier or Van der Meer scans)
and direct beam-beam collision offset measurements
we have two methods providing potentially a large sample of measurements with a precision of O(20keV)
-- more simulations needed to ascertain feasibility of IP dispersion measurement

## Slide 22
Energy shifts from EM interaction between the bunches
This was discussed already in the EPOl paper
Section 7.5.2 and 8.1.
The critical point is that
the EM forces being conservative, they do not
modify the centre-of-mass energy,
they modify both :
the beam energies and the crossing angle
net effect is about 60 keV correction
“The determination of the average centre-of-mass energy therefore requires
the average beam energy from pilot bunches with resonant depolarization (+ correction for energy losses as above)
the measurement of the crossing angle in collision
the determination of the crossing angle increase due to beam-beam effects”

## Slide 23
With 106 dimuon events, expected to be recorded in ~10 minutes at the Z pole (exp)
the crossing angle (taken as the peak of the fitted Voigtian function) can be determined
with a sub-microrad statistical precision: = 29.9998 0.0003 mrad
It is proposed is to perform in each filling a progressive mesurement of crossing angle with increasing beam charges
it is also shown that the
result can be obtained from
the natural variation of intensity
during each fill.
NB Issues of stability and systematics
are really crucial here
 more understanding/discussion
needed!

## Slide 24
the point-to-point uncertainty dominates the physics output. It can be controlled in two ways 1. compare the momentum as measured with the polarimter spectrometer between different
energies (monitored constantly at each energy)  Magnet must be very precisely monitored (<10-6) and dedicated monitoring of the main beam after the collision and magnet should be discussed.
this requires dedicated design of polarimeter
2. use the e+e-  +- events in the detectors to measure ECM for each of the energies.
 monitor experimental magnet to (<10-6) precision + QED issues etc..
Assigning energy shift errors to absolute or point to point (recap from arXiv:1909.12245)

## Slide 25
Assigning energy shift errors to absolute or point to point
For the Z line-shape measurement (and for asymmetries)
the point-to-point errors dominate.
The above error estimates O(20 keV) are really applicable for the Absolute Scale Uncertainty. (in addition to error in RDP Ebeam, for which this analysis need to be done too)
The point to point errors are normally much smaller.
 keep the running conditions and calibration methods IDENTICAL (as much as possible)
for the (typically 3 or 3 groups) of data taken
below at and above the Z peak (88,91,94 GeV Ecm)
Typically:
statistical errors  point-to-point
Method uncertainties  absolute scale

## Slide 26
Conclusions
We have outlined the main methods and excellent potential precision for the control of energy shifts
It is too early to give new estimates but aim to give new values with significant improvements for the Feasibility Study report.
ENERGY LOSSES
-- the boost measurements in the experiments basically provide measurements of the energy losses at keV levels on daily basis. Uncertainty anlysis to be made including impact of beamstrahlung.
Collision offsets x OSVD
-- vernier scans and beam beam deflection measurements provide collision offsets and IP dispersion measurements
at 20 keV level every time a dispersion measurement is made.
-- many questions remain e.g.
-- reliability of full charge pilot bunches as reference
-- sensitivity of OSVD measurement to resulting beam beam collision offsets in all four experiments at once.
Beam beam transverse attraction
-- beam-crossing angle measurement when bunch charges are increased measures what we need (stability issues?)
Point-to-point uncertainties
These effects will not generate large point-to-point errors provided running conditions are kept identical for the scan points
They will contribute to absolute energy scale error. All experiments should measure the same Z mass!