## Slide 1
Positron production, capture and acceleration until the damping ring
Iryna Chaikovska
Laboratoire de Physique des 2 Infinis Irène Joliot-Curie (IJCLab)
CNRS, Université Paris-Saclay
on behalf of the WP3 team (FCC-ee injector update studies)
F. Alharthi, R. Chehab, V. Mytrochenko (IJCLab), S. Doebert, J.-L. Grenard, B. Humann, A. Latina, A. Lechner,
R. Mena Andrade, A. Perillo Marcone, Y. Zhao (CERN), B. Auchmann, P. Craievich, M. Duda, J. Kosse, M. Schaer, N. Vallis, R. Zennaro (PSI), L. Bandiera, M. Soldani, A. Sytov (INFN/Ferrara), A. Bacci, M. Rossetti Conti (INFN/Milano), Y. Enomoto (KEK), P. Martyshkin
FCCIS: 'This project has received funding from the European Union's Horizon 2020 research and innovation programme under the European Union's Horizon 2020 research and innovation programme under grant agreement No 951754.'
This work was done under the auspices of CHART (Swiss Accelerator Research and Technology) Collaboration, https://chart.ch - CHART Scientific Report 2022: https://chart.ch/reports/

## Slide 2: FCC-ee pre-injector layout (positron source)
Beam energy | 6 GeV
Bunch charge | ~5.6 nC (max)
Bunch length | 1 mm
Bunch transverse size | ≳ 0.5 mm
Talk on DR by C. Milardi (LNF)
Nb of bunches per pulse | 2
Bunch separation | 25 ns
Repetition rate | 200 Hz
Beam power | ~13.3 kW (max)
e- drive beam

## Slide 3: FCC-ee positron source: requirements
Ne-/bunch ⨯ ηe+Accepted ≥ 5.4 nC/bunch ⨯ 2.5
The complete filling for Z running => Requirement ~2.75 ⨯ 1010 e+/bunch (4.4 nC) at the linac end
*A safety margin of 2.5 is currently applied for the whole studies.
All the studies are focused on the operation scheme: 6 GeV, 2 bunches/pulse, 200 Hz rep. rate
➜ positron flux of ~1.1⨯1013 e+/s (⨯2.5). Demonstrated at SLC (a world record for existing accelerators): ~6 ⨯1012 e+/s
Accepted e+ yield is a function of primary beam characteristics + target + capture system + DR acceptance
To estimate the accepted yield:
energy window cut: (1540 ± 58.5) MeV → (±3.8% @ 1.54 GeV)
time window cut: 40° RF (~16.7 mm/c @2 GHz)
Positron source basic scheme
or 5.4 nC accepted in the DR

## Slide 4: FCC-ee positron source: positron production
Conventional scheme: bremsstrahlung and pair conversion (mainly studied until now)
Hybrid scheme (crystal-based positron source) use the intense radiation emitted by high-energy (some GeV) electrons channeled along a crystal axis => channeling radiation.
Schemes under consideration now
Studies on the target-converter shape in progress (tapered target, rod target, granular target)
The final choice will be done based on the simulated performances
*According to SLC experience, W74Re26 material has a PEDD limit of 35 J/g (safe value to avoid target failure)
Target thickness | 5 X0 17.5 mm
Production rate | ~14 Ne+/Ne-
PEDD* | f(e- beam)
Deposited power | f(e- beam)

## Slide 5: Hybrid scheme: positron production optimization for FCC-ee (in progress)
Radiation enhancement in the tungsten (W) crystals aligned along <111> axes
< 100 MeV : photon yield increase ≈ 4.3
Full spectrum : photon yield increase ≈ 3.7
L. Bandiera et al., Eur. Phys. J. C (2022) 82:699
→ Comparable e+ production rate but lower thermal load
→ Capture simulations in progress
R. Chehab et al., in Proc. of the 1989 IEEE Particle Accelerator Conf., 1989, pp. 283–285
towards conceptual design

## Slide 6: Positron capture: matching device
FC: lower peak field and aperture, fixed target position, challenging power source working at 200 Hz, robust and reliable solution…
HTS solenoid: higher peak field and aperture, flexibility on the field profile and target position, DC operation, innovative solution in application for e+ capture…
Matching device => a fast phase space rotation to transform the small size and high divergence in big sizes and low divergence beam.
Flux Concentrator (FC)
Originally designed by BINP (P. Martyshkin). Starting collaboration with KEK and CERN.
High-Temperature Superconducting (HTS) solenoid designed by PSI (J. Kosse, B. Auchmann and M. Duda)

## Slide 7: Positron capture: capture linac
Baseline structure: large-aperture (Φ = 60 mm) TW L-band @ 2 GHz, 9π/10, 3-meter long, 20 MV/m. F3 structure designed by H. Pommerenke and A. Grudiev (CERN). 5 RF structures are used to accelerate the e+ beam up to ~200 MeV.
Baseline solenoid configuration: 0.5 T NC solenoid. Configuration designed by M. Schaer, R. Zennaro (PSI). For simplification, 0.5 T uniform NC field used (as the difference in final results was found to be small).
F3 structure
The capture linac is encapsulated inside a solenoid with the axial magnetic field of ~0.5 T

## Slide 8: FC-based positron capture system (I)
FCC-ee FC original design is made by BINP. Very simple model (not realistic in terms of ohmic loss and high-power requirement for the pulsed power supply). Needs more realistic simulations.
FC-based capture system successfully works at SuperKEKB → starting point for the FCC-ee capture system studies. FC is currently considered as a baseline for the ILC e--driven and CLIC positron sources.
Compared to SuperKEKB FC, high rep. rate (up to 300 Hz) and ideally higher max. field value/aperture are requested for the future collider projects.
Make use of the SuperKEKB experiences and join the effort on the FC design between FCC/ILC/CLIC collaborations to arrive to a more realistic model.
Prototype of the positron source for ILC

## Slide 9: FC-based positron capture system (II)
Accepted e+ yield @ DR | 2.7
Norm. emittance [mm*rad] | 11.9
Energy spread (RMS) [%] | 1.1
Bunch length (RMS) [mm] | 2.6
@ 1.54 GeV (DR entrance)
  Application of the SuperKEKB FC to the FCC-ee positron source
SuperKEKB Flux Concentrator
BTARGET ~1.1 T

## Slide 10: FC-based positron capture system (III)
Accepted e+ yield @ DR | 4.4
Norm. emittance [mm*rad] | 12.2
Energy spread (RMS) [%] | 1.2
Bunch length (RMS) [mm] | 2.9
BTARGET ~3.5 T
  In the FCC CDR, the baseline for the capture system is based on the BINP FC
Simulation results update (capture linac)
BINP Flux Concentrator

## Slide 11: HTS-based positron capture system
Optimized target position in HTS
solenoid
  We consider the same HTS solenoid design and cryostat aperture as for P3 e+ production experiment at PSI (72 mm)
High peak field (~15 T, ~12 T at target exit)
Large aperture (Ф = 30-40 mm)
Flexible target position (can be placed inside the bore)
DC operation
HTS solenoid integrated in the cryostat
PSI
18.2 T @15K@2kA reached for stack of 4 coils
BTARGET ~12 T
Target

## Slide 12: Current baseline: positron capture system –version 1
Capture system -version 1
Positron production: conventional scheme (e- beam size on target = 1 mm rms)
Matching device is based on the SC solenoid (5 HTS coils, 72 mm bore including shielding). Min beam aperture (w/o significant yield loss): 30- 32 mm (Maximum shielding thickness: ~21 mm)
Capture linac is based on the F3 RF structures
NC long solenoid B = 0.5 T (realistic conventional design based on short coils)
@ 1.54 GeV (DR entrance)
Accepted e+ yield @ DR | 6.5
Norm. emittance [mm*rad] | 13.7
Energy spread (RMS) [%] | 1.4
Bunch length (RMS) [mm] | 2.9

## Slide 13: Optimization studies toward better performance
Overall parameter scanning (target thickness, distances, etc. )
Matching device field profile
RF structure length
Distance between the target and the first RF structure
Overall optimization (GIOTTO, etc.)
…
  Target and capture system studies are in progress to provide the optimized positron bunch 6D phase space matched to the positron linac and DR
GIOTTO results:
∆ W/W (1) = 0.99 %,
∆ Z (1) = 2.4 mm
Beam size (1) = 8.7 mm
Acc. Yield = 7
n rms x,y = 9.6103 mmmrad
Capture system –version 0

## Slide 14
Dedicated talk by R. Mena Andrade (CERN)
  Currently, the radiation load and target design studies focused exclusively on the HTS solenoid-based system (capture system –version 1)
Radiation load studies and status of target design
FLUKA model of the FCC-ee positron source to assess
Heat load on the target/HTS solenoid/capture linac/solenoid
Total deposited power
Power density
Long term radiation effects
Dose
Displacement per atom (DPA)
→ Design feasibility and mechanical integration
→ Reliability of the positron source system

## Slide 15: Positron linac up to 1.54 GeV
Vacuum chamber dimensions
e+/e- distributions before e- absorber (chicane center)
e- absorber
ECS is used to increase the number of e+ within the DR energy acceptance (±3.8% ).
The solenoid focusing is used until ~735 MeV of e+ beam energy.
After the matching section at ~735 MeV, the e+ beam passes to a quadrupole focusing.
e+ and e- bunches are separated in the end of the capture system by a chicane at ~200 MeV (e+ losses limited to ~ 15 %)

## Slide 16: Summary of the simulation results
Drive beam parameters | Alternative FC-based capture system |  | Capture system –v1
Matching device | BINP FC | SuperKEKB FC | HTS solenoid
Matching device aperture | 2a=8-44mm | 2a=7-52mm | 2amin=30 mm (bore 72mm)
Matching device peak magnetic field (@Target) [T] | 7.5 (3.5) | 4.4 (1.1) | 15 (12)
e- beam bunch charge [nC] / e- beam power [kW] | 3.1 / 7.4 | 5 / 12 | 2.1 / 5
Target deposited power [kW] / PEDD [J/g] | 1.7 / 11.1 | 2.9 / 18.3 | 1.2 / 3.1
Positron yield @CS [Ne+/Ne-] | 4.9 | 3.3 | 8
Positron yield @DR [Ne+/Ne-] | 4.4 | 2.7 | 6.5
Normalized emittance (rms) [mm.rad] | 12.2 | 11.9 | 13.7
Energy spread (rms) [%] | 1.2 | 1.1 | 1.4
Bunch length (rms) [mm] | 2.9 | 2.6 | 2.9
e+ beam bunch charge [nC] | 13.5 | 13.5 | 13.5

## Slide 17: Conclusions and outlook
The studies on the FCC-ee positron source are well advanced: positron production, HTS technology feasibility for matching device, capture linac (RF structures and solenoid). So far, no showstoppers found that prevent a SC solenoid matching device. Studies ongoing.
FC-based capture system requires a realistic model capable to work at the FCC-ee operation parameters. Collaborative work is very essential.
Two capture system layouts (based on the FC and SC solenoid) will be eventually compared in detail in terms of the performance and cost for the mid-term project review.
Positron linac has a robust design with full tracking simulations from production target to damping ring using the realistic field maps.
Thermal and radiation load studies: FLUKA model is available for capture system –version 1. Still to be developed for the FC-based capture system.
Design and integration of the production target are under investigations and to be studied for both schemes.

## Slide 19: Positron source performances
What are the main challenges?
High intensity
Emittance
Polarization
Reliability and radiation environment
Demonstrated (a world record for existing accelerators): SLC e+ source ~6e12 e+/s

## Slide 20: Future collider project challenges
Linear Collider projects: high request for polarization, requested intensity should be produced in “one shot”.
Circular Collider projects: polarization is under discussion, requirements are relaxed due to stacking and top-up injection
Demonstrated (a world record for existing accelerators): SLC e+ source ~6e12 e+/s
~2.4
~0.1
100
1.88
0.04
2