## Slide 1: Reference implementation scenario & work with the host states J. Gutleber (CERN)

## Slide 2
Collaborative work of almost 120 people over several years

## Slide 3
A balance of stakes
« Avoid-Reduce-Compensate » approach to develop iteratively a well-balanced reference scenario
Territorial impact limitation leads to
Societal acceptance
Technical feasibility and cost control lead to
Acceptable project risks
Performance of particle collider leads to
scientific excellence

## Slide 4: Approach “Eviter-Reduire-Compenser”
Note: approach required by French environmental law. Similar concept anchored in swisss project authorisation process.

## Slide 5: Reminder of layouts studied
12-site layout:
Mirror geometry
grouping together
three experiment
sites (PL, PA, PB)
8-site layout:
Basic 45 degree sector module
repeated eight times

## Slide 6
More than 100 scenarios developed & analysed
Multi-criteria approach covering 37 aspects
Legal and administrative aspects – 5 criteria
Connectivity – 2 criteria
Availability of services – 2 criteria
Accessibility of infrastructures – 6 criteria
Land plot related aspects – 9 criteria
Environnement – 8 criteria
Accelerator configuration – 3 criteria
Cost of construction
Risks linked to the construction

## Slide 7
Identifier les exigences et les contraintes pour la mise en œuvre technique et territoriale nécessaire dans le cadre des études de placement.
ETAPE 1: PLANIFIER
ETAPE 2: DEVELOPPER
Adapter les ouvrages souterrains et les sites de surface aux exigences et contraintes identifiés. Enregistrer les incompatibilités techniques rencontrées.
ETAPE 3: CONTROLER
Analyser la pertinence de l'hypothèse de travail. Si le scénario semble inacceptable, l’ajuster (étape 4). Sinon, conserver pour les études plus détaillées.
Développer des mesures « Éviter-Réduire-Compenser » pour répondre aux points inacceptables identifiés dans le scénario (étape 3)
ETAPE 4: AJUSTER

## Slide 8
Geology & topography
Territorial constraints
Yellow: Limit of investigation in 2014
Red: Limit of investigation evolved in 2017
Crosses: Elevation unfavourable
RED: AVOID
ORANGE: ONLY IF NOT OTHERWISE FEASIBLE
YELLOW: REDUCE

## Slide 9: Exclusion zones
Failles et formations calcaires du Vuache
Plateau calcaire du Jura
Haute montagne (900 m)
Protection des eaux et zones naturelles sans accès aménagé
Réservoirs d’eau et nature protégées
Urbanisation dense et territoires émergents
Zone de protection stricte, du paysage et de la renaturalisation
Urbanisation dense
Haute altitude
Zones résidentielles et zones agricoles
Terrain difficile d’accès et reservoirs d’eau
Zones de protection des eaux, du paysage. Haute altitude
Urbanisation dense et nature
Densément peuplé
Urbanisation dense et territoires émergents
Forêt protégée
Lac trop profond

## Slide 10
CERN Prevessin,
SPS BA4
Challex au sud de la D884,
à l’est des eaux souterraines
Vulbens/Dingy-en-Vuache,
au nord de l’A40
Dingy-en-Vuache au sud de l’A40
Sectreur Minzier selon accessibilité
Nord & sud de l’A410 quelques parcelles isolées
Charvonnex, Groisy, Villy entre l’A41,
voie ferrée et route d’Annecy,
au sud de la A410
Au nord d’Ollières, quelques parcelles isolées
Pallanterie
Choulex/Presinge
Ferney-Voltaire/CERN LHC Pt8
Quelques parcelles au
sud de Cranves-Salves
Quelques parcelles au
sud de Bonne
Ouest de l’A40
Quelques parcelles à Contamine sur Arve
Quelques parcelles à Arenthon
Nord de Roche-s.-Foron et zone industrielle de Etaux
Ligne de 700 m proche de la voie ferré au sud de Roche-s.-Foron
CERN, Meyrin
Une parcelle de 3 ha à côté de la D2 dans le vallé de la Fillière
Nord-est de Choisy
Residual areas

## Slide 11: Reference scenario PA31 surface site locations
PF
PG
PH
PJ
PD
PL
PA
PB
1. PA – Ferney Voltaire (FR, 01) – experiment
2. PB – Choulex (CH) – technical
3. PD – Nangy (FR, 74) – experiment
4. PF – Etaux/La Roche-sur-Foron (FR, 74) - technical
5. PG – Charvonnex/Groisy (FR, 74) - experiment
6. PH – Cercier/Marlioz (FR, 74) – technical, main RF
7. PJ – Vulbens/Dingy en Vuache (FR, 74) – experiment
8. PL – Challex (FR, 01) – technical, booster RF

## Slide 12: Scenario PA31 parameters
Straight section @IP: 1 400 m
Straight technical section: 2032 m
Sum of arcs: 76 929.609 m
Total length: 90 658.828 m
FCC-hh RF length required is: 90 657.4 m
Therefore some further minor adjustment of the trace is currently taking place to produce an ee/hh integrated trace that meets both requirements and limits the necessary the tunnel widening on both sides of the IPs.
Inclination: 0.5% (about a line from PD to PJ with PA moving upwards and PG downwards)
Shaft depths:
PA: 201 m (2 shafts) PB: 201 m (1 shaft displaced ca. 150 m along LSS) PD: 181 m (2 shafts) PF: 400 m (1 shaft 300 m to 600 m inside the ring) PG: 226 m (2 shafts) PH: 235 m (1 shaft) PJ: 253 m (2 shafts) PL: 250 m (1 shaft displaced 1 000 m along LSS)

## Slide 13: Optimisation of scenario since CDR publication
Element | CDR | Feasibility study | Change | Effect
Number of surface sites sites | 12 | 8 | ▼ | BETTER
Synergies with CERN infrastructures | 1 | 1 (+ Prevessin) | - | NEUTRAL
Land surface needs | 108 ha | ~ 41 ha | ▼ | BETTER
Total circumference | 97.75 km | 90.66 km (-7.25 %) | ▼ | BETTER
Sum of arcs | 83.75 km | 76.93 km (- 8.1%) | ▼ | WORSE
IP straight lengths | 1400 m | 1400 m | - | NEUTRAL
Amount of excavated materials | 9 m3 | 8 m3 | ▼ | BETTER
Possible interaction points for hh/ee | 4/2 | 4/4 | ▲ | BETTER
Lengths of access roads | 3.5 km | 3.5 - 2.5 km | ▼ | BETTER
Number of shafts | 20 | 12 | ▼ | BETTER
Ecological surfaces affected | 23 ha | 8 ha | ▼ | BETTER
Access synergies | 4/12 (33 %) | 7/8 (87%) | ▲ | BETTER
Synergy potentials public infrastructures | 2/12 (16%) | 5/8 (62 %) | ▲ | BETTER
Synergy potentials private structures | 5/12 (41%) | 8/8 (100%) | ▲ | BETTER

## Slide 14: PA0-0.1 – the 12 site CDR scenario 2018

## Slide 15: PA31-3.0 – the 8 site reference scenario

## Slide 16: Implementation scenario documentation
With the definition of a “reference implementation scenario”, FCC entered a new phase
Engagement of national actors has started in late 2022
  Communes
  Notified bodies
  Host state government representatives
  Associations
This requires a managed and single source of information to provide national stakeholders with reliable, trustworthy and managed information relevant to them in their language.
The single reference documentation is FCCIS deliverable 3, currently titled “Synthèse des contraintes et opportunités d’implantation”.
Made available via the Zenodo Open Access platform.
Document and data sets are properly versioned and undergo a quality management process.
Geolocalised information is kept in an FCC Environmental Information System, which has been put in place between 2022 and 2023 (to be gradually opened).

## Slide 17
Deliverable on the development and feasibility of implementation scenarios developed in the frame of the EU co-funded H2020 project FCCIS by CERN, Cerema and Latitude Durable
One scenario (PA31-1.0) is standing out from all the others
First version of the documentation released for work with host states and as project-internal reference
Micro-optimisations with stakeholders
  1.0 – published as reference in February 2023
  2.x – various trials to improve the siting for CE
  3.0 – adjustment of circumference after RF review
  4.0 – result of the optimisation with communes and CE to be openly published in autumn
https://doi.org/10.5281/zenodo.7614421

## Slide 18: Reference information kept in the document
Scenario development methodology
Summary of project requirements, constraints (invariants)
Territorial description & kown constraints
  Topography, geology, water, urbanism, nature, demography, economy, structured networks
Project risks
Scenario evolution
Detailed placement scenario documentation
Environmental aspects
Infrastructure environmental effects
  e.g. noise, em fields, radiation, traffic, waste
Regulatory and legal aspects to be considered
Real estate aspects
  Needs, available plots, constraints
Water aspects
  Needs, available and protected resources, supply concepts, infrastructures to be built
Electricity aspects
  Needs, available infrastructures,supply concepts, infrastructures to be built
Transport aspects
  Needs, available infrastructures, infrastructures to be built
Civil structure overviews
  Needs on surface and equipment
  Underground structure concepts
Matex challenges and strategy
Synergy and development opportunities

## Slide 19: Reference data kept in the EIS
Physical environment
Natural environment
Strategic infrastructures
Human environment
Territorial sensibility
Environmental aspect analysis results
Urbanistic conditions and planning
Geophysical & geotechnical investigation results (to be done, 2024/2025)
Existing pollution
Climate information
Collider traces and their characteristics
Site location options
Technical infrastructure locations & characteristics
Needs of technical annexes (grid connection, water intakes, roads)
Surface site concepts
  Based on simple “blocks”
Road and train accesses
Construction data (TBM, matex, …)
Opportunity locations & capacities
  Water, agriculture, forests, waste heats, schools, public institutions, etc.

## Slide 20: Subsurface investigations
Geophysical and geotechnical investigations in selected zones to understand the stability of the soil and to build a more detailed geological 3D model.
Interactions with host state notified bodies for the authorisations and to optimise the locations to limit the impacts of the campaign.
Interactions with affected land plot owners to obtain the permits and to optimise the locations to limit the impacts of the campaign.

## Slide 21: Environmental aspects analysis
The analysis of environmental aspects in zones of surface site candidates is ongoing. The required environmental analysis for the authorisations of the subsurface investigations has started. Both activities take place over a time frame of 12 to 18 months. They include continuous and close interactions with local authorities and residents of the territory.

## Slide 22: Scheduled activities
Classic nature inventory establishment, endangered species localisation, recordings of environmental conditions, agricultural study, water, air, traffic, noise and light pollution analysis.
Acoustic techniques to gather reliable data on the sub-surface conditions without a need for drillings in areas where insufficient information about the geological conditions exist today.
Exploration drillings in areas where geological conditions need to be clarified to be able to make reliable cost and CE project schedule estimates.
Identification of opportunities and synergies that emerge from an FCC in the region together with territorial stakeholders. Optimise the surface site locaitons and layouts. Analyse the socio-economic impact potentials in greater detail.
2024
2023
2024
2023/24

## Slide 23: Territorial dialogue
Communication plan established
Tripartite working meetings to assure advancement in phase
Regular visits of territorial stakeholders at CERN
Information “kit” produced and used
Additional info materials (videos, sheets and leaflets) developed as the need arises, e.g.
info about seismic investigation and geotechnical investigations
Socio-economic impact data
Calendar of upcoming visits with descriptions of activities on sites and photos

## Slide 24
Web site:
fcc-faisabilite.eu

## Slide 25: Regular meetings with regional stakeholders
Government services
France:
Region Auvergne-Rhône-Alpes
Prefectures, sous-prefectures
DDT, DREAL
CGDD, CCPG and others coming
Switzerland:
Department of Foreign Affairs
Department of Economic Affairs, Education and Research
State of Geneva
Elected representatives of the people
France:
Conseil dêpartemental Haute-Savoie & Ain
All communes affected by the trace
Communautés d’agglomération
Switzerland:
All communes affected by the trace
A range of interest groups

## Slide 26: Regular meetings with regional stakeholders
Challex, Ain, France

## Slide 27: Reference scenario feedback
Feedback from all communes hosting surface sites in France and in Switzerland so far positive.
For surface sites so far no showstoppers.
Some communes enthusiastic about the potentials for co-development.
All communes in France and in Switzerland expressed the need for top-level government support for a project of national and international interest towards the government representatives in the working meetings.
Individual meetings
Collective meetings
Meeting planned

## Slide 28: Typical concerns of people that we meet
Concerns/interests typically expressed:
Land consumption (ZAN, SdA)
Management of the excavated materials including their transport
Water consumption
Electricity landlines
Need for creation of local jobs
Housing needs for construction workers and engineers due to already stressed housing situation in the region
Integration with landscape, typical rural architecture
Traffic increase in congested zones
Synergy potentials typically evoked:
Integration of surface sites in local education programmes from children to adult levels
Local employment and service supply opportunities
  as for instance also successfully implemented by SKA in South Africa
Visitor centers and tourism development
Integration into public transport concepts
Integration with public services (healthcare, security, emergency)
Supply of residual cooling water for agriculture and re-naturalisation
Supply of waste heat for heating, food processing and industrial processes

## Slide 29: Complementary studies
Carried out:
Mining the Future – technologies for innovative excavated materials re-use > Followup needed
Access to french highway system
Renewable energy source supply feasibility
Job creation
Regional impact on high-tech suppliers
Training value for students and post-docs
Tourism effects
Open ICT development impacts
Common good value
Ongoing or planned:
Access to the french national electricity grid
Local electricity connection
Excavated materials local re-use
Excavated materials deposit
Access to railroad system
Waste heat supply feasibility & socio-economy
Water intake
Supply of residual water

## Slide 30: Conclusions
The placement methodology and the evolution of scenarios has been documented.
An Environmental Information System (EIS) is being put in place to document all relevant aspects of the choice and further evolution in detail as required by the legal frameworks.
A reference scenario has been identified and a rationale for its selection has been documented.
The territory is continuously evolving, therefore neither completeness nor correctness of the supplied information can be assured for a long period of time. No obvious alternative scenario potentials have been identified.
Land plot reservation for study purposes started.
Analysis of environmental aspects at the surface site locations has started.
Scenario PA31 has been verified with communes affected by surface site and so far no showstoppers have been identified
Development on synergy potentials with communes has started.
The permitting and authorisation process for the geophysical and geotechnical investigations scheduled for 2024 is ongoing.
Dedicated support and contributions from government services in both countries required to advance on the validation of the scenario and the territorial optimisation for local excavated materials re-use.