## Slide 1: FCC ACCELERATOR STATUS and R&D Tor Raubenheimer FCC IS Workshop December 5-9, 2022
SPACE FOR ADDITIONAL LOGOS

## Slide 2: Introduction

## Slide 3: FCC-ee Luminosity
Luminosity vs. electricity consumption
Highest lumi per AC site power of all proposals
Electricity cost ~200 CHF per Higgs boson
FCC-ee efficient L from Z to 𝑡𝑡 ̅
  Thanks to twin-aperture magnets, SRF, efficient RF power, top-off injection
Accumulate >2.5 ab-1 with ~0.5x106 H produced per IP
Accumulate >75 ab-1 with ~2x1012 Z produced per IP
Run plan naturally starts at Z but is under discussion

## Slide 4: Challenges and Drivers
High beam energy  large circumference to reduce synchrotron radiation and strong luminosity dependance on energy
  Large circumference  challenging tuning and tolerances and long runs for facilities
  Tunnel radiation  may limit in-tunnel electronics
High luminosity  strong beam-beam with beamstrahlung and reduced lifetimes
  High beam current  large RF power with collective instabilities and collimation
  Requires top-up injection and large dynamic aperture

## Slide 5: Outline
Overall requirements and status
Parameters
Main e+/e- rings beam optics
Collective effects, Dynamic aperture, Injection, Collimation, …
SRF and Energy efficiency
Full-energy booster and e+/e- injector
R&D Issues

## Slide 6: Accelerator Design Status
New ~90 km circumference placement with 8 access points
Layout with 4 IP’s that is consistent with upgrade to FCC-hh
Optimizing allocation of straight sections
New FCC-ee optics to optimize beam-beam
400 MHz and 800 MHz RF systems
Starting tunnel integration studies for RF and Arc sections
Full energy booster that will fit in FCC tunnel for top-up injection
e+ / e- injector to fill booster 24 / 7

## Slide 7: Basic Design Choices
Double ring e+e- collider
Common footprint with FCC-hh, except around IPs
Asymmetric IR layout and optics to limit synchrotron radiation towards the detector
Perfect 4-fold superperiodicity allowing 2 or 4 IPs; large horizontal crossing angle 30 mrad, crab-waist collision optics
Synchrotron radiation power 50 MW/beam at all beam energies
Top-up injection scheme for high luminosity Requires booster synchrotron in collider tunnel
Or MR RF?
Or Booster RF?

## Slide 8: Accelerator Placement Optimization
J. Gutleber, V. Mertens

## Slide 9: Placement Impact
New PA31 layout proposed in 2021
PA31-1.0 had a 91.2 km circumference
Needed to modify to have matched harmonic number for injector chain  91.1 km (Dec. 2021)
Further circumference reduction needed to support surface sites leading to 90.8 km optics (Summer 2022)
Settling on 90.7 km circumference with a harmonic number of 121,200 at 400.79 MHz which supports surface sites as well FCC-hh injector chain

## Slide 10: FCC-ee layout consistent with FCC-hh
FCC-ee
FCC-hh
Or MR RF?
Or Booster RF?

## Slide 11
FCC-ee Parameters
K. Oide, Nov. 2022

## Slide 12: FCC-ee Arc FODO optics
Configuration for arc optics with long ~100 m cells at Z & W and short ~50 m cells at Zh and t-tbar
  Reduces εx at high E and increases αc at low E
K. Oide

## Slide 13: FCC-ee IR optics
CDR optics, ttbar 182.5 GeV
beam
Novel ‘virtual’ crab waist combining local vertical chromaticity correction
  Crab waist was demon- strated at DAFNE
  Crab waist is also being used at SuperKEKB
Optimized optics configurations for each of the 4 working points
K. Oide

## Slide 14: FCC-ee IR geometry
FCC-ee and FCC-hh IP’s moved to same location to reduce IR tunnel width
Asymmetric IR layout is chosen to minimize the incoming synchrotron radiation
  Photon Ecrit < 100 keV from magnets within ~500 m of IP
  Collimators and masks further protect detectors
  Optimization is ongoing as part of MDI effort
A. Ciarma

## Slide 15: FCC-ee Tuning and Correction
Extensive studies on emittance tuning and dynamic aperture
  Emittance tuning looks good given a ‘reasonable’ set of errors
  Working to develop beam-based alignment models to combine with mechanical alignment specifications
  Sets requirements on diagnostics but eases installation and stability requirements
T. Charles

## Slide 16: FCC-ee Dynamic Aperture
Large dynamic aperture is needed for top-up injection and lifetime due to high beamstrahlung energy tails
  Dynamic aperture optimized with ~150 families of sextupoles
  Aperture is good without errors but still need to improve error correction

## Slide 17: Alternate Ring Optics
Nominal arc cells are 90-degree FODO cells
  Consider cell concepts from LC damping rings or light sources that may have better chromatic behavior  better DA
P. Raimondi

## Slide 18: FCC-ee Collective effects
Single bunch instabilities calculated with impedance, beam-beam, and ring optics but there is complicated interplay
  Building detailed impedance model: vacuum chamber, RF, bellows, BPMs, collimators working with Super KEKB, EIC, ….
  Longitudinal wake and beam-beam constrains tunes
  Beam-beam stabilizes the transverse mode-coupling instability

## Slide 19: FCC-ee Long-range Collective effects
Multibunch instabilities constrain bunch spacing
  Requires low SEY and ng on vacuum chamber to avoid significant e-cloud
  Damped RF cavities and electron cloud limits Δt ≥ 15 ns – ongoing studies
Large ring circumference limits feedback gain
  Developing integrated simulations for collective effects with feedback
Fatih Yaman, STFC Luca Sabato, EPFL
FCC IS and CHART

## Slide 20: FCC-ee Accelerator Layout
The arc cells are repeated 2000 times around the ring
  Critical to understand and optimize the layout for cost, installation, alignment, operation, and maintenance
  Includes placement of the main rings and the Booster
The RF regions are also tightly constrained
  Optimize cryomodule lengths and waveguides
Preliminary single cantilever dipole supports
Common girder for main collider quadrupoles & sextupoles
HL-LHC jacks
Common support for booster’s quadrupoles & sextupoles
HL-LHC 2t Universal Adjustment Platform (UAP)
C. Tetrault
F. Carra et al

## Slide 21: FCC-ee SRF Systems
Baseline uses established SRF technologies in use at CERN
800 MHz for booster and 400 MHz at Z, W, Zh while adding 800 MHz at t-tbar
  Z with very high current  120 MV of low frequency (400 MHz) single-cell cavities with RF dedicated to e+ or e-
  Upgrade to 2-cell cavities at W with 1 GV in each ring
  Increase to 2.1 GV shared between e+ and e- at Zh
  Add 9 GV of 5-cell 800 MHz to e+ and e- rings along with a total of 11 GV 800 MHz for the booster
Consider more aggressive options as alternates in future

## Slide 22: FCC-ee SRF Systems
F. Peauger and O. Brunner

## Slide 23: FCC-ee SRF R&D
400 MHz Cu/Nb cavities with Q0 of >3e9 at 12 MV/m and 4.5K
  Require strong damping of single-cell cavities to reduce HOMs at Amp-level current
  Coupler design for ~MW RF power
  Compact cryomodule design for W, Zh, and t-tbar
800 MHz Nb cavities with Q0 of >3e10 at 25 MV/m and 2K
  Require strong damping of HOMs in 5-cell cavities for 100 mA
  Recently increased Q0 spec from 2e10 to >3e10
  Coupler design for 250 kW RF power
  Compact cryomodule design for t-tbar

## Slide 24: FCC-ee 400 and 800 MHz SRF Systems
R&D is on-going around the world on high Q0 cavities
400 MHz is based on thin-film coatings of Cu cavities while 800 MHz are bulk Nb
LHC is pushing the 400 MHz development of HiPIMS sputtering
Jlab tested a bare 800 MHz cavity

## Slide 25: High Q0 SRF Systems
LCLS-II developed new N2 doping approach  is operating cryomodules at 1.3 GHz with Q0 = 2.7x1010 at 16 MV/m
PIP-II is developing high Q cavities at 650 MHz
LCLS-II-HE has built two cryomodules with Q0 = 2.7x1010 and >21 MV/m
LCLS-II
PIP-II

## Slide 26: Developing High Q Cavities
Development of cavities is guided by theory but still very much an exploration
LCLS-II developed 2/6 N2 recipe; LCLS-II-HE 2/0 and 3/60 recipes; ILC low-T bake; PIP-II mid-T bake

## Slide 27
Sustainability compared with other Higgs factories
Patrick Janot
CLIC | ILC | C3 | FCC-ee | CEPC
0.8 | 0.9 | 0.9 | 1.1 | 2.0
TWh / year for the “Higgs factory” centre-of-mass energy
    √s = 240 GeV for CEPC/FCC-ee, 250 GeV for ILC/C3, 380 GeV for CLIC
CLIC | ILC | C3 | CEPC | FCC-ee
30 | 20 | 21 | 10 | 3.3
Energy consumption in MWh / Higgs
      becomes 2 MWh / Higgs for FCC-ee with 4 IPs
CLIC@CERN | ILC@KEK | C3@FNAL | CEPC@China | FCC-ee@CERN
2.1 | 7.8 | 8.5 | 6.1 | 0.24
0.14 ton CO2 / Higgs for FCC-ee with 4 IPs
Present carbon footprint for electrical energy in tons CO2 / Higgs
https://indico.cern.ch/event/1178975/
P. Janot and A. Blondel, Who is the greenest? - The environmental footprint of future Higgs boson studies, arXiv 2208.10466 (2022); https://arxiv.org/abs/2208.10466

## Slide 28: FCC-ee Power Consumption
Roughly 300 MW operating at Higgs
  Complete power accounting
High efficiency RF sources (150 MW) 80  90%
High Q RF Cavities (20 MW)
Magnet systems (40 MW)
  Dipole quite efficient
  Quadrupole and sextupole magnets simplified and power reduced with smaller bore or HTS
  Cable losses may be reduced with in-tunnel PS
Efficient cooling and ventilation (40 MW)

## Slide 29: HTS Arc Quadrupole / Sextupole / Dipole
Develop HTS magnets for arc quadrupole / sextupoles
  Reduce power consumption with nested quadrupole and sextupole
  Cryo-coolers for compact installation
  Add weak dipoles to reduce SR power by 10% at Z and 20% at Higgs
HTS4 R&D program supported by CHART led by M. Koratzinos
  Produce a 1-m protype section leveraging HTS development as part of CHART
  Understand radiation environment and magnet and cooler radiation damage
CERN Courier, Nov. 2022

## Slide 30: Full Energy Booster
Booster ramps from 20 GeV to Main Ring energy
  Accumulate electrons or positrons for injection to Main Ring
  Accumulation times of ~25 seconds at Z
  Damp beams and transients to Main Ring equilibrium values
  Alternate injection of e- and e+ to maintain +/- 3 to 5% charge
Layouts are being developed with IP Bypasses, Inj/Ext, and RF
  Arc cell structure mirrors Main Ring
  Laminated magnet concepts are being considered
  Developing integrated model of arc structure including both Main Rings and Booster
  Collective effects, dynamic aperture and tolerances are being studied

## Slide 31: FCC-ee Pre-Injector
Design concept being developed with PSI
  High brightness e- source and efficient e+ source with damping ring to generate pairs of 6 GeV bunches at 200 Hz (for Z)
  Acceleration to Booster at ~20 GeV in SPS (CDR) or high energy linac (FCC IS)
P. Craievich, A. Grudiev

## Slide 32: FCC-ee Pre-Injector R&D

## Slide 33: FCC-ee MDI and IR design
Complicated integration with SC quadrupoles, solenoids, IR chamber, LumiCal, shielding, and diagnostics
M. Boscolo M. Koratzinos, B. Parker, et al
Quadrupoles thanks to M. Koratzinos

## Slide 34: FCC-ee IR Magnet R&D
Many similarities with EIC IR
Direct Wind Tapered Double Helical Coil
H. Witte
Double Helical CCT
Grooved Double Helical Coil Support
M. Koratzinos
FCC R&D CCT Magnet
Baseline FCC-ee Coils and Beam Pipe

## Slide 35: FCC-ee IR Mock-up
IP chamber: critical for performance, MDI
Step 1: Central IP vacuum chamber (test cooling and vacuum systems), AlBeMet162 & steel transition (shape of transition, EBW process), Bellows (vacuum and thermal tests), Welding (EBW for elliptical geometry), C-fibre support structure
Step 2: Trapezoidal vacuum chamber with remote vacuum connection, first quadrupole QC1, cryostat, beam pipe and quadrupole and cryostat support, vibration & alignment sensors
support tube with carbon fiber cylinder

## Slide 36: FCC-ee Alternative technologies
Developing technologies with significant potential impact in parallel to baseline, e.g.
  HTS arc quadrupole/sextupole magnets
  High efficiency RF sources
  Radiation hard electronics
  HE linac as a pre-booster
  Positron target using crystal channeling
  Advanced cooling tower design
  Advanced cryogenic design
  …
M. Koratzinos
Combined function HTS magnet

## Slide 37: Synergistic Programs
Collaborators around the world
Many synergies with other large accelerator projects
  Super KEKB (KEK)
  CEPC (China)
  Electron Ion Collider (BNL / Jlab)
  PIP-II (Fermilab)
  Synchrotron radiation facilities (world-wide)
30
Companies
34
Countries
147
Institutes
EC
H2020

## Slide 38: FCC accelerator summary and timeline
Finalizing layouts with correct circumference
FCC-ee baseline parameters are established
  Main ring substems, full-energy booster, and injector all being defined
Technical systems making good progress
  Vacuum, magnets, SRF, cryogenics, diagnostics, integration, …
  Already most efficient Higgs solution but working to improve overall h
  Extensive world-wide R&D program
Luminosity requires all systems work together in large facility
  Still many challenges in developing robust integrated design
Will have baseline established in 2023 and optimize further to complete feasibility study at end of 2025

## Slide 39: Thank you for your attention.
39
SPACE FOR ADDITIONAL LOGOS
Name of the speaker/author
Date / Name of the event