## Slide 1: Upgraded portable muography detector for faster infrastructure measurement
Tadahiro Kin*, Wataru Sekiguchi, and Hamid Basiri
Muographers’23
June. 18-23, 2023
Centro Congressi Federico II
IGSES, Kyushu University, Japan
applicable to multi-purposes muography test

## Slide 2: Outline
Introduction
Features of upgraded portable muography detector
Experiments for detector performance test
Summary & prospects
Results and discussion

## Slide 3: Outline
Features of upgraded portable muography detector
Experiments for detector performance test
Summary & prospects
Results and discussion
Introduction

## Slide 4: Introduction
Targets of Kyushu University’s Muography
Underground Cavity
10 cm to 50 m
Tunnel
Cavity
Corrosion
Bridge
1 cm to 20 cm
Permeation
Dam
1 m to 100 m
Plant 1 cm to 5 m
Fire Bricks Loss
Target with required dynamic range to reveal interested structures
Magnetic Field
10 cm to 50 m (depends on a target)
Recently, we also added
“magnetic field muography”
→ Please join the last date presentation by Hamid BASIRI (my PhD course student).

## Slide 5: Introduction
Prototype portable muography detector
K. Chaiwongkhot et al., IEEE Trans. Nucl. Sci. 65, 2316 (2018).
134 mm
134 mm
muon
PSF
32 MPPCs
muon position sensitive detector (mu-PSD)
Temperature Control System (DT ~0.3 oC)
DAQ: EASIROC Module (64ch MPPC readout module)
Square (2 x 2 mm2) cross section
  Sensitive Area 14 x 14 cm2
  Angular Resolution ~8 mrad
Muon Identificati PS ex. trigger
Cost: ~$18,000

## Slide 6: Introduction
Results by the prototype detector
K. Chaiwongkhot et al., IEEE Trans. Nucl. Sci. 65, 2316 (2018).
Open
Ceiling
Space
Room Area
Room Area
Library
Basement
detector position
C-Cube, Kyushu Univ.
Prototype Muography Detector
Location:
・ C-Cube, Chikusi campus, Kyushu Univ., Japan
・ 3.5 meters below the ground
Measurement Time：
・Foreground: 390 hours (16 days)
・ Open sky: 235 hours (10 days) beside the building
Detector Temperature：
・ 17.0±0.3 oC
Test measurement

## Slide 7: Introduction
Results by the prototype detector
Open-sky Measurement
0~40o Open Air
40o
Experimental Room
East
West
C-Cube, Kyushu Univ.
Detector was placed at 3.5m below Ground
Foreground Measurement
Muon Intensity
Low
High
Absorption Rate Map
10o
20o
30o
40o
Zenith Angle
EAST
SOUTH
NORTH
WEST
Attenuation Rate
Low
High

## Slide 8: Introduction
Results by the prototype detector
Simulation (concrete only)
Experimental result
The building includes a lot of experiment rooms which equip large instruments.
Difference is mainly caused by the lack of them in the simulation.
Concrete thickness [cm]

## Slide 9: Introduction
MPPCs are consumables, but replacement is hard work.
Detection are of a single MPPC is 9 mm2, but connected four fibers whose sum of cross section area is 4 mm2 4 = 16 mm2.
Issues on the prototype detector to be updated
For the future applications, such as dams and underground structure measurements, require shorter measurement time.

## Slide 10: Outline
Introduction
Features of upgraded portable muography detector
Experiments for detector performance test
Summary & prospects
Results and discussion

## Slide 11: Features of upgraded detector
Muon position sensitive detector
Prototype mu-PSD
134 mm
134 mm
Upgraded mu-PSD
296 mm
296 mm
9 PSFs (2 x 2 mm2) for each MPPC
Laser processing acrylic light guide
MPPC
4.9 times larger sensitive area
NC fabricated
“light-guide” support

## Slide 12: Features of upgraded detector
Optimization of acrylic light guide shape
Candidates
Three position measurement of 90Sr beta-ray source
→ light detection efficiency and uniformity check
short linear edge
parabola edge
long linear edge
light guide
source positions

## Slide 13: Features of upgraded detector
Optimization of acrylic light guide shape
①
②
③
Average pulse height of MIP muons |  | 波高値 [-] | 
 | A | B | C
① | 1265.2 ± 2.0 | 1435.7 ± 1.6 | 1294.2 ± 2.2
② | 1288.3 ± 1.7 | 1388.2 ± 1.6 | 1295.3 ± 1.8
③ | 1517.1 ± 2.1 | 1605.1 ± 2.1 | 1497 ± 2.1

## Slide 14: Features of upgraded detector
Data acquisition system
EASIROC module
for 64-ch MPPC readout
34 pins half-pitch connectors
16-ch MPPCs and 1-ch thermometer
MPPCs
Shielded twisted pair cable
Flat cable conversion board
Flat cable
Flat cable
Just insert

## Slide 15: Features of upgraded detector
Larger
muon Position
Sensitive
Detector
New cabling systes
for robust MPPC
Connection
Upgraded in 2022 !!
Whole size (portable):
  W 800 x L 800 x H 500 mm3
Larger sensitive area:
  296 x 296 mm2 (4.9 times)
Easy maintenance:
  by robustDAQ system cabling

## Slide 16: Outline
Introduction
Features of upgraded portable muography detector
Experiments for detector performance test
Summary & prospects
Results and discussion

## Slide 17: Detector performance test
8 mrad sized lead blocks placed on the roof
Experiment 1
Lead blocks placed at 0 degrees of zenith angle
Measurement time: 140 hours
Experiment 2
Lead blocks placed at 16.3 degrees of zenith angle and azimuthal 180 degrees of azimuthal angle.
(3-pixel shift from Experiment 1)
Measurement time: 220 hours
Experiment conditions
azimuthal
angle
Upgraded detector
Experient 1
Experient 2
Lead
Photo of
lead blocks

## Slide 18: Outline
Introduction
Features of upgraded portable muography detector
Experiments for detector performance test
Summary & prospects
Results and discussion

## Slide 19: Performance test results
Chart: 
Elapsed time [hour]
Counting rate [cph]
(red line)
Atmospheric pressure [hPa]
(blue line)
Detector stability –before air pressure correction -
Chart: 

## Slide 20: Performance test results
Elapsed time [hour]
Counting rate [cph]
(red line)
Detector stability –after air pressure correction -
Chart: 
Negative correlation
-18.7 cph/hPa
→ Sufficiently stable

## Slide 21: Performance test results
Elapsed time [hour]
Counting rate [cph]
(red line)
Detector stability –after air pressure correction -
Chart: 
Negative correlation
-18.7 cph/hPa
We expected 20,000 cph by the larger sensitive area. But photon lost between PSF and light guide and attenuation by longer PSF decreased 20% of photons.
→ But 4 times faster compared with prototype.

## Slide 22: Performance test results
実験結果
Experiment 1
←zenith angle
Lead block position
absorption ratio [%]
Experiment 2
Lead block position
Absorption by lead block 4.4 ± 0.8%
simulation 5.3 ± 0.5%
absorption ratio [%]
Lead blocks were observed within single pixel, ~8 mrad
with expected absorption ratio, i.e. density.
Absorption by lead block 5.8 ± 0.8%
simulation 6.6 ± 0.4%

## Slide 23: Outline
Introduction
Features of upgraded portable muography detector
Experiments for detector performance test
Summary & prospects
Results and discussion

## Slide 24: Summary and prospects
4 times faster stable counting rate by larger sensitive area
8 mrad angular resolution
5% absorption can be detected with less than 20% of statistical uncertainty
Summary: Our 2nd detector was fabricated.
Prospects
Test survey of underground during drilling tunnel.
Scattering muography by combination with prototype.
Applied for test measurement of Magic-µ (magnetic field imaging by cosmic-ray muons).