## Slide 1: The cybersecurity in ALICE - as seen from user’s perspective
Peter Chochula
CERN/ALICE

## Slide 2: The ALICE experiment at CERN LHC
Experiment
Size: 16 x 26 metres (some detectors placed >100m from the interaction point)
Mass: 10,000,000 kg
Detectors: 20
Magnets: 2
Basic task – study of heavy ion collisions at LHC
The design of ALICE allows for p-p studies as well
The ALICE Collaboration:
Members: 1300
Institutes: 116
Countries: 33

## Slide 3
ALICE - a very visible object, designed to detect the invisible...

## Slide 12: Operational since the very beginning
Historically first particles in LHC were detected by ALICE pixel detector
Injector tests, June 15 2008

## Slide 13: First proton collisions
Luminosity monitor (V0)

## Slide 14: First ion collisions

## Slide 15: What do we do?
CERN is trying to answer many questions
Where does the mass come from?
  How does the matter behave at temperatures higher than in the middle of the Sun?
    Why is the mass of protons and neutrons 100times higher than the mass of contained quarks?
        Can we release quarks from protons and neutrons?
          Why is the mass of the Universe much higher that we can explain?
            Where did all the antimatter go?
              ......????????????????????????????????????????????????????????????????
1012 C
1015 C
1017 C
The particle collisions allow us to recreate conditions which existed very short (ms) after the Big Bang
3 minúty
0,01 ms
10-12 s
10-20 s
10-43 s
10-29 s
1012 C
1015 C
1017 C

## Slide 16
ALICE is primary interested in ion collisions
  Focus on last weeks of LHC operation in 2011 (Pb-Pb collisions)
During the year ALICE is being improved
In parallel, ALICE participates in p-p programme
So far, in 2011 ALICE delivered:
  1000 hours of stable physics data taking
  2.0 109 events collected
  2.1 PB of data
  5300 hours of stable cosmics datataking, calibration and technical runs
  1.7 1010 events
  3.5 PB of data
    IONS STILL TO COME IN 2011!

## Slide 17
Where is the link to cyber security?
The same people who built and exploit ALICE are also in charge of its operation
  In this talk we focus only at part of the story, the Detector Control System (DCS)

## Slide 18
The ALICE Detector Control System (DCS)

## Slide 19
Detector Controls System
DETECTORS & detector-like
systems
External Services and Systems
Electricity
Ventilation
Cooling
Gas
Magnets
Safety
Access Control
LHC
Configuration
Database
Archival
Database
Devices
Devices
Devices
Devices
SCADA
1000 ins/s
Up to 6GB
Infrastructure
B-field
Space Frame
Beam Pipe
Radiation
Environment
Alice Systems
DAQ
TRIGGER
HLT
Conditions
Database
ECS
OFFLINE
SPD
PHS
FMD
T00
SDD
SSD
TPC
TRD
TOF
HMP
V00
PMD
MTR
MCH
ZDC
ACO
AD0
TRI
LHC
PIT

## Slide 20
GAS
COOLING
HV
LV
FEE
ALICE on-detector electronics
Detector devices
DCS data storage
(ORACLE, fileservers)
Data Consumers
Offline
(GRID)
Operator UIs
DCS data processing farm
LHC
Magnets
Safety
FEE
External sub-systems
300 000 values/s
read by software
30 000 values/s
Injected into PVSS
1000 values/s
Written to ORACLE after smoothing in PVSS
>200 values/s
Sent to consumers
Dataflow in ALICE DCS
  6GB of data is needed to fully configure ALICE for operation
  Several stages of filtering applied to acquired data

## Slide 21: Building blocks of ALICE DCS
HVPS
LVPS
FEE
…
18 detectors with different requirements
  Effort to device standardization
    Still large diversity mainly in FEE part
      Large number of busses (CANbus, JTAG, Profibus, RS232, Ethernet, custom links…)
1200 network-attached devices
270 crates (VME and power supplies)
4 000 controlled voltage channels

## Slide 22
HVPS
LVPS
FEE
…
DEVICE ACCESS and ABSTRACTION
Device DRIVER
Device DRIVER
Device DRIVER
Device DRIVER
OPC SERVER
OPC SERVER
FED SERVER
FED SERVER
180 000 OPC items
100 000 Front-End (FED) services
1 000 000 parameters supervised by the DCS
Monitored at typical rate of 1Hz
Hardware diversity is managed through standard interfaces
  OPC servers for commercial devices
  FED servers for custom hardware
    Provides hardware abstraction, uses CERN DIM (TCP/IP based) protocol for communication

## Slide 23
CENTRAL SYSTEMS
DETECTOR SYSTEM
DETECTOR SYSTEM
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
HVPS
LVPS
FEE
…
DEVICE ACCESS and ABSTRACTION
Device DRIVER
Device DRIVER
Device DRIVER
Device DRIVER
OPC SERVER
OPC SERVER
FED SERVER
FED SERVER
Core of the DCS is based on commercial SCADA system PVSSII
110 detector computers
60 backend servers
DCS Oracle RAC (able to process up to 150 000 inserts/s)
BACKEND SYSTEMS
DNS
FS
MON
RAC
ACC

## Slide 24: PVSSII Architecture
      PVSSII system is composed of specialized program modules (managers)
      Managers communicate via TCP/IP
      ALICE DCS is built from 100 PVSS systems composed of 900 managers
      PVSSII is extended by JCOP and ALICE frameworks on top of which User applications are built
CTL
API
DM
EM
DRV
DRV
DRV
UI
UI
UI
User Application
ALICE Framework
JCOP Framework
PVSSII

## Slide 25
User Interface
Manager
Data
Manager
Driver
Driver
Driver
User Interface
Manager
User Interface
Manager
Event
Manager
API
Manager
Control
Manager
In a scattered system, the managers can run on dedicated machines
In a simple system all managers run on the same machine

## Slide 26
Distribution
Manager
Distribution
Manager
Distribution
Manager
User Interface
Manager
Data
Manager
Driver
Driver
Driver
User Interface
Manager
User Interface
Manager
Event
Manager
API
Manager
Control
Manager
User Interface
Manager
Data
Manager
Driver
Driver
Driver
User Interface
Manager
User Interface
Manager
Event
Manager
API
Manager
Control
Manager
User Interface
Manager
Data
Manager
Driver
Driver
Driver
User Interface
Manager
User Interface
Manager
Event
Manager
API
Manager
Control
Manager
In a distributed system several PVSSII systems (simple or scatered) are interconnected

## Slide 27
CENTRAL SYSTEMS
DETECTOR SYSTEM
DETECTOR SYSTEM
PVSS
PVSS
PVSS
HVPS
LVPS
FEE
…
DEVICE ACCESS and ABSTRACTION
Device DRIVER
Device DRIVER
Device DRIVER
Device DRIVER
OPC SERVER
OPC SERVER
FED SERVER
FED SERVER
Each detector DCS is built as a distributed PVSSII system
  Mesh, no hierarchical topology
  Detector specific
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS

## Slide 28
CENTRAL SYSTEMS
DETECTOR SYSTEM
DETECTOR SYSTEM
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
HVPS
LVPS
FEE
…
DEVICE ACCESS and ABSTRACTION
Device DRIVER
Device DRIVER
Device DRIVER
Device DRIVER
OPC SERVER
OPC SERVER
FED SERVER
FED SERVER
ALICE DCS is built as a distributed system of detector systems
Central servers connect to ALL detector systems
    global data exchange
    synchronization
    Monitoring…

## Slide 29
PVSS
CENTRAL SYSTEMS
DETECTOR SYSTEM
DETECTOR SYSTEM
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
HVPS
LVPS
FEE
…
DEVICE ACCESS and ABSTRACTION
Device DRIVER
Device DRIVER
Device DRIVER
Device DRIVER
OPC SERVER
OPC SERVER
FED SERVER
FED SERVER
OPERATIONS LAYER
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
PVSSII distributed system is not a natural system representation for the operator
ALICE DCS Is modeled as a FSM using CERN SMI++ tools
  Hide experiment complexity
  Focus on operational aspect

## Slide 30
PVSS
CENTRAL SYSTEMS
DETECTOR SYSTEM
DETECTOR SYSTEM
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
PVSS
HVPS
LVPS
FEE
…
DEVICE ACCESS and ABSTRACTION
Device DRIVER
Device DRIVER
Device DRIVER
Device DRIVER
OPC SERVER
OPC SERVER
FED SERVER
FED SERVER
OPERATIONS LAYER
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
CH
UI LAYER

## Slide 31: DCS Computing model
Two categories of DCS computers:
  Worker nodes – executing the controls tasks and running detector specific software
  Operator node – used by operators to interact with the system
FED
PVSS
PVSS
PVSS
PVSS
ON
WN

## Slide 32
ALICE network architecture

## Slide 33: Remote access to the DCS network
No direct user access to the ALICE network
Remote access to ALICE network Is possible via the application gateways
  User makes RDP connection to the gateway
  From the gateway further connection is granted to the network
ALICE Network
General Purpose Network
Application gateway

## Slide 34
ALICE host exposed to NetA:
Can see all NetA and ALICE hosts
Can be seen by all NetA hosts
ALICE Network
NetA
NetB host trusted by ALICE:
Can see all ALICE and NetB hosts
Can be seen by all ALICE hosts
NetB
TRUSTED
EXPOSED

## Slide 35: Are we there?
The simple security cookbook recipe seems to be:
  Use the described network isolation
  Implement secure remote access
  Add firewalls and antivirus
  Restrict the number of remote users to absolute minimum
  Control the installed software and keep the systems up to date
Are we there?
  No, this is the point, where the story starts to be interesting

## Slide 36: Remote access
Why would we need to access systems remotely?
ALICE is still under construction, but experts are based in the collaborating institutes
  Detector groups need DCS to develop the detectors directly in situ
    There are no test benches with realistic systems in the institutes, the scale matters
ALICE takes physics and calibration data
  On-call service and maintenance for detector systems are provided remotely

## Slide 37: The user challenge
Natural expectation would be that there are few users requiring access to the controls system
The today’s reality is more than 400 authorized accounts...
  Rotation of experts in the institutes is very frequent
    Many tasks are carried out by students (graduate or PhD)
  Commitments to collaboration expect shift coverage
    Shifters come to CERN to cover 1-2 weeks and then are replaced by colleagues

## Slide 38
How do we manage the users?

## Slide 39: Authorization and authentication
User authentication is based on CERN domain credentials
  No local DCS accounts
  All users must have CERN account (no external accounts allowed)
Authorization is managed via groups
  Operators have rights to logon to operator nodes and use PVSS
  Experts have access to all computers belonging to their detectors
  Super experts have access everywhere
Fine granularity of user privileges can be managed by detectors at the PVSS level
  Only certain people are for example allowed to manipulate very high voltage system etc.

## Slide 40: Operator access to computers
CR3
ACR
ON
WN
ON
WN
Detector 1
Detector 2
Central Systems
ON
Detector 1
operator
Detector 2
operator
Central
operator

## Slide 41
Could there be an issue?

## Slide 42: Authentication trap
During the operation, the detector operator uses many windows, displaying several parts of the controlled system
  Sometimes many ssh sessions to electronic cards are opened and devices are operated interactively
At shift switchover old operator is supposed to logoff and new operator to logon
  In certain cases the re-opening of all screens and navigating to components to be controlled can take 10-20 minutes, during this time the systems would run unattended
    During beam injections, detector tests, etc. the running procedures may not be interrupted
Shall we use shared accounts instead?
  Can we keep the credentials protected?

## Slide 43: Information leaks
Sensitive information, including credentials, can leak
  Due to lack of protection
  Due to negligence/ignorance

## Slide 44: ….in scripts
echo " ----- make the network connections -----"
rem --- net use z: \\alidcsfs002\DCS_Common XXXXXX /USER:CERN\dcsoper
rem --- net use y: \\alidcscom031\PVSS_Projects XXXXXX /USER:CERN\dcsoper
echo " ------ done ---------"
rem ---ping 1.1.1.1 -n 1 -w 2000 >NULL
These examples are real, original passwords in clear text are replaced by XXXXXX in this presentation
# Startup Batch Program for the LHC Interface Desktop
#
# Auth : deleted v1.0 4/8/2011
# - rdesktop -z -f -a 16 -k en-us -d CERN -u dcsoper -p XXXXXX -s “D:
\PVSS_Profiles\ACRLHCDesk.bat” alidcscom054
rdesktop -z -g2560x1020 -a 16 -k en-us -d CERN -u
START C:\Programs\PVSS\bin\PVSS00ui.exe -proj lhc_ui -user operator:XXXXXX
-p lhcACRMonitor/lhcACRDeskTopDisplay.pnl,$panels:BackGround:lhcBackground/
lhcBackgroundMain.pnl;Luminosity_Leveling:lhcLuminosity/
lhcLuminosityLumiLevelling.pnl;Collisions_Schedule:BPTX/
lhc_bptxMonitor.pnl;V0_Control:lhcV00Control/lhcV00ControlMain.

## Slide 45: …. In documentation
The relevant parameters are
• Window dimension : 1920x1050;
• RDT credential : host = alidcscom054, user = dcsoper, password = XXXXXX;
• shell command to start : D:\PVSS_Profiles\ACRLHCBigScreen.bat
• panel to reference : lhcACRMonitor/lhcACRMain.pnl
Twikies
Printed manuals
Web pages
Reports
Thesis
Entries like this :
Can be found in
…..
We protect our reports and guides, but institutes republish them very often on their unprotected servers

## Slide 46: ... or even worse!

## Slide 47: Using shared accounts
In general, the use of shared accounts is undesired
However, if we do not allow for it, users start to share their personal credentials
Solution – use of shared accounts (detector operator, etc.) only in the control room
  Restricted access to the computers
  Autologon without the need to enter credentials
  Logon to remote hosts via scripts using encrypted credentials (like RDP file)
  Password known only to admins and communicated to experts only in emergency (sealed envelope)
Remote access to DCS network allows only for physical user credentials

## Slide 48
OK, so we let people to work from the control room and remotely.
Is this all?

## Slide 49: Data exchange
The DCS data is required for physics reconstructions, so it must be made available to external consumers
The systems are developed in institutes, and the elaborated software must be uploaded to the network
Some calibration data is produced in external institutes, using semi-manual procedures
  Resulting configurations must find a way to the front end electronics
Daily monitoring tasks require access to the DCS data from any place at any time
How do we cope with that requests?

## Slide 50: Getting data OUT of DCS
GPN
ALICE DCS Network
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver

## Slide 51: DCS WWW monitoring
WWW is probably the most attractive target for intruders
WWW is the most requested service by institutes
ALICE model:
  Users are allowed to prepare a limited number of PVSS panels, displaying any information requested by them
  Dedicated servers opens these panels periodically and creates snaphosts
  The images are automatically transferred to central Web servers
Advantage:
  There is no direct link via the WWW and ALICE DCS, but the web still contains updated information
Disadvantage/challenges:
  Many

## Slide 52: WWW monitoring

## Slide 53: Getting data OUT of DCS
GPN
ALICE DCS Network
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver

## Slide 54: Getting data OUT of DCS
GPN
ALICE DCS Network
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Public WWW server
WWW generator

## Slide 55: Data for OFFLINE
Certain DCS data is required for offline reconstruction
  Conditions data
  Configuration settings
  Calibration parameters
Conditions data is stored in ORACLE and sent to OFFLINE via dedicated client-server machinery
Calibration, configuration, memory dumps, etc. are stored on private fileserver and provided to offline
OFFLINE shuttle collects the data at the end of each run

## Slide 56: Getting data OUT of DCS
GPN
ALICE DCS Network
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Public WWW server
WWW generator

## Slide 57: Getting data OUT of DCS
GPN
ALICE DCS Network
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Public WWW server
WWW generator
Trusted OFFLINE server
File exchange server
DCS Database
DB access server

## Slide 58: Data to ALICE online systems
During the runs, DCS status is published to other online systems for synchronization purposes
  Run can start only if DCS is ready
  Run must be stopped if DCS needs to perform safety related operations
  Etc.
Conditions data is sent to online and quasi-online systems for further processing
  Data quality monitoring
  Calibration parameters for HLT
  Etc.

## Slide 59: Getting data OUT of DCS
GPN
ALICE DCS Network
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Public WWW server
WWW generator
Trusted OFFLINE server
File exchange server
DCS Database
DB access server

## Slide 60: Getting data OUT of DCS
GPN
ALICE DCS Network
ALICE DAQ
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Trusted DAQ fileserver
Public WWW server
WWW generator
Trusted OFFLINE server
File exchange server
DCS Database
DIM/DIP servers
Trusted DIM consumers
HLT
DB access server
Trusted HLT gateway

## Slide 61: External data published to other sources
DCS provides feedback to other systems
  LHC
  Safety
  ...

## Slide 62: Getting data OUT of DCS
GPN
ALICE DCS Network
ALICE DAQ
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Trusted DAQ fileserver
Public WWW server
WWW generator
Trusted OFFLINE server
File exchange server
DCS Database
DIM/DIP servers
Trusted DIM consumers
HLT
DB access server
Trusted HLT gateway

## Slide 63: Getting data OUT of DCS
GPN
ALICE DCS Network
ALICE DAQ
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Trusted DAQ fileserver
Technical network
Public WWW server
WWW generator
Trusted OFFLINE server
File exchange server
DCS Database
Trusted DIP consumers
DIM/DIP servers
Trusted DIM consumers
HLT
DB access server
Trusted HLT gateway

## Slide 64: Getting data OUT of DCS
GPN
ALICE DCS Network
ALICE DAQ
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Trusted DAQ fileserver
Technical network
Public WWW server
WWW generator
Trusted OFFLINE server
File exchange server
DCS Database
Trusted DIP consumers
DIM/DIP servers
Trusted DIM consumers
HLT
DB access server
Trusted HLT gateway

## Slide 65: Getting data OUT of ALICE
A number of servers in different domains need to be trusted
  The picture still does not contain all the infrastructure needed to get the exchange working (nameserves, etc.)
Filetransfer OUT of the DCS network is not limited
  Autotriggered filetransfers
  Data exchange on client request

## Slide 66: Getting data to ALICE DCS
All file transfers to ALICE DCS are controlled
  Users upload the data to public fileservers (CERN security apply) and send transfer request
  After checking the files (antivirus scans), data is uploaded to private DCS fileservers and made visible to DCS computers
Automatic data flow to ALICE DCS is possible only via publisher/subscriber model
  DCS clients subscribe to LHC services, environment monitors, safety systems …. and data is injected into the PVSS

## Slide 67: Getting data IN to DCS
GPN
ALICE DCS Network
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
MANUAL
procedure

## Slide 68: Getting data IN to DCS
GPN
ALICE DCS Network
ALICE DAQ
DCS Worker Nodes
Exposed gateway
Public DCS fileserver
Private fileserver
Trusted DAQ fileserver
Technical network
Trusted DIP publishers
DIM/DIP clients
Trusted DIM publishers
HLT
Trusted HLT publishers

## Slide 69
Are people happy with this system?
One example for all

## Slide 70
From: XXXXXXXX [mailto:XXXXXXX@YYYYYYYY.ZZ]
Sent: Tuesday, February 1, 2011 11:03 PM
To: Peter Chochula
Subject: Putty
Hi Peter
Could you please install Putty on com001? I’d like to bypass this annoying upload procedure
Grazie
UUUUUUUUUUUU

## Slide 71
Few more
  Attempt to upload software via cooling station with embedded OS
  Software embedded in the frontend calibration data
  …..
  We are facing a challenge here
  … and of course we follow all cases….
  The most dangerous issues are critical last minute updates

## Slide 72: DCS
Detector Controls System
DETECTORS & detector-like
systems
External Services and Systems
Electricity
Ventilation
Cooling
Gas
Magnets
Safety
Access Control
LHC
Configuration
Database
Archival
Database
Devices
Devices
Devices
Devices
SCADA
1000 ins/s
Up to 6GB
Infrastructure
B-field
Space Frame
Beam Pipe
Radiation
Environment
Alice Systems
DAQ
TRIGGER
HLT
Conditions
Database
ECS
OFFLINE
72
SPD
PHS
FMD
T00
SDD
SSD
TPC
TRD
TOF
HMP
V00
PMD
MTR
MCH
ZDC
ACO
AD0
TRI
LHC
PIT
... And the whole IT infrastructure and services
(domain services, web, DNS, installation services, databases,...)

## Slide 73: Firewalls
In the described complex environment firewalls are a must
  Can be the firewalls easily deployed on controls computers?

## Slide 74: Firewalls
The firewalls cannot be installed on all devices
  Majority of controls devices run embedded operating systems
    PLC, front-end boards, oscilloscopes,...
  The firewalls are MISSING or IMPOSSIBLE to install on them

## Slide 75: Firewalls
Are (simple) firewalls (simply) manageable on controls computers?

## Slide 76: Firewalls
There is no common firewall rule to be used
The DCS communication involves many services, components and protocols
  DNS, DHCP, WWW, NFS, DFS,
  DIM, DIP, OPC, MODBUS, SSH,
  ORACLE clients, MySQL clients
  PVSS internal communication
Efficient firewalls must be tuned per system

## Slide 77: Firewalls
The DCS configuration is not static
  Evolution
  Tuning (involves moving boards and devices across detectors)
  Replacement of faulty components
Each modification requires a setup of firewall rules by expert
  Interventions can happen only during LHC access slots, with limited time for the actions
    Can the few central admins be available 24/7?

## Slide 78: System Complexity
Example of the cross-system connectivity as seen by monitoring tools
  Red dots represent PVSS systems

## Slide 79: Firewalls
Firewalls must protect the system but should not prevent its functionality
  Correct configuration of firewalls on all computers (which can run firewalls) is an administrative challenge
  Simple firewalls are not manageable and sometimes dangerous
    for example Windows firewall turns on full protection in case of domain connectivity loss
      Nice feature for laptops
        Killing factor for controls system which is running in emergency mode due to restricted connectivity
And yes, most violent viruses attack the ports, which are vital for the DCS and cannot be closed...

## Slide 80: Antivirus
Antivirus is a must in such complex system
But can they harm? Do we have resources for them?

## Slide 81: Antivirus
Controls systems were designed 10-15 years ago
  Large portion of the electronics is obsolete (PCI cards, etc.) and requires obsolete (=slow) computers
Commercial software is sometimes written inefficiently and takes a lot of resources without taking advantage of modern processors
  Lack of multithreading forces the system to run on fast cores (i.e. Limited number of cores per CPU)

## Slide 82: Antivirus
Operational experience shows that fully operational antivirus will start interacting with the system preferably in critical periods like the End of Run
  When systems produce conditions data (create large files)
  When detectors change the conditions (communicate a lot)
    adopt voltages as a reaction to beam mode change
    Recovery from trips causing the EOR...

## Slide 83: Antivirus and firewall finetuning
Even a tuned antivirus typically shows on top 5 resource hungry processes
CPU core affinity settings require huge effort
  There are more than 2300 PVSS managers in ALICE DCS, 800 DIM servers, etc.
The solutions are:
  Run firewall and antivirus with very limited functionality
  Run good firewalls and antivirus on the gates to the system

## Slide 84: Software versions and updates
It is a must to run the latest software with current updates and fixes
  Is this possible?

## Slide 85: Software versions and updates
ALICE operates in 24/7 mode without interruption
Short technical stops (4 days each 6 weeks) are not enough for large updates
  DCS supervises the detector also without beams
  DCS is needed for tests
Large interventions are possible only during the long technical stops - around Christmas
Deployment of updates requires testing, which can be done only on the real system
Most commercial software excludes the use of modern systems (lack of 64 bit support)
Front-end boards run older OS versions and cannot be easily updated
ALICE deploys critical patches when operational conditions allow for it
  Whole system is carefully patched during the long stops

## Slide 86: Conclusions
The cybersecurity importance is well understood in ALICE and is given high priorities
The nature of a high energy physics experiment excludes a straightforward implementation of all desired features
  Surprisingly , the commercial software is a significantly limiting factor here
Implemented procedures and methods are gradually developing in ALICE
The goal is to keep ALICE safe until 2013 (LHC long technical stop) and even safer afterwards