## Slide 1: Transverse stability in RCS and TESLA cavity Preliminary considerations
Alexej Grudiev
4/10/2022

## Slide 2: Single-turn stability limit in MC RCS from David Amorim. 2022-09-06_HEMAC_RCS1_impedance_resonator_scan_v2.pdf (cern.ch)
Some RCS parameters:
  f_RF = 1.3GHz
  C = 5990m
  Einj = 63.1GeV/c
  dE = 14.2 GeV/c per turn
  N_turns = 20
  V_RF = 20.1 GV
  Sigma_z = 25mm
Single turn stability limit: Rs/Q*f^2 = 100 [MΩ/m*GHz^2]

## Slide 3: ILC cavity parameters, reminder from:R/Q in linacΩ SRF cavity parameter model for HEC RF system design (cern.ch)
Max R/Q

## Slide 4: One HOM from LL ILC cavity and S-turn stability
Some RF cavity parameters:
  Active Acc. Gradient: 30 MV/m
  Cavity length: L_cav~1m
  V_cav: 30MV
  N_cav = 20100/30 = 670
Max R/Q HOM: R/Q = 32 linacΩ/cm^2 => Rs/Q = R/Q/2*c/ω = 3.1 kΩ/m per cavity
For 670 cavities: Rs/Q = 2.1 MΩ/m
f = 2.45 GHz,
Ncav*Rs/Q*f^2 = 12.6 [MΩ/m*GHz^2] < 100, Single turn stability limit from David
It is below stability limit by about factor 8 for one HOM.
In fact, all HOMs must be taken into account for S-turn stability calculation

## Slide 5: Stability for several HOMs
Wake of single mode expressed as
In SRF , and for short bunch t_max << 1/fres
Stability limit: Rs/Q*fres^2 = 100 =>
In fact, Stability limit ==
In the case of N modes:
Stability limit for total S-turn wake:
Taking into account the bunch spectrum limit the number of relevant HOMs in the sum

## Slide 6: Physical interpretation of stability limit
t
W(t)
Head
Tail
Transverse kick depends on the derivative of the wake
t
W(t)
Head
Tail
HOM_1
HOM_2
Σ HOM_i

## Slide 7: Stability for several HOMs up to 3 GHz
This is closer to the stability limits calculated by David: Rs/Q*f^2 = 100
BUT it is still factor 3 lower. More detailed studies needed

## Slide 8: Closed expression of total Transverse wake.
Karl Bane (2003, SLAC-PUB-9663)
Wake per meter length
Derivative of the wake
per meter length :
Total wake of 670 cavities:
Stability limit:
Big discrepancy between KB model and HOM sum. Probably due to KB model applicability for s << s0=1.6mm, where derivative is very high and for s > s0 it goes down -> less kick on the witness particle
Nevertheless KB model can be used for beam dynamic simulations where Wx will be convoluted with realistic bunch distribution
The wake derivative is about factor 9 larger than stability limit. Hm!?
s0=1.6mm !

## Slide 9: KB wake and discrepancy with HOM estimate
Wake
Big (~x10) reduction from
W’_x(0) -> W’_x(~σz=8mm)
Wake derivative