## Slide 1: GF PoP – R2E assessment
G. Mazzola1, L. S. Esposito1, K. Bilko1, R. G. Alia1 1 SY/STI
SPS PoP Workshop 24-25 October 2022

## Slide 2: Introduction
Two main subjects investigated for R2E assessment:
SPS-LSS6/ARC6 Benchmark
FLUKA setup and beam loss mechanism validation
GF PoP – R2E
R2E studies for GF electronic components installation in service tunnel

## Slide 3
SPS-LSS6/ARC6 Benchmark
FLUKA setup and beam loss mechanism validation

## Slide 4: Benchmark R2E – SPS LSS6/ARC6
Benchmark of different detectors measurements in SPS-LSS6/ARC6 sectors through FLUKA MC code
Validation of assumption on beam loss mechanisms for the specific sectors considered
Consolidation of work process and FLUKA setup for GF-PoP/R2E related studies

## Slide 5: Detectors
by Kacper Bilko (R2E project)

## Slide 6: Simulation setup
SPS tunnel and relative optics recreated starting from TWISS file → creation of FLUKA input
Simulation geometry:
  From QF62010 to QD62410 in order to cover LSS6 and ARC6 → Four complete periods ()
  Service tunnel for GF PoP electronics implemented
  Detectors: BLMs, OF along all tunnel (standard and non-standard position), RPLs, nMOS

## Slide 7: Simulation assumption
Assumption on main source of beam loss for LSS6/ARC6:
beam - residual gas interaction in the vacuum pipe
  Pressure inside the vacuum tube provided by Chiara Pasquino (TE-VSC) → → Constant gas profile: 7.5e-9mbar Value checked through Timber: pump and gauge valve in the 651 sector of SPS in VAC hierarchy
  H2 and H2 -like ideal gases are considered as residual in the vacuum pipe
  Nominal intensity 1.19e19 proton/year injected in SPS → Main contribute: 1e19 proton/year at 400GeV/c extracted towards North Area
  Considering the inelastic scattering cross section of 400GeV/c proton with H, the time of particles in the SPS machine and the revolution frequency
↓
Number of beam - gas interactions / year =
N.B. Total number of proton lost in SPS = → ~20% of proton injected (IPP meeting – SPS Radiation Survey)

## Slide 8: Data TID – LSS6
Results from 2018 and 2021 are available for BLMs
OF is in a non-standard position along LSS → difficult interpretation of results
Peak reached with BLM621 = 1148Gy in 2021 BLM620 ~ 0.16Gy → not reliable in 2021
by Kacper Bilko

## Slide 9: Data TID – ARC6
Results for BLMs and OF (in standard position) available for all ARC6
Values OF multiplied for a factor 11.8 for comparison with BLMs results
Peak reached with OF after QD62210 ~ 60Gy
by Kacper Bilko

## Slide 10: FLUKA Dose
BLM# | Gy FLUKA | Gy measured
BLM620 | 1.97E-03 | 0.16
BLM621 | 1.44E-02 | 1148.00
BLM622 | 3.44E-03 | 137.00
BLM623 | 4.07E-03 | 126.00
BLM624 | 2.61E-03 | 17.10
Values from simulation are lower of a factor on average
Data from BLM620 not reliable
Trend of results comparable with the data
FLUKA results normalized using calculated beam-gas interactions

## Slide 11: FLUKA Dose
Data for OF from start 2022 to mid-September 2022 → factor 1.25 to take in consideration all year (approximation)
High oscillation for values obtained in LSS6
Peak after QD62210, OF goes from non-standard position to standard position
FLUKA results are lower of a value → → discrepancy between BLM and OF results

## Slide 12: FLUKA Dose – Primaries calculation
BLM results from FLUKA and the relative measurements are fitted in order to calculate the number of primaries needed for each BLM
Number of primaries obtained for each BLM is averaged
TID from OF is recomputed with the new normalization factor
Normalization factor =

## Slide 13: Discussion (1)
Considering the high discrepancy between data and simulation: beam-gas losses as main source investigated
Online TID scored by BLMs in the simulated sector during the NA slow extraction
-TID peak at injection of protons and not during flat top -No constant behavior as expected if the main source is the beam-gas loss

## Slide 14: Discussion (2)
Considering the discrepancy between OF and BLM results: energy of beam lost investigated
IPP meeting – SPS Radiation Survey
Beam uncaptured during injection and not during flat top → proton has not reached the 400GeV/c. The proton is lost at lower energy and thus the dose gradient is different

## Slide 15: FLUKA Dose – 14GeV/c proton
Same setup and same assumption on the beam loss mechanism → beam-gas interaction
Number of primaries computed through the fit of BLM results →
Discrepancies between OF and BLM still present but reduced from a factor ~ 10 to a factor ~3

## Slide 16
GF PoP – R2E
R2E studies GF electronic components installation in service tunnel

## Slide 17: GF PoP – R2E
FLUKA setup:
  Same geometry and model → → Service tunnel detailed with holes to LSS6
  Beam - gas interaction as source
  400GeV/c proton run → worst case analyzed
  Normalization factor calculated fitting BLM results for 400GeV/c case →
Scoring – R2E quantities [1][2] :
  High Energy Hadron Equivalent Fluence = proportional to the number of SEU (Single Event Upset) due to hadrons of energy > 20MeV. Neutron of lower energies are weighted according to the ratio of their SEU cross section to the one of > 20 MeV hadrons
  Silicon 1 MeV-neutron Equivalent Fluence = fluence weighted by a damage function
  Thermal Neutron Equivalent Fluence = proportional to the number of SEU's due to thermal neutrons. Neutrons of higher energies are weighted according to the ratio of their capture cross section to the one of thermal neutrons (following the 1/v law)
  Total Ionizing Dose

## Slide 18: R2E limits @ CERN
General idea: no use of commercial electronics in region where the radiation levels are significantly above the cosmic background
Limits of radiation-safe area for electronic system at CERN: → → → Above these levels, Single Event Effect are a threat for the successful operation
Cumulative radiation effects are significant at dose level above ~10Gy
Specific electronic requirements needed for more detailed analyses

## Slide 19: FLUKA – TID Results
During proton run, electronics for GF PoP is non-operational → Cumulative radiation effects:
At laser location reached values of TID ~
TID in side tunnel – Hole for laser included
TID in side tunnel

## Slide 20: FLUKA – 1MeV-Neu Eq Results
During proton run, electronics for GF PoP is non-operational → Cumulative radiation effects:
At laser location reached values of Si 1MeV- Neu Eq Fluence
1MeV Neu. Eq. Fluence in side tunnel – Hole for laser included
1MeV Neu. Eq. Fluence in side tunnel

## Slide 21: FLUKA – ThN and HEH Results
Levels of Th. Neutrons and HEH in the service tunnel above the limit for a radiation-safe area
Th. Neutron eq. fluence in side tunnel
HEH eq. fluence in side tunnel – Effect of holes visible

## Slide 22: Conclusion
The assumption of beam-gas as the main source of beam losses in LSS6/ARC6 resulted to be wrong → → difficulties in simulation of real situation due to complex system
Discrepancies between OF and BLM pose some difficulties in obtaining a right parametrization fit using beam-gas as main source
Using the fitted normalization factor, in the worst case of 400GeV/c proton losses, R2E results in service tunnel are above the limits defined for a radiation-safe area and cumulative radiation effects are evaluated

## Slide 23: Next Step
Deployment of new detectors (RPLs and BatMONs) in the side tunnel. Through the fit of detectors’ results, a more precise estimation of R2E quantities in the service tunnel could be computed
Simulation with Partially Stripped Ions for R2E studies → beam-gas interaction is expected to be the main source of losses → electronics in position and operative

## Slide 25: BACK UP SLIDES

## Slide 26: References
[1] K. Roeed, M. Brugger and C. Pignard
PTB irridiation tests of the LHC radiation monitor (RadMon)
CERN ATS Note 2011-012, 2011 http://cds.cern.ch/record/1329478?ln=es
[2] K. Roeed, M. Brugger, D. Kramer et al.
Method for measuring mixed field radiation levels relevant for SEEs at the LHC
IEEE Transactions on Nuclear Science, vol. 59, no. 4, pp. 1040-1047, 2012.

## Slide 27: HEH/ThN results - zx