## Slide 1: Annual report second year of PhD course
Matteo Magherini
Tutor: Alessandro Rossi

## Slide 2: Overview
CMS outer tracker upgrade for high luminosity
  Anatomy of tracker modules for upgrade
  DAQ for CMS HiLumi modules
MUonE experiment test and deployment
  Physics case
  Measure
  Detector
  Data Acquisition
  Test beam results

## Slide 3: CMS outer tracker upgrade for high luminosity

## Slide 4: CMS outer tracker
Hi-Lumi upgrade of LHC after LS3 (~2026)
  Peak Luminosity ~7.5x1034cm-2s-1
  Expected Pile-up ~200
  Higher rates and radiation dose wrt Run3
  New Magnets (11T)
  Etc..
Necessary upgrade of current tracker:
  leakage current or full depletion voltage limitations  big part of current tracker will be inoperational
  Higher radiation level  upgraded tracker target: integrated luminosity of 3000 fb−1
  Efficient tracking + Higher pileup  Increase of granularity needed
  Contribution to level-1 trigger  selection of interesting physics at the first trigger stage is extremely challenging at high luminosity
CMS Ph1 tracker
CMS Ph2 tracker

## Slide 5: CMS outer tracker
HL-LHC  higher collision rate Most of charged particles have low pT  pT selection at readout level in order to reduce the L1 tracking input data size
pT modules
Two silicon sensors with small spacing in a module
Flex hybrid in order to get data from both sensors to one ASIC  Select track «stubs»
Different sensor spacing for different detector region
Tunable correlation windows
Inner Tracker

## Slide 6: CMS outer tracker
PS Modules
  3 different spacing : 1.6mm & 2.6mm & 4mm
  One strip sensor: 2.5cm x 100μm strips
  One macro Pixel sensor : 1.5mm x 100μm pixels
  Sensor dimension 5cm x 10 cm
    two column of 960 strips
    32x960 pixels
2S Modules
  2 different spacing : 1.8mm & 4mm
  2 micro strip sensors with 5cm x 90μm strips
  Sensor dimension are 10cm x 10cm
    two column of 1016 strips

## Slide 7: CMS outer tracker
PS Modules
  3 different spacing : 1.6mm & 2.6mm & 4mm
  One strip sensor: 2.5cm x 100μm strips
  One macro Pixel sensor : 1.5mm x 100μm pixels
  Sensor dimension 5cm x 10 cm
    two column of 960 strips
    32x960 pixels
2S Modules
  2 different spacing : 1.8mm & 4mm
  2 micro strip sensors with 5cm x 90μm strips
  Sensor dimension are 10cm x 10cm
    two column of 1016 strips

## Slide 8: DAQ for CMS modules
Stubs: average position of the seed cluster + average position of the correlation cluster
  L1 trigger
  40 MHz readout
Hits: information on ALL the strips/pixel in a module (one bit per strip/pixel)
  Final DAQ
  750 kHz readout

## Slide 9: Involvement for DAQ chain
Passage from test system (uDTC) to final readout system (DTC)
  From readout via optical + IPBus + computation in resident CPU  optical + computation in FPGAs in the board
  Transition of the calibration software for 2S modules  calibration SW for PS has just been deployed on the test system, time to transition also that!

## Slide 10: MUonE

## Slide 11: MUonE Physics case - Introduction
Anomalous magnetic moment of a lepton as precison test for SM
  Can be (very) precisely calculated in SM framework
  But… it’s flavor dependent!
Electron
  ge-2 determined with high precision
  Sensitivity to new particles limited by a ~(m/M)2 factor
Muon
  Sensitivity to an higher mass region [GeV, TeV]
  State of art: 4σ discrepancy from SM prediction

## Slide 12: State of the art
FNAL g-2 Run1 results:

## Slide 13: Present theoretical uncertainties

## Slide 14: aμHLO: LO Hadronic contribution
Traditionally computed via a dispersion integral using hadronic production cross sections in electron-positron annihilation at low energies
QCD lactice calculation still not competitive
  …at least up to the FNAL g-2 results…
Borsanyi, S., Fodor, Z., Guenther, J.N. et al.
Leading hadronic contribution to the muon magnetic moment from lattice QCD - Nature 593, 51–55 (2021).

## Slide 15: Measuring aμHLO – how to
MUonE: high precision measurement of aμHLO
  160 GeV μ beam on e- target at CERN
Hadronic contribution to the effective electromagnetic coupling, ∆𝜶had(q2) for space-like squared four-momentum transfers q2 = t < 0, via scattering data

## Slide 16: Measuring aμHLO– how to
Experimental kinematic limit:
0 < -t < 0.161 GeV
or
  0< x <0.93
~87% of the area  extrapolated to 100% with functional model of Δαhad (t)

## Slide 17: Measuring aμHLO– key element
Measure of the scattering angles precise tracking and at high rate
Best solution: 2S modules from CMS

## Slide 18: MUonE Detector
High Intensity μ beam (160GeV)
x 40

## Slide 19: MUonE DAQ chain
CMS
MUonE

## Slide 20: MUonE DAQ chain

## Slide 21: Data Structure from the 10 GB link
On the sink PC 1.2 GB raw files are saved
Raw files structure:
Decoding of raw data  different readable formats for analysers

## Slide 22: MUonE – 2022 test beam setup
*First time*: 6 modules readout at high intensity
One completely equipped station + target  first possibility to reconstruct tracks and study MUonE capabilities and resolution
Stress test for DAQ final system  20 MHz muon beam ~ half of the expected rate in CMS for HiLumi

## Slide 23: Data Quality Monitoring
Deployment of DQM tools:
  Fast
  Interactive
  Keeping track of both firmware errors and hardware conditions
  With an eye on scalability for the future
  In progress: adding fast reconstruction of tracks

## Slide 24: Offline analysis
Firsts results from tracking of this year TB – ended yesterday
First simple tracking with just a single particle passing through the detector  estimate of residuals
Results around what expected ~ 100 um resolution  preliminar! Alignment still to be done

## Slide 25: Offline analysis
Firsts results from tracking of this year TB – ended yesterday
First simple tracking with just a single particle passing through the detector  estimate of residuals
Results around what expected ~ 100 um resolution  preliminar! Alignment still to be done
First track reconstruction in 2D performed
Position of the interaction vertex with target

## Slide 26: Offline analysis
Firsts results from tracking of this year TB – ended yesterday
First simple tracking with just a single particle passing through the detector  estimate of residuals
Results around what expected ~ 100 um resolution  preliminar! Alignment still to be done
First track reconstruction in 2D performed
You can recognize budget material
Position of the interaction vertex without target

## Slide 27: Plans for the next year
Continuous work on passage from test DAQ system  final DAQ system. First step: transition of the whole calibration code for PS modules
Analysis on test beam dataset:
  Alignment of the modules – never done still with stubs data stream
  Studies on track reconstruction algorithms
  Estimate of MUonE capability, resolution and extrapolation to sensitivity of the whole experiment
  Characterization of CMS 2S modules
  Characterization of failures in high intensity for DAQ firmware

## Slide 28: Backup

## Slide 29: Educational activities
INFN School of Statistics 2022 [1]
Standard Model at the LHC 2022 [2]

## Slide 30: DAQ for CMS modules
Notes: SSA -> short strip ASIC

## Slide 31: Key element
The key elemet to achieve the precision required is the measure of the scattering angles
Experimental needs:
  PID to separate electron and muon  ECAL + μ-filter
  Precise tracking for angles  Tracker
  Electron energy measurement to add redoundancy and reduce systematicsECAL

## Slide 32: DAQPath inclusion and testing

## Slide 33
https://arxiv.org/pdf/1911.08123.pdf