## Slide 1: SPS: MicroTCA LLRF and new power system
Arthur Spierer on behalf of the SPS LLRF and RF power teams
7 and 14 of October 2022

## Slide 2: SPS: Super Proton Synchrotron
Injector for LHC and fixed target experiments
Visit of the LLRF Faraday cage and RF power amplifiers on the surface
200 MHz travelling wave cavities
Cern Control Center (CCC)
SPS/LHC map

## Slide 3: SPS RF Upgrade 2019-2020
Completely new RF system
  From 6 to 8 Cavities
  New 1.6MW solid-state amplifier systems
New digital LLRF
  MTCA for 200MHz Cavity-Controllers (RF feedback)
  MTCA for Beam Control (beam based loops)
SPS Solid-state amplifier system
SPS low-level RF system (MTCA)
image courtesy of G. Hagmann

## Slide 4: SPS LLRF Architecture
White-Rabbit network
  to broadcast frequency program and setpoints
  to synchronize clocks/RF
10 Gbits links to transmit cavity voltages and damper signals
Direct sampling at 125 Msps of the 200MHz RF
  Resampling to track sweeping RF
  Low noise clock generators
VME
MTCA
SPS low-level Architecture, image courtesy of G. Hagmann

## Slide 5: SPS LLRF Architecture
White-Rabbit network
  to broadcast frequency program and setpoints
  to synchronize clocks/RF
10 Gbits links to transmit cavity voltages and damper signals
Direct sampling at 125 Msps of the 200MHz RF
  Resampling to track sweeping RF
VME
MTCA
QSFP-SFP RTM
AFCZ MicroTCA FMC carrier
SIS8300-KU
DRTM_DS8VM1

## Slide 6: One example!
Lead ions slip-stacking
  Independent control of all cavities
  Amplitude and frequency modulation within the turn
  Control two beam in the machine!
Enjoy your visit!
4 bunches 100ns
4 bunches 100ns
8 bunches 50ns
Cycle time ->
Buckets (beam current transformer)

## Slide 8: References
[1] Paper architecture