## Slide 1: Summary of low heating MKP-L impedance studies
M. Barnes, M. Beck, G. Rumolo, C. Zannini
Acknowledgments: F. Caspers, M. Diaz, L. Ducimetiere, V. Namora,
F. Pelloux, B. Salvant, Y. Sillanoli, P. Trubacova

## Slide 2: Overview
Introduction
Benchmarks of impedance model and impedance optimization
Impedance measurements on the final assembly

## Slide 3: Overview
Introduction
Benchmarks of impedance model and impedance optimization
Impedance measurements on the final assembly

## Slide 4
MKP-S
MKP-L
Beam
#1
#2
#3
#4
SPS injection kicker (MKPs)
Injection kickers are needed for beam injection in the SPS but unfortunately their contribution to the machine longitudinal and transverse impedance is relevant

## Slide 5
SPS injection kicker (MKPs)
Real part of the longitudinal impedance
MKP4 broadband kicker magnet resonance has lower frequency and higher peak value
MKPS
MKPL

## Slide 6
Power loss ratio between MKPL and MKPS
450 GeV (top energy)
26 GeV
(injection energy)
Notes: Spiegarla meglio

## Slide 7: MKPL beam induced heating
Issue during the HV test of the low impedance prototype
Designed of the shielding to be modified: connection of the serigraphy to HV
Several impedance simulation and measurements performed
Installation foreseen during YETS 2022/2023
scenario |  | trains | Injected p/b
scrubbing week | 2022 scrubbing | 4x72 | 2.00E+11
typical week | 2022 operation | 4x48 | 1.67E+11
 | 2022 MD | 4x72 | 2.22E+11
scrubbing week | 2023 scrubbing | 4x72 | 2.60E+11
typical week | 2023 operation | 4x48 | 2.00E+11
 | 2023 MD | 4x72 | 2.56E+11
typical week | 2024 operation | 4x48 | 2.00E+11
 | 2024 MD | 4x72 | 2.56E+11

## Slide 8: Overview
Introduction
Benchmarks of impedance model and impedance optimization
Impedance measurements on the final assembly

## Slide 9: MKPL beam induced heating
A criticality of the MKPL at LIU intensities was predicted already in 2013 (slides)
First observation of heating during 2014 scrubbing run in good agreement with the expectation from the model
Possible mitigations of the MKP beam induced heating investigated from the beginning of 2015

## Slide 10: MKP impedance reduction
  Concept with longitudinal serigraphy exists (4, 5 and 6 stripes)
Q20 | PL per LHC fill cycle
MKP-L | 874 W
MKP-S | 234 W
MKP-L ser. (6 stripes) | 28 W
MKP-L ser. (4 stripes) | 99 W
M. Beck
CERN-THESI015-374

## Slide 11: MKP impedance validation
Good agreement between simulation model and measurements
Impedance validation with bench measurements in October 2020

## Slide 12: Issue experienced during HV test
Serigraphy finger closest to HV busbar shows most damage
Connection to HV of the serigraphy has been considered as the best solution of the sparking issue.
In the original design the serigraphy was grounded.
Design solution were investigated to solve the issue
HV conductor
Ground conductor

## Slide 13: Design optimization
Impedance/wake model from CST simulation (MKP-L with 5 stripes serigraphy)
Best trade-off between impedance and high voltage breakdown mitigation
Initial low impedance MKPL model
Connection of serigraphy to HV, finger length optimization, only 4 fingers used ……

## Slide 14: Design optimization
fdist
fL
To preserve kicker field quality
Aperture limitations
Ceramic robustness
Impedance optimization: design constraints
Design the narrow resonance far away from dangerous spectrum lines
Strategy
Frequency increases with fdist and descreases with fL

## Slide 15: Design optimization: test on vetronite box
Low power measurements have been performed to benchmark the simulation model with serigraphy connected to HV
Serigraphy fingers on the outside part of the vetronite box (top and bottom)

## Slide 16: Design optimization: test on vetronite box
Measurements turned out to be very useful to improve the simulation model with serigraphy connected to HV
As for the serigraphy connected to ground also with serigraphy connected to HV the impedance is efficiently reduced
Details at the IWG#50 link

## Slide 17: Design optimization: test on vetronite box
Good agreement in the frequency change versus finger length
Frequency deviation between measurements and model is expected to be below 2 MHz
Uncertainty on dielectric properties and alignment of the vetronite block
Measurements turned out to be very useful to improve the simulation model with serigraphy connected to HV
Details at the IWG#50 link

## Slide 18: Comparing measurements and simulations: Test on V3 serigraphy
Simulations performed with εr=9.9
A variation in the range 8.4-11.4 of εr will cause a ± 1 MHz variation in the frequency
HV busbar
[Hz]

## Slide 19: Comparing measurements and simulations: Test on V4 serigraphy
Simulations performed with εr=9.9
A variation in the range 8.4-11.4 of εr will cause a ± 1 MHz variation in the frequency
link
Details on serigraphy versions
[MHz]

## Slide 20: Beam induced power loss
Both from measurements and simulations the new MKPL is expected to exhibit a beam induced power loss significantly lower than the present MKPS

## Slide 21: Overview
Introduction
Benchmarks of impedance model and impedance optimization
Impedance measurements on the final assembly

## Slide 22: MKPL impedance measurements on the final assembly: all individual modules and full assembly

## Slide 23: MKPL impedance measurements on the final assembly: all individual modules and full assembly

## Slide 24: Beam induced power loss on the final assembly
Both from measurements and simulations the new MKPL is expected to exhibit a beam induced power loss significantly lower than the present MKPS
Worst case on single module measurements

## Slide 25: Summary
The beam coupling impedance model of the MKPL can reproduce measurements observations with high degree of accuracy
  Uncertainty on first resonance frequency expected to be within 2 MHz
The design has been optimized to find a trade-off between kicker functionality and beam coupling impedance
  Serigraphy termination, number of serigraphy fingers, distance between fingers, finger lengths, ......
Longitudinal and transverse impedance measurements have been performed on the final assembly
  The new MKPL is expected to heat up less than the present MKPS
  Impact on beam stability to be studied on the final version (found to be negligible on initial version)

## Slide 26: Thank you for the attention

## Slide 27: MKPL impedance measurements on the final assembly: transverse impedance
PRELIMINARY

## Slide 28: Beam induced power loss
Both from measurements and simulations the new MKPL is expected to exhibit a beam induced power loss significantly lower than the present MKPS

## Slide 29: MKPL impedance measurements on the final assembly: all individual modules and full assembly

## Slide 30: Power loss in kickers along cycle