## Slide 1
Expected radiation dose
to the triplets/D1
1st Meeting of the LHC Triplet Task Force 2022 October 14th
Francesco Cerutti

## Slide 2
Radiation origin and measurements
Dose in the ATLAS and CMS triplet coils: a recap
Assumptions
Forecast
The separation dipole (warm D1), the Matching Section and the Dispersion Suppressor
LHCb
Ion operation (ALICE)
OUTLINE

## Slide 3
THE RADIATION SOURCE
150 W absorbed in the TAS absorber
650 W going through the TAS
of which
150 W absorbed in the triplet
950 W towards each (L&R) side
@ 1034 cm-2 s-1 , i.e. 8.5 108 s-1 inelastic collision rate
cold magnets
proton-proton inelastic reaction
with 7.5 10-10
Higgs bosons
7 TeV p + 7 TeV p
with 6.5 TeV beams (80mb) ~125 W (magnet end uncertainties) prediction at 1034 cm-2 s-1
vs 115-135 W measurements (TE-CRG-OP) in the triplet cold mass

## Slide 4
BLM VALIDATION
[D. Prelipcean, in Phys. Rev. AB 25, 091001 (2022)]
2018
6.5 TeV beams

## Slide 5
THE DOSE IN THE COILS [I]
correctors:
MCBX: larger aperture
MQSX: coils off mid planes
MC S/T X & MC O/OS/SS X
p-p @√s=14 TeV
85 mb inel xs
Dose distribution is not constant

## Slide 6
x
THE DOSE IN THE COILS [II]
regular inversion of the crossing angle polarity in ATLAS [LMC #225, 2015 Jul 8th]
x
p-p @√s=14 TeV
85 mb inel xs

## Slide 7
THE DOSE IN THE COILS [III]
The peak dose values here reported are obtained with a resolution of about 3 mm in radius, 2° in azimuthal angle and 10 cm along the magnet length, namely averaging over a volume of less than 0.4 cm3 in the triplet quadrupole coils.
As for uncertainty management, in the related case of quench limit (mW/cm3), a safety factor of 3 was taken at design between the expected quench limit and the simulated peak power density (averaged over the whole radial thickness of the coils). On the contrary, no safety factor was taken for long term damage.

## Slide 8
0
p
p/2
3p/2
x
0
p
p/2
3p/2
x
A MULTIDIMENSIONAL
PROBLEM
Each configuration has to be weighted
with the respective integrated lumi
Independence from b*,
i.e. beam divergence and luminous region size
Relevant parameters:
beam energy
crossing plane
vertical crossing angle sign
crossing angle value
beam screen orientation
p-p @√s=14 TeV
85 mb inel xs
not considered for Run 3
(substantial benefit only in IR5 thanks to the polarity inversion
and lower crossing angle)

## Slide 9
RUN 3 SCENARIO
 | up to now | 2022 | 2023 | 2024 | 2025 | reaching
beam energy [TeV] |  | 6.8 |  |  | 6.8 | 
integrated lumi [fb-1] | 190 | 35 | 85 | 85 | 85 OR 42.5 + 42.5 | 480
lumi averaged half cross. angle [urad] |  | -156 (-160) | -149 (-160) | +149 (+160) | +149 / +149 -149 (+160) / (+160) (-160) | 

## Slide 10
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up [MGy] | 4 | 8.5 (8.5)
IR1 down [MGy] | 3.5 | 8.5 (8.5)
IR5 up [MGy] | 2.5 | 6
IR5 down [MGy] | 2.5 | 6
IR5 outward [MGy] | 3 | 7 (7.5)
MCBX1
Dose on the external coil layer (that provides the horizontal kick) is not shown but remains below 4 MGy per 300 fb-1
In case of horizontal crossing (CMS), the peak lies outside the coil region
p-p @√s=14 TeV
85 mb inel xs
As for the internal coil layer (that provides the vertical kick), the coil region is in the vertical plane, where the peak lies

## Slide 11
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up [MGy] | 3 | 7 (7)
IR1 down [MGy] | 3.5 | 7.5 (7.5)
IR5 inward [MGy] | 3.5 | 8 (8)
MQSX
p-p @√s=14 TeV
85 mb inel xs
In case of horizontal crossing (CMS), the peak lies outside the coil region

## Slide 12
MCOSX3
 | up to now
integrated lumi [fb-1] | 190
IR1 up [MGy] | 5.5
IR1 down [MGy] | 7.5
IR5 up [MGy] | 4
IR5 down [MGy] | 4
IR5 inward [MGy] | 3
up to 2024 end
395
14.5 (15)
15 (15)
9
9
7 (7.5)
inner layer
phi = 0
phi = ± p
phi = p/2
phi = - p/2
In IR1, the peak dose on the skew octupole coils is expected to have already challenged the reference limit
The peaks lie outside the coil region
p-p @√s=14 TeV
85 mb inel xs

## Slide 13
IN SUMMARY: MAIN QUADRUPOLES
error bars reflect the margin given by the crossing angle variation along the fill and mostly
the IR1 polarity inversion in the middle of 2025

## Slide 14
IN SUMMARY: MCBX & MQSX
error bars reflect the margin given by the crossing angle variation along the fill and mostly
the IR1 polarity inversion in the middle of 2025

## Slide 15
IN SUMMARY: HIGHER ORDER CORRECTORS
error bars reflect the margin given by the crossing angle variation along the fill and mostly
the IR1 polarity inversion in the middle of 2025

## Slide 16
2017+2018 DOSE (KGy per 115 fb-1)
1: 40 8: 50 120-135 (!)
2: 45 9: 90 (!) 160-175 (!)
3: 50 11: 55 50-70
4: 70 10: 15 (!) 50-70
(!) data asymmetry
(!) simulation overestimation
8
9
10
11
10 kGy
50 MGy
peak in the front coil
dosimeter
location
WHAT ABOUT THE D1? [I]
ATLAS
[Inigo Sancho Fernandez et al. ]

## Slide 17
WHAT ABOUT THE D1? [II]
MBXW.A4 | up to now | up to 2024 end | + 2025 (as 2023/2024)
integrated lumi [fb-1] | 190 | 395 | 480
IR1 [MGy] | 30 | 70 | 85
[Paolo Fessia, LMC #309, 2017 Jun 28th]
Shield installation under consideration

## Slide 18
THE REST OF THE INSERTION …
The highest peak dose is expected to be reached on the IP side of the Q5 assembly in IR5 (CMS):
up to ~10 MGy in the quadrupole on the right side, with quite some sensitivity to TCL4 collimator half-gap (from 1 to 11 MGy as opening from 14 to 19 s);
for the weaker MCBC corrector on the left side, this peak is outside the coil region
The second peak is in the half cell 9 corrector on the left side of ATLAS and CMS: almost 2 MGy after 480 fb-1
IP5
MQML5/6 MCBC MQML 5/6 MCBC
… AND THE DS
R5.B1
with TCL4 @ 19 s

## Slide 19
SUMMARY
The regular inversion of the crossing angle polarity in ATLAS allows to accumulate a total of about 400 fb-1 without exceeding – apart from systematic uncertainties – the 30 MGy reference limit for the main quadrupoles. The b* levelling at non constant (minimal) crossing angle offers a few percent additional margin.
An additional Run-III year (with 85 fb-1 more), bringing the total integrated luminosity close to 500 fb-1, would lead to reaching the above dose limit. In this case, the change of polarity in ATLAS mid 2025 (after achieving half of the annual lumi) is recommended.
Assuming a limit of 6 MGy for the corrector magnets in the triplet, this is expected to be reached in the four MCBX.1 and four MQSX by the end of 2024 and (largely) surpassed by then in the octupoles and dodecapoles (around ATLAS).
The most impacted D1 module (MBXW.A4 left and right of ATLAS) is expected to be locally subject to mild damage by the end of 2024, rising to moderate damage after an additional year.
For the weak points in the MS and DS (MCBC correctors), timely solutions are planned for HL-LHC.

## Slide 20
IR8
After a 28 fb-1 Run 3, a cumulated dose of about 6 MGy is expected to be reached in the Q1.1R8 coils.
In parallel, the front coils of the short compensators would reach 10-12 MGy. The installation of tungsten shields, as already implemented in IR7, looks like an advisable measure for an YETS.
UPPER
IP front coils
LOWER
7 TeV beams
+200 mrad V (ext)
R8

## Slide 21
2018
6.5 TeV beams
Chart: Distance from IP8 [m]
| -222.17280000000028 | -218.44280000000072 | -179.03280000000086 | -175.88280000000304 | -169.99279999999999 | -168.71280000000115 | -166.36280000000261 | -161.61280000000261 | -146.43280000000232 | -142.39280000000144 | -138.98280000000159 | -138.48280000000159 | -133.10280000000057 | -130.60280000000057 | -127.0528000000013 | -121.98280000000159 | -117.32280000000173 | -114.49279999999999 | -74.992799999999988 | -67.512800000000425 | -62.612800000002608 | -58.712800000001153 | -53.462800000001153 | -50.652799999999843 | -49.652799999999843 | -46.542800000002899 | -43.702800000002753 | -41.842800000002171 | -40.842800000002171 | -38.722799999999552 | -37.472799999999552 | -35.292800000002899 | -34.292800000002899 | -32.362800000002608 | -29.85280000000057 | -26.672800000000279 | -25.672800000000279 | -23.432800000002317 | -19.942800000000716 | 20.237199999999575 | 23.437200000000303 | 25.64719999999943 | 26.64719999999943 | 29.797199999997247 | 32.297199999997247 | 34.297199999997247 | 35.297199999997247 | 37.457199999997101 | 38.64719999999943 | 40.807199999999284 | 41.807199999999284 | 43.617199999996956 | 47.217199999999139 | 49.64719999999943 | 50.64719999999943 | 53.627199999998993
Simulation | 2.6683e-10 | 9.2698e-10 | 3.4801e-10 | 6.4288e-11 | 2.6967e-10 | 1.2407e-10 | 7.6453e-10 | 3.2891e-10 | 4.5982e-10 | 7.0712e-11 | 8.256e-11 | 1.5786e-10 | 4.2094e-10 | 1.2257e-10 | 6.0917e-10 | 4.6908e-09 | 2.3245e-09 | 3.9015e-09 | 9.4533e-09 | 6.7066e-10 | 3.748e-10 | 1.6595e-09 | 8.9861e-11 | 1.0596e-10 | 1.4251e-10 | 9.0195e-10 | 1.0638e-10 | 1.1756e-10 | 1.0588e-10 | 1.2724e-10 | 1.0054e-10 | 2.0283e-10 | 3.4926e-10 | 8.0408e-10 | 4.9519e-10 | 5.0729e-10 | 7.8322e-10 | 6.9811e-09 | 1.8798e-08 | 1.5953e-08 | 1.0071e-08 | 9.2948e-10 | 3.9674e-10 | 3.1464e-10 | 7.2982e-10 | 3.5953e-10 | 1.5169e-10 | 1.3633e-10 | 1.3717e-10 | 1.4768e-10 | 1.1306e-10 | 9.8872e-11 | 1.098e-09 | 1.2741e-10 | 1.7739e-10 | 9.3115e-11
Data 2018 | 3.4299e-10 | 9.7625e-10 | 1.1263e-09 | 2.303e-11 | 9.3018e-11 | 3.1679e-11 | 3.2727e-10 | 2.0874e-10 | 3.5519e-10 | 2.5096e-11 | 2.8202e-11 | 7.8065e-11 | 1.9426e-10 | 5.7174e-11 | 3.0351e-10 | 4.6074e-09 | 2.6023e-09 | 1.368e-08 | 6.3752e-10 | 4.5054e-10 | 4.2606e-10 | 1.3921e-09 | 9.8004e-11 | 9.1828e-11 | 8.843e-11 | 7.1969e-10 | 1.1494e-10 | 1.0729e-10 | 9.9578e-11 | 1.442e-10 | 1.0042e-10 | 1.4247e-10 | 2.3092e-10 | 7.9383e-10 | 4.1689e-10 | 3.9231e-10 | 6.0771e-10 | 5.0421e-09 | 3.216e-08 | 1.9385e-08 | 8.026e-09 | 6.44e-10 | 3.1845e-10 | 2.8567e-10 | 6.826e-10 | 2.1944e-10 | 9.4201e-11 | 7.2142e-11 | 6.4843e-11 | 8.0695e-11 | 8.1605e-11 | 1.0941e-10 | 5.649e-10 | 8.961e-11 | 8.9056e-11 | 1.1966e-10
LHCb
Q1
Q2
Q3
D1
BLM VALIDATION
[A. Ciccotelli, submitted to Phys. Rev. AB]

## Slide 22
most exposed
(high order) correctors
2023-2025 (@ √s=13.6 TeV)
THE DOSE IN THE COLD COILS [I]

## Slide 23
3 PEAK DOSE [MGy] 2.5 4.5 (~6 on 1R8)
by the end of Run 3 (+2025)
THE DOSE IN THE COLD COILS [II]

## Slide 24
IONS  IR2
in the coils
p-Pb in ATLAS
6.5 Z TeV beams (√sNN = 8.16 TeV)
-140 urad vertical crossing
Pb-Pb in ATLAS
6.37 Z TeV beams (√sNN = 5.02 TeV)
+160 urad vertical crossing
[M. Sabaté-Gilarte, doi:10.18429/JACoW-IPAC2021-WEXA06]

## Slide 25
BACKUP

## Slide 26
Q1 UP TO NOW
 | Run-I | 2015 | 2016 | 2017 | 2018 | up to now
beam energy [TeV] | 3.5 / 4 | 6.5 |  |  |  | 
integrated lumi [fb-1] | 30 | 5 | 40 | 50 | 65 | 190
lumi averaged half cross. angle [urad] | -145 | -205 | -180 | +135 | +144 | 
IR1 up [MGy] | 0.3 | 0.2 | 1.3 | 3.0 | 4.0 | 8.5
IR1 down [MGy] | 0.7 | 0.3 | 2.6 | 1.6 | 2.0 | 7
IR5 up [MGy] | 0.4 | 0.2 | 1.5 | 1.9 | 2.5 | 6.5
IR5 down [MGy] | 0.4 | 0.2 | 1.5 | 1.9 | 2.5 | 6.5
IR5 outward [MGy] | 0.5 | 0.2 | 1.9 | 2.1 | 2.8 | 7.5
[see 10th LHC Run-III Configuration Meeting, 2019 Mar 1st, https://indico.cern.ch/event/796630]
assuming here
an inelastic xs (including diffractive) rising from 73 mb to 81 mb for Ebeam increasing from 3.5 TeV to 6.8 TeV
and a peak dose dependence, as established from the calculation of some configurations at different energies, as (Ebeam)3/2

## Slide 27
 | up to now | 2022 | 2023 | 2024 | up to 2024 end
beam energy [TeV] |  | 6.8 |  |  | 
integrated lumi [fb-1] | 190 | 35 | 85 | 85 | 395
lumi averaged half cross. angle [urad] |  | -156 (-160) | -149 (-160) | +149 (+160) | 
IR1 up [MGy] | 8.5 | 1.2 | 2.9 | 5.6 (5.7) | 18.5 (18.5)
IR1 down [MGy] | 7 | 2.3 (2.4) | 5.6 (5.7) | 2.9 | 18 (18)
IR5 up [MGy] | 6.5 | 1.4 | 3.5 | 3.5 | 15
IR5 down [MGy] | 6.5 | 1.4 | 3.5 | 3.5 | 15
IR5 outward [MGy] | 7.5 | 1.7 (1.7) | 4.0 (4.1) | 4.0 (4.1) | 17 (17.5)
Q1 AFTER Run-III
assuming here
an inelastic xs (including diffractive) rising from 73 mb to 81 mb for Ebeam increasing from 3.5 TeV to 6.8 TeV
and a peak dose dependence, as established from the calculation of some configurations at different energies, as (Ebeam)3/2

## Slide 28
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up [MGy] | 11 | 23 (23.5)
IR1 down [MGy] | 9 | 23 (23.5)
IR5 up [MGy] | 4.5 | 10.5
IR5 down [MGy] | 4.5 | 10.5
IR5 outward [MGy] | 7.5 | 17.5 (17.5)
Q2A
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up [MGy] | 4.5 | 10.5 (10.5)
IR1 down [MGy] | 5 | 10.5 (10.5)
IR1 inward [MGy] | 5.5 | 12
IR5 inward [MGy] | 10.5 | 24 (24.5)
AND Q2B

## Slide 29
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up [MGy] | 1.5 | 3 (3.5)
IR1 down [MGy] | 1.5 | 3.5 (3.5)
IR1 inward [MGy] | 1 | 3
IR5 up [MGy] | 1 | 2
IR5 down [MGy] | 1 | 2
IR5 inward [MGy] | 2 | 4 (4)
MCBX2

## Slide 30
Q3
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up [MGy] | 2 | 4.5 (5)
IR1 down [MGy] | 2.5 | 5 (5)
IR5 up IP [MGy] | 1 | 3
IR5 down IP [MGy] | 1 | 3
IR5 inward [MGy] | 1 | 3 (3)
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up non-IP [MGy] | 4.5 | 11 (11)
IR1 down non-IP [MGy] | 5 | 11 (11)
IR1 inward [MGy] | 4.5 | 10
IR1 up IP [MGy] | 4.5 | 10 (10)
IR1 down IP [MGy] | 4.5 | 10 (10)
IR5 inward [MGy] | 7.5 | 16.5 (17)
AND MCBX3

## Slide 31
MCTX3
 | up to now | up to 2024 end
integrated lumi [fb-1] | 190 | 395
IR1 up [MGy] | 7 | 18 (18.5)
IR1 down [MGy] | 8.5 | 18 (18.5)
IR5 up IP [MGy] | 4.5 | 10
IR5 down IP [MGy] | 4.5 | 10
IR5 inward [MGy] | 4.5 | 10 (10.5)
In IR1, the peak dose on the dodecapole coils is expected to have already challenged the reference limit
p-p @√s=14 TeV
85 mb inel xs

## Slide 32
MCSX3
 | up to now
integrated lumi [fb-1] | 190
IR1 up [MGy] | 2.5
IR1 down [MGy] | 3
IR5 up [MGy] | 1.5
IR5 down [MGy] | 1.5
IR5 inward [MGy] | 2
up to 2024 end
395
6 (6)
6 (6)
4
4
4.5 (4.5)
In case of vertical crossing (ATLAS), the peak lies outside the coil region
p-p @√s=14 TeV
85 mb inel xs

## Slide 33
MCOX3
 | up to now
integrated lumi [fb-1] | 190
IR1 up [MGy] | 5.5
IR1 down [MGy] | 6.5
IR5 up [MGy] | 3.5
IR5 down [MGy] | 3.5
IR5 inward [MGy] | 2.5
up to 2024 end
395
13.5 (14)
13.5 (14)
8
8
6 (6)
middle layer
phi = 0
phi = ± p
phi = p/2
phi = - p/2
p-p @√s=14 TeV
85 mb inel xs

## Slide 34
MCSSX3
 | up to now
integrated lumi [fb-1] | 190
IR1 up [MGy] | 3.5
IR1 down [MGy] | 4.5
IR5 up [MGy] | 2
IR5 down [MGy] | 2
IR5 inward [MGy] | 1.5
up to 2024 end
395
9 (9)
9 (9)
5
5
4 (4)
outer layer
phi = 0
phi = ± p
phi = p/2
phi = - p/2
p-p @√s=14 TeV
85 mb inel xs

## Slide 35
 | with variable angle (with fixed angle) | + 2025 (as 2023/2024)
MAIN QUADRUPOLE | PEAK DOSE [MGy] | 
 | after 395 fb-1 | after 480 fb-1
Q1 IR1 | 18.5 (18.5) | 23.5 (24) / * 22.5 (23)
Q1 IR5 | 17 (17.5) | 21 (21.5)
Q2A IR1 | 23 (23.5) | 30.5 (31) / * 28 (29)
Q2A IR5 | 17.5 (17.5) | 21.5 (21.5)
Q2B IR1 | 12 | 15
Q2B IR5 | 24 (24.5) | 29.5 (30)
Q3 IR1 | 11 (11) | 14.5 (14.5) / * 13.5 (13.5)
Q3 IR5 | 16.5 (17) | 20.5 (21)
IN SUMMARY: MAIN QUADRUPOLES [I]
* assuming IR1 polarity inversion in the middle of 2025

## Slide 36
 | with variable angle (with fixed angle) | + 2025 (as 2023/2024)
CORRECTOR MAGNET | PEAK DOSE [MGy] | 
 | after 395 fb-1 | after 480 fb-1
MCBX1 IR1 | 8.5 (8.5) | 11 (11) / * 10.5 (10.5)
MCBX1 IR5 | 6 | 7.5
MCBX2 IR1 | 3.5 (3.5) | 4 (4) / * 4 (4)
MCBX2 IR5 | 2 | 2.5
MQSX IR1 | 7.5 (7.5) | 9 (9) / * 9 (9)
MQSX IR5 | 8 (8) | 9.5 (9.5)
MCBX3 IR1 | 5 (5) | 6 (6.5) / * 6 (6)
MCBX3 IR5 | 3 | 3.5
IN SUMMARY: MCBX & MQSX [I]
* assuming IR1 polarity inversion in the middle of 2025

## Slide 37
 | with variable angle (with fixed angle) | + 2025 (as 2023/2024)
CORRECTOR MAGNET | PEAK DOSE [MGy] | 
 | after 395 fb-1 | after 480 fb-1
MCSX3 IR1 | 6 (6) | 8 (8) / * 7.5 (7.5)
MCSX3 IR5 | 4.5 (4.5) | 5.5 (5.5)
MCTX3 IR1 | 18 (18.5) | 24 (25) / * 22 (23)
MCTX3 IR5 | 10 (10.5) | 12.5 (12.5)
MCSSX3 IR1 | 9 (9) | 12 (12) / * 11 (11)
MCSSX3 IR5 | 5 | 6
MCOX3 IR1 | 13.5 (14) | 18.5 (19) / * 17 (17.5)
MCOX3 IR5 | 8 | 9.5
MCOSX3 IR1 | 15 (15) | 19.5 (20) / * 18.5 (18.5)
MCOSX3 IR5 | 9 | 11
IN SUMMARY: HIGHER ORDER CORRECTORS [I]
* assuming IR1 polarity inversion in the middle of 2025