## Slide 1: Off-line TAS measurements of the long-lived nuclei 152,155Tb and 76,77Br for their relevance in medicine and neutrino physics.
E. Nácher
Instituto de Física Corpuscular – CSIC, Valencia (Spain)
J.A. Briz
Universidad Complutense de Madrid, Madrid (Spain)
U. Köster
ILL, Grenoble (France) / CERN, Geneve (Switzerland)
et al.

## Slide 2: Intro: Beta decay and TAS
Beta decay: often the first source of experimental information on nuclear structure far from the drip lines. Info on nuclear structure: decay scheme and beta strength (Sb)
Measuring the Sb(E) means measuring the beta intensity distribution Ib(E): very far from trivial (explanation coming next…)
We propose here to measure accurately the Ib(E) distribution in the b+/EC-decay of 76,77Br and 152,155Tb using the Total Absorption Spectroscopy (TAS) technique (explanation coming next…)

## Slide 3: The experimental technique
AZ
AZ-1
b+
g
real feeding
Very fragmented Ib/EC distribution and g de-excitation pattern.
Medium mass and heavy nuclei: large level density at high energy.
Why don’t we just measure at the IDS?

## Slide 4: The experimental technique
AZ
AZ-1
b+
g
real feeding
apparent feeding
HPGe
HPGe
g1
g2
g1’
Very fragmented Ib/EC distribution and g de-excitation pattern.
HPGe arrays do the great job of the level scheme and gamma branching ratios, but not so great at Ib/EC(E) and Sb(E)
Medium mass and heavy nuclei: large level density at high energy.
Hardy et al., Physics Letters B 71 (1977)
Why don’t we measure just at the IDS?

## Slide 5: The experimental technique
AZ
AZ-1
b+
g
real feeding
apparent feeding
HPGe
HPGe
g1
g2
g1’
Why don’t we measure just at the IDS?
76Br decay: 38 unplaced gamma rays: wrong levels, wrong gamma strength, wrong beta population and beta strength…
152Tb decay: 635 gamma rays detected,
248 remain unplaced

## Slide 6: The experimental technique
Total Absorption Spectroscopy (Ideal case)
g1
g2
b
E2
E1
E2
E
N
g2
g1
NaI
Ib/EC
Review of the TAS technique: Rubio et al., J. Phys. G 44 (2017)
Development of TAS analysis techniques: Taín et al., NIM A571 (2007)

## Slide 7: The experimental technique
Lucrecia, the TAS at ISOLDE
  Main NaI(Tl) cylinder: Ø38 cm x 38 cm
  Ancillary detectors: Ge telescope + plastic scintillator

## Slide 8: The experimental technique
One example to illustrate what we can do close to the stability valley: 64Ga decay
64Ga
GEANT4 - ENSDF
TAS measurement
TAS recalculated spectrum
This case, along with 66Ga, are relevant for isospin mixing studies

## Slide 9: The isotopes of interest
Radio-isotopes used in medicine: important to know accurately the beta intensity distribution Ib(E). This tells us:
  The total EC/b+ ratio (specially relevant for PET isotopes)
  The ratio between energy per decay in the form of g-rays and the energy per decay in the form of b particles (relevant for all isotopes used in medicine)
Essential to calculate the dose administered to the patient and its spatial distribution both in diagnosis using PET or SPECT cameras and in treatment (brachytherapy and theranostics). Used by simulation codes and therapy planners.
The beta decay of radio-isotopes of use or potential use in medicine must be well studied and the Ib(E) must be accurate and reliable

## Slide 10: The isotopes of interest
76Br, 152Tb and 155Tb are used in medicine within radiolabelled molecules for PET and SPECT imaging or as theranostic pairs for treatment.
PET/CT image of a patient with neuroendocrine neoplasm of the terminal ileum obtained after injection of 152Tb-DOTATOC
Taken from Richard P. Baum et al., “Clinical evaluation of the radiolanthanide terbium-152: first-in-human PET/CT with 152Tb-DOTATOC” , Dalton Transactions 42 (2017), DOI: 10.1039/c7dt01936j
Fig. taken from a talk by Nick van der Meulen (PSI)

## Slide 11: The isotopes of interest
These three isotopes, among others, have been identified by Nichols [NIC22]
as needing for a TAGS measurement
76Br, 152Tb and 155Tb are used in medicine as radiolabelled molecules for PET and SPECT imaging or as theranostic pairs for treatment.
[NIC22] Nichols A. L., "Status of the decay data for medical radionuclides". Radiochim. Acta 110, 609-644 (2022)

## Slide 12: The isotopes of interest
The absolute mass of the neutrino can be directly studied in a model-independent way by examining the slight distortion of the electron-capture spectrum (full energy!!) near the endpoint [GAS17, AKE21].
77Br comes from the same T-IS as 76Br for free and is one of the most promising ultra-low Q-value decay [GAM19]. It is an allowed transition 400 eV below the window.
[AKE21] M. Aker, et al., "First direct neutrino-mass measurement with sub-eV sensitivity" Nature Physics 18 (2022) 160
[GAS17] L. Gastaldo, K. Blaum, K. Chrysalidis, T. Day Goodacre, et al., Eur. Phys. J.: Spec. Top. 226, 1623 (2017)
[GAM19] N.D. Gamage, et al., "Identification and investigation of possible ultra-low Q value β decay candidates", Hyperfine Interact. 2019, 240
1364.27
3/2- from (n,n’g)
?

## Slide 13: The isotopes of interest
The absolute mass of the neutrino can be directly studied in a model-independent way by examining the slight distortion of the electron spectrum near the endpoint [GAS17, AKE21].
77Br comes from the same T-IS as 76Br for free and is one of the most promising ultra-low Q-value decay [GAM19]. It is an allowed transition 400 eV below the window.
T1/2 ~ 2 days  different sources starting at 5 kBq and doubling activity (up to 80 kBq) allow for a very long measurement accumulating huge statistics.
[AKE21] M. Aker, et al., "First direct neutrino-mass measurement with sub-eV sensitivity" Nature Physics 18 (2022) 160
[GAS17] L. Gastaldo, K. Blaum, K. Chrysalidis, T. Day Goodacre, et al., Eur. Phys. J.: Spec. Top. 226, 1623 (2017)
[GAM19] N.D. Gamage, et al., "Identification and investigation of possible ultra-low Q value β decay candidates", Hyperfine Interact. 2019, 240

## Slide 14: Beam-time request
  We need to measure activities ranging from 5 to 10 kBq, this means producing sources of 5 to 80 kBq max, easily achievable in some long (seconds to minutes) collections at GLM or LA1… or even from MEDICIS!
  With a normal behaviour of target-ion-source we should not need more than 1 shift per ion source: 1 shift for Br isotopes, 1 shift for Tb isotopes. These shifts do not need any specific allocation in the Schedule, but should just be added to an ongoing experiment using the appropriate T-IS.
  We do need purity: may require some decay time before measuring (rare earths contamined by Ce or Eu molecular compounds), or radiochemical separation at PSI (?)

## Slide 15
Off-line TAS measurements of the long-lived nuclei 152,155Tb and 76,77Br for their relevance in medicine and neutrino physics
-> Funding guaranteed for the next 3 years
-> 1 PhD student 3 yr (+1?) fully devoted to this project

## Slide 16: Backup slides

## Slide 17: ANALYSIS
Red spots: high-resolution results, last level at
2.9 MeV (Ph. Dessagne et al. Eur. Phys. J. 20 (2004))
76Sr is one of the most striking cases in which MOST of the B(GT) was missing in high-resolution experiments
E. Nacher, Istros 2019

## Slide 18: Nuclear deformation around A=70
b-decay of 72,74Kr and 76,78,80Sr measured in different runs during 2001-2002 at ISOLDE.
The shape of the ground state can be inferred from the B(GT) distribution.
  E. Nácher, A. Algora et al, Phys. Rev. Lett. 92 (2004)
  E. Poirier, F. Marechal et al, Phys. Rev. C69 (2004)

## Slide 19
A total of 295 levels and 1064 gamma-rays
Gamma photopeak efficiency: 19% at 1332 keV
SbHR / SbTAS = 0.4
Pandemonium: TAS vs Cluster-Cube
A. Algora et al., PRC 68 (2003) 034301

## Slide 20: Total Absorption Spectroscopy
g2
g1
g1
g2
b-feeding
E2
E1
E2
E
Ib
NaI
N
Ideal case

## Slide 21
g2
g1
NaI
Real case
E2
E
N
EC
X-ray detector
E2
E
Ib
Unfolding
algorithm (EM)
2 photons (511 keV)
back to back
Positron detector
E2
b+
E
N
Total Absorption Spectroscopy
Review of the TAS technique: Rubio et al., J. Phys. G 44 (2017)
Development of TAS analysis techniques: Taín et al., NIM A571 (2007)

## Slide 22: Analysis of TAS data
The TAS inverse problem [1]:
Expectation-Maximisation algorithm [2] applied to this problem [1]:
[1] J. L. Taín et al., Nucl. Inst. and Methods A 571 (2007) 728
[2] A. P. Dempster et al., J. R. Statist. Soc. B 39 (1977) 1.

## Slide 23: The Response Function
b-decay of 24Na: test bench for our simulations
24Mg
1369
0
24Na
4123
4123
2754
1369
5235
5235
At ~5 kHz:
1h… 1e-4
10h… 1e-5
100h… 1e-6
200h... 5e-7

## Slide 24: The Response Function
b-decay of 24Na: test bench for our simulations
24Mg
1369
0
24Na
4123
4123
1369
2754
5235

## Slide 25: Ultra-low EC decay and mn
EC-decay of 163Ho: calorimetric measurement, distortion at the endpoint
Ultra-low Q-value decay: 2.6 keV (400 eV in our case 77Br)

## Slide 26: Ultra-low EC decay and mn
b-decay of 115In: b.r. ~ 1e-2
Ultra-low Q-value decay: 120 eV!! (400 eV in our case 77Br)
f(Z=53, Q-E=10 keV) = 1.5e-5 f(Z=35, Q-E=10 keV) = 6.2e-6

## Slide 27: RIPLE-3 calc…