## Slide 1: Particle Accelerators in the XXI Century
Maurizio Vretenar CERN ATS-DO (Project Office) JUAS 2023

## Slide 2: Outline and Motivations for this Seminar
This Seminar is intended as an “appetizer” to introduce you to the Science and Technology of Particle Accelerators
Goals:
Give a general overview of accelerator technologies and applications, with no maths;
Give some hints to guide your study and your future choices.
Outline:
Accelerators as instruments
Accelerator and innovation
Key accelerator challenges
Accelerators for society
The future…

## Slide 3: Accelerators: our access to the subatomic world
When we extract particles from an atom (protons, electrons, charged nuclei) and we accelerate them we concentrate enormous amounts of energy in tiny volumes
proton
Particle accelerators are our door to access the subatomic dimension… to study and exploit the atom and its components
Where will this energy go? An accelerated subatomic particle sent towards an atom will:
Deliver some energy to the electrons.
Deliver some energy to the nucleus (after penetrating the Coulomb barrier).
Energy in an LHC bunch (1.15 1011 protons) is 1.3 105 J, in the full beam (2808 bunches) 3.6 108 J.
Energy density of an LHC bunch at interaction point (30 cm, 16x16 mm2) ≈ 0.5 1012 J/m3

## Slide 4: Accelerators can modify the nuclei and create new particles
If the energy is sufficiently high, the particles in the beam transfer energy to the nucleus and its components (and are then scattered, reflected or absorbed).
Collisions between particles and nuclei can break and modify the nucleus, to generate new elements and transform the matter!)
It’s the dream of the ancient alchemists coming true!
In high energy particle collisions new particles are generated, converting matter into energy
E = m c2
NUCLEAR PHYSICS
PARTICLE PHYSICS

## Slide 5: Accelerators can produce intense secondary beams
Accelerated electrons produce X-ray beams by interaction with a metal target (bremsstrahlung) or by synchrotron radiation in accelerator magnets)
Accelerated protons produce neutron beams by spallation reactions in a heavy metal target
X-rays generated by accelerators are commonly used in medicine
Both X-rays and neutrons generated from accelerators are used for advanced imaging in many fields: life sciences, condensed matter, energy, material science, cultural heritage, life sciences, pharmaceuticals,…
Additional applications are appearing for other types of secondary beams.

## Slide 6: Accelerators can precisely deliver energy
A «beam» of accelerated particles is like a small “knife” penetrating into the matter
Particles can penetrate in depth
(different from lasers!).
A particle beam can deliver energy to a very precisely defined area, interacting with the electrons and with the nucleus.
Particle beams are used in medical and industrial applications,
e.g. to cure cancer, delivering their energy at a well-defined depth inside the body (Bragg peak)
Lasers and accelerators have comparable peak energy densities, but different interactions and penetration

## Slide 7: Accelerators have a long history…
Question:
How old are particle accelerators?

## Slide 8: Modern particle accelerators are 95 years old
In 1928 a PhD Thesis introduced the basic concept of modern particle accelerators, using periodic acceleration provided by electric field at Radio-Frequency (RF).
This was a major step from the previous DC (constant voltage) acceleration, limited to few MeV
Rolf Wideröe’s PhD thesis, 1928, University of Aachen – he was 26 years old!
Acceleration of potassium ions 1+ with 25kV of RF at 1 MHz  50 keV acceleration in a 88 cm long glass tube) “at a cost of four to five hundred marks”, less than 2’000 € today!
use of Radio-Frequency technology (at the time limited to 1-2 MHz) → marrying radio technology and accelerators.
Use of a drift tube separating 2 accelerating gaps → invention of periodic acceleration.
complete accelerator: ion source, RF accelerator, detector, all in vacuum.
Ion source
Accelerating tube at
V=V0sinwt
Detector
RF generator
(from R. Wideroe’s thesis)
(image credit: Wikimedia commons)

## Slide 9: At the roots of innovation
What were the ingredients of Rolf Wideröe’s innovation?
He was young and curious (PhD student, fresh ideas and time available)
He was under pressure to complete his thesis («necessity is the mother of invention»)
He was merging information and experience from different fields (cross-fertilisation)
He was going all the way down to practical realisation (to «innovate»).
The Oslo Manual (OECD/Eurostat, 2005), defines innovation as “the implementation of a new or significantly improved product or process …”

## Slide 10: Innovation in the particle accelerator field
1931………….1945/48….1952…………..1965/90’s….…
Cyclotron: cyclic acceleration with magnets (Lawrence)
Application of WW2 radar technology to accelerators (Hansen, Alvarez)
Strong focusing (Courant, Livingston, Snyder, Christofilos)
Superconducting magnets and acc. cavities
Succession of enabling technologies (technology leaps)
Energy
2009 Livingston plot, Symmetry magazine
(for colliders, energy to reach same c.o.m. energy in collision with proton at rest)
S. Livingston, 1959:
Accelerator energy increases by a factor of 10 every 6 years
(Moore’s law of accelerators)
XXI century
?
2008: the Large Hadron Collider

## Slide 11: Particle Accelerators in 2023
Updated Livingstone-type chart (Wikipedia 2014, uploaded by J.Nash, Imperial College)
We have reached the end of exponential growth…
but the field has never been so flourishing!
TIARA Need for Accelerator Scientists report, 2013: 3’700 people engaged in accelerator science in Europe, growing to 4’400 by 2018.
As many as 50 ongoing accelerator construction or upgrade projects listed in the 2017 IPAC Conference (13 America, 11 Asia, 26 Europe)
?
How many particle accelerators there are in the world, and where are they?

## Slide 12: Multiple challenges for accelerator science
12
For all XXth century, fundamental science has been the driving force for the development of new accelerators, with its continuous quest for high energies required to discover new particles.
In this early XXI century, we are moving to a new paradigm where together with particle physics applied science (photon and neutron science) and healthcare appear as driving forces for innovation.
Advanced medicine and new materials are key technology drivers of the XXIst century.
There are more than 35’000 particle accelerators in operation around the world:
Research |  | 6%
 | Particle Physics | 0,5%
 | Nuclear Physics, solid state, materials | 0,5%
 | Biology | 5%
Medical Applications |  | 35%
 | Diagnostics/treatment with X-ray or electrons | 33%
 | Radio-isotope production | 2%
 | Proton or ion treatment | 0,1%
Industrial Applications |  | 60%
 | Ion implantation | 34%
 | Cutting and welding with electron beams | 16%
 | Polymerization | 7%
 | Neutron testing | 3.5%
 | Non destructive testing | 2,3%
What is the role of accelerators in this transition?

## Slide 13: Accelerators in transition – for physics and for society
Transition to new more affordable and sustainable technologies for basic science
Transition from basic science as main technology driver to a multiple system where basic and applied science, medicine and industry will together drive accelerator development.
Transition from a centralised configuration based on large laboratories to a distributed scheme (project clusters of small and large laboratories and industry)
Fundamental science
Applied science (photon and neutron sources)
Societal applications (medicine, industry, environment, etc.)
Limitations related to size, cost, energy.
New ideas and technologies
The electron linac for cancer radiotherapy, the most widespread accelerator in the world (> 12000 units)
innovation

## Slide 14: Reaching the limits of sustainability ?
Particle physics has been from the very beginning the technology driver for the development of particle accelerators: the quest for new particles at increasingly higher energies has motivated the development, construction and financing of increasingly large accelerators. And now?
Physics:
After the discovery of the Higgs boson the Standard Model is complete – many questions remain open (origin of dark matter and energy, antimatter asymmetry, etc.) and their solutions may be related to new unknown particles, but so far no clear predictions exist to be verified by an accelerator.
«Nature», July 2014
Accelerators:
The size, cost and energy consumption of the accelerators required to go beyond the standard model rise questions on the long term sustainability of accelerator-based particle physics.
Difficulty to justify new large projects
Difficulty to implement new large projects
The recent (2022) international crisis has shown that energy reduction is a must for future project, and that governance models based on science globalisation will be increasingly difficult to implement.

## Slide 15: The big challenges for accelerator science
We need new ideas (innovation!) and a collaborative and creative environment for these ideas to grow
Making accelerator-based particle physics research sustainable over the long-term, increasing at the same time the benefits of particle accelerators for society are the main challenges to the accelerator community in this XXIst century.
From the LHC (27 km) to the Future Circular Collider (100 km)
How does this translate into technical challenges?

## Slide 16: Multiple dimensions of accelerator R&D

## Slide 17: Frontier accelerators – economic sustainability
Where is the limit of sustainability? It depends on the economical environment and on the priorities of a given society.
To remain within the present limits we need an effort to produce innovative technologies.
scaling of present technology
reduction in cost with new technologies?
Moving along this line was made possible by new technologies
(colliders – antiproton production and storage – superconductivity)
Plot courtesy of P. Lebrun
collider
p-pbar
collider
superconducting
collider
FCC-ee
FCC-pp

## Slide 18: Step 1: smaller accelerators
Synchrotrons: p/q=Br
Need to maximise magnetic field
Superconductivity is mandatory, the limitations is the critical current density Jc for SC magnets
Linear accelerators: W=El
Need to maximise electric field
Limitations: arcing between electrodes, field emission, etc.
(and RF power, proportional to V2 !)

## Slide 19: The magnetic field frontier in superconducting magnets
R&D towards a 20 T HTS dipole magnet, develop 10 kA cable.
REBCO (rare earth barium copper oxyde) deposition on stainless substrate, tape arranged in Roebel cables.
values of 900-1200 A/mm2 at 4.2 K , 18-20 T have been obtained
Three technologies under consideration
1. NbTi (Niobium Titanium as in the LHC): mature but limited to about 9T field.
2. Nb3Sn (Niobium Tin) technology has seen a great boost in the past decade (factor 3 in JC w/r to ITER) but is not yet used in an accelerator – The HL-LHC upgrade will be the first one.
3. HTS (High-Temperature Superconductor) technology still in the experimental phase (Production quantities, homogeneity and cost need to evolve!) but can be a disruptive technology for future high-field magnets.
Right: layered structures with sections of different conductors
Left: new magnet designs are required for HTS
Courtesy L. Rossi, CERN

## Slide 20: HTS magnets – reducing cost is the main challenge
HTS allows reducing the size of the accelerator but not (yet) the cost.
HTS is presently about 5 times the cost of Nb3Sn, but other communities (e.g. fusion) could contribute to reducing the price in the next years.
Is superconducting magnet technology approaching saturation ? Large increase in cost for small performance improvements
(courtesy of P. Lebrun)
100 CHF (=100$) of YBCO HTS tape built by Bruker HTS for CERN

## Slide 21: The electric field frontier – superconducting cavities
Bulk Nb
Multi-layer
SRF Thin Film
TRENDS:
Nitrogen infusion process (FNAL) and other doping techniques: high Q operation, gradients ∼45 MV/m
Coating of Nb with a thin layer of Nb3Sn (allows operation at larger , improved cryogenic efficiency)
Coating of Cu cavites with Nb by HiPIMS (High Power Impulse Magnetron Sputtering,
Long-term goal: 60 → 90 MV/m

## Slide 22: The electric field frontier – normal conducting cavities
Pulsed systems, characterised by a BreakDown Rate (BDR), pulses lost because of vacuum arcing in the structure
Most advanced results by the Compact Linear Collider (CLIC) study based at CERN (X-band, 12 GHz)
Large international collaboration to understand the physics of breakdown phenomena.
100 MV/m gradient can be achieved (and exceeded)
… but power scales as the square of gradient! High gradient means smaller dimensions but higher power consumption.

## Slide 23: The sustainability frontier – energy and efficiency
Electrical power consumption (MW) for LHC and future projects (estimated) |  | 
 | normal | Stand-by
LHC | 122 | 89
HL-LHC | 141 | 101
ILC | 230 | 
CLIC 500 GeV | 235 | 167
CLIC 1.5 TeV | 364 | 190
FCC hh | 580 | 300?
Future large projects require huge amounts of electrical power
Example: the ILC needs about 1/3 of a Fukushima-type nuclear reactor, or in alternative 200 large windmills (80m diameter, 2.5 MW, 50% efficiency) covering a 100 km distance.
Total electricity consumption (GWh/y) | 
PSI | 125
ESRF | 60
ISIS | 70
KVI | 4
INFN | 25
ALBA-CELLS | 20
GSI | 60
CERN | 1200
SOLEIL | 37
ESS | 317
MAX IV | 66
DESY | 150
Power flow of PSI cyclotron: grid to beam efficiency 13%
A particle accelerators is a device that converts electrical energy from the grid into high-quality kinetic energy at sub-atomic scale (beam energy).
After a series of transformations, most of the energy is lost into low-quality heat.
Efficiency can be increased using special devices (e.g. permanent magnets, high-efficiency RF sources, SC RF cavities, etc.) but there is an intrinsic efficiency limit related to the “high-quality” of the energy produced by the accelerator and to its use.
Recuperation of heat is possible, but very inefficient because of low temperatures and distance.
Most of the electricity used by a particle accelerator goes to heating water and air – intrinsic limitation due to the “quality” of the energy stored in the beam

## Slide 24: New acceleration techniques using lasers and plasmas
Accelerating field of today’s RF cavities or microwave technology is limited to <100 MV/m
  Several tens of kilometers for future linear colliders
Plasma can sustain up to three orders of magnitude much higher gradient
  SLAC (2007): electron energy doubled from 42GeV to 85 GeV over 0.8 m  52GV/m gradient
Lasers can produce huge transverse electric fields (TV/m !)
Can we convert the transverse fields into longitudinal and use them for acceleration?
(1) Micro/Nano-Accelerators
(2) Plasma Accelerators
Use a plasma to convert the transverse electrical field of the laser (or the space charge force of a beam driver) into a longitudinal electrical field, by creating plasma waves.
The «accelerator on a chip»
Send THz Laser into Dielectric Waveguide (Micro-Accelerator)

## Slide 25: Towards a plasma-based linear collider?
Main challenges
W.P. Leemans & E. Esarey, Physics Today, March 2009

## Slide 26: Other options for high energy: muon collider
Colliding muons:
Muons are leptons, similar to electrons but heavier (207 times),
produced by pion decay or electron/positron annihilation, have a lifetime of only 2.2 ms.
Critical components:
Muon production complex (proton or positron beam, MAP or LEMMA)
Muon acceleration complex
Neutrino radiation
Excellent in term of power/luminosity, potential for cost savings
Many critical technical challenges requiring R&D
Low EMittance Muon Accelerator
Positrons on target, annihilation

## Slide 27: Accelerator for society
The Economist, October 2013

## Slide 28: Accelerators for medicine and industry
28
>35000 accelerators in use world-wide:
  44% for radiotherapy
  41% for ion implantation
  9% for industrial applications
  4% low energy research
  1% medical isotope production
  <1% research
Treating cancer
Making better semi-conductors
“Curing” materials:
sterilisation; carbon dating; treating flue gases or water; etc
Microanalysis of materials, mass spectroscopy, PIXE, etc
PET and SPECT medical imaging
Radiotherapy electron linac
Proton cyclotron for radioisotope production
The IBA Rhodotron for production of intense electron beams
A commercial system for ion implantation
A tandem accelerator for material and artwork analysis

## Slide 29: Particle accelerators: a formidable tool for medicine
Particles beams can activate the nuclei generating radiation that can destroy cancerous cells or can be detected from outside.
The energy deposited by a proton or ion beam has a well-defined peak (Bragg peak) inside the body: can destroy the cancer cells with minimum damage to other tissues.
Accelerators are the way to realise the old dream of a bloodless surgery and imaging: penetrate into the human body to treat diseases and to observe internal organs without using surgical tools.
≈ 75
12
>300
0
≈ 14’000
7
≈ 1’500
0
Cancer treatment
Imaging
New cancer treatments
≈ 16’000 particle accelerators operating for medicine worldwide, in cancer therapy and imaging
M. Vretenar | NIMMS
Operating facilities
Notes: One step back

## Slide 30: Treating cancer with particle beams
5 – 25 MeV e-beam
Tungsten target
>14,000 in operation worldwide!
Electron Linac (linear accelerator) for X-ray radiation therapy of cancer
Proton Cyclotrons and Ion (Carbon) synchrotrons for particle therapy of cancer
Different from X-rays, protons and ions deposit their energy at a given depth inside the tissues, minimising the dose to the organs close to the tumour. (“Bragg peak”)
>100 centres for protons, 12 for carbon

## Slide 31: Compact accelerators for medicine
AMIT superconducting cyclotron for isotope production (CIEMAT, Spain)
RFQ linac system for isotope production in hospitals (CERN)
The trend is to move the accelerator inside the hospital, but how can we miniaturise the accelerator ?
The challenges are the same as for future particle physics facilities: high field SC magnets, high-gradient and high frequency accelerating structures.
CLIC 12 Ghz technology for FLASH therapy in hospitals (CERN, CHUV)
Carbon ion cancer therapy facility in <1000 m2 based on a superconducting synchrotron (CERN, SEEIIST)

## Slide 32: Environmental applications of accelerators
Low-energy electrons can break molecular bonds and be used for:
Flue gas treatment (cleaning of SOx from smokes of fossil fuel power plants)
Wastewater and sewage treatment
Treatment of marine diesel exhaust gases (removal of SOx and NOx).
Maritime transport is the largest contributor to air pollution: a cruise ship emits as much sulphur oxides as 1 million cars!
Ships burn Heavy Fuel Oil, cheap but rich in Sulphur. Diesels (high efficiency) emit Nitrogen oxides and particulate matter.
New legislation is going to drastically limit SOx and NOx emissions from shipping, with priority to critical coastal areas.
So far, technical solutions exist to reduce SOx or NOx, but there is no economically viable solution for both.
150 kV electron accelerator to break the high order molecules that are then cleaned by a water jet (scrubber)
Hybrid Exhaust Gas Cleaning Retrofit Technology for International Shipping (HERTIS)
A project based on a patent from INCT Warsaw promoted by a collaboration of research institutions (including CERN), accelerator industry, shipyards, maritime companies, maritime associations (Germany, UK, Switzerland, Poland, Latvia, Italy).
From engine
To air

## Slide 33: Accelerators for art
particle accelerator
particle beam
Emission of radiation of characteristic energies (X-rays, g, particles…)
Radiation detection and spectral analysis
Ion Beam Analysis (e.g. PIXE, Proton Induced X-ray Emission)
A beam of particles (protons) from an accelerator is sent on a sample (e.g. a painting)
The atoms are excited and emit different types of radiation (X-rays, gammas, etc.)
Different atomic elements emit X-rays at different energies – Spectral analysis from one or more detectors allows determination of the chemical composition (e.g. of the pigments).
Ritratto Trivulzio by Antonello da Messina, 1476 – analysis at INFN-LABEC (Florence)
2 m
Portable PIXE system based on an RFQ linac being built by CERN and LABEC

## Slide 34: Some conclusions - at the roots of innovation
Particle accelerators are facing a critical moment in their evolution.
The expectations on accelerators from basic science, applied science, medicine and industry are increasing but some of our technologies are still the same as Wideröe’s invention almost 100 years ago.
There is today a lot of space and encouragement for innovative ideas!
But, what are the ingredients of innovation? Remember the first slide on Wideröe’s invention!
  Merge inputs from different science and technology fields (look around you!)
  Challenge the established traditions (but respect experience!)
  Take risks (but foresee mitigations!)
The 4 industrial revolutions (4th still ongoing!)
Image credit: B. Horvath, S. Mundi, 2018
Particle accelerators can become crucial actors of the
4th industrial revolution
allowing industry and medicine to exploit technologies based on the usage of subatomic particles

## Slide 35: The final words…
Particle accelerators are a vibrant and growing field, in full transition from basic science to applied science and to wider societal applications.
But to drive this transition and to push further the frontiers of accelerators we need fresh ideas, technology jumps, and (why not!), some change in paradigm.
The secret for the success are novel ideas by young people developed in a collaborative environment, jumping across borders between different scientific fields.
To achieve this we need multinational research programmes with wide support from governments and scientific communities, but above all…
Thank you for your attention! maurizio.vretenar@cern.ch