## Slide 1
David Alesini
(INFN-LNF, Frascati, Rome, Italy)
Linacs

## Slide 2
LINAC APPLICATIONS
Injectors for synchrotrons
Medical applications: radiotherapy
Industrial applications
National security
Material treatment
Ion implantation
Material/food sterilization
Free Electron Lasers
Spallation sources for neutron production
Material testing for fusion nuclear reactors
Nuclear waste treatment and controlled fission for energy production (ADS)
104 LINACs operating around the world

## Slide 3
LINAC: BASIC DEFINITION AND MAIN COMPONENTS
LINAC (linear accelerator) is a system that allows to accelerate charged particles through a linear trajectory by electromagnetic fields.
Particle source
Accelerated beam
Accelerating structures
Focusing elements: quadrupoles and solenoids
Transverse dynamics of accelerated particles
Longitudinal dynamics of accelerated particles
LINAC BEAM DYNAMICS
LINAC COMPONENTS AND TECHNOLOGY
1st PART OF THE LECTURE
2nd PART OF THE LECTURE

## Slide 4
LINAC TECHNOLOGY
The overall LINAC has to be designed to obtain the desired beam parameters in term of:
-output energy/energy spread
-beam current (charge)
-long. and transverse beam dimensions/divergence (emittance)
…
Having, in general, constraints in term of:
-space
-cost
-power consumption
-available power sources
…

## Slide 5
LINAC: BASIC DEFINITION AND MAIN COMPONENTS
LINAC (linear accelerator) is a system that allows to accelerate charged particles through a linear trajectory by electromagnetic fields.
Particle source
Accelerated beam
Accelerating structures
Focusing elements: quadrupoles and solenoids
Transverse dynamics of accelerated particles
Longitudinal dynamics of accelerated particles
LINAC BEAM DYNAMICS
LINAC COMPONENTS AND TECHNOLOGY

## Slide 6
ACCELERATION
BENDING AND FOCUSING
Transverse Dynamics
Longitudinal Dynamics
LORENTZ FORCE: ACCELERATION AND FOCUSING
The basic equation that describes the acceleration/bending/focusing processes is the Lorentz Force.
Particles are accelerated through electric fields and are bended and focused through magnetic fields.
To accelerate, we need a force in the direction of motion
2nd term always perpendicular to motion => no energy gain

## Slide 7
The first historical linear particle accelerator was built by the Nobel prize Wilhelm Conrad Röntgen (1900). It consisted in a vacuum tube containing a cathode connected to the negative pole of a DC voltage generator. Electrons emitted by the heated cathode were accelerated while flowing to another electrode connected to the positive generator pole (anode). Collisions between the energetic electrons and the anode produced X-rays.
The energy gained by the electrons travelling from the cathode to the anode is equal to their charge multiplied the DC voltage between the two electrodes.
ACCELERATION: SIMPLE CASE
+
Electric field
Voltage V
Cathode
Anode
Particle energies are typically expressed in electron-volt [eV], equal to the energy gained by 1 electron accelerated through an electrostatic potential of 1 volt:
1 eV=1.6x10-19 J

## Slide 8
PARTICLE VELOCITY VS ENERGY: LIGHT AND HEAVY PARTICLES
Light particles (as electrons) are practically fully relativistic (1, >>1) at relatively low energy and reach a constant velocity (c). The acceleration process occurs at constant particle velocity
Heavy particles (protons and ions) are typically weakly relativistic and reach a constant velocity only at very high energy. The velocity changes a lot during the acceleration process.
rest mass m0
rest energy E0 (=m0c2)
total energy E
relativistic mass m
velocity v
momentum p (=mv)
Kinetic energy W=E-E0
Relativistic factor =v/c (<1)
Relativistic factor =E/E0 (1)
Single particle
This implies important differences in the technical characteristics of the accelerating structures. In particular for protons and ions we need different types of accelerating structures, optimized for different velocities and/or the accelerating structure has to vary its geometry to take into account the velocity variation.
+
Heavy particles
Light particles
Kin. Energy [MeV]
e-
p+
1


## Slide 9
PARTICLE ACCELERATION: ELECTRIC FIELD
Particles are accelerated through electric fields
1 V
109-1010 V
100-200 V
E
Incandescent filament
cathode
anode
Vacuum chamber
Electron beam
1000 V
Energy gain V
105 V

## Slide 10
To increase the achievable maximum energy, Van de Graaff invented an electrostatic generator based on a dielectric belt transporting positive charges to an isolated electrode hosting an ion source. The positive ions generated in a large positive potential were accelerated toward ground by the static electric field.
DC voltage as large as 10 MV can be obtained (E10 MeV). The main limit in the achievable voltage is the breakdown due to insulation problems.
APPLICATIONS OF DC ACCELERATORS
ELECTROSTATIC ACCELERATORS
750 kV Cockcroft-Walton
Linac2 injector at CERN from 1978 to 1992
LIMITS OF ELECTROSTATIC ACCELERATORS
DC particle accelerators are in operation worldwide, typically at V<15MV (Emax=15 MeV), I<100mA.
They are used for:
 material analysis
 X-ray production,
 ion implantation for semiconductors
 first stage of acceleration (particle sources)

## Slide 11
RF Accelerators : Wideröe “Drift Tube LINAC” (DTL)
Basic idea: the particles are accelerated by the electric field in the gap between electrodes connected alternatively to the poles of an AC generator. This original idea of Ising (1924) was implemented by Wideroe (1927) who applied a sine-wave voltage to a sequence of drift tubes. The particles do not experience any force while travelling inside the tubes (equipotential regions) and are accelerated across the gaps. This kind of structure is called Drift Tube LINAC (DTL).
L1
Ln
(protons and ions)
If the length of the tubes (or, equivalently, the distances between the centers of the accelerating gaps) increases with the particle velocity during the acceleration such that the time of flight between gaps is kept constant and equal to half of the RF period, the particles are subject to a synchronous accelerating voltage and experience an energy gain of ∆E=q∆V at each gap crossing.
In principle a single RF generator can be used to indefinitely accelerate a beam, avoiding the breakdown limitation affecting the electrostatic accelerators.
The Wideroe LINAC is the first RF LINAC

## Slide 12
DC ACCELERATION: ENERGY GAIN
We consider the acceleration between two electrodes in DC.
Ez
source
rate of energy gain per unit length
z (direction of acceleration)
energy gain per electrode pair
DV
+
-
z
Ez
gap
t
E
W=E-E0
Energy-momentum relation
Lorentz force

## Slide 13
We consider now the acceleration between two electrodes fed by an RF generator
Ez
source
z
z
gap
RF ACCELERATION: BUNCHED BEAM
tinj
E
Only these particles are accelerated
These particles are not accelerated and basically are lost during the acceleration process
t
charge
DC acceleration
t
charge
RF acceleration
Bunched beam (in order to be synchronous with the external AC field, particles have to be gathered in non-uniform temporal structure)
RF period

## Slide 14
We consider now the acceleration between two electrodes fed by an RF generator
Ez
source
z
z
gap
RF ACCELERATION: ENERGY GAIN
-L/2
+L/2
Hyp. of symmetric accelerating field
Peak gap voltage
T<1
Transit time factor
Injection phase
Average accelerating field in the gap
Average accelerating field seen by the particle
t=z/v

## Slide 15
Derive the general expression of the transit time factor of an accelerating gap of length L, with constant accelerating field, in which the field is oscillating at fRF and that accelerate particles with relativistic factor β.
Remembering that the light wavelength in free space is given by RF=c/fRF, for which value of the accelerating gap length L, T is equal to zero?
Calculate the numerical value of T for L=10 cm, fRF=1 GHz and ultra-relativistic electrons (β=1).
Calculate the accelerating voltage as a function of the gap length L assuming an injection phase on crest (inj=0)
EXERCISE 1: TRANSIT TIME FACTOR

## Slide 16
DRIFT TUBE LENGTH AND FIELD Synchronization
+
-
Ez
z
vn
Ln
Ln+1
Ln+2
+
-
Ez
z
Ln
Ln+1
Ln+2
vn+1
If now we consider a DTL structure, we have that at each gap the maximum energy gain is En=qVacc and the particle increase its velocity accordingly to the previous relativistic formulae. It is convenient to refer to the center of each gap as follows:
z
E
En
qVacc
z
v
vn
 In order to be synchronous with the accelerating field at the center of each gap, the distance between the centers of the gaps (Ln) has to be increased as:
The energy gain per unit length (i.e. the average accelerating gradient times q) is given by:
[eV/m]
(protons and ions or electrons at extremely low energy)
En+1
vn+1
Gap n
Gap n+1
=average particle velocity between the gap n and n+1

## Slide 17
ACCELERATION WITH HIGH rf FREQUENCIES: RF CAVITIES
There are two important consequences of the previous obtained formulae:
The condition Ln<<RF (necessary to model the tube as an equipotential region) requires <<1. The Wideröe technique can not be applied to relativistic particles.
Moreover when particles get high velocities the drift spaces get longer and one looses on the efficiency. The average accelerating gradient (Eacc [V/m]) increase pushes towards small RF (high frequencies).
High frequency, high power sources became available after the 2nd world war pushed by military technology needs (such as radar). Moreover, the concept of equipotential DT can not be applied at small RF and the power lost by radiation is proportional to the RF frequency.
As a consequence we must consider accelerating structures different from drift tubes.
The solution consists of enclosing the system in a cavity which resonant frequency matches the RF generator frequency.
Each cavity can be independently powered from the RF generator
waveguide
Ez
Ez

## Slide 18
RF CAVITIES
High frequency RF accelerating fields are confined in cavities.
The cavities are metallic closed volumes were the e.m fields has a particular spatial configuration (resonant modes) whose components, including the accelerating field Ez, oscillate at some specific frequencies fRF (resonant frequency) characteristic of the mode.
The modes are excited by RF generators that are coupled to the cavities through waveguides, coaxial cables, etc…
The resonant modes are called Standing Wave (SW) modes (spatial fixed configuration, oscillating in time).
The spatial and temporal field profiles in a cavity have to be computed (analytically or numerically) by solving the Maxwell equations with the proper boundary conditions.
B
E
Courtesy E. Jensen

## Slide 19
Alvarez's structure can be described as a special DTL in which the electrodes are part of a resonant macrostructure.
ALVAREZ STRUCTURES
The DTL operates in 0 mode for protons and ions in the range =0.05-0.5 (fRF=50-400 MHz, RF=6-0.7 m) 1-100 MeV;
The beam is inside the “drift tubes” when the electric field is decelerating. The electric field is concentrated between gaps;
The drift tubes are suspended by stems;
Quadrupole (for transverse focusing) can fit inside the drift tubes.
In order to be synchronous with the accelerating field at each gap the length of the n-th drift tube Ln has to be:
Ez
z
© Encyclopaedia Britannica, inc
(protons and ions)

## Slide 21
ALVAREZ STRUCTURES: EXAMPLES
CERN LINAC 2 tank 1:
200 MHz 7 m x 3 tanks, 1 m diameter, final energy 50 MeV.
CERN LINAC 4: 352 MHz frequency, Tank diameter 500 mm, 3 resonators (tanks), Length 19 m, 120 Drift Tubes, Energy: 3 MeV to 50 MeV, =0.08 to 0.31  cell length from 68mm to 264mm.

## Slide 22
A proton beam is injected into a DTL (Alvarez structure) working at fRF=300 MHz, with a kinetic energy Win=4 MeV. Calculate:
the distance between the first two centers of the accelerating gaps (Lgaps) assuming a constant velocity of the proton beam between the first two gaps and a negligible increase of the velocity due to the accelerating field;
if the structure is composed by 40 accelerating gaps (Ngaps) and the average accelerating voltage per gap is Vacc=0.5 MV, calculate final proton beam kinetic energy.
EXERCISE 2: ALVAREZ STRUCTURES
REMEMBER
proton rest energy m0_pc2=E0_p=938 MeV
velocity of light c=2.998e8

## Slide 23
EXERCISE 3: ALVAREZ STRUCTURES AND TRANSIT TIME FACTOR
Particles at β=0.5 are accelerated through an ideal DTL operating at fRF=400 MHz. Assuming a uniform accelerating RF field (ERF) along the gap, calculate the accelerating gap length (L) that maximize the energy gain of the accelerated particles.

## Slide 24
HIGH  cavities: CYLINDRICAL STRUCTURES
When the  of the particles increases (>0.5) one has to use higher RF frequencies (>400-500 MHz) to increase the accelerating gradient per unit length
the DTL structures became less efficient (effective accelerating voltage per unit length for a given RF power);
Cylindrical single (or multiple cavities) working on the TM010-like mode are used
H
E
For a pure cylindrical structure (also called pillbox cavity) the first accelerating mode (i.e. with non zero longitudinal electric field on axis) is the TM010 mode. It has a well known analytical solution from Maxwell equation.
Real cylindrical cavity
(TM010-like mode because of the shape and presence of beam tubes and couplers)
(electrons or protons and ions at high energy)

## Slide 25
SW CAVITIES PARAMETERS: Vacc, Pdiss, W
We suppose that the cavities are powered at a constant frequency fRF. The maximum energy gain of a particle crossing the cavity at a velocity v (c for electrons) is obtained integrating the time-varying accelerating field sampled by the particle along the trajectory:
To compare and qualify different cavities is necessary to define some parameter that characterize each accelerating structure.
Real cavities have losses.
Surface currents (related to the surface magnetic field ) “sees” a surface resistance and dissipate energy, so that a certain amount of RF power must be provided from the outside to keep the accelerating field at the desired level. The total dissipated power is:
ACCELERATING VOLTAGE
DISSIPATED POWER
STORED ENERGY
The total e.m. energy stored in the cavity:
MODE TM010
  NC cavity (Cu at 1 GHz)
  SC cavity (Nb at 1 GHz)
B
E
Ez
z
E field lines
More general form

## Slide 26
QUALITY FACTOR
SHUNT IMPEDANCE
The shunt impedance is the parameter that qualifies the efficiency of an accelerating mode. The highest is its value, the larger is the obtainable accelerating voltage for a given power. Traditionally, it is the quantity to optimize in order to maximize the accelerating field for a given dissipated power:
ACCELERATING VOLTAGE (Vacc)
DISSIPATED POWER (Pdiss)
STORED ENERGY (W)
  NC cavity Q104
  SC cavity Q1010
The R/Q is a pure geometric qualification factor. It does not depend on the cavity wall conductivity. R/Q of a single cell is of the order of 100.
  NC cavity R1M
SW CAVITIES PARAMETERS: R, Q, R/Q
  SC cavity R1T
SHUNT IMPEDANCE PER UNIT LENGTH
Example:
  R1M
Pdiss=1 MW
Vacc=1MV
For a cavity working at 1 GHz with a structure length of 10 cm we have an average accelerating field of 10 MV/m

## Slide 27
The previous quantities plays crucial roles in the evaluation of the cavity performances. Let us consider the case of a cavity powered by a source (klystron) at a constant frequency in CW and at a fixed power (Pin).
SW CAVITIES : EQUIVALENT CIRCUIT AND BANDWIDTH
Pin=1 MW
R/Q=100
Critical coupling (Pdiss=Pin)
fres=1 GHz
Frequency domain
BANDWIDTH
Pin
Modulator and klystron
waveguide
cavity
The reachable Vacc for a given power is proportional to Q
L
R/2
C
Ig
1:n
Z0
in
High power transfer line
Matched source
coupler
cavity
Z0
Vacc

## Slide 28
SW CAVITIES : FILLING TIME AND DISSIPATED POWER
Time domain
FILLING TIME
Prefl to the generator (it that has to be protected!)
Pdiss 1/Q
One needs several filling times to completely fill the cavity
Let us now consider the case of a cavity powered by a source (klystron) in pulsed mode at a frequency fRF=fres. The accelerating voltage has an exponential behavior and reach the steady state regime asymptotically with a certain filling time (F) that is proportional to the quality factor of the resonator.
The reachable Vacc for a given power is proportional to Q but, on the other hand, the filling time is Q
[MV]
Example:
  Q10000
fRF=1 GHz
F=3.1 s
To reach a given voltage the required power is inversely proportional to the Q-factor

## Slide 29
A SW cavity is feed by an RF generator with constant power, calculate after how much time the field in the cavity is 90% the field at full regime supposing that the cavity operate at fRF=1.3 GHz and has an equivalent Q factor of 10000.
EXERCISE 4: FILLING TIME

## Slide 30
MULTI-CELL SW CAVITIES
R
nR
In a multi-cell structure there is one RF input coupler. As a consequence the total number of RF sources is reduced, with a simplification of the layout and reduction of the costs;
The shunt impedance is n time the impedance of a single cavity
They are more complicated to fabricate than single cell cavities;
The fields of adjacent cells couple through the cell irises and/or through properly designed coupling slots.
Pin
.
Pin
(electrons or protons and ions at high energy)

## Slide 31
MULTI-CELL SW CAVITIES:  MODE STRUCTURES
The N-cell structure behaves like a system composed by N coupled oscillators with N coupled multi-cell resonant modes.
The modes are characterized by a cell-to-cell phase advance given by:
.
The multi cell mode generally used for acceleration is the , /2 and 0 mode (DTL as example operate in the 0 mode).
The cell lengths have to be chosen in order to synchronize the accelerating field with the particle traveling into the structure at a certain velocity
Ez
z
Ez
z
0 mode
 mode
For ions and protons the cell lengths have to be increased along the linac that will be a sequence of different accelerating structures matched to the ion/proton velocity.
For electron, =1, d=RF/2 and the linac will be made of an injector followed by a series of identical accelerating structures, with cells all the same length.
(electrons or protons and ions at high energy)
EXAMPLE: 4 cell cavity operating on the -mode

## Slide 32
 MODE STRUCTURES: EXAMPLES
LINAC 4 (CERN) PIMS (PI Mode Structure) for protons: fRF=352 MHz, >0.4
Each module has 7 identical cells
100 MeV
160 MeV
1.28 m
1.55 m
12 tanks
European XFEL (Desy): electrons
All identical =1
Superconducting cavities

## Slide 33
A -mode structure, operating at fRF=400 MHz, is made up of N=8 cells and is used to accelerate protons. Each single cell has a shunt impedance R=3 M and a length Lcell=15 cm. Calculate:
the total shunt impedance of the -mode structure;
the accelerating voltage if the total dissipated power into the cavity is Pdiss=1 MW;
the average accelerating field;
the average  of the proton beam accelerated by this structure.
EXERCISE 5:  MODE STRUCTURES

## Slide 34
MULTI-CELL SW CAVITIES: /2 MODE STRUCTURES
It is possible to demonstrate that over a certain number of cavities (>10) working on the  mode, the overlap between adjacent modes can be a problem (as example the field uniformity due to machining errors is difficult to tune).
The criticality of a working mode depend on the frequency separation between the working mode and the adjacent mode
the /2 mode from this point of view is the most stable mode. For this mode it is possible to demonstrate that the accelerating field is zero every two cells. For this reason, the empty cells are put of axis and coupling slots are opened from the accelerating cells to the empty cells.
this allow to increase the number of cells to >20-30 without problems
 mode
0 mode
fres
fres_
/2 mode
fres_/2
z
Ez
Side Coupled Cavity (SCC)
fRF=800 - 3000 MHz for proton (=0.5-1) and electrons
Phase advance per cell
(electrons or protons and ions at high energy)
Dispersion curve
Multi cell cavity modes
Axial coupled

## Slide 35
SCC STRUCTURES: EXAMPLES
Spallation Neutron Source Coupled Cavity Linac (protons)
4 modules, each containing 12 accelerator segments CCL and 11 bridge couplers. The CCL section is a RF Linac, operating at 805 MHz that accelerates the beam from 87 to 186 MeV and has a physical installed length of slightly over 55 meters.
segment
Accelerating cell
Coupling cell

## Slide 36
TRAVELLING WAVE (TW) STRUCTURES
To accelerate charged particles, the electromagnetic field must have an electric field along the direction of propagation of the particle.
The field has to be synchronous with the particle velocity.
Up to now we have analyzed the standing standing wave (SW) structures in which the field has basically a given profile and oscillate in time (as example in DTL or resonant cavities operating on the TM010-like).
Ez
z
Direction of propagation
Ez
z
P RF in
P RF in
P RF out
P RF TW
There is another possibility to accelerate particles: using a travelling wave (TW) structure in which the RF wave is co-propagating with the beam with a phase velocity equal to the beam velocity.
Typically these structures are used for electrons because in this case the phase velocity can be constant all over the structure and equal to c. On the other hand it is difficult to modulate the phase velocity itself very quickly for a low  particle that changes its velocity during acceleration.
field profile
Time oscillation
(electrons)

## Slide 37
TW CAVITIES: CIRCULAR WAVEGUIDE AND DISPERSION CURVE
In TW structures an e.m. wave with Ez0 travel together with the beam in a special guide in which the phase velocity of the wave matches the particle velocity (v). In this case the beam absorbs energy from the wave and it is continuously accelerated.
As example if we consider a simple circular waveguide the first propagating mode with Ez0 is the TM01 mode.
Nevertheless by solving the wave equation it turns out that an e.m. wave propagating in this constant cross section waveguide will never be synchronous with a particle beam since the phase velocity is always larger than the speed of light c.
(propagation constant)
=2f (f=RF generator frequency)
k*
CIRCULAR WAVEGUIDE
RF
tan()=vph
k2*
RF_2
Dispersion curve
Ez
z
cut-off
(electrons)
k

## Slide 38
In order to slow-down the wave phase velocity, iris-loaded periodic structure have to be used.
MODE TM01
MODE TM01-like
IRIS LOADED STRUCTURE
Periodic (in z) wih period D (from Floquet theorem)
TW CAVITIES: IRIS LOADED STRUCTURES
CIRCULAR WAVEGUIDE
The field in this type of structures is that of a special wave travelling within a spatial periodic profile.
The structure can be designed to have the phase velocity equal to the speed of the particles.
This allows acceleration over large distances (few meters, hundred of cells) with just an input coupler and a relatively simple geometry.
RF
k*
k
/D

(electrons)
D
Beam direction
Metal irises
They are used especially for electrons (constant particle velocityconstant phase velocity, same distance between irises, easy realization)

## Slide 39
PHASOR NOTATION: RECAP.
Phasor of the longitudinal electric field (complex quantity)
With a more general notation we can consider the phasors of the accelerating field.
Peak accelerating voltage
(i.e.: the maximum accelerating voltage that can be reached for a particular injection phase (=0))

## Slide 40
TW CAVITIES PARAMETERS: r, , vg
Similarly to the SW cavities it is possible to define some figure of merit for the TW structures
Group velocity [m/s]: the velocity of the energy flow in the structure (1-2% of c).
Shunt impedance per unit length [/m]. Similarly to SW structures the higher is r, the higher the available accelerating field for a given RF power.
Field attenuation constant [1/m]: because of the wall dissipation, the RF power flux and the accelerating field decrease along the structure.
Working mode [rad]: defined as the phase advance over a period D. For several reasons the most common mode is the 2/3

## Slide 41
TW CAVITIES: EQUIVALENT CIRCUIT AND FILLING TIME
In a TW structure, the RF power enters into the cavity through an input coupler, flows (travels) through the cavity in the same direction as the beam and an output coupler at the end of the structure is connected to a matched power load.
If there is no beam, the input power, reduced by the cavity losses, goes to the power load where it is dissipated.
In the presence of a large beam current, however, a fraction of the TW power is transferred to the beam.
In a purely periodic structure, made by a sequence of identical cells (also called “constant impedance structure”),  does not depend on z and both the RF power flux and the intensity of the accelerating field decay exponentially along the structure :
The filling time is the time necessary to propagate the RF wave-front from the input to the end of the section of length L is:
L
Differently from SW cavities after one filling time the cavity is completely full of energy

## Slide 42
Exercise 6: TW STRUCTURES
B) Demonstrate that if we define the shunt impedance per unit length as:
the average accelerating field “seen” by an ultrarelativistic particle (z=ct) along the structure can be expressed as:
A) Demonstrate that if we define the attenuation constant as:
the power flow along the structure scales as:
C) Demonstrate that the total accelerating voltage is given by:

## Slide 43
A SLAC-type TW structure accelerate ultra-relativistic electrons. The structure length is L=3m and it can be simplified as a structure with a group velocity is vg=1.1% the velocity of light. Calculate:
the filling time;
if we suppose that the structure has a field attenuation constant =0.2 m-1, calculate the total accelerating voltage if the accelerating field at the beginning of the structure is EINPUT=20 MV/m;
Calculate the average accelerating field
if the average dissipated power per unit length in the structure, corresponding to the previous value of the accelerating field, is pdiss= 20 MW/m calculate the shunt impedance per unit length.
Exercise 7: TW STRUCTURES

## Slide 44
A constant impedance TW structure, accelerates ultra-relativistic electrons (β=1). The cavity has the following parameters: =0.25 m-1 ; shunt impedance r=65 MOhm/m and a total length of 2 m. Calculate:
the input power to have an energy gain of the particles of 60 MeV
if the group velocity vg is 1% the speed of light, which is the filling time of the structure?
Exercise 8: TW STRUCTURES

## Slide 45
TW CAVITIES: PERFORMANCES (1/2)
Just as an example we can consider a C-band (5.712 GHz) accelerating cavity of L=2 m long made in copper.
r=82 [M/m]
=0.36 [1/m]
vg/c=1.7%
F=400 ns (very short if compared to SW!)
Output power (dissipated into the RF load): it is not convenient to have very long RF structures because their efficiency decreases over a certain length (2-3 m depending on the operating frequency).
Input power
Field attenuation due to the copper dissipations
F

## Slide 46
TW CAVITIES: CONSTANT GRADIENT STRUCTURES INTRODUCTION
In order to keep the accelerating field constant along the LINAC structure, the group velocity has to be reduced along the structure itself. This can be achieved by a reduction of the iris diameters.
In general constant gradient structures are more efficient than constant impedance ones, because of the more uniform distribution of the RF power along them.
Reduction due to the attenuation (losses)
Reduction due to irises modulation
Constant along the linac

## Slide 47
LINAC TECHNOLOGY: MATERIALS

## Slide 48
The cavities (and the related LINAC technology) can be of different material:
copper for normal conducting (NC, both SW than TW) cavities;
Niobium for superconducting cavities (SC, SW);
We can choose between NC or the SC technology depending on the required performances in term of:
accelerating gradient (MV/m);
RF pulse length (how many bunches we can contemporary accelerate);
Duty cycle (see next slide): pulsed operation (i.e. 10-100 Hz) or continuous wave (CW) operation;
Average beam current.
…
ACCELERATING CAVITY TECHNOLOGY
Dissipated power into the cavity walls is related to the surface currents
Frequency [GHz]
NIOBIUM
Between copper and Niobium there is a factor 105-106
COPPER

## Slide 49
RF STRUCTURE AND BEAM STRUCTURE: NC vs SC
The “beam structure” in a LINAC is directly related to the “RF structure”. There are two possible type of operations:
CW (Continuous Wave) operation  allow, in principle, to operate with a continuous (bunched) beam
PULSED operation  there are RF pulses at a certain repetition rate (Duty Cycle (DC)=pulsed width/period)
SC structures allow operation at very high Duty Cycle (>1%) up to a CW operation (DC=100%) (because of the extremely low dissipated power) with relatively high gradient (>20 MV/m). This means that a continuous (bunched) beam can be accelerated.
NC structures can operate in pulsed mode at very low DC (10-2-10-1 %) (because of the higher dissipated power) with, in principle, larger peak accelerating gradient(>30 MV/m). This means that one or few tens of bunches can be, in general, accelerated. NB: NC structures can also operate in CW but at very low gradient because of the dissipated power.
Bunch spacing
RF pulses
RF power
t
Amplitude
103-108 RF periods
time

## Slide 50
A multi cell SW cavity, operating on the -mode at 1 GHz, accelerates protons at β=0.5. The cavity is a 9 cell structure. Assuming a negligible variation of the particle velocity through the cavity itself calculate:
the distance between the centers of the accelerating cells;
assuming a shunt impedance of the single cell (R) of 1 M, calculate the dissipated power to have an effective accelerating voltage on the overall structure of Vacc=10 MV;
Calculate the average accelerating field;
If the cavity is fed by 4 s rf pulses with a repetition rate of 100 Hz, calculate the Duty Cycle.
EXERCISE 9:  MODE STRUCTURES AND DUTY CYCLE

## Slide 51
EXAMPLE: SWISSFEL LINAC (PSI)

## Slide 52
EXAMPLES: EUROPEAN XFEL