## Slide 1
BCCM: commissioning experience and status
230th Machine Protection Panel Meeting, 21/10/22
Marek Gasior, Tom Levens
SY-BI-IQ

## Slide 2
BCCM (dI/dt) system
NRLP – Non-Reflective Low-Pass (≈ 80 MHz)
RFA – RF Amplifier
ED – Envelope Detector
ALP – Active Low-Pass (≈ 2 MHz)
shared BPMs:
system A: BPMYA.5R4.B1+B2 system B: BPMYA.6R4.B1+B2
The system is based on BPM signals shared with the LHC beam position measurement system (passive RF splitters)
The beam position dependence is removed by summing the four electrode signals
Analog operations on the signals: low-pass filtering, amplification, envelope detection + rectification + level shifting, low pass filtering
Digitization: 16-bit, 40 MHz sampling synchronous to the circulating beam (one revolution period is exactly 3564 ADC clocks). The 40 MHz ADC B1 and B2 clocks are derived from the 400 MHz RF frequencies received by optical fibers from the RF system.
One turn “raw intensity” is a sum of ADC samples above a “beam presence threshold” minus “no beam offset”, selected from one turn 3564 samples
One turn “raw dI/dt signal” is a difference of the one turn raw integrals from two consecutive turns
“Raw dl/dt signals” in the five other integration windows are calculated as running sums of the one-turn “raw dI/dt signals”
Every turn each of the “raw dI/dt signals” are compared to its corresponding raw dump threshold level and potential beam dump triggers are generated. All real-time calculations are done in the FPGA in an integer arithmetic.
The BCCM absolute intensities in elementary charges are calculated by scaling the “raw intensities” using a “BCCM/BCT scaling factor”. The factor is a constant for each system and is obtained by matching the beam intensity evaluated by the BCCM to the corresponding BCT readings.
The absolute dump thresholds in elementary charges are translated into “raw dump thresholds” using the same “BCCM/BCT scaling factor”.

## Slide 3
BCCM (dI/dt) system
rack BY05.UA47
https://ibic2022.vrws.de/papers/wep06.pdf

## Slide 4
Dump threshold tables
Window [turn] | 1 | 4 | 16 | 64 | 225 | 1125
 0.5 | 6 | 6 | 6 | 6 | 6 | 6
 0.5 | 3 | 3 | 3 | 3 | 2 | 0.5
Energy [TeV] | Losses [1e11] |  |  |  |  | 
Window [turn] | 1 | 4 | 16 | 64 | 225 | 1125
 0.5 | 1 | 1 | 1 | 1 | 1 | 1
 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.3 | 0.08
Energy [TeV] | Relative losses [‰] (FS = 6e14) |  |  |  |  | 
Window [turn] | 1 | 4 | 16 | 64 | 225 | 1125
 0.5 | 6 | 6 | 6 | 6 | 6 | 10
 0.5 | 3 | 3 | 3 | 3 | 5 | 10
Energy [TeV] | Losses [1e11] |  |  |  |  | 
Window [turn] | 1 | 4 | 16 | 64 | 225 | 1125
 0.5 | 1 | 1 | 1 | 1 | 1 | 1.7
 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.8 | 1.7
Energy [TeV] | Relative losses [‰] (FS = 6e14) |  |  |  |  | 
OLD
NEW

## Slide 5
BCCM (– dI/dt) polarity convention
dI/dt positive = intensity decrease (here the beam dump)
dI/dt negative = intensity increase (here beam injections)
The focus is on beam losses, so that on the positive “– dI/dt” signals

## Slide 6
BCCM operation – absolute intensity measurement

## Slide 7
BCCM operation – perturbations during the ramp

## Slide 8
BCCM operation – perturbations during the ramp

## Slide 9
RF longitudinal blow-up: missing on B1, present on B2

## Slide 10
RF longitudinal blow-up: missing on B1, present on B2

## Slide 11
Injection longitudinal oscillations

## Slide 12
Optimization of the integration window length
Two longest integration windows set for tests to 420 and 840 turns since 15/08
Observed some 30 % reduction of the spurious beam loss maxima during the RF longitudinal blow-up

## Slide 13
1st order low pass compensation
BCCM A.B1 with the compensation
BCCM B.B1 with no compensation
The BPMs used by the BCCM are high-pass systems with the cut-off ≈ 200 MHz (16 pF + 50 Ω)
Their frequency characteristic was flattened by a 1st order low-pass (≈ 12 MHz) at the expense of 80 % signal loss. Ongoing tests of the low-pass on systems A and comparing to systems B without the compensation (since 28/09).
The low-pass is sometimes very effective
Some issues with the “stability of the signal baseline”
20e11

## Slide 14
1st order low pass compensation
BCCM B.B1 with no compensation
BCCM A.B1 with the compensation
FBCT B1

## Slide 15
1st order low pass compensation
25e11

## Slide 16
1st order low pass compensation
BCCM A.B1 with the compensation
BCCM A.B2 with the compensation
BCCM B.B1 with no compensation
BCCM B.B2 with no compensation
3e11
3e11

## Slide 17
Conclusions and options to investigate
During the 2022 run the four BCCM systems have been evolving quite a bit and have been continuously tested with beam
The hardware and FESA are “almost final” and very reliable
Operational extensive data logging implemented, including continuous turn-by-turn logging of the most important data and on-demand 73-turn snapshots of the 40 MHz raw ADC samples (currently stored also every beam dump)
The residual bunch length dependence of the BPM signals is the only known problem with the current implementation of the system. The problem shows up during beam injections, the RF longitudinal blow-up and beam instabilities.
The new dump threshold levels for the two longest integration windows help a lot to fulfil all the system specifications
New lengths of the two longest integration windows are being tested. Still to be decided whether they are helping enough.
A 1st order low-pass filter compensating the 1st order high-pass characteristic of the BPM reduces the bunch length dependence. Unfortunately, the low-pass causes issues with the “stability of the signal baseline”.
Options to investigate:
A less aggressive 1st order low-pass, with the hope to improve the “stability of the signal baseline”
FBCTs with the flat frequency characteristic as the beam signal source

## Slide 18
Spare slides

## Slide 19
25 ns data: BCCM vs FBCT
one turn of BCCM data
one turn of FBCT data