## Slide 1
MKI-Cool RF Damper Cooling:
Interlock Strategy
M.J. Barnes
Acknowledgements
C. Baud, G. Bellotto, C. Bracco, C. Boucly, O. Crespo-Lopez,
L. Ducimetière, Y. Dutheil, T. Gharsa, L. Govertsen, C. Lolliot, N. Magnin, V. Namora, T. Stadlbauer, P. Trubacova

## Slide 2: Beam Induced Heating - Reminder
Alumina tube
(installed in MKI aperture)
MKI magnet
Vacuum tank
Injected/
circulating beam
To reduce beam induced heating, MKIs refurbished during LS1 have 24 screen conductors (c.f. 15 before LS1), inserted in slots on the inside of an alumina tube
An alumina tube is installed in the aperture of each MKI kicker magnet
A set of ferrite rings is installed on each end of the alumina tube
Slots on alumina tube, to insert screen conductors
Beam
Alumina tube
24 screen conductors (one each 15 degrees, since LS1)
Ferrite rings
Alumina tube
Highly non-linear beam induced power deposition in the ferrite yoke of an MKI
With HL-LHC type beams, the RF damper and part of the ferrite yoke would reach its Curie temperature (temporary loss of magnetic properties)

## Slide 3: MKI8D: upgraded MKI
Redesigned ferromagnetic rings (damper), on the upstream end of the alumina tube, outside of the magnet aperture, relocates beam induced power from the ferrite yoke to the damper
RF damper is not at pulsed high voltage
Reduced yoke temperature w.r.t. LS1 MKI’s – but still need to further reduce temperatures for HL-LHC type beams
Upgraded MKI installed, in Point 8, during YETS 2017/18 (MKI8D):
Damper
(some ferrite rings exposed to beam)
Magnet
Beam
Screen conductors
Alumina tube
Conductive sleeve
Metallic cylinder

## Slide 4
RF damping element
(CMD10 ferrite cylinder: Curie temperature of ~250˚C)
Beam
Screen conductors
Alumina tube
Pipes for water cooling
PT100 location
(Tube_Up)
RF Damper of MKI-Cool
MKI cool = RF damping element + water cooling
MKI-Cool is expected to be significantly below the ferrites Curie temperature for HL-LHC type beams.

## Slide 5
Eletta flow monitor (with direct reading dial): with independently adjustable upper and lower flow alarm (µ-switches):
Status of low-flow micro-switch (dry contact) to be readback by SY-ABT
Status of high-flow monitor micro-switch to be readback by SY-ABT
2*PT100 on cooling pipes (outside MKI vacuum tank)
PT100 on RF damper (previous slide)
‘Turbine’ (analogue signal) to be installed to readback analogue signal α flow-rate (radiation resistant)
MKI-Cool cooling circuit
PT100
Existing water pipes
Pipes to be installed
Flow monitor (S25GSS15 A/R 0.4-2 l/min Eau EPDM)
Manual valve
Beam
MKI8D
Flow: ~1.5 m/s ( ~1.5 l/min)
Heat exchanger
(Demineralized water)
MKI8C
MKI8B
MKI8A
~4 bar
≤16 bar
Pressure regulator
200µm strainer
Needle valve to reduce pressure

## Slide 6
Interlocks:
The low-flow micro-switch (dry contact), from the Eletta flow-monitor, will be used as an interlock:
• Prevent injection if water flow is too low (use few s time-constant);
• Request a beam dump if water flow is to low (to prevent possible boiling of water in cooling pipe and resulting high pressure): use few s time-constant. The low-flow micro-switch will be cabled to an SY-ABT PLC for requesting a beam-dump to the BIS
The upper flow alarm will be used as a warning;
Request a beam dump if RF Damper Temperature (Tube_Up) exceeds X°C e.g. 50°C (~34°C max expected): use few s time-constant. This temperature interlock will be implemented in the ABT PLC (a Beam dump will be requested through the BIS). Since the temperature data will be in a FESA class, it is available, in the future, to also implement as an interlock in SIS.
Note: input and output water temperatures, water flow-rate, and PT100s within MKI vacuum tank to be logged (WinCC and NXCALS).
MKI-Cool Additional Interlocks (c.f. ‘regular’ MKIs)

## Slide 7: Thank you for your attention

## Slide 8
Backup Slides

## Slide 9
PT100 locations in MKIs
MKIs refurbished during LS1 have four PT100s under vacuum:
Magnet_Up and Magnet_Down (on side plates)
Tube_Up and Tube_Down (close to ferrite rings on alumina tube)
The MKI8D (MKIMA04-T09) and MKI Cool (MKIMA08-T11 -> MKI8C) have two additional PT100s installed under vacuum.
For MKI8D: measurements of only 4 PT100s could be readback/logged.
8 additional wires to UA are required for reading back of other 2 under vacuum PT100s.
Tube_Down on MKI8D
Magnet_Down on MKI8D
Alumina tube and screen conductors

## Slide 10
8 additional wires required to readback all PT100s under vacuum
8 additional wires required to readback both PT100s outside vacuum (cooling water temperature)
5 additional wires required to readback status of flow micro-switches
2 additional wires for readback of analogue flow-rate
MKI-Cool Readback

## Slide 12
Accepted with Warning by WENNINGER Jorg (BE-OP)
Ok - clearly an important component test
I am however surprised to discover a SIS interlock that was never discussed before with OP. As an interlock that is supposed to dump the beam after passing through many SW layers, there is a significant risk of false dumps due to controls issues. Such an interlock requires a lot of precautions in the implementation, in particular timeout periods that should typically be set to 20 seconds, possibly with fail-unsafe logic in case of signal absence. It is not clear from the document whether this is consistent with the requirements.
In reply to the comment from Jorg Wenninger:
Thanks for your comment.
A FESA class will be created to push the temperature data to NXCALS. Hence, the temperature interlock on the RF damper will be implemented in the ABT PLC and we will request a Beam dump from the PLC (through the BIS). In any case, this is a ¿secondary interlock¿ as the primary interlock is the water flow.
Since the temperature data is in the FESA class, it is available if, in the future, we want to implement the interlock in SIS.
In reply to Markus ZERLAUTH:
Thanks for your comments and corrections.
Impedance wise the foreseen 3-4 intensity steps should be sufficient to qualify the expected performance of the MKI cool. However, even though the alumina tube is coated internally with Cr2O3 (as per the MKI8D exchanged during YETS 2017/2018) dynamic vacuum could initially limit the intensity ramp up. Lotta METHER gave a summary of the MKI8D beam conditioning at the 29th SPS MPC (in the context of beam conditioning the low impedance MKP-L). Her presentation is here:
https://indico.cern.ch/event/1208316/contributions/5081442/attachments/2526205/4345060/SPS_MPC_20221011_SPS_scrubbing_2023.pdf
Comment from Impedance Working Group:
As already stated in the previous version of this document, the Impedance Working Group supports the installation of the MKI-COOL.
Transverse beam dynamics studies were performed by Nicolas Mounet and showed that the impact of the MKI-COOL on transverse stability is expected to be negligible (https://indico.cern.ch/event/881273/). This point and its reference should be added to the document in Chapter 5. Measurements of the transverse impedance were not performed on this modified MKI-COOL, but they will be performed on the next MKI-COOL to be modified in the upcoming weeks
Selected Comments on https://edms.cern.ch/document/2010448/1.1

## Slide 13: Cr2O3 coating in MKI8D, installed in YETS 2017/2018
Before YETS: Pressure in MKI8D interconnect used to be a factor of ∼3 (2012, 2015 and 2017) and ∼12 (2016) higher than that of Q5-MKI2D
After YETS: This factor is not observed anymore. No other vacuum modifications were done, so pressure reduction is attributed to Cr2O3 coating 👍
Alumina tube with Cr2O3 coating on the inside

## Slide 14: Expected conditioning of coated alumina tube
From: https://indico.cern.ch/event/1208316/contributions/5081442/attachments/2526205/4345060/SPS_MPC_20221011_SPS_scrubbing_2023.pdf
With current MKP-L, no evident conditioning after installation in 2014, nor after LS2
Cr2O3 coated alumina also used in MKI8D, installed in LHC during YETS 17/18
  Clear conditioning visible after installation in 2018
In MKI8D area scrubbing slowed down after ~30 kC of proton dose, with the dynamic pressure rise reduced by 2 orders of magnitude

## Slide 15
From: https://indico.cern.ch/event/1195594/contributions/5086753/attachments/2524482/4341538/MKICool-Conditioning_LIBD_11102022.pdf

## Slide 16
From: https://indico.cern.ch/event/1195594/contributions/5086753/attachments/2524482/4341538/MKICool-Conditioning_LIBD_11102022.pdf

## Slide 17
From: https://indico.cern.ch/event/1195594/contributions/5086753/attachments/2524482/4341538/MKICool-Conditioning_LIBD_11102022.pdf

## Slide 18
Chart: Temperature (°C)
| Ring#1 | Ring#2 | Ring#3 | Ring#4 | Ring#5 | Ring#6 | Ring#7 | Ring#8 | Ring#9 | Yoke#1 | Yoke#2 | Yoke#3 | Yoke#4 | Yoke#5 | Yoke#6 | Yoke#7 | Yoke#8 | Yoke#9 | Yoke#10
Reference: 117 mm overlap | 41.1808 | 22.5052 | 36.7878 | 12.1324 | 10.1738 | 9.5257 | 11.4007 | 21.0685 | 80.539 | 55.7011 | 18.9771 | 14.8889 | 12.9762 | 13.7528 | 13.957 | 10.6024 | 7.1065 | 5.5027
Modified: 40 mm overlap | 0.70553 | 0.52059 | 5.6483 | 177.5312 | 139.9225 | 44.3284 | 16.1079 | 8.5438 | 5.8769 | 4.245 | 2.7908 | 3.1624 | 3.9376 | 4.3006 | 4.0343 | 2.2334 | 2.0911 | 2.851
117 mm overlap | 352.33 | 355.35 | 356.2 | 354.47 | 355.88 | 358.64 | 362.9 | 376.59 | 376.63 | 267.48 | 244.98 | 219.19 | 202.3 | 189.91 | 179.92 | 169.25 | 158.57 | 149.85 | 144.55
40 mm overlap | 383.48 | 410.33 | 454.33 | 524.34 | 530.65 | 513.94 | 459.28 | 414.41 | 379.7 | 215.92 | 183.95 | 167.03 | 154.12 | 143.36 | 133.63 | 125.01 | 118.1 | 113.51 | 110.71
117 mm overlap with cooled rings | 29.854 | 27.659 | 25.417 | 24.093 | 23.571 | 25.564 | 29.543 | 36.793 | 43.005 | 173.47 | 164.01 | 153.99 | 147.49 | 143.66 | 139.4 | 132.59 | 124.99 | 118.35 | 114.42
40 mm overlap with cooled rings | 15.208 | 15.692 | 17.149 | 18.435 | 18.429 | 17.213 | 15.863 | 15.353 | 15.22 | 41.139 | 41.767 | 42.372 | 42.886 | 43.21 | 43.352 | 43.328 | 43.384 | 43.467 | 43.465
Curie rings | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200
Curie yokes | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125
Decision: Combined solution of reducing the overlap length and installing a cooling system around the rings.
Cooling ferrite rings with reduced overlap length
15/01/2021
Slide Courtesy of L. Vega Cid (PhD thesis defense: 15/1/2021)
Notes: Heat:
Reduction from 616 W to 450W.
Relocation of the power loss from the yokes to the rings, cooled more easily, as not at pulsed high voltage. First yoke is reduced by a factor of 13, while it is increased by a factor of 15 in the hottest ring, Ring#5.
Cooling:
No cooling: This is still a high temperature considering that the power generated has been reduced to 4W. This can be explained by the increased temperature of the rings, higher than 500ºC which causes significant thermal conduction via the alumina tube, and radiation to the yokes.
Cooling: For simplification purposes the cooling was represented in the thermal model by setting the external surface of the rings at 20

## Slide 19
Final proposal
Chart: Temperature (ºC)
 | 364 | 4.2 | 1.9 | 1.3 | 1.4 | 2.1 | 2.4 | 2.2 | 1.5 | 1.1 | 0.9
Without cooling system | 593.66 | 189.97 | 179.6 | 155.75 | 141.64 | 131.11 | 122.55 | 115.65 | 110.19 | 105.95 | 103.13
With cooling system | 79.649 | 46.595 | 43.772 | 43.588 | 43.291 | 43.299 | 43.324 | 43.022 | 42.523 | 41.943 | 41.408
 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125 | 125
 | 250 | 250
15/01/2021
Slide Courtesy of L. Vega Cid (PhD thesis defense: 15/1/2021)