## Slide 1: HOM Mitigation
Dealing with Higher Order Modes in Accelerating Structures
Nicoleta Baboi, DESY
CAS course on 'RF in Accelerators‘ Berlin, Germany
30 June 2023

## Slide 2: Contents
1. Introduction
2. Avoid HOMs
3. Compensate HOM effects
4. Uses of HOMs
5. Summary

## Slide 3: Contents
1. Introduction
2. Avoid HOMs
3. Compensate HOM effects
4. Uses of HOMs
5. Summary
  Wakefields
  HOMs
  Issues due to HOMs

## Slide 4: 1. Intro: What do you know about HOMs?
?
From this school only!

## Slide 5: 1. Intro: Wakefields
Courtesy of S.A. Udongwo
Brief reminder
Wake: definition from Merriam-Webster (https://www.merriam-webster.com/dictionary/wake) (among other meanings)
  1: the track left by a moving body (such as a ship) in a fluid (such as water); broadly: a track or path left
  2: aftermath (the period immediately following a usually ruinous event)
In an accelerator
  1: Electromagnetic “track” left behind by the beam
  2: “Usually ruinous”? → can be → one has to know the possible danger in order to avoid it
   Know your wakefields

## Slide 6: 1. Intro: Wakefields
Different types:
  Geometrical, resistive wall, rugosity
  Longitudinal or transverse
  Short or long range
Short-range wakefields:
  effects within the bunch: increase in energy spread, emittance
  Often treated in time domain
Long-range wakefields:
  effects from bunch to bunch: increase of multi-bunch energy spread or emittance
  Usually treated in frequency domain → HOMs
Brief reminder (2)
This lecture
  Long-range wakes/multi-bunch effects
  Geometrical wakes
  In accelerating structures
W. Barletta, USPAS 2010
Single bunch beam breakup (“banana” effect)
see lecture on “Impedances and wakefields” by Andrea Mostacci
and many others!

## Slide 7: 1. Intro: Wakefields
Beam breakup observed at SLAC 1966
Found to be due to the beam interaction with one dipole mode
Why worry with long-range wakes?
pulse cut for currents above some threshold
R.B. Neal (ed.), The Stanford two mile accelerator, 1968

## Slide 8: 1. Intro: Higher Order Modes
Longitudinal wakefields can be described as a sum of HOMs for cylindrically symmetric structures
Longitudinal loss factor: (V/pC) or equivalent R/Q factor (linac definition):
  → Strength of interaction between beam and mode → Given only by geometry
    s: distance behind the excitation particle
    Un: energy stored in the mode
    Vn: voltage seen by the particle
Brief reminder: Longitudinal long-range wakefields
n = mode count
http://spiff.rit.edu/classes/phys283/lectures/damped/damped.html

## Slide 9: 1. Intro: Higher Order Modes
The quality factor gives the decay time
→ The material of the structure gives the intrinsic Q0 of a mode
Additional components (ports) can also damp the HOMs → Qext
Brief reminder: Longitudinal long-range wakefields (2)
http://spiff.rit.edu/classes/phys283/lectures/damped/damped.html

## Slide 10: 1. Intro: Higher Order Modes
Transverse wakes: strongest contribution is usually given by dipole modes
  (transverse dipole wake)
Transverse dipole kick factor:
        (V/pC/mm2)
        (normalized to beam offset squared, sometimes also to the structure length)
     It is enough to calculate the longitudinal loss factor (orR/Q) (Panofsky-Wenzel theorem)
Brief reminder: Transverse long-range wakefields

## Slide 11: 1. Intro: Higher Order Modes
Resonant frequency
Loss factor or equivalent
    ;
Quality factor:
    ;
Field distribution, polarization etc.
Know your HOMs!
Brief reminder: Characteristics of resonant modes
wn
Dwn
https://en.wikipedia.org/wiki/Resonance
http://spiff.rit.edu/classes/phys283/lectures/damped/damped.html
Notes: Q0 vs. Qext!!
Dipoles, quads etc. -> always in pairs (polarizations)

## Slide 12: 1. Intro: Higher Order Modes
f (GHz)
Beam excited spectrum
M. Dehler, IBIC2013, WEBL3
J. Wei, HOMSC2018
X-band structure at the Swiss-FEL
TESLA cavity at FLASH/European XFEL
Brief reminder: HOM spectra (examples)
DESY
Notes: Show some mode geometries (TM010, TM110, TE111 etc.)

## Slide 13: 1. Intro: Higher Order Modes
J. Wei, FEL Seminar, DESY, 20.08.2019
TESLA cavity
TE111
Monopole modes:
  Always excited
Dipole, quadrupole modes etc.
  Excited only by off-axis beams
  Come in pairs (polarizations) with equal frequencies for circularly symmetric structures
Zoom into measured spectrum (dipole mode)
  Frequency split due to asymmetries
  Polarization not always horizontal and vertical
Brief reminder: Dipole modes
Notes: Show some mode geometries (TM010, TM110, TE111 etc.)

## Slide 14: 1. Intro: Issues due to HOMs
C. Bohn, K. Ng, LINAC 2000
Bunch offset
Transversely: increase in multi-bunch emittance
HOM effects on the beam
Longitudinally: increase in multi bunch energy spread
Chen Xu, AAC 2016
Worst effects at low energies
Extreme case: beam breakup

## Slide 15: 1. Intro: Issues due to HOMs
Power damped into the accelerating structures or other components
BESSY VSR: HOM power estimated: of the order of 1 kW propagating out of the cold string; tens of W in each HOM load
Further HOM effects
A. Tsakanian, IPAC2018, WEPML048
BESSY VSR cold string

## Slide 16: 1. Intro: HOM Mitigation
Avoid them
Compensate their effects
Use them
Ways to deal with HOMs
Notes: We restrict here mainly to long range effects, from bunch to bunch

## Slide 17: Contents
1. Introduction
2. Avoid HOMs
3. Compensate HOM effects
4. Uses of HOMs
5. Summary
Accelerating Structure Design
Accelerator Design

## Slide 18: 2. Avoid HOMs: Structure Design
Optimize the cell geometry for low loss factors for HOMs, while aiming at high value for the accelerating mode
  Remember: the loss factor depends only on the geometry
For multi-cell structures pay particular attention to the quasi synchronous modes
Geometry
Dispersion diagram of a TESLA cavity
(single cell simulation with periodic boundaries)
fundamental band
1st dipole band
2nd dipole band
accelerating mode
“light line” (vph = c)
Courtesy of S.A. Udongwo
Notes: Basically what you want to maximize for the main mode, you want to minimize for the HOMs: lower R/Q, lower Q

## Slide 19: 2. Avoid HOMs: Structure Design
Avoid to have HOMs with frequency matching a bunch harmonics
  That would give a resonant amplification along bunch train
Detune cells along (long) structure
  Vary cell dimensions along a NC structure  overall HOM effects decohere
Geometry (2)
R.M. Jones, CAS 2010
Interleaving of cell frequencies of a structure for CLIC

## Slide 20: 2. Avoid HOMs: Structure Design
Choose material of the cavity walls for low HOM quality factors Q0.
However this is decided by the purpose of the cavity: choice of technology, type of beam to be accelerated, etc.
This determines the Q0 of the HOMs
Material

## Slide 21: 2. Avoid HOMs: Structure Design
Add something to extract HOM fields, but leave accelerating fields untouched
  if
How much damping is enough?
Requirement: from BBU models or beam dynamics calculations
  e.g.
  lecture on “Longitudinal instabilities & Intensity effects” by Elena Shaposhnikova
  W. Lou et al., PRAB-ST 22, 112801 (2019)
  N. Baboi, EPAC2000, THP3B05
HOM damping: Requirement

## Slide 22: 2. Avoid HOMs: Structure Design
Add ports in each cell: waveguides, couplers
Notch filter at the accelerating frequency
  Particularly good for trapped modes in detuned structures
R.M. Jones, CAS 2010
Damped Detuned Structure
HOM damping in each cell
T. Shintake, PAC’95
HOM-free linear accelerating structure using choke mode cavity

## Slide 23: 2. Avoid HOMs: Structure Design
Add ports at the end of the accelerating structure: waveguides, couplers
Notch filter at the accelerating frequency
HOM damping at end of structure
HL-LHC RFD HOM coupler
E. Montesinos, SRF2021
Q0 and Qext
S. Glukhov, PhD thesis, TU Darmstadt, 2022
TESLA cavity used in MESA
HOM couplers

## Slide 24: 2. Avoid HOMs: Structure Design
Damping materials: HOM absorbers in the beam pipe
The accelerating frequency is below the cut off of the beam pipe
HOM damping in the beam pipe
A. Tsakanian, IPAC2018, WEPML048
BESSY VSR cold string
R. Rimmer, eeFACT2022, WEXAS0101
591 MHz 1-cell SRF cavity at BNL
HOM absorbers

## Slide 25: 2. Avoid HOMs: Accelerator design
Design optics such that the HOM effects are not dramatic
  E.g. Recirculation Arcs Lattice Optimization in ERLs
  Add non-linear elements etc.
Choose bunch frequency (or design accelerator) such that the strongest HOMs are not at bunch multipoles, so that they do not add up coherently
  Often not a real option
Accelerator design
S. Glukhov, PhD thesis, TU Darmstadt, 2022

## Slide 26: 2. Avoid HOMs: Accelerator design
Make 2 or more slightly different designs (classes) for the accelerating structure such that the long-range wakefields do not add up coherently from structure to structure
Structure interleaving
N. Joshi, EuCARD-2 Meeting, 2017
Interleaving for CLIC structures

## Slide 27: Contents
1. Introduction
2. Avoid HOMs
3. Compensate HOM effects
4. Uses of HOMs
5. Summary
Fast Feedbacks
Beam Alignment
Cavity detuning and retuning

## Slide 28: 3. Compensate HOMs: Fast Feedbacks
Longitudinal HOMs induce a variation of the bunch energy, and therefore the bunch arrival time (or beam phase)
  Measure beam arrival time, energy etc. → feedback to LLRF
Transverse HOMs induce a spread in the bunch orbit (multi-bunch emittance growth)
  Fast orbit feedback
Compensation of spread in bunch arrival time and beam offset
Beam Monitor
LLRF Controller
Accelerating Cavity
V. Schlott, EPAC 2006, THPCH096

## Slide 29: 3. Compensate HOMs: Beam Alignment
Transverse effects mainly from dipole modes
The dipole fields depend only on the offset of the exciting bunch
 Monitor dipole modes through couplers, and align the beam to minimize their strength
Beam alignment to avoid transverse HOM excitation
Wakefield monitors
beam
Dedicated alignment monitors in a X-band structure
M. Dehler, PRST-AB 12, 062001 (2009)
Beam offset [mm]
Amplitude of dipole mode signal versus exciting bunch offset for a TESLA cavity
N. Baboi, HOMSC2016

## Slide 30: 3. Compensate HOMs: Retuning
It may happen that one HOM unluckily hits a beam spectrum line
   Resonant amplification of HOM field
Detune and retune the operating mode back to the resonance
  HOMs move because of small inelastic deformation
Cavity detuning and retuning
N. Solyak, IPAC10, TUPEA020
Detuning and retuning a 1.3 GHz ILC-type cavity

## Slide 31: Contents
1. Introduction
2. Avoid HOMs
3. Compensate HOM effects
4. Uses of HOMs
5. Summary
Diagnostic of Accelerating Structures
Diagnostic of Beam

## Slide 32: 4. Use HOMs
Monitor HOMs through damping couplers
  Measure cell alignment
    Due to varying cell dimensions along detuned structure, the modes are localized in part of it giving information on different cells
  Monitor SC cavity alignment in cryo-module
    Monitor dipole mode
Diagnostic of accelerating structures
S. Molloy, Meas. Sci. Technol. 18, 2314 (2007)
Transverse offset of SC TESLA cavities in cryo-module
Wakefield monitors
X-band rf structure with integrated alignment monitors
M. Dehler, PRST-AB 12, 062001 (2009)

## Slide 33: 4. Use HOMs
Beam offset [mm]
Monitor selected HOMs (e.g. with downconverting electronics)
Diagnostic of beam
BP filter
Mixer
ADC
HOM signal
Phase difference
accelerating RF field
beam excited HOM
N. Baboi, HOMSC2016
RF phase measurement wrt to beam
Beam position measurement with dipole modes (like with a cavity BPM)

## Slide 34: Contents
1. Introduction
2. Avoid HOMs
3. Compensate HOM effects
4. Uses of HOMs
5. Summary

## Slide 35: Summary
HOMs can decrease the beam quality to an unacceptable degree
Avoid HOM excitation
  Design of accelerating structure
  Design of accelerator
Compensate excited HOMs
  Feedbacks
  Beam alignment
  Detune and retune cavity
Use the excited HOMs
  Measure the cell or cavity alignment
  Measure beam offset, beam phase
HOM mitigation
Only a selection of methods was shown
There are many more methods to mitigate HOMs
Know your HOMs!

## Slide 36
Nicoleta Baboi
Machine Diagnostics and Instrumentation MDI
nicoleta.baboi@desy.de
+49 40 8998 3052
Thank you!