Emittance tuning bumps for CLIC ML at 380 GeV
1. Andrii Pastushenko
2. 08.11.2022

---
Outline
Introduction
CLIC performance goals
ML current performance and motivation
Emittance tuning knobs construction
Knobs definition
Identifying the principle directions
Orthogonal knobs construction
Tuning simulations
Conclusions

---
Introduction
CLIC schematic layout

---
Introduction
Performance goals
Each section has design emittance value, that includes the growths coming from static and dynamic errors.
Perfect machine
Static imperfections
Static and dynamic imperfections
\mathcal{L} = 4.3\times10\textsuperscript{34}\text{cm}^{-2}\text{s}^{-1}
\mathcal{L} = 2.3\times10\textsuperscript{34}\text{cm}^{-2}\text{s}^{-1}
\mathcal{L} = 1.55\times10\textsuperscript{34}\text{cm}^{-2}\text{s}^{-1}

---
Introduction
Performance goals
The vertical budgets are the similar to the 3 TeV design. Typically, it is easier to meet the budget for 380 GeV.
Integrated simulations starting from the exit of the DR to the IP including static errors give the average luminosity of 1:
With ground motion included:
90% of the machines reach the lumi of:
1 C. Gohil, et. al. “Luminosity performance of the Compact Linear Collider at 380 GeV with static and dynamic imperfections”, 2020,PhysRevAccelBeams.23.101001
\mathcal{L} = 2.35 \times 10\textsuperscript{34} \text{cm}^{-2} \text{s}^{-1}
\mathcal{L} = (2.8 \pm 0.3) \times 10\textsuperscript{34} \text{cm}^{-2} \text{s}^{-1}
\mathcal{L} = (3.0 \pm 0.4) \times 10\textsuperscript{34} \text{cm}^{-2} \text{s}^{-1}

---
ML current performance and motivation
Current design foresees 10 nm vertical normalized emittance with 5 + 5 nm budget for static and dynamic imperfections.
The budget is respected with the usage of 1-2-1 correction, Dispersion Free Steering, and RF structures alignments.
Emittance tuning bumps/knobs are designed to control the residual emittance → potential to reduce the budget dedicated for the static imperfections → higher lumi at the IP.

---
ML current performance and motivation
Imperfections overview
Accelerating elements, quadrupoles, BPMs, wake monitors

---
Prealignment and BBA techniques
Beam-based alignment
Current ML alignment routines consist of:
One-to-one correction
The quadrupoles are moved to steer the beam through the BPM centers.
Dispersion free steering
The quadrupoles are moved to minimize the orbit and dispersion simultaniously.
Accelerating structures realignment with the wake monitors
The girders’ supports are moved to minimize the wake monitors reading in the structures.

---
Prealignment and BBA techniques
Simulation of the BBA
Summary (results from 2 are well reproduced):
100% of the machines < 4 nm
95% of the machines < 2 nm
Rms of 0.98 nm
Rms emittance growth:
1-2-1: 235.09 nm
DFS: 25.84 nm
RF align.: 0.98 nm
2 N. Blaskovic Kraljevic, D. Schulte, “Beam-based beamline element alignment for the main linac of the 380 GeV stage of CLIC”, IPAC 2019, http://jacow.org/ipac2019/papers/mopmp018.pdf

---
Knobs definition
The term knob is used for the set of changes that can be applied to the lattice (offsets, ..) to modify it.
The remaining emittance growth after beam based alignment is due to the wakefields of the misaligned accelerating structures.
The key idea is to add the vertical displacement to compensate the unwanted wakefield kicks.

---
Identifying the principle directions
Identifying the remaining emittance growth after the BBA
We simulate the BBA (1-2-1 → DFS → RF align.) for 1000 machines with different error seeds and evaluate the macroparticles coordinates and angles at the ML exit.
We use the macroparticle model of the beam.
For each seed we calculate the corresponding vector in the normalized phase space. The length of that vector is the emittance growth 3.
For the calculations we use the bunch of 11 slices with 5 macroparticles per slice (55 total).
The tracking is done with Placet.
To identify the key directions in the normalized phase space that statistically contribute to the emittance growth the most, we use Principal Component Analysis (PCA).
3 P. Eliasson, D. Schulte, “Design of main linac emittance tuning bumps for the Compact Linear Collider and the International Linear Collider”, 2008, 10.1103/PhysRevSTAB.11.011002
\Delta \epsilon^2_y

---
Identifying the principle directions
PCA
Example of the PCA applied to the data.
For the data analysis further on, utilizying Python modules, such as Pandas, Sklearn, and Numpy.
\epsilon^2_{y} - \epsilon^2_{y, 0} = \langle Y | Y \rangle

---
Identifying the principle directions
PCA
Each principal direction is characterized with its variance.
..or it can be transformed to the emittance growth.
\epsilon^2_{y} - \epsilon^2_{y, 0} = \langle Y | Y \rangle

---
Identifying the principle directions
PCA
Based on this data we build the function of the residual emittance growth as the function of the number of the principle directions we correct.
For example:
We correct 0 directions → ~0.98nm (what we have after rf alignment)
5 directions → ~0.3 nm
10 directions → ~0.08 nm
..
For the further analysis, 10 principle directions was taken.

---
Orthogonal knobs construction
To correct the coordinates along the principal directions we want to offset the girder with the accelerating structure on it. (We used all the girders/quads in the lattice)
Also, we want to adjust the quads to compensate for the orbit change.
We build the response matrix as
We want to find the sets of the girders/quads offsets that form the basis that corresponds to the principal directions. We will call these sets the tuning knobs.
The solution are the columns of . - is the pseudo-inverse of the response matrix. - is the target value (set to 1 nm).
\lambda \hat{R}^{\dagger}
\hat{R}^{\dagger}
\lambda
R_{ij} = \frac{\Delta Y_{p,i}}{\Delta y_{offset, j}}

---
Orthogonal knobs construction
When we apply the knob, the function is quadratic:
For small changes, could be also aproximated as
\epsilon^2_{y} - \epsilon^2_{y, 0} = \langle Y_p | Y_p \rangle
\epsilon_{y} \propto \langle Y_p | Y_p \rangle

---
Tuning simulations
We perform the knob scans after the RF alignment
Each knob is scanned once.
After the knobs tuning:
100% of the machines - < 0.8 nm
95% of the machines - < 0.5 nm
RMS 0.12 nm

---
Tuning simulations
Structures displacements
Fast convergence, but large structure displacements.
Unacceptably large structure displacements, especially in the first 150 elements

---
Tuning simulations
Things to address
Reduce the number of the structures involved. Some structures are uninvolved in the tuning.
Limit the structures offsets.
We constructed the knobs on the girders vertical offsets. Instead, the movement of the articulation points should be investigated.

---
Tuning simulations
without RF alignment
Similarly we built the set of the knobs to be used after the DFS in the event some/all wake monitors fail to work.
With 10 knobs, 95% of the machines reached < 3.5 nm.
With larger number of knobs, it is possible to reduce that value and even reduce the budget.

---
Conclusions
The tuning bumps are promising to reduce the emittance budget for static errors.
The realistic value of the budget to be evaluated taking into account the issues like large structures offsets,
The tuning bumps constructed this way can also be used to reduce the emittance in the case of some/all wake monitors failure.

---
Thanks for your attention!

---
Back-up slides

---
Macroparticle model of the beam
Macroparticle beam
Particle beam
The beam is represented by a set of macroparticles.
The beam is cut longitudinaly into slices with 1 or more macroparticles in it to represent the energy distribution.
Each macroparticle has typical set of coordinates as normal particle, but also the variations such as , , etc., and also the weight.
\sigma_{yy}
\sigma_{yy'}

---
Macroparticle model of the beam
Beam emittance
In the macroparticle model of the beam, vertical emittance writes as:
M is the number of macroparticles, (yi, y’i) are coordinates of i-th macroparticle, and , , are the variances, when the all macroparticles are centered. +
Dropping the 4th order terms in this eq:
with
Each seed is represented by the vector composed of coordinates and angles of M macroparticles [y1, y2, y3, .. y’1, y’2, .. ]T.
\epsilon_y^2 = \gamma^2[(\sum_{i, j = 1}^Mr_{i, j}y_i y_j + \widetilde{\sigma}_{yy}) (\sum_{i, j = 1}^Mr_{i, j}y'_i y'_j + \widetilde{\sigma}_{y'y'})- (\sum_{i, j = 1}^Mr_{i, j}y_i y'_j + \widetilde{\sigma}_{yy'})^2]
\widetilde{\sigma}_{yy}
\widetilde{\sigma}_{yy'}
\widetilde{\sigma}_{y'y'}
r_{ij} = w_i(\delta_{ij} - w_j)
\epsilon^2_{y} - \epsilon^2_{y, 0} = \gamma^2 \begin{bmatrix} \langle y| & \langle y'|\\ \end{bmatrix} \hat{M} \begin{bmatrix} |y \rangle \\ |y' \rangle \end{bmatrix}
\hat{M} = \begin{bmatrix} \widetilde{\sigma}_{y', y'} \hat{R} & -\widetilde{\sigma}_{y, y'}\hat{R} \\ -\widetilde{\sigma}_{y, y'} \hat{R} & \widetilde{\sigma}_{y, y} \hat{R}\\ \end{bmatrix}

---
Macroparticle model of the beam
Beam emittance
Matrix is real, symmetric, and positive definite → applying Cholesky decomposition:
We have the normalized set of coordinates , so the emittance growth is:
Further, in the data analysis, we will be using the normalized coordinates.
\gamma^2 \hat{M} = \hat{L}\hat{L}^T
| Y \rangle
\epsilon^2_{y} - \epsilon^2_{y, 0} = \langle Y | Y \rangle
\hat{M}

---
Macroparticle model of the beam
Emittance for several configurations of number of slices and macroparticles

---
Macroparticle model of the beam
Beam emittance
Emittance contributions:
DFS
RF align.