## Slide 1: Forward Physics Facility (FPF) ARUP Introduction Meeting
Kincső Pál, John Osborne SCE-DOD-FS
Date: 21/10/2022

## Slide 2: Outline
Proposed location
Proposed Design
Scope and Aims of the CE study

## Slide 3: Forward Physics Facility Proposed location
3
Location approx. 617m from ATLAS interaction point (IP1), on the French CERN site, 10m away from the LHC tunnel
ATLAS IP1
LHC
New facility

## Slide 4: Forward Physics Facility Proposed Design
4
An 88m deep access shaft with a 9.1m internal diameter
A 65m long and 9.65m wide experimental cavern
  Experiments centralized on the line of sight, 1.5m above the floor
  Floor is parallel to LoS, 1.25% fall
  Trench under the LAr detector to catch any escaped cold gas
  Safety corridor used as an emergency escape route

## Slide 5: Forward Physics Facility Proposed Design
5
Proposed surface buildings
  Access building
  Electrical building
  Cooling & Ventilation building
Site used as a spoil disposal area for previous CERN projects
Ground levels between 453-455m, approx. 7 m above the surrounding area

## Slide 6: Scope and Aims of the CE study
6
Task 1: Civil Engineering Cost Estimate Review
  Delivery date: end of 2022
  Carry out a cost estimation review of the proposed CE cost (approx. 31m CHF) and provide comments or suggestions
Task 2: Interpretation of the soil investigations
  Delivery date: end of April 2023

## Slide 7: Site Investigation Works
7
New core will be drilled the full depth of the proposed shaft early in 2023
Position marked

## Slide 8
Thank you!